## Slide 1: SUBELEMENT E3
RADIO WAVE PROPAGATION
[3 Exam Questions - 3 Groups]
Notes: Extra Question Pool 2016. The Western Washington Ham Training Team makes these slides available to teach Amateur Technician Radio Licensing Classes. Daniel Stevens KL7WM, Training Coordinator, Howard Swartz, W7HS, Slide master, Dustin Lomax, KF7FK, Leading Instructor, LW Abel, K7LWA, Enthusiasm Leader.

## Slide 2
E3A Electronmagnetic waves;:Earth-Moon-Earth communications; meteor scatter; microwave troprospheric and scatter propagation; aurora propgation
E3B Propagation and technique, trans-equatorial; long path; gray-line; multi-path propagation
E3C Propagation and technique, Aurora propagation; selective fading; radio-path horizon; take-off angle over flat or sloping terrain; effects of ground on propagation; less common propagation modes

## Slide 3: E3A01 What is the approximate maximum separation measured along the surface of the Earth between two stations communicating by Moon bounce?
A. 500 miles, if the Moon is at perigee
B. 2000 miles, if the Moon is at apogee
C. 5000 miles, if the Moon is at perigee
D. 12,000 miles, if the Moon is visible by both stations

## Slide 4: E3A01 What is the approximate maximum separation measured along the surface of the Earth between two stations communicating by Moon bounce?
A. 500 miles, if the Moon is at perigee
B. 2000 miles, if the Moon is at apogee
C. 5000 miles, if the Moon is at perigee
D. 12,000 miles, if the Moon is visible by both stations

## Slide 5: E3A02 What characterizes libration fading of an EME signal?
A. A slow change in the pitch of the CW signal
B. A fluttery irregular fading
C. A gradual loss of signal as the Sun rises
D. The returning echo is several Hertz lower in frequency than the transmitted signal

## Slide 6: E3A02 What characterizes libration fading of an EME signal?
A. A slow change in the pitch of the CW signal
B. A fluttery irregular fading
C. A gradual loss of signal as the Sun rises
D. The returning echo is several Hertz lower in frequency than the transmitted signal

## Slide 7: E3A03 When scheduling EME contacts, which of these conditions will generally result in the least path loss?
A. When the Moon is at perigee
B. When the Moon is full
C. When the Moon is at apogee
D. When the MUF is above 30 MHz

## Slide 8: E3A03 When scheduling EME contacts, which of these conditions will generally result in the least path loss?
A. When the Moon is at perigee
B. When the Moon is full
C. When the Moon is at apogee
D. When the MUF is above 30 MHz

## Slide 9: E3A04 What do Hepburn maps predict?
A. Sporadic E propagation
B. Locations of auroral reflecting zones
C. Likelihood of rain-scatter along cold or warm fronts
D. Probability of tropospheric propagation

## Slide 10: E3A04 What do Hepburn maps predict?
A. Sporadic E propagation
B. Locations of auroral reflecting zones
C. Likelihood of rain-scatter along cold or warm fronts
D. Probability of tropospheric propagation

## Slide 11: E3A05 Tropospheric propagation of microwave signals often occurs along what weather related structure?
A. Gray-line
B. Lightning discharges
C. Warm and cold fronts
D. Sprites and jets

## Slide 12: E3A05 Tropospheric propagation of microwave signals often occurs along what weather related structure?
A. Gray-line
B. Lightning discharges
C. Warm and cold fronts
D. Sprites and jets

## Slide 13: E3A06 Which of the following is required for microwave propagation via rain scatter?
A. Rain droplets must be electrically charged
B. Rain droplets must be within the E layer
C. The rain must be within radio range of both stations
D. All of these choices are correct

## Slide 14: E3A06 Which of the following is required for microwave propagation via rain scatter?
A. Rain droplets must be electrically charged
B. Rain droplets must be within the E layer
C. The rain must be within radio range of both stations
D. All of these choices are correct

## Slide 15: E3A07 Atmospheric ducts capable of propagating microwave signals often form over what geographic feature?
A. Mountain ranges
B. Forests
C. Bodies of water
D. Urban areas

## Slide 16: E3A07 Atmospheric ducts capable of propagating microwave signals often form over what geographic feature?
A. Mountain ranges
B. Forests
C. Bodies of water
D. Urban areas

## Slide 17: E3A08 When a meteor strikes the Earth's atmosphere, a cylindrical region of free electrons is formed at what layer of the ionosphere?
A. The E layer
B. The F1 layer
C. The F2 layer
D. The D layer

## Slide 18: E3A08 When a meteor strikes the Earth's atmosphere, a cylindrical region of free electrons is formed at what layer of the ionosphere?
A. The E layer
B. The F1 layer
C. The F2 layer
D. The D layer

## Slide 19: E3A09 Which of the following frequency range is most suited for meteor scatter communications?
A. 1.8 MHz - 1.9 MHz
B. 10 MHz - 14 MHz
C. 28 MHz - 148 MHz
D. 220 MHz - 450 MHz

## Slide 20: E3A09 Which of the following frequency range is most suited for meteor scatter communications?
A. 1.8 MHz- 1.9 MHz
B. 10 MHz - 14 MHz
C. 28 MHz - 148 MHz
D. 220 MHz - 450 MHz

## Slide 21: E3A10 Which type of atmospheric structure can create a path for microwave propagation?
A. The jet stream
B. Temperature inversion
C. Wind shear
D. Dust devil

## Slide 22: E3A10 Which type of atmospheric structure can create a path for microwave propagation?
A. The jet stream
B. Temperature inversion
C. Wind shear
D. Dust devil

## Slide 23: E3A11 What is a typical range for tropospheric propagation of microwave signals?
A. 10 miles to 50 miles
B. 100 miles to 300 miles
C. 1200 miles
D. 2500 miles

## Slide 24: E3A11 What is a typical range for tropospheric propagation of microwave signals?
A. 10 miles to 50 miles
B. 100 miles to 300 miles
C. 1200 miles
D. 2500 miles

## Slide 25: E3A12 What is the cause of auroral activity?
A. The interaction in the F2 layer between the solar wind and the Van Allen belt
B. A low sunspot level combined with tropospheric ducting
C. The interaction in the E layer of charged particles from the Sun with the Earth’s magnetic field
D. Meteor showers concentrated in the extreme northern and southern latitudes

## Slide 26: E3A12 What is the cause of auroral activity?
A. The interaction in the F2 layer between the solar wind and the Van Allen belt
B. A low sunspot level combined with tropospheric ducting
C. The interaction in the E layer of charged particles from the Sun with the Earth’s magnetic field
D. Meteor showers concentrated in the extreme northern and southern latitudes

## Slide 27: E3A13 Which emission mode is best for aurora propagation?
A. CW
B. SSB
C. FM
D. RTTY

## Slide 28: E3A13 Which emission mode is best for aurora propagation?
A. CW
B. SSB
C. FM
D. RTTY

## Slide 29: E3A14 From the contiguous 48 states, in which approximate direction should an antenna be pointed to take maximum advantage of aurora propagation?
A. South
B. North
C. East
D. West

## Slide 30: E3A14 From the contiguous 48 states, in which approximate direction should an antenna be pointed to take maximum advantage of aurora propagation?
A. South
B. North
C. East
D. West

## Slide 31: E3A15 What is an electromagnetic wave?
A. A wave of alternating current, in the core of an electromagnet
B. A wave consisting of two electric fields at parallel right angles to each other
C. A wave consisting of an electric field and a magnetic field oscillating at right angles to each other
D. A wave consisting of two magnetic fields at right angles to each other

## Slide 32: E3A15 What is an electromagnetic wave?
A. A wave of alternating current, in the core of an electromagnet
B. A wave consisting of two electric fields at parallel right angles to each other
C. A wave consisting of an electric field and a magnetic field oscillating at right angles to each other
D. A wave consisting of two magnetic fields at right angles to each other

## Slide 33: E3A16 Which of the following best describes electromagnetic waves traveling in free space?
A. Electric and magnetic fields become aligned as they travel
B. The energy propagates through a medium with a high refractive index
C. The waves are reflected by the ionosphere and return to their source
D. Changing electric and magnetic fields propagate the energy

## Slide 34: E3A16 Which of the following best describes electromagnetic waves traveling in free space?
A. Electric and magnetic fields become aligned as they travel
B. The energy propagates through a medium with a high refractive index
C. The waves are reflected by the ionosphere and return to their source
D. Changing electric and magnetic fields propagate the energy

## Slide 35: E3A17 What is meant by circularly polarized electromagnetic waves?
A. Waves with an electric field bent into a circular shape
B. Waves with a rotating electric field
C. Waves that circle the Earth
D. Waves produced by a loop antenna

## Slide 36: E3A17 What is meant by circularly polarized electromagnetic waves?
A. Waves with an electric field bent into a circular shape
B. Waves with a rotating electric field
C. Waves that circle the Earth
D. Waves produced by a loop antenna

## Slide 37: E3B Propagation and technique
Transequatorial propagation; long path; gray-line; multi-path; ordinary and extraordinary waves; chordal hop, sporadic E mechanisms

## Slide 38: E3B01 What is transequatorial propagation?
A. Propagation between two mid-latitude points at approximately the same distance north and south of the magnetic equator
B. Propagation between any two points located on the magnetic equator
C. Propagation between two continents by way of ducts along the magnetic equator
D. Propagation between two stations at the same latitude

## Slide 39: E3B01 What is transequatorial propagation?
A. Propagation between two mid-latitude points at approximately the same distance north and south of the magnetic equator
B. Propagation between any two points located on the magnetic equator
C. Propagation between two continents by way of ducts along the magnetic equator
D. Propagation between two stations at the same latitude

## Slide 40: E3B02 What is the approximate maximum range for signals using transequatorial propagation?
A. 1000 miles
B. 2500 miles
C. 5000 miles
D. 7500 miles

## Slide 41: E3B02 What is the approximate maximum range for signals using transequatorial propagation?
A. 1000 miles
B. 2500 miles
C. 5000 miles
D. 7500 miles

## Slide 42: E3B03 What is the best time of day for transequatorial propagation?
A. Morning
B. Noon
C. Afternoon or early evening
D. Late at night

## Slide 43: E3B03 What is the best time of day for transequatorial propagation?
A. Morning
B. Noon
C. Afternoon or early evening
D. Late at night

## Slide 44: E3B04 What is meant by the terms extraordinary and ordinary waves?
A. Extraordinary waves describe rare long skip propagation compared to ordinary waves which travel shorter distances
B. Independent waves created in the ionosphere that are elliptically polarized
C. Long path and short path waves
D. Refracted rays and reflected waves

## Slide 45: E3B04 What is meant by the terms extraordinary and ordinary waves?
A. Extraordinary waves describe rare long skip propagation compared to ordinary waves which travel shorter distances
B. Independent waves created in the ionosphere that are elliptically polarized
C. Long path and short path waves
D. Refracted rays and reflected waves

## Slide 46: E3B05 Which amateur bands typically support long-path propagation?
A. 160 metersto 40 meters
B. 30 meters to 10 meters
C. 160 meters to 10 meters
D. 6 meters to 2 meters

## Slide 47: E3B05 Which amateur bands typically support long-path propagation?
A. 160 meters to 40 meters
B. 30 meters to 10 meters
C. 160 to 10 meters
D. 6 meters to 2 meters

## Slide 48: E3B06 Which of the following amateur bands most frequently provides long-path propagation?
A. 80 meters
B. 20 meters
C. 10 meters
D. 6 meters

## Slide 49: E3B06 Which of the following amateur bands most frequently provides long-path propagation?
A. 80 meters
B. 20 meters
C. 10 meters
D. 6 meters

## Slide 50: E3B07 Which of the following could account for hearing an echo on the received signal of a distant station?
A. High D layer absorption
B. Meteor scatter
C. Transmit frequency is higher than the MUF
D. Receipt of a signal by more than one path

## Slide 51: E3B07 Which of the following could account for hearing an echo on the received signal of a distant station?
A. High D layer absorption
B. Meteor scatter
C. Transmit frequency is higher than the MUF
D. Receipt of a signal by more than one path

## Slide 52: E3B08 What type of HF propagation is probably occurring if radio signals travel along the terminator between daylight and darkness?
A. Transequatorial
B. Sporadic-E
C. Long-path
D. Gray-line

## Slide 53: E3B08 What type of HF propagation is probably occurring if radio signals travel along the terminator between daylight and darkness?
A. Transequatorial
B. Sporadic-E
C. Long-path
D. Gray-line

## Slide 54: E3B09 At what time of year is Sporadic E propagation most likely to occur?
A. Around the solstices, especially the summer solstice
B. Around the solstices, especially the winter solstice
C. Around the equinoxes, especially the spring equinox
D. Around the equinoxes, especially the fall equinox

## Slide 55: E3B09 At what time of year is Sporadic E propagation most likely to occur?
A. Around the solstices, especially the summer solstice
B. Around the solstices, especially the winter solstice
C. Around the equinoxes, especially the spring equinox
D. Around the equinoxes, especially the fall equinox

## Slide 56: E3B10 What is the cause of gray-line propagation?
A. At midday, the Sun super heats directly the ionosphere causing increased refraction of radio waves
B. At twilight and sunrise, D-layer absorption is low while E-layer and F-layer propagation remains high
C. In darkness, solar absorption drops greatly while atmospheric ionization remains steady
D. At mid afternoon, the Sun heats the ionosphere decreasing radio wave refraction and the MUF

## Slide 57: E3B10 What is the cause of gray-line propagation?
A. At midday, the Sun super heats directly the ionosphere causing increased refraction of radio waves
B. At twilight and sunrise, D-layer absorption is low while E-layer and F-layer propagation remains high
C. In darkness, solar absorption drops greatly while atmospheric ionization remains steady
D. At mid afternoon, the Sun heats the ionosphere decreasing radio wave refraction and the MUF

## Slide 58: E3B11 At what time of day is Sporadic-E propagation most likely to occur?
A. Around sunset
B. Around sunrise
C. Early evening
D. Any time

## Slide 59: E3B11 At what time of day is Sporadic-E propagation most likely to occur?
A. Around sunset
B. Around sunrise
C. Early evening
D. Any time

## Slide 60: E3B12 What is the primary characteristic of chordal hop propagation?
A. Propagation away from the great circle bearing between stations
B. Successive ionospheric reflections without an intermediate reflection from the ground
C. Propagation across the geomagnetic equator
D. Signals reflected back toward the transmitting station

## Slide 61: E3B12 What is the primary characteristic of chordal hop propagation?
A. Propagation away from the great circle bearing between stations
B. Successive ionospheric reflections without an intermediate reflection from the ground
C. Propagation across the geomagnetic equator
D. Signals reflected back toward the transmitting station

## Slide 62: E3B13 Why is chordal hop propagation desirable?
A. The signal experiences less loss along the path compared to normal skip propagation
B. The MUF for chordal hop propagation is much lower than for normal skip propagation
C. Atmospheric noise is lower in the direction of chordal hop propagation
D. Signals travel faster along ionospheric chords

## Slide 63: E3B13 Why is chordal hop propagation desirable?
A. The signal experiences less loss along the path compared to normal skip propagation
B. The MUF for chordal hop propagation is much lower than for normal skip propagation
C. Atmospheric noise is lower in the direction of chordal hop propagation
D. Signals travel faster along ionospheric chords

## Slide 64: E3B14 What happens to linearly polarized radio waves that split into ordinary and extraordinary waves in the ionosphere?
A. They are bent toward the magnetic poles
B. Their polarization is randomly modified
C. They become elliptically polarized
D. They become phase-locked
~~

## Slide 65: E3B14 What happens to linearly polarized radio waves that split into ordinary and extraordinary waves in the ionosphere?
A. They are bent toward the magnetic poles
B. Their polarization is randomly modified
C. They become elliptically polarized
D. They become phase-locked
~~

## Slide 66: E3C Propagation
Radio-path horizon; less common propagation modes; propagation prediction techniques and modeling; space weather parameters and amateur radio

## Slide 67: E3C01 What does the term ray tracing describe in regard to radio communications?
A. The process in which an electronic display presents a pattern
B. Modeling a radio wave's path through the ionosphere
C. Determining the radiation pattern from an array of antennas
D. Evaluating high voltage sources for X-Rays

## Slide 68: E3C01 What does the term ray tracing describe in regard to radio communications?
A. The process in which an electronic display presents a pattern
B. Modeling a radio wave's path through the ionosphere
C. Determining the radiation pattern from an array of antennas
D. Evaluating high voltage sources for X-Rays

## Slide 69: E3C02 What is indicated by a rising A or K index?
A. Increasing disruption of the geomagnetic field
B. Decreasing disruption of the geomagnetic field
C. Higher levels of solar UV radiation
D. An increase in the critical frequency

## Slide 70: E3C02 What is indicated by a rising A or K index?
A. Increasing disruption of the geomagnetic field
B. Decreasing disruption of the geomagnetic field
C. Higher levels of solar UV radiation
D. An increase in the critical frequency

## Slide 71: Solar Flare / Sun Spots

## Slide 72: Aurora Borealis

## Slide 73: E3C03 Which of the following signal paths is most likely to experience high levels of absorption when the A index or K index is elevated?
A. Transequatorial propagation
B. Polar paths
C. Sporadic-E
D. NVIS

## Slide 74: E3C03 Which of the following signal paths is most likely to experience high levels of absorption when the A index or K index is elevated?
A. Transequatorial propagation
B. Polar paths
C. Sporadic-E
D. NVIS

## Slide 75: E3C04 What does the value of Bz (B sub Z) represent?
A. Geomagnetic field stability
B. Critical frequency for vertical transmissions
C. Direction and strength of the interplanetary magnetic field
D. Duration of long-delayed echoes

## Slide 76: E3C04 What does the value of Bz (B sub Z) represent?
A. Geomagnetic field stability
B. Critical frequency for vertical transmissions
C. Direction and strength of the interplanetary magnetic field
D. Duration of long-delayed echoes

## Slide 77: E3C05 What orientation of Bz (B sub z) increases the likelihood that incoming particles from the Sun will cause disturbed conditions?
A. Southward
B. Northward
C. Eastward
D. Westward

## Slide 78: E3C05 What orientation of Bz (B sub z) increases the likelihood that incoming particles from the Sun will cause disturbed conditions?
A. Southward
B. Northward
C. Eastward
D. Westward

## Slide 79: E3C06 By how much does the VHF/UHF radio horizon distance exceed the geometric horizon?
A. By approximately 15 percent of the distance
B. By approximately twice he distance
C. By approximately 50 percent of the distance
D. By approximately four times the distance

## Slide 80: E3C06 By how much does the VHF/UHF radio horizon distance exceed the geometric horizon?
A. By approximately 15 percent of the distance
B. By approximately twice the distance
C. By approximately 50 percent of the distance
D. By approximately four times the distance

## Slide 81: E3C07 Which of the following descriptors indicates the greatest solar flare intensity?
A. Class A
B. Class B
C. Class M
D. Class X

## Slide 82: E3C07 Which of the following descriptors indicates the greatest solar flare intensity?
A. Class A
B. Class B
C. Class M
D. Class X

## Slide 83: Radiowave take off pattern

## Slide 84: E3C08 What does the space weather term G5 mean?
A. An extreme geomagnetic storm
B. Very low solar activity
C. Moderate solar wind
D. Waning sunspot numbers

## Slide 85: E3C08 What does the space weather term G5 mean?
A. An extreme geomagnetic storm
B. Very low solar activity
C. Moderate solar wind
D. Waning sunspot numbers

## Slide 86: Pedersen Ray
Paths 4 and 5 shown above are Pedersen rays or high-angle rays. These rays are not refracted sufficiently to return directly
to the earth but don't have a high enough angle to penetrate (like ray 6). They get trapped in the ionosphere often exiting
where there is a big gradient in electron density (at dusk and dawn). The plots below are the result of both high and low
angle rays being present at the same time. An effect that we are normally unaware of!
Given this model, we might reasonably expect to see four components on an oblique path as it fades out: o and x wave from
the low angle path and o and x waves from the high angle path. Each with different Doppler shifts.

## Slide 87: E3C09 How does the intensity of an X3 flare compare to that of an X2 flare?
A. 10 percent greater
B. 50 percent greater
C. Twice as great
D. Four times as great

## Slide 88: E3C09 How does the intensity of an X3 flare compare to that of an X2 flare?
A. 10 percent greater
B. 50 percent greater
C. Twice as great
D. Four times as great

## Slide 89: E3C10 What does the 304A solar parameter measure?
A. The ratio of X-Ray flux to radio flux, correlated to sunspot number
B. UV emissions at 304 angstroms, correlated to solar flux index
C. The solar wind velocity at 304 degrees from the solar equator, correlated to solar activity
D. The solar emission at 304 GHz, correlated to X-Ray flare levels

## Slide 90: E3C10 What does the 304A solar parameter measure?
A. The ratio of X-Ray flux to radio flux, correlated to sunspot number
B. UV emissions at 304 angstroms, correlated to solar flux index
C. The solar wind velocity at 304 degrees from the solar equator, correlated to solar activity
D. The solar emission at 304 GHz, correlated to X-Ray flare levels

## Slide 91: E3C11 What does VOACAP software model?
A. AC voltage and impedance
B. VHF radio propagation
C. HF propagation
D. AC current and impedance

## Slide 92: E3C11 What does VOACAP software model?
A. AC voltage and impedance
B. VHF radio propagation
C. HF propagation
D. AC current and impedance

## Slide 93: E3C12 How does the maximum distance of ground-wave propagation change when the signal frequency is increased?
A. It stays the same
B. It increases
C. It decreases
D. It peaks at roughly 14 MHz

## Slide 94: E3C12 How does the maximum distance of ground-wave propagation change when the signal frequency is increased?
A. It stays the same
B. It increases
C. It decreases
D. It peaks at roughly 14 MHz

## Slide 95: E3C13 What type of polarization is best for ground-wave propagation?
A. Vertical
B. Horizontal
C. Circular
D. Elliptical

## Slide 96: E3C13 What type of polarization is best for ground-wave propagation?
A. Vertical
B. Horizontal
C. Circular
D. Elliptical

## Slide 97: E3C14 Why does the radio-path horizon distance exceed the geometric horizon?
A. E-region skip
B. D-region skip
C. Downward bending due to aurora refraction
D. Downward bending due to density variations in the atmosphere

## Slide 98: E3C14 Why does the radio-path horizon distance exceed the geometric horizon?
A. E-region skip
B. D-region skip
C. Downward bending due to aurora refraction
D. Downward bending due to density variations in the atmosphere

## Slide 99: E3C15 What might a sudden rise in radio background noise indicate?
A. A meteor ping
B. A solar flare has occurred
C. Increased transequatorial propagation likely
D. Long-path propagation is occurring

## Slide 100: E3C15 What might a sudden rise in radio background noise indicate?
A. A meteor ping
B. A solar flare has occurred
C. Increased transequatorial propagation likely
D. Long-path propagation is occurring

## Slide 101: End of SUBELEMENT E3
WAVE PROPAGATION