## Slide 1: SUBELEMENT E6
CIRCUIT COMPONENTS
[6 Exam Questions - 6 Groups]
Notes: Extra Question Pool 2016. The Western Washington Ham Training Team makes these slides available to teach Amateur Technician Radio Licensing Classes. Daniel Stevens KL7WM, Training Coordinator, Howard Swartz, W7HS, Slide master, Dustin Lomax, KF7FK, Leading Instructor, LW Abel, K7LWA, Enthusiasm Leader.

## Slide 2
E6A Semiconductor materials and devices: semiconductor materials germanium, silicon, P-type, N-type; transistor types: NPN, PNP, junction, field-effect transistors: enhancement mode; depletion mode; MOS; CMOS; N-channel; P-channel
E6B Semiconductor diodes
E6C Integrated circuits: TTL digital integrated circuits; CMOS digital integrated circuits; gates
E6D Optical devices and toroids: cathode-ray tube devices; charge-coupled devices (CCDs); liquid crystal displays (LCDs); toroids: permeability, core material, selecting, winding
E6E Piezoelectric crystals and MMICs: quartz crystals; crystal oscillators and filters; monolithic amplifiers
E6F Optical components and power systems: photoconductive principles and effects, photovoltaic systems, optical couplers, optical sensors, and optoisolators

## Slide 3: E6A Semiconductor materials and devices
semiconductor materials; germanium, silicon, P-type, N-type; transistor types: NPN, PNP, junction, field-effect transistors: enhancement mode; depletion mode; MOS; CMOS; N-channel; P-channel

## Slide 4: Transistor Construction

## Slide 5: E6A01 In what application is gallium arsenide used as a semiconductor material in preference to germanium or silicon?
A. In high-current rectifier circuits
B. In high-power audio circuits
C. In microwave circuits
D. In very low frequency RF circuits

## Slide 6: E6A01 In what application is gallium arsenide used as a semiconductor material in preference to germanium or silicon?
A. In high-current rectifier circuits
B. In high-power audio circuits
C. In microwave circuits
D. In very low frequency RF circuits

## Slide 7: E6A02 Which of the following semiconductor materials contains excess free electrons?
A. N-type
B. P-type
C. Bipolar
D. Insulated gate

## Slide 8: E6A02 Which of the following semiconductor materials contains excess free electrons?
A. N-type
B. P-type
C. Bipolar
D. Insulated gate

## Slide 9: E6A03 Why does a PN-junction diode not conduct current when reverse biased?
A. Only P-type semiconductor material can conduct current
B. Only N-type semiconductor material can conduct current
C. Holes in P-type material and electrons in the N-type material are separated by the applied voltage, widening the depletion region
D. Excess holes in P-type material combine with the electrons in N-type material, converting the entire diode into an insulator

## Slide 10: E6A03 Why does a PN-junction diode not conduct current when reverse biased?
A. Only P-type semiconductor material can conduct current
B. Only N-type semiconductor material can conduct current
C. Holes in P-type material and electrons in the N-type material are separated by the applied voltage, widening the depletion region
D. Excess holes in P-type material combine with the electrons in N-type material, converting the entire diode into an insulator

## Slide 11: E6A04 What is the name given to an impurity atom that adds holes to a semiconductor crystal structure?
A. Insulator impurity
B. N-type impurity
C. Acceptor impurity
D. Donor impurity

## Slide 12: E6A04 What is the name given to an impurity atom that adds holes to a semiconductor crystal structure?
A. Insulator impurity
B. N-type impurity
C. Acceptor impurity
D. Donor impurity

## Slide 13: E6A05 What is the alpha of a bipolar junction transistor?
A. The change of collector current with respect to base current
B. The change of base current with respect to collector current
C. The change of collector current with respect to emitter current
D. The change of collector current with respect to gate current

## Slide 14: E6A05 What is the alpha of a bipolar junction transistor?
A. The change of collector current with respect to base current
B. The change of base current with respect to collector current
C. The change of collector current with respect to emitter current
D. The change of collector current with respect to gate current

## Slide 15: E6A06 What is the beta of a bipolar junction transistor?
A. The frequency at which the current gain is reduced to 1
B. The change in collector current with respect to base current
C. The breakdown voltage of the base to collector junction
D. The switching speed of the transistor

## Slide 16: E6A06 What is the beta of a bipolar junction transistor?
A. The frequency at which the current gain is reduced to 1
B. The change in collector current with respect to base current
C. The breakdown voltage of the base to collector junction
D. The switching speed of the transistor

## Slide 17: E6A07 Which of the following indicates that a silicon NPN junction transistor is biased on?
A. Base-to-emitter resistance of approximately 6 to 7 ohms
B. Base-to-emitter resistance of approximately 0.6 to 0.7 ohms
C. Base-to-emitter voltage of approximately 6 to 7 volts
D. Base-to-emitter voltage of approximately 0.6 to 0.7 volts

## Slide 18: E6A07 Which of the following indicates that a silicon NPN junction transistor is biased on?
A. Base-to-emitter resistance of approximately 6 to 7 ohms
B. Base-to-emitter resistance of approximately 0.6 to 0.7 ohms
C. Base-to-emitter voltage of approximately 6 to 7 volts
D. Base-to-emitter voltage of approximately 0.6 to 0.7 volts

## Slide 19: E6A08 What term indicates the frequency at which the grounded-base current gain of a transistor has decreased to 0.7 of the gain obtainable at 1 kHz?
A. Corner frequency
B. Alpha rejection frequency
C. Beta cutoff frequency
D. Alpha cutoff frequency

## Slide 20: E6A08 What term indicates the frequency at which the grounded-base current gain of a transistor has decreased to 0.7 of the gain obtainable at 1 kHz?
A. Corner frequency
B. Alpha rejection frequency
C. Beta cutoff frequency
D. Alpha cutoff frequency

## Slide 21: E6A09 What is a depletion-mode FET?
A. An FET that exhibits a current flow between source and drain when no gate voltage is applied
B. An FET that has no current flow between source and drain when no gate voltage is applied
C. Any FET without a channel
D. Any FET for which holes are the majority carriers

## Slide 22: E6A09 What is a depletion-mode FET?
A. An FET that exhibits a current flow between source and drain when no gate voltage is applied
B. An FET that has no current flow between source and drain when no gate voltage is applied
C. Any FET without a channel
D. Any FET for which holes are the majority carriers

## Slide 23: E6A10 In Figure E6-2, what is the schematic symbol for an N-channel dual-gate MOSFET?
A. 2
B. 4
C. 5
D. 6

## Slide 24: E6A10 In Figure E6-2, what is the schematic symbol for an N-channel dual-gate MOSFET?
A. 2
B. 4
C. 5
D. 6

## Slide 25: E6A11 In Figure E6-2, what is the schematic symbol for a P-channel junction FET?
A. 1
B. 2
C. 3
D. 6

## Slide 26: E6A11 In Figure E6-2, what is the schematic symbol for a P-channel junction FET?
A. 1
B. 2
C. 3
D. 6

## Slide 27: E6A12 Why do many MOSFET devices have internally connected Zener diodes on the gates?
A. To provide a voltage reference for the correct amount of reverse-bias gate voltage
B. To protect the substrate from excessive voltages
C. To keep the gate voltage within specifications and prevent the device from overheating
D. To reduce the chance of the gate insulation being punctured by static discharges or excessive voltages

## Slide 28: E6A12 Why do many MOSFET devices have internally connected Zener diodes on the gates?
A. To provide a voltage reference for the correct amount of reverse-bias gate voltage
B. To protect the substrate from excessive voltages
C. To keep the gate voltage within specifications and prevent the device from overheating
D. To reduce the chance of the gate insulation being punctured by static discharges or excessive voltages

## Slide 29: E6A13 What do the initials CMOS stand for?
A. Common Mode Oscillating System
B. Complementary Mica-Oxide Silicon
C. Complementary Metal-Oxide Semiconductor
D. Common Mode Organic Silicon

## Slide 30: E6A13 What do the initials CMOS stand for?
A. Common Mode Oscillating System
B. Complementary Mica-Oxide Silicon
C. Complementary Metal-Oxide Semiconductor
D. Common Mode Organic Silicon

## Slide 31: E6A14 How does DC input impedance at the gate of a field-effect transistor compare with the DC input impedance of a bipolar transistor?
A. They are both low impedance
B. An FET has low input impedance; a bipolar transistor has high input impedance
C. An FET has high input impedance; a bipolar transistor has low input impedance
D. They are both high impedance

## Slide 32: E6A14 How does DC input impedance at the gate of a field-effect transistor compare with the DC input impedance of a bipolar transistor?
A. They are both low impedance
B. An FET has low input impedance; a bipolar transistor has high input impedance
C. An FET has high input impedance; a bipolar transistor has low input impedance
D. They are both high impedance

## Slide 33: E6A15 Which semiconductor material contains excess holes in the outer shell of electrons?
A. N-type
B. P-type
C. Superconductor-type
D. Bipolar-type

## Slide 34: E6A15 Which semiconductor material contains excess holes in the outer shell of electrons?
A. N-type
B. P-type
C. Superconductor-type
D. Bipolar-type

## Slide 35: E6A16 What are the majority charge carriers in N-type semiconductor material?
A. Holes
B. Free electrons
C. Free protons
D. Free neutrons

## Slide 36: E6A16 What are the majority charge carriers in N-type semiconductor material?
A. Holes
B. Free electrons
C. Free protons
D. Free neutrons

## Slide 37: E6A17 What are the names of the three terminals of a field-effect transistor?
A. Gate 1, gate 2, drain
B. Emitter, base, collector
C. Emitter, base 1, base 2
D. Gate, drain, source

## Slide 38: E6A17 What are the names of the three terminals of a field-effect transistor?
A. Gate 1, gate 2, drain
B. Emitter, base, collector
C. Emitter, base 1, base 2
D. Gate, drain, source

## Slide 39: E6B Diodes

## Slide 40: E6B01 What is the most useful characteristic of a Zener diode?
A. A constant current drop under conditions of varying voltage
B. A constant voltage drop under conditions of varying current
C. A negative resistance region
D. An internal capacitance that varies with the applied voltage

## Slide 41: E6B01 What is the most useful characteristic of a Zener diode?
A. A constant current drop under conditions of varying voltage
B. A constant voltage drop under conditions of varying current
C. A negative resistance region
D. An internal capacitance that varies with the applied voltage

## Slide 42: E6B02 What is an important characteristic of a Schottky diode as compared to an ordinary silicon diode when used as a power supply rectifier?
A. Much higher reverse voltage breakdown
B. Controlled reverse avalanche voltage
C. Enhanced carrier retention time
D. Less forward voltage drop

## Slide 43: E6B02 What is an important characteristic of a Schottky diode as compared to an ordinary silicon diode when used as a power supply rectifier?
A. Much higher reverse voltage breakdown
B. Controlled reverse avalanche voltage
C. Enhanced carrier retention time
D. Less forward voltage drop

## Slide 44: E6B03 What special type of diode is capable of both amplification and oscillation?
A. Point contact
B. Zener
C. Tunnel
D. Junction

## Slide 45: E6B03 What special type of diode is capable of both amplification and oscillation?
A. Point contact
B. Zener
C. Tunnel
D. Junction

## Slide 46: E6B04 What type of semiconductor device is designed for use as a voltage-controlled capacitor?
A. Varactor diode
B. Tunnel diode
C. Silicon-controlled rectifier
D. Zener diode

## Slide 47: E6B04 What type of semiconductor device is designed for use as a voltage-controlled capacitor?
A. Varactor diode
B. Tunnel diode
C. Silicon-controlled rectifier
D. Zener diode

## Slide 48: E6B05 What characteristic of a PIN diode makes it useful as an RF switch or attenuator?
A. Extremely high reverse breakdown voltage
B. Ability to dissipate large amounts of power
C. Reverse bias controls its forward voltage drop
D. A large region of intrinsic material

## Slide 49: E6B05 What characteristic of a PIN diode makes it useful as an RF switch or attenuator?
A. Extremely high reverse breakdown voltage
B. Ability to dissipate large amounts of power
C. Reverse bias controls its forward voltage drop
D. A large region of intrinsic material

## Slide 50: E6B06 Which of the following is a common use of a hot-carrier diode?
A. As balanced mixers in FM generation
B. As a variable capacitance in an automatic frequency control circuit
C. As a constant voltage reference in a power supply
D. As a VHF / UHF mixer or detector

## Slide 51: E6B06 Which of the following is a common use of a hot-carrier diode?
A. As balanced mixers in FM generation
B. As a variable capacitance in an automatic frequency control circuit
C. As a constant voltage reference in a power supply
D. As a VHF / UHF mixer or detector

## Slide 52: E6B07 What is the failure mechanism when a junction diode fails due to excessive current?
A. Excessive inverse voltage
B. Excessive junction temperature
C. Insufficient forward voltage
D. Charge carrier depletion

## Slide 53: E6B07 What is the failure mechanism when a junction diode fails due to excessive current?
A. Excessive inverse voltage
B. Excessive junction temperature
C. Insufficient forward voltage
D. Charge carrier depletion

## Slide 54: E6B08 Which of the following describes a type of semiconductor diode?
A. Metal-semiconductor junction
B. Electrolytic rectifier
C. CMOS-field effect
D. Thermionic emission diode

## Slide 55: E6B08 Which of the following describes a type of semiconductor diode?
A. Metal-semiconductor junction
B. Electrolytic rectifier
C. CMOS-field effect
D. Thermionic emission diode

## Slide 56: E6B09 What is a common use for point contact diodes?
A. As a constant current source
B. As a constant voltage source
C. As an RF detector
D. As a high voltage rectifier

## Slide 57: E6B09 What is a common use for point contact diodes?
A. As a constant current source
B. As a constant voltage source
C. As an RF detector
D. As a high voltage rectifier

## Slide 58: E6B10 In Figure E6-3, what is the schematic symbol for a light-emitting diode?
A. 1
B. 5
C. 6
D. 7

## Slide 59: E6B10 In Figure E6-3, what is the schematic symbol for a light-emitting diode?
A. 1
B. 5
C. 6
D. 7

## Slide 60: E6B11 What is used to control the attenuation of RF signals by a PIN diode?
A. Forward DC bias current
B. A sub-harmonic pump signal
C. Reverse voltage larger than the RF signal
D. Capacitance of an RF coupling capacitor

## Slide 61: E6B11 What is used to control the attenuation of RF signals by a PIN diode?
A. Forward DC bias current
B. A sub-harmonic pump signal
C. Reverse voltage larger than the RF signal
D. Capacitance of an RF coupling capacitor

## Slide 62: E6B12 What is one common use for PIN diodes?
A. As a constant current source
B. As a constant voltage source
C. As an RF switch
D. As a high voltage rectifier

## Slide 63: E6B12 What is one common use for PIN diodes?
A. As a constant current source
B. As a constant voltage source
C. As an RF switch
D. As a high voltage rectifier

## Slide 64: E6B13 What type of bias is required for an LED to emit light?
A. Reverse bias
B. Forward bias
C. Zero bias
D. Inductive bias

## Slide 65: E6B13 What type of bias is required for an LED to emit light?
A. Reverse bias
B. Forward bias
C. Zero bias
D. Inductive bias

## Slide 66: E6C Digital ICs:
Families of digital ICs; gates; Programmable Logic Devices (PLDs)

## Slide 67: E6C01 What is the function of hysteresis in a comparator?
A. To prevent input noise from causing unstable output signals
B. To allow the comparator to be used with AC input signal
C. To cause the output to change states continually
D. To increase the sensitivity

## Slide 68: E6C01 What is the function of hysteresis in a comparator?
A. To prevent input noise from causing unstable output signals
B. To allow the comparator to be used with AC input signal
C. To cause the output to change states continually
D. To increase the sensitivity

## Slide 69: E6C02 What happens when the level of a comparator’s input signal crosses the threshold?
A. The IC input can be damaged
B. The comparator changes its output state
C. The comparator enters latch-up
D. The feedback loop becomes unstable

## Slide 70: E6C02 What happens when the level of a comparator’s input signal crosses the threshold?
A. The IC input can be damaged
B. The comparator changes its output state
C. The comparator enters latch-up
D. The feedback loop becomes unstable

## Slide 71: E6C03 What is tri-state logic?
A. Logic devices with 0, 1, and high impedance output states
B. Logic devices that utilize ternary math
C. Low power logic devices designed to operate at 3 volts
D. Proprietary logic devices manufactured by Tri-State Devices

## Slide 72: E6C03 What is tri-state logic?
A. Logic devices with 0, 1, and high impedance output states
B. Logic devices that utilize ternary math
C. Low power logic devices designed to operate at 3 volts
D. Proprietary logic devices manufactured by Tri-State Devices

## Slide 73: E6C04 What is the primary advantage of tri-state logic?
A. Low power consumption
B. Ability to connect many device outputs to a common bus
C. High speed operation
D. More efficient arithmetic operations

## Slide 74: E6C04 What is the primary advantage of tri-state logic?
A. Low power consumption
B. Ability to connect many device outputs to a common bus
C. High speed operation
D. More efficient arithmetic operations

## Slide 75: E6C05 What is an advantage of CMOS logic devices over TTL devices?
A. Differential output capability
B. Lower distortion
C. Immune to damage from static discharge
D. Lower power consumption

## Slide 76: E6C05 What is an advantage of CMOS logic devices over TTL devices?
A. Differential output capability
B. Lower distortion
C. Immune to damage from static discharge
D. Lower power consumption

## Slide 77: E6C06 Why do CMOS digital integrated circuits have high immunity to noise on the input signal or power supply?
A. Larger bypass capacitors are used in CMOS circuit design
B. The input switching threshold is about two times the power supply voltage
C. The input switching threshold is about one-half the power supply voltage
D. Input signals are stronger

## Slide 78: E6C06 Why do CMOS digital integrated circuits have high immunity to noise on the input signal or power supply?
A. Larger bypass capacitors are used in CMOS circuit design
B. The input switching threshold is about two times the power supply voltage
C. The input switching threshold is about one-half the power supply voltage
D. Input signals are stronger

## Slide 79: E6C07 What best describes a pull-up or pull-down resistor?
A. A resistor in a keying circuit used to reduce key clicks
B. A resistor connected to the positive or negative supply line used to establish a voltage when an input or output is an open circuit
C. A resistor that insures that an oscillator frequency does not drive lower over time
D. A resistor connected to an op-amp output that only functions when the logic output is false

## Slide 80: E6C07 What best describes a pull-up or pull-down resistor?
A. A resistor in a keying circuit used to reduce key clicks
B. A resistor connected to the positive or negative supply line used to establish a voltage when an input or output is an open circuit
C. A resistor that insures that an oscillator frequency does not drive lower over time
D. A resistor connected to an op-amp output that only functions when the logic output is false

## Slide 81: E6C08 In Figure E6-5, what is the schematic symbol for a NAND gate?
A. 1
B. 2
C. 3
D. 4

## Slide 82: E6C08 In Figure E6-5, what is the schematic symbol for a NAND gate?
A. 1
B. 2
C. 3
D. 4

## Slide 83: E6C09 What is a Programmable Logic Device (PLD)?
A. A device to control industrial equipment
B. A programmable collection of logic gates and circuits in a single integrated circuit
C. Programmable equipment used for testing digital logic integrated circuits
D. An algorithm for simulating logic functions during circuit design

## Slide 84: E6C09 What is a Programmable Logic Device (PLD)?
A. A device to control industrial equipment
B. A programmable collection of logic gates and circuits in a single integrated circuit
C. Programmable equipment used for testing digital logic integrated circuits
D. An algorithm for simulating logic functions during circuit design

## Slide 85: E6C10 In Figure E6-5, what is the schematic symbol for a NOR gate?
A. 1
B. 2
C. 3
D. 4

## Slide 86: E6C10 In Figure E6-5, what is the schematic symbol for a NOR gate?
A. 1
B. 2
C. 3
D. 4

## Slide 87: E6C11 In Figure E6-5, what is the schematic symbol for the NOT operation (inverter)?
A. 2
B. 4
C. 5
D. 6

## Slide 88: E6C11 In Figure E6-5, what is the schematic symbol for the NOT operation (inverter)?
A. 2
B. 4
C. 5
D. 6

## Slide 89: E6C12 What is BiCMOS logic?
A. A logic device with two CMOS circuits per package
B. A FET logic family based on bimetallic semiconductors
C. A logic family based on bismuth CMOS devices
D. An integrated circuit logic family using both bipolar and CMOS transistors

## Slide 90: E6C12 What is BiCMOS logic?
A. A logic device with two CMOS circuits per package
B. A FET logic family based on bimetallic semiconductors
C. A logic family based on bismuth CMOS devices
D. An integrated circuit logic family using both bipolar and CMOS transistors

## Slide 91: E6C13 Which of the following is an advantage of BiCMOS logic?
A. Its simplicity results in much less expensive devices than standard CMOS
B. It is totally immune to electrostatic damage
C. It has the high input impedance of CMOS and the low output impedance of bipolar transistors
D. All of these choices are correct

## Slide 92: E6C13 Which of the following is an advantage of BiCMOS logic?
A. Its simplicity results in much less expensive devices than standard CMOS
B. It is totally immune to electrostatic damage
C. It has the high input impedance of CMOS and the low output impedance of bipolar transistors
D. All of these choices are correct

## Slide 93: E6C14 What is the primary advantage of using a Programmable Gate Array (PGA) in a logic circuit?
A. Many similar gates are less expensive than a mixture of gate types
B. Complex logic functions can be created in a single integrated circuit
C. A PGA contains its own internal power supply
D. All of these choices are correct
~~

## Slide 94: E6C14 What is the primary advantage of using a Programmable Gate Array (PGA) in a logic circuit?
A. Many similar gates are less expensive than a mixture of gate types
B. Complex logic functions can be created in a single integrated circuit
C. A PGA contains its own internal power supply
D. All of these choices are correct
~~

## Slide 95: E6D Toroidal and Solenoidal Inductors:
permeability, core material, selecting, winding; transformers; Piezoelectric devices

## Slide 96: E6D01 How many turns will be required to produce a 5-microhenry inductor using a powdered-iron toroidal core that has an inductance index (A L) value of 40 microhenrys/100 turns?
A. 35 turns
B. 13 turns
C. 79 turns
D. 141 turns

## Slide 97: E6D01 How many turns will be required to produce a 5-microhenry inductor using a powdered-iron toroidal core that has an inductance index (A L) value of 40 microhenrys/100 turns?
A. 35 turns
B. 13 turns
C. 79 turns
D. 141 turns
N turns = 100 x (√ (L / AL)) or
N turns = 100 x (√ (5 / 40)) or 35.35 turns

## Slide 98: E6D02 What is the equivalent circuit of a quartz crystal?
A. Motional capacitance, motional inductance, and loss resistance in series, all in parallel with a shunt capacitor representing electrode and stray capacitance
B. Motional capacitance, motional inductance, loss resistance, and a capacitor representing electrode and stray capacitance all in parallel
C. Motional capacitance, motional inductance, loss resistance, and a capacitor representing electrode and stray capacitance all in series
D. Motional inductance and loss resistance in series, paralleled with motional capacitance and a capacitor representing electrode and stray capacitance

## Slide 99: E6D02 What is the equivalent circuit of a quartz crystal?
A. Motional capacitance, motional inductance ,and loss resistance in series, all in parallel with a shunt capacitor representing electrode and stray capacitance
B. Motional capacitance, motional inductance, loss resistance, and a capacitor representing electrode and stray capacitance all in parallel
C. Motional capacitance, motional inductance, loss resistance, and a capacitor representing electrode and stray capacitance all in series
D. Motional inductance and loss resistance in series, paralleled with motional capacitance and a capacitor representing electrode and stray capacitance

## Slide 100: E6D03 Which of the following is an aspect of the piezoelectric effect?
A. Mechanical deformation of material by the application of a voltage
B. Mechanical deformation of material by the application of a magnetic field
C. Generation of electrical energy in the presence of light
D. Increased conductivity in the presence of light

## Slide 101: E6D03 Which of the following is an aspect of the piezoelectric effect?
A. Mechanical deformation of material by the application of a voltage
B. Mechanical deformation of material by the application of a magnetic field
C. Generation of electrical energy in the presence of light
D. Increased conductivity in the presence of light

## Slide 102: E6D04 Which materials are commonly used as a slug core in a variable inductor?
A. Polystyrene and polyethylene
B. Ferrite and brass
C. Teflon and Delrin
D. Cobalt and aluminum

## Slide 103: E6D04 Which materials are commonly used as a slug core in a variable inductor?
A. Polystyrene and polyethylene
B. Ferrite and brass
C. Teflon and Delrin
D. Cobalt and aluminum

## Slide 104: E6D05 What is one reason for using ferrite cores rather than powdered-iron in an inductor?
A. Ferrite toroids generally have lower initial permeability
B. Ferrite toroids generally have better temperature stability
C. Ferrite toroids generally require fewer turns to produce a given inductance value
D. Ferrite toroids are easier to use with surface mount technology

## Slide 105: E6D05 What is one reason for using ferrite cores rather than powdered-iron in an inductor?
A. Ferrite toroids generally have lower initial permeability
B. Ferrite toroids generally have better temperature stability
C. Ferrite toroids generally require fewer turns to produce a given inductance value
D. Ferrite toroids are easier to use with surface mount technology

## Slide 106: E6D06 What core material property determines the inductance of a toroidal inductor?
A. Thermal impedance
B. Resistance
C. Reactivity
D. Permeability

## Slide 107: E6D06 What core material property determines the inductance of a toroidal inductor?
A. Thermal impedance
B. Resistance
C. Reactivity
D. Permeability

## Slide 108: E6D07 What is the usable frequency range of inductors that use toroidal cores, assuming a correct selection of core material for the frequency being used?
A. From a few kHz to no more than 30 MHz
B. From less than 20 Hz to approximately 300 MHz
C. From approximately 10 Hz to no more than 3000 kHz
D. From about 100 kHz to at least 1000 GHz

## Slide 109: E6D07 What is the usable frequency range of inductors that use toroidal cores, assuming a correct selection of core material for the frequency being used?
A. From a few kHz to no more than 30 MHz
B. From less than 20 Hz to approximately 300 MHz
C. From approximately 10 Hz to no more than 3000 kHz
D. From about 100 kHz to at least 1000 GHz

## Slide 110: E6D08 What is one reason for using powdered-iron cores rather than ferrite cores in an inductor?
A. Powdered-iron cores generally have greater initial permeability
B. Powdered-iron ores generally maintain their characteristics at higher currents
C. Powdered-iron cores generally require fewer turns to produce a given inductance
D. Powdered-iron cores use smaller diameter wire for the same inductance

## Slide 111: E6D08 What is one reason for using powdered-iron cores rather than ferrite cores in an inductor?
A. Powdered-iron cores generally have greater initial permeability
B. Powdered-iron ores generally maintain their characteristics at higher currents
C. Powdered-iron cores generally require fewer turns to produce a given inductance
D. Powdered-iron cores use smaller diameter wire for the same inductance

## Slide 112: E6D09 What devices are commonly used as VHF and UHF parasitic suppressors at the input and output terminals a transistor HF amplifier?
A. Electrolytic capacitors
B. Butterworth filters
C. Ferrite beads
D. Steel-core toroids

## Slide 113: E6D09 What devices are commonly used as VHF and UHF parasitic suppressors at the input and output terminals a transistor HF amplifier?
A. Electrolytic capacitors
B. Butterworth filters
C. Ferrite beads
D. Steel-core toroids

## Slide 114: E6D10 What is a primary advantage of using a toroidal core instead of a solenoidal core in an inductor?
A. Toroidal cores confine most of the magnetic field within the core material
B. Toroidal cores make it easier to couple the magnetic energy into other components
C. Toroidal cores exhibit greater hysteresis
D. Toroidal cores have lower Q characteristics

## Slide 115: E6D10 What is a primary advantage of using a toroidal core instead of a solenoidal core in an inductor?
A. Toroidal cores confine most of the magnetic field within the core material
B. Toroidal cores make it easier to couple the magnetic energy into other components
C. Toroidal cores exhibit greater hysteresis
D. Toroidal cores have lower Q characteristics

## Slide 116: E6D11 How many turns will be required to produce a 1-mH inductor using a core that has an inductance index (A L) value of 523 millihenrys/1000 turns?
A. 2 turns
B. 4 turns
C. 43 turns
D. 229 turns

## Slide 117: E6D11 How many turns will be required to produce a 1-mH inductor using a core that has an inductance index (A L) value of 523 millihenrys/1000 turns?
A. 2 turns
B. 4 turns
C. 43 turns
D. 229 turns
N turns = 1000 x (√ (L / AL)) or
N turns = 1000 x (√ (1 / 523)) or 43.7 turns

## Slide 118: E6D12 What is the definition of saturation in a ferrite core inductor?
A. The inductor windings are over coupled
B. The inductor’s voltage rating is exceeded causing a flashover
C. The ability of the inductor’s core to store magnetic energy has been exceeded
D. Adjacent inductors become over-coupled

## Slide 119: E6D12 What is the definition of saturation in a ferrite core inductor?
A. The inductor windings are over coupled
B. The inductor’s voltage rating is exceeded causing a flashover
C. The ability of the inductor’s core to store magnetic energy has been exceeded
D. Adjacent inductors become over-coupled

## Slide 120: E6D13 What is the primary cause of inductor self-resonance?
A. Inter-turn capacitance
B. The skin effect
C. Inductive kickback
D. Non-linear core hysteresis

## Slide 121: E6D13 What is the primary cause of inductor self-resonance?
A. Inter-turn capacitance
B. The skin effect
C. Inductive kickback
D. Non-linear core hysteresis

## Slide 122: E6D14 Which type of slug material decreases inductance when inserted into a coil?
A. Ceramic
B. Brass
C. Ferrite
D. Powdered-iron

## Slide 123: E6D14 Which type of slug material decreases inductance when inserted into a coil?
A. Ceramic
B. Brass
C. Ferrite
D. Powdered-iron

## Slide 124: E6D15 What is current in the primary winding of a transformer called if no load is attached to the secondary?
A. Magnetizing current
B. Direct current
C. Excitation current
D. Stabilizing current

## Slide 125: E6D15 What is current in the primary winding of a transformer called if no load is attached to the secondary?
A. Magnetizing current
B. Direct current
C. Excitation current
D. Stabilizing current

## Slide 126: E6D16 What is the common name for a capacitor connected across a transformer secondary that is used to absorb transient voltage spikes?
A. Clipper capacitor
B. Trimmer capacitor
C. Feedback capacitor
D. Snubber capacitor

## Slide 127: E6D16 What is the common name for a capacitor connected across a transformer secondary that is used to absorb transient voltage spikes?
A. Clipper capacitor
B. Trimmer capacitor
C. Feedback capacitor
D. Snubber capacitor

## Slide 128: E6D17 Why should core saturation of a conventional impedance matching transformer be avoided?
A. Harmonics and distortion could result
B. Magnetic flux would increase with frequency
C. RF susceptance would increase
D. Temporary changes of the core permeability could result

## Slide 129: E6D17 Why should core saturation of a conventional impedance matching transformer be avoided?
A. Harmonics and distortion could result
B. Magnetic flux would increase with frequency
C. RF susceptance would increase
D. Temporary changes of the core permeability could result

## Slide 130: E6E Analog ICs
: MMICs, CCDs, Device packages

## Slide 131: E6E01 Which of the following is true of a charge-coupled device (CCD)?
A. Its phase shift changes rapidly with frequency
B. It is a CMOS analog-to-digital converter
C. It samples an analog signal and passes it in stages from the input to the output
D. It is used in a battery charger circuit

## Slide 132: E6E01 Which of the following is true of a charge-coupled device (CCD)?
A. Its phase shift changes rapidly with frequency
B. It is a CMOS analog-to-digital converter
C. It samples an analog signal and passes it in stages from the input to the output
D. It is used in a battery charger circuit

## Slide 133: E6E02 Which of the following device packages is a through-hole type?
A DIP
B. PLCC
C Ball grid array
D SOT

## Slide 134: E6E02 Which of the following device packages is a through-hole type?
A DIP
B. PLCC
C Ball grid array
D SOT

## Slide 135: E6E03 Which of the following materials is likely to provide the highest frequency of operation when used in MMICs?
A. Silicon
B. Silicon nitride
C. Silicon dioxide
D. Gallium nitride

## Slide 136: E6E03 Which of the following materials is likely to provide the highest frequency of operation when used in MMICs?
A. Silicon
B. Silicon nitride
C. Silicon dioxide
D. Gallium nitride

## Slide 137: E6E04 Which is the most common input and output impedance of circuits that use MMICs?
A. 50 ohms
B. 300 ohms
C. 450 ohms
D. 10 ohms

## Slide 138: E6E04 Which is the most common input and output impedance of circuits that use MMICs?
A. 50 ohms
B. 300 ohms
C. 450 ohms
D. 10 ohms

## Slide 139: E6E05 Which of the following noise figure values is typical of a low-noise UHF preamplifier?
A. 2 dB
B. -10 dB
C. 44 dBm
D. -20 dBm

## Slide 140: E6E05 Which of the following noise figure values is typical of a low-noise UHF preamplifier?
A. 2 dB
B. -10 dB
C. 44 dBm
D. -20 dBm

## Slide 141: E6E06 What characteristics of the MMIC make it a popular choice for VHF through microwave circuits?
A. The ability to retrieve information from a single signal even in the presence of other strong signals.
B. Plate current that is controlled by a control grid
C. Nearly infinite gain, very high input impedance, and very low output impedance
D. Controlled gain, low noise figure, and constant input and output impedance over the specified frequency range

## Slide 142: E6E06 What characteristics of the MMIC make it a popular choice for VHF through microwave circuits?
A. The ability to retrieve information from a single signal even in the presence of other strong signals.
B. Plate current that is controlled by a control grid
C. Nearly infinite gain, very high input impedance, and very low output impedance
D. Controlled gain, low noise figure, and constant input and output impedance over the specified frequency range

## Slide 143: E6E07 Which of the following is typically used to construct a MMIC-based microwave amplifier?
A. Ground-plane construction
B. Microstrip construction
C. Point-to-point construction
D. Wave-soldering construction

## Slide 144: E6E07 Which of the following is typically used to construct a MMIC-based microwave amplifier?
A. Ground-plane construction
B. Microstrip construction
C. Point-to-point construction
D. Wave-soldering construction

## Slide 145: E6E08 How is voltage from a power supply normally furnished to the most common type of monolithic microwave integrated circuit (MMIC)?
A. Through a resistor and/or RF choke connected to the amplifier output lead
B. MMICs require no operating bias
C. Through a capacitor and RF choke connected to the amplifier input lead
D. Directly to the bias voltage (VCC IN) lead

## Slide 146: E6E08 How is voltage from a power supply normally furnished to the most common type of monolithic microwave integrated circuit (MMIC)?
A. Through a resistor and/or RF choke connected to the amplifier output lead
B. MMICs require no operating bias
C. Through a capacitor and RF choke connected to the amplifier input lead
D. Directly to the biasvvoltage (VCC IN) lead

## Slide 147: E6E09 Which of the following component package types would be most suitable for use at frequencies above the HF range?
A. TO-220
B. Axial lead
C. Radial lead
D. Surface mount

## Slide 148: E6E09 Which of the following component package types would be most suitable for use at frequencies above the HF range?
A. TO-220
B. Axial lead
C. Radial lead
D. Surface mount

## Slide 149: E6E10 What is the packaging technique in which leadless components are soldered directly to circuit boards?
A. Direct soldering
B. Virtual lead mounting
C. Stripped lead
D. Surface mount

## Slide 150: E6E10 What is the packaging technique in which leadless components are soldered directly to circuit boards?
A. Direct soldering
B. Virtual lead mounting
C. Stripped lead
D. Surface mount

## Slide 151: E6E11 What is a characteristic of DIP packaging used for integrated circuits?
A. Package mounts in a direct inverted position
B. Low leakage doubly insulated package
C. Two chips in each package (Dual In Package)
D. A total of two rows of connecting pins placed on opposite sides of the package (Dual In-line Package)

## Slide 152: E6E11 What is a characteristic of DIP packaging used for integrated circuits?
A. Package mounts in a direct inverted position
B. Low leakage doubly insulated package
C. Two chips in each package (Dual In Package)
D. A total of two rows of connecting pins placed on opposite sides of the package (Dual In-line Package)

## Slide 153: E6E12 Why are high-power RF amplifier ICs and transistors sometimes mounted in ceramic packages?
A. High-voltage insulating ability
B. Better dissipation of heat
C. Enhanced sensitivity to light
D. To provide a low-pass frequency response

## Slide 154: E6E12 Why are high-power RF amplifier ICs and transistors sometimes mounted in ceramic packages?
A. High-voltage insulating ability
B. Better dissipation of heat
C. Enhanced sensitivity to light
D. To provide a low-pass frequency response

## Slide 155: E6F Optical components
photoconductive principles and effects, photovoltaic systems, optical couplers, optical sensors, and optoisolators; LCDs

## Slide 156: E6F01 What is photoconductivity?
A. The conversion of photon energy to electromotive energy
B. The increased conductivity of an illuminated semiconductor
C. The conversion of electromotive energy to photon energy
D. The decreased conductivity of an illuminated semiconductor

## Slide 157: E6F01 What is photoconductivity?
A. The conversion of photon energy to electromotive energy
B. The increased conductivity of an illuminated semiconductor
C. The conversion of electromotive energy to photon energy
D. The decreased conductivity of an illuminated semiconductor

## Slide 158: E6F02 What happens to the conductivity of a photoconductive material when light shines on it?
A. It increases
B. It decreases
C. It stays the same
D. It becomes unstable

## Slide 159: E6F02 What happens to the conductivity of a photoconductive material when light shines on it?
A. It increases
B. It decreases
C. It stays the same
D. It becomes unstable

## Slide 160: E6F03 What is the most common configuration of an optoisolator or optocoupler?
A. A lens and a photomultiplier
B. A frequency modulated helium-neon laser
C. An amplitude modulated helium-neon laser
D. An LED and a phototransistor

## Slide 161: E6F03 What is the most common configuration of an optoisolator or optocoupler?
A. A lens and a photomultiplier
B. A frequency modulated helium-neon laser
C. An amplitude modulated helium-neon laser
D. An LED and a phototransistor

## Slide 162: E6F04 What is the photovoltaic effect?
A. The conversion of voltage to current when exposed to light
B. The conversion of light to electrical energy
C. The conversion of electrical energy to mechanical energy
D. The tendency of a battery to discharge when used outside

## Slide 163: E6F04 What is the photovoltaic effect?
A. The conversion of voltage to current when exposed to light
B. The conversion of light to electrical energy
C. The conversion of electrical energy to mechanical energy
D. The tendency of a battery to discharge when used outside

## Slide 164: E6F05 Which describes an optical shaft encoder?
A. A device which detects rotation of a control by interrupting a light source with a patterned wheel
B. A device which measures the strength of a beam of light using analog to digital conversion
C. A digital encryption device often used to encrypt spacecraft control signals
D. A device for generating RTTY signals by means of a rotating light source.

## Slide 165: Optical shaft encoder

## Slide 166: Optical shaft encoder

## Slide 167: E6F05 Which describes an optical shaft encoder?
A. A device which detects rotation of a control by interrupting a light source with a patterned wheel
B. A device which measures the strength of a beam of light using analog to digital conversion
C. A digital encryption device often used to encrypt spacecraft control signals
D. A device for generating RTTY signals by means of a rotating light source.

## Slide 168: E6F06 Which of these materials is affected the most by photoconductivity?
A. A crystalline semiconductor
B. An ordinary metal
C. A heavy metal
D. A liquid semiconductor

## Slide 169: E6F06 Which of these materials is affected the most by photoconductivity?
A. A crystalline semiconductor
B. An ordinary metal
C. A heavy metal
D. A liquid semiconductor

## Slide 170: E6F07 What is a solid state relay?
A. A relay using transistors to drive the relay coil
B. A device that uses semiconductors to implement the functions of an electromechanical relay
C. A mechanical relay that latches in the on or off state each time it is pulsed
D. A passive delay line

## Slide 171: E6F07 What is a solid state relay?
A. A relay using transistors to drive the relay coil
B. A device that uses semiconductors to implement the functions of an electromechanical relay
C. A mechanical relay that latches in the on or off state each time it is pulsed
D. A passive delay line

## Slide 172: E6F08 Why are optoisolators often used in conjunction with solid state circuits when switching 120VAC?
A. Optoisolators provide a low impedance link between a control circuit and a power circuit
B. Optoisolators provide impedance matching between the control circuit and power circuit
C. Optoisolators provide a very high degree of electrical isolation between a control circuit and the circuit being switched
D. Optoisolators eliminate the effects of reflected light in the control circuit

## Slide 173: E6F08 Why are optoisolators often used in conjunction with solid state circuits when switching 120VAC?
A. Optoisolators provide a low impedance link between a control circuit and a power circuit
B. Optoisolators provide impedance matching between the control circuit and power circuit
C. Optoisolators provide a very high degree of electrical isolation between a control circuit and the circuit being switched
D. Optoisolators eliminate the effects of reflected light in the control circuit

## Slide 174: E6F09 What is the efficiency of a photovoltaic cell?
A. The output RF power divided by the input DC power
B. The effective payback period
C. The open-circuit voltage divided by the short-circuit current under full illumination
D. The relative fraction of light that is converted to current

## Slide 175: E6F09 What is the efficiency of a photovoltaic cell?
A. The output RF power divided by the input DC power
B. The effective payback period
C. The open-circuit voltage divided by the short-circuit current under full illumination
D. The relative fraction of light that is converted to current

## Slide 176: E6F10 What is the most common type of photovoltaic cell used for electrical power generation?
A. Selenium
B. Silicon
C. Cadmium Sulfide
D. Copper oxide

## Slide 177: E6F10 What is the most common type of photovoltaic cell used for electrical power generation?
A. Selenium
B. Silicon
C. Cadmium Sulfide
D. Copper oxide

## Slide 178: E6F11 What is the approximate open-circuit voltage produced by a fully-illuminated silicon photovoltaic cell?
A. 0.1 V
B. 0.5 V
C. 1.5 V
D. 12 V

## Slide 179: E6F11 What is the approximate open-circuit voltage produced by a fully-illuminated silicon photovoltaic cell?
A. 0.1 V
B. 0.5 V
C. 1.5 V
D. 12 V

## Slide 180: E6F12 What absorbs the energy from light falling on a photovoltaic cell?
A. Protons
B. Photons
C. Electrons
D. Holes

## Slide 181: E6F12 What absorbs the energy from light falling on a photovoltaic cell?
A. Protons
B. Photons
C. Electrons
D. Holes

## Slide 182: E6F13 What is a liquid crystal display (LCD)?
A. A modern replacement for a quartz crystal oscillator which displays its fundamental frequency
B. A display utilizing a crystalline liquid and polarizing filters which becomes opaque when voltage is applied
C. A frequency-determining unit for a transmitter or receiver
D. A display that uses a glowing liquid to remain brightly lit in dim light

## Slide 183: E6F13 What is a liquid crystal display (LCD)?
A. A modern replacement for a quartz crystal oscillator which displays its fundamental frequency
B. A display utilizing a crystalline liquid and polarizing filters which becomes opaque when voltage is applied
C. A frequency-determining unit for a transmitter or receiver
D. A display that uses a glowing liquid to remain brightly lit in dim light

## Slide 184: E6F14 Which of the following is true of LCD displays?
A. They are hard to view in high ambient light conditions
B. They may be hard view through polarized lenses
C. They only display alphanumeric symbols
D. All of these choices are correct

## Slide 185: E6F14 Which of the following is true of LCD displays?
A. They are hard to view in high ambient light conditions
B. They may be hard view through polarized lenses
C. They only display alphanumeric symbols
D. All of these choices are correct

## Slide 186: End of SUBELEMENT E6
CIRCUIT COMPONENTS