## Slide 1: SUBELEMENT E5
ELECTRICAL PRINCIPLES
[4 Exam Questions - 4 Groups]
Notes: Extra Question Pool 2016. The Western Washington Ham Training Team makes these slides available to teach Amateur Technician Radio Licensing Classes. Daniel Stevens KL7WM, Training Coordinator, Howard Swartz, W7HS, Slide master, Dustin Lomax, KF7FK, Leading Instructor, LW Abel, K7LWA, Enthusiasm Leader.

## Slide 2
E5A Resonance and Q: characteristics of resonant circuits: series and parallel resonance; definitions and effects of Q; half-power bandwidth; phase relationships in reactive circuits
E5B Time constants and phase relationships: RLC time constants: definition; time constants in RL and RC circuits; phase angle between voltage and current; phase angles of series RLC; phrase angle of inductance vs susceptance; and susceptance
E5C Coordinate systems: and phasors in electronics: Rectangular Coordinates; Polar Coordinates; Phasors
E5D AC and RF energy in real circuits: skin effect; electrostatic and electromagnetic fields; reactive power; power factor; electrical length of conductors at UHF and microwave frequencies

## Slide 3: E5A01 What can cause the voltage across reactances in series to be larger than the voltage applied to them?
A. Resonance
B. Capacitance
C. Conductance
D. Resistance

## Slide 4: E5A01 What can cause the voltage across reactances in series to be larger than the voltage applied to them?
A. Resonance
B. Capacitance
C. Conductance
D. Resistance
Resonance is when the inductive reactance and capacitive reactance are equal. In this condition the current flowing in the circuit is limited only by the circuit resistance.

## Slide 5: E5A02 What is resonance in an electrical circuit?
A. The highest frequency that will pass current
B. The lowest frequency that will pass current
C. The frequency at which the capacitive reactance equals the inductive reactance
D. The frequency at which the reactive impedance equals the resistive impedance

## Slide 6: E5A02 What is resonance in an electrical circuit?
A. The highest frequency that will pass current
B. The lowest frequency that will pass current
C. The frequency at which the capacitive reactance equals the inductive reactance
D. The frequency at which the reactive impedance equals the resistive impedance

## Slide 7: E5A03 What is the magnitude of the impedance of a series RLC circuit at resonance?
A. High, as compared to the circuit resistance
B. Approximately equal to capacitive reactance
C. Approximately equal to inductive reactance
D. Approximately equal to circuit resistance

## Slide 8: E5A03 What is the magnitude of the impedance of a series RLC circuit at resonance?
A. High, as compared to the circuit resistance
B. Approximately equal to capacitive reactance
C. Approximately equal to inductive reactance
D. Approximately equal to circuit resistance

## Slide 9: E5A04 What is the magnitude of the impedance of a circuit with a resistor, an inductor and a capacitor all in parallel, at resonance?
A. Approximately equal to circuit resistance
B. Approximately equal to inductive reactance
C. Low, as compared to the circuit resistance
D. Approximately equal to capacitive reactance

## Slide 10: E5A04 What is the magnitude of the impedance of a circuit with a resistor, an inductor and a capacitor all in parallel, at resonance?
A. Approximately equal to circuit resistance
B. Approximately equal to inductive reactance
C. Low, as compared to the circuit resistance
D. Approximately equal to capacitive reactance

## Slide 11: E5A05 What is the magnitude of the current at the input of a series RLC circuit as the frequency goes through resonance?
A. Minimum
B. Maximum
C. R/L
D. L/R

## Slide 12: E5A05 What is the magnitude of the current at the input of a series RLC circuit as the frequency goes through resonance?
A. Minimum
B. Maximum
C. R/L
D. L/R

## Slide 13: E5A06 What is the magnitude of the circulating current within the components of a parallel LC circuit at resonance?
A. It is at a minimum
B. It is at a maximum
C. It equals 1 divided by the quantity 2 times Pi, multiplied by the square root of inductance L multiplied by capacitance C
D. It equals 2 multiplied by Pi, multiplied by frequency, multiplied by inductance

## Slide 14: E5A06 What is the magnitude of the circulating current within the components of a parallel LC circuit at resonance?
A. It is at a minimum
B. It is at a maximum
C. It equals 1 divided by the quantity 2 times Pi, multiplied by the square root of inductance L multiplied by capacitance C
D. It equals 2 multiplied by Pi, multiplied by frequency, multiplied by inductance

## Slide 15: E5A07 What is the magnitude of the current at the input of a parallel RLC circuit at resonance?
A. Minimum
B. Maximum
C. R/L
D. L/R

## Slide 16: E5A07 What is the magnitude of the current at the input of a parallel RLC circuit at resonance?
A. Minimum
B. Maximum
C. R/L
D. L/R

## Slide 17: E5A08 What is the phase relationship between the current through and the voltage across a series resonant circuit at resonance?
A. The voltage leads the current by 90 degrees
B. The current leads the voltage by 90 degrees
C. The voltage and current are in phase
D. The voltage and current are 180 degrees out of phase

## Slide 18: E5A08 What is the phase relationship between the current through and the voltage across a series resonant circuit at resonance?
A. The voltage leads the current by 90 degrees
B. The current leads the voltage by 90 degrees
C. The voltage and current are in phase
D. The voltage and current are 180 degrees out of phase

## Slide 19: E5A09 How is the Q of an RLC parallel resonant circuit calculated?
A. Reactance of either the inductance or capacitance divided by the resistance
B. Reactance of either the inductance or capacitance multiplied by the resistance
C. Resistance divided by the reactance of either the inductance or capacitance
D. Reactance of the inductance multiplied by the reactance of the capacitance

## Slide 20: E5A09 How is the Q of an RLC parallel resonant circuit calculated?
A. Reactance of either the inductance or capacitance divided by the resistance
B. Reactance of either the inductance or capacitance multiplied by the resistance
C. Resistance divided by the reactance of either the inductance or capacitance
D. Reactance of the inductance multiplied by the reactance of the capacitance

## Slide 21: E5A10 How is the Q of an RLC series resonant circuit calculated?
A. Reactance of either the inductance or capacitance divided by the resistance
B. Reactance of either the inductance or capacitance times the resistance
C. Resistance divided by the reactance of either the inductance or capacitance
D. Reactance of the inductance times the reactance of the capacitance

## Slide 22: E5A10 How is the Q of an RLC series resonant circuit calculated?
A. Reactance of either the inductance or capacitance divided by the resistance
B. Reactance of either the inductance or capacitance times the resistance
C. Resistance divided by the reactance of either the inductance or capacitance
D. Reactance of the inductance times the reactance of the capacitance

## Slide 23: E5A11 What is the half-power bandwidth of a parallel resonant circuit that has a resonant frequency of 7.1 MHz and a Q of 150?
A. 157.8 Hz
B. 315.6 Hz
C. 47.3 kHz
D. 23.67 kHz

## Slide 24: E5A11 What is the half-power bandwidth of a parallel resonant circuit that has a resonant frequency of 7.1 MHz and a Q of 150?
A. 157.8 Hz
B. 315.6 Hz
C. 47.3 kHz
D. 23.67 kHz
BW= Frequency / Q or 7,100 KHz/150 or 47.3 KHz

## Slide 25: E5A12 What is the half-power bandwidth of a parallel resonant circuit that has a resonant frequency of 3.7 MHz and a Q of 118?
A. 436.6 kHz
B. 218.3 kHz
C. 31.4 kHz
D. 15.7 kHz

## Slide 26: E5A12 What is the half-power bandwidth of a parallel resonant circuit that has a resonant frequency of 3.7 MHz and a Q of 118?
A. 436.6 kHz
B. 218.3 kHz
C. 31.4 kHz
D. 15.7 kHz
BW= Frequency / Q or 3,700 KHz/118 or 31.36 KHz

## Slide 27: E5A13 What is an effect of increasing Q in a resonant circuit?
A. Fewer components are needed for the same performance
B. Parasitic effects are minimized
C. Internal voltages and circulating currents increase
D. Phase shift can become uncontrolled
~~

## Slide 28: E5A13 What is an effect of increasing Q in a resonant circuit?
A. Fewer components are needed for the same performance
B. Parasitic effects are minimized
C. Internal voltages and circulating currents increase
D. Phase shift can become uncontrolled
~~

## Slide 29: E5A14 What is the resonant frequency of a series RLC circuit if R is 22 ohms, L is 50 microhenrys and C is 40 picofarads?
A. 44.72 MHz
B. 22.36 MHz
C. 3.56 MHz
D. 1.78 MHz

## Slide 30: E5A14 What is the resonant frequency of a series RLC circuit if R is 22 ohms, L is 50 microhenrys and C is 40 picofarads?
F = 1 / (2π√(L x C))
F = 1 / ( 2π√( (50 x 40) x (10-6 x 10-12 ) )
F = 1 / (2π√( 2000) ) x 1 / √(10-18 )
F = 1 / (6.28 x 44.721) x 1 / (10-9 )
F = 1 / (280.85) x 1 / (10-9 )
F = 0. 003 560 617 x 10 9
F = 003 560 617. = 3.56 MHz.
F = 1,000 / (2π√(L x C))

## Slide 31: Calculation Resonant Frequency
Freq = 1 / (2π√(L x C))
Multiply L and C
Take the square root
Multiply by 6.28
Clear memory ( MC )
Add to memory ( M+ )
Entry 1 divide
Recall memory ( RM )
If microhenrys and picofariads
Multiply by 1,000 to get MHz

## Slide 32: E5A14 What is the resonant frequency of a series RLC circuit if R is 22 ohms, L is 50 microhenrys and C is 40 picofarads?
A. 44.72 MHz
B. 22.36 MHz
C. 3.56 MHz
D. 1.78 MHz
For frequency in MHz, Inductance in micro-henrys and capacitance in picofarads: F(resonance) =1,000 / (2π√(L x C))
F(resonance)=1,000 / (2π√(L x C)) = 1,000 / (6.28√(50 x 40)) = 3.56 MHz

## Slide 33: E5A15 Which of the following can increase Q for inductors and capacitors?
A. Lower losses
B. Lower reactance
C. Lower self-resonant frequency
D. Higher self-resonant frequency

## Slide 34: E5A15 Which of the following can increase Q for inductors and capacitors?
A. Lower losses
B. Lower reactance
C. Lower self-resonant frequency
D. Higher self-resonant frequency

## Slide 35: E5A16 What is the resonant frequency of a parallel RLC circuit if R is 33 ohms, L is 50 microhenrys and C is 10 picofarads?
A. 23.5 MHz
B. 23.5 kHz
C. 7.12 kHz
D. 7.12 MHz

## Slide 36: E5A16 What is the resonant frequency of a parallel RLC circuit if R is 33 ohms, L is 50 microhenrys and C is 10 picofarads?
F = 1 / (2π√(L x C))
F = 1 / ( 2π√( (50 x 10) x (10-6 x 10-12 ) )
F = 1 / (2π√( 500) ) x 1 / √(10-18 )
F = 1 / (6.28 x 22.360) x 1 / (10-9 )
F = 1 / (140.425) x 1 / (10-9 )
F = 0. 007 121 235 x 10 9
F = 007 121 235. = 7.12 MHz.
F = 1,000 / (2π√(L x C))

## Slide 37: E5A16 What is the resonant frequency of a parallel RLC circuit if R is 33 ohms, L is 50 microhenrys and C is 10 picofarads?
A. 23.5 MHz
B. 23.5 kHz
C. 7.12 kHz
D. 7.12 MHz
F(resonance)=1,000 / (2π√(L x C)) = 1 / (6.28√(50 x 10)) = 7.121 MHz

## Slide 38: E5A17 What is the result of increasing the Q of an impedance-matching circuit?
A. Matching bandwidth is decreased
B. Matching bandwidth is increased
C. Matching range is increased
D. It has no effect on impedance matching

## Slide 39: E5A17 What is the result of increasing the Q of an impedance-matching circuit?
A. Matching bandwidth is decreased
B. Matching bandwidth is increased
C. Matching range is increased
D. It has no effect on impedance matching

## Slide 40: E5B Time constants and phase relationships
RLC time constants; definition; time constants in RL and RC circuits; phase angle between voltage and current; phase angles of series RLC; phase angle of inductance vs susceptance; admittance and susceptance

## Slide 41: Time Constants Tutorial
When a voltage is applied to a capacitor through a resistance (all circuits have resistance) it takes time for the voltage across the capacitor to reach the applied voltage. At the instant the voltage is applied the current in the circuit is at a maximum limited only by the circuit resistance. As time passes the voltage across the capacitor rises and the current decreases until the capacitor charge reaches the applied voltage at which point the current goes to zero.
The voltage across the capacitor will rise to 63.2 % of the applied voltage in one time constant. The time constant in seconds is calculated by multiplying the resistance in megohms by the capacitance in microfarads. TC= R(ohms) x C(farads) or in terms of more common values --TC= R (megohms) x C(microfarads)
For example, 100 volts applied to 1μF capacitor with a series one megohm resistor will charge to 63.2 volts in one second.
Remember that TC= R (megohms) x C(microfarads) or TC= 1x1 or 1 second and the charge after 1 time constant will be 63.2% of the applied 100 volts, or 63.2 volts

## Slide 42: E5B01 What is the term for the time required for the capacitor in an RC circuit to be charged to 63.2% of the applied voltage?
A. An exponential rate of one
B. One time constant
C. One exponential period
D. A time factor of one

## Slide 43: E5B01 What is the term for the time required for the capacitor in an RC circuit to be charged to 63.2% of the applied voltage?
A. An exponential rate of one
B. One time constant
C. One exponential period
D. A time factor of one
Time Constants | Charge % of applied voltage | Discharge % of starting voltage
1 | 63.2 | 36.8
2 | 86.5 | 13.5
3 | 95 | 5
4 | 98.2 | 1.8
5 | 99.3 | .7

## Slide 44: E5B02 What is the term for the time it takes for a charged capacitor in an RC circuit to discharge to 36.8% of its initial voltage?
A. One discharge period
B. An exponential discharge rate of one
C. A discharge factor of one
D. One time constant

## Slide 45: E5B02 What is the term for the time it takes for a charged capacitor in an RC circuit to discharge to 36.8% of its initial voltage?
A. One discharge period
B. An exponential discharge rate of one
C. A discharge factor of one
D. One time constant
Time Constants | Charge % of applied voltage | Discharge % of starting voltage
1 | 63.2 | 36.8
2 | 86.5 | 13.5
3 | 95 | 5
4 | 98.2 | 1.8
5 | 99.3 | .7

## Slide 46: E5B03 What happens to the phase angle of a reactance when it is converted to a susceptance?
A. It is unchanged
B. The sign is reversed
C. It is shifted by 90 degrees
D. The susceptance phase angle is the inverse of the reactance phase angle

## Slide 47: E5B03 What happens to the phase angle of a reactance when it is converted to a susceptance?
A. It is unchanged
B. The sign is reversed
C. It is shifted by 90 degrees
D. The susceptance phase angle is the inverse of the reactance phase angle

## Slide 48: E5B04 What is the time constant of a circuit having two 220 microfarad capacitors and two 1 megohm resistors, all in parallel?
A. 55 seconds
B. 110 seconds
C. 440 seconds
D. 220 seconds

## Slide 49: E5B04 What is the time constant of a circuit having two 220 microfarad capacitors and two 1 megohm resistors, all in parallel?
A. 55 seconds
B. 110 seconds
C. 440 seconds
D. 220 seconds
TC (seconds) = R (megohms) x C (microfarads)
TC =(1/2) x (220 x 2)
TC= 0.5 x 440
TC= 220 seconds
Remember that capacitors in parallel add and resistors of equal value in parallel are equal to one resistor divided by the number of resistors.

## Slide 50: E5B05 What happens to the magnitude of a reactance when it is converted to a susceptance?
A. It is unchanged
B. The sign is reversed
C. It is shifted by 90 degrees
D. The magnitude of the susceptance is the reciprocal of the magnitude of the reactance

## Slide 51: E5B05 What happens to the magnitude of a reactance when it is converted to a susceptance?
A. It is unchanged
B. The sign is reversed
C. It is shifted by 90 degrees
D. The magnitude of the susceptance is the reciprocal of the magnitude of the reactance

## Slide 52: E5B06 What is susceptance?
A. The magnetic impedance of a circuit
B. The ratio of magnetic field to electric field
C. The inverse of reactance
D. A measure of the efficiency of a transformer

## Slide 53: E5B06 What is susceptance?
A. The magnetic impedance of a circuit
B. The ratio of magnetic field to electric field
C. The inverse of reactance
D. A measure of the efficiency of a transformer

## Slide 54: SINE, COSINE and TANGENTS
Sine = B / C = 4 /5 = .80
Cosine = A / C = 3/ 5 = .60
Tangent = B / A = 4 /3 =1.25
C B 5 4
Angle is 53 degrees
A 3
Angle 53 degrees

## Slide 55: 25
There are 4 angles
14 degrees
400
37 degrees
45 degrees
53 degrees
y
4 Triangles
100
14 degree
y
100
100
45 degree
y
300
400
300
400
37 degree
53 degree
500
500
141.4

## Slide 56: 3, 4, 5 Triangles
A2 + B 2 = C2
C = P A2 + B2 5
500 4
5 400
500 3
300
3
4 300
400 Angle 53 degrees
Angle 37 degrees

## Slide 57: E5B07 What is the phase angle between the voltage across and the current through a series RLC circuit if XC is 500 ohms, R is 1 kilohm, and XL is 250 ohms?
A. 68.2 degrees with the voltage leading the current
B. 14.0 degrees with the voltage leading the current
C. 14.0 degrees with the voltage lagging the current
D. 68.2 degrees with the voltage lagging the current

## Slide 58: E5B07 What is the phase angle between the voltage across and the current through a series RLC circuit if XC is 500 ohms, R is 1 kilohm, and XL is 250 ohms?
A. 68.2 degrees with the voltage leading the current
B. 14.0 degrees with the voltage leading the current
C. 14.0 degrees with the voltage lagging the current
D. 68.2 degrees with the voltage lagging the current
Net Reactance = XL – XC = 250 – 500 = -250 ohms
Degrees is anti-Tangent = (250 / 1000) = 0.25 = 14 degrees
Since capacitance is greater than inductance,
it is a negative angle and Voltage lags current

## Slide 59: E5B08 What is the phase angle between the voltage across and the current through a series RLC circuit if XC is 100 ohms, R is 100 ohms, and XL is 75 ohms?
A. 14 degrees with the voltage lagging the current
B. 14 degrees with the voltage leading the current
C. 76 degrees with the voltage leading the current
D. 76 degrees with the voltage lagging the current

## Slide 60: E5B08 What is the phase angle between the voltage across and the current through a series RLC circuit if XC is 100 ohms, R is 100 ohms, and XL is 75 ohms?
A. 14 degrees with the voltage lagging the current
B. 14 degrees with the voltage leading the current
C. 76 degrees with the voltage leading the current
D. 76 degrees with the voltage lagging the current
Net Reactance = XL – XC = 75 – 100 = -25 ohms
Degrees is anti-Tangent = (25 / 100) = 0.25 = 14 degrees
Since capacitance is greater than inductance,
it is a negative angle and Voltage lags current

## Slide 61: E5B09 What is the relationship between the current through a capacitor and the voltage across a capacitor?
A. Voltage and current are in phase
B. Voltage and current are 180 degrees out of phase
C. Voltage leads current by 90 degrees
D. Current leads voltage by 90 degrees

## Slide 62: E5B09 What is the relationship between the current through a capacitor and the voltage across a capacitor?
A. Voltage and current are in phase
B. Voltage and current are 180 degrees out of phase
C. Voltage leads current by 90 degrees
D. Current leads voltage by 90 degrees

## Slide 63: E5B10 What is the relationship between the current through an inductor and the voltage across an inductor?
A. Voltage leads current by 90 degrees
B. Current leads voltage by 90 degrees
C. Voltage and current are 180 degrees out of phase
D. Voltage and current are in phase

## Slide 64: E5B10 What is the relationship between the current through an inductor and the voltage across an inductor?
A. Voltage leads current by 90 degrees
B. Current leads voltage by 90 degrees
C. Voltage and current are 180 degrees out of phase
D. Voltage and current are in phase

## Slide 65: E5B11 What is the phase angle between the voltage across and the current through a series RLC circuit if XC is 25 ohms, R is 100 ohms, and XL is 50 ohms?
A. 14 degrees with the voltage lagging the current
B. 14 degrees with the voltage leading the current
C. 76 degrees with the voltage lagging the current
D. 76 degrees with the voltage leading the current

## Slide 66: E5B11 What is the phase angle between the voltage across and the current through a series RLC circuit if XC is 25 ohms, R is 100 ohms, and XL is 50 ohms?
A. 14 degrees with the voltage lagging the current
B. 14 degrees with the voltage leading the current
C. 76 degrees with the voltage lagging the current
D. 76 degrees with the voltage leading the current
Net Reactance = XL – XC = 50 – 25 = + 25 ohms
Degrees is anti-Tangent = (25 / 100) = 0.25 = 14 degrees
Since capacitance is less than inductance,
it is a positive angle and Voltage leads current

## Slide 67: E5B12 What is admittance?
A. The inverse of impedance
B. The term for the gain of a field effect transistor
C. The turns ratio of a transformer
D. The unit used for Q factor

## Slide 68: E5B12 What is admittance?
A. The inverse of impedance
B. The term for the gain of a field effect transistor
C. The turns ratio of a transformer
D. The unit used for Q factor

## Slide 69: E5B13 What letter is commonly used to represent susceptance?
A. G
B. X
C. Y
D. B

## Slide 70: E5B13 What letter is commonly used to represent susceptance?
A. G
B. X
C. Y
D. B

## Slide 71: E5C Coordinate systems
and phasors in electronics: Rectangular coordinates; Polar Coordinates; Phasors

## Slide 72: E5C01 Which of the following represents a capacitive reactance in rectangular notation?
A. –jX
B. +jX
C. X
D. Omega

## Slide 73: E5C01 Which of the following represents a capacitive reactance in rectangular notation?
A. –jX
B. +jX
C. X
D. Omega

## Slide 74: E5C02 How are impedances described in polar coordinates?
A. By X and R values
B. By real and imaginary parts
C. By phase angle and amplitude
D. By Y and G values

## Slide 75: E5C02 How are impedances described in polar coordinates?
A. By X and R values
B. By real and imaginary parts
C. By phase angle and amplitude
D. By Y and G values

## Slide 76: E5C03 Which of the following represents an inductive reactance in polar coordinates?
A. A positive real part
B. A negative real part
C. A positive phase angle
D. A negative phase angle

## Slide 77: E5C03 Which of the following represents an inductive reactance in polar coordinates?
A. A positive real part
B. A negative real part
C. A positive phase angle
D. A negative phase angle

## Slide 78: E5C04 Which of the following represents a capacitive reactance in polar coordinates?
A. A positive real part
B. A negative real part
C. A positive phase angle
D. A negative phase angle

## Slide 79: E5C04 Which of the following represents a capacitive reactance in polar coordinates?
A. A positive real part
B. A negative real part
C. A positive phase angle
D. A negative phase angle

## Slide 80: E5C05 What is the name of the diagram used to show the phase relationship between impedances at a given frequency?
A. Venn diagram
B. Near field diagram
C. Phasor diagram
D. Far field diagram

## Slide 81: E5C05 What is the name of the diagram used to show the phase relationship between impedances at a given frequency?
A. Venn diagram
B. Near field diagram
C. Phasor diagram
D. Far field diagram

## Slide 82: E5C06 What does the impedance 50–j25 represent?
A. 50 ohms resistance in series with 25 ohms inductive reactance
B. 50 ohms resistance in series with 25 ohms capacitive reactance
C. 25 ohms resistance in series with 50 ohms inductive reactance
D. 25 ohms resistance in series with 50 ohms capacitive reactance

## Slide 83: E5C06 What does the impedance 50–j25 represent?
A. 50 ohms resistance in series with 25 ohms inductive reactance
B. 50 ohms resistance in series with 25 ohms capacitive reactance
C. 25 ohms resistance in series with 50 ohms inductive reactance
D. 25 ohms resistance in series with 50 ohms capacitive reactance

## Slide 84: E5C07 What is a vector?
A. The value of a quantity that changes over time
B. A quantity with both magnitude and an angular component
C. The inverse of the tangent function
D. The inverse of the sine function

## Slide 85: E5C07 What is a vector?
A. The value of a quantity that changes over time
B. A quantity with both magnitude and an angular component
C. The inverse of the tangent function
D. The inverse of the sine function

## Slide 86: E5C08 What coordinate system is often used to display the phase angle of a circuit containing resistance, inductive and/or capacitive reactance?
A. Maidenhead grid
B. Faraday grid
C. Elliptical coordinates
D. Polar coordinates

## Slide 87: E5C08 What coordinate system is often used to display the phase angle of a circuit containing resistance, inductive and/or capacitive reactance?
A. Maidenhead grid
B. Faraday grid
C. Elliptical coordinates
D. Polar coordinates

## Slide 88: E5C09 When using rectangular coordinates to graph the impedance of a circuit, what does the horizontal axis represent?
A. Resistive component
B. Reactive component
C. The sum of the reactive and resistive components
D. The difference between the resistive and reactive components

## Slide 89: E5C09 When using rectangular coordinates to graph the impedance of a circuit, what does the horizontal axis represent?
A. Resistive component
B. Reactive component
C. The sum of the reactive and resistive components
D. The difference between the resistive and reactive components

## Slide 90: E5C10 When using rectangular coordinates to graph the impedance of a circuit, what does the vertical axis represent?
A. Resistive component
B. Reactive component
C. The sum of the reactive and resistive components
D. The difference between the resistive and reactive components

## Slide 91: E5C10 When using rectangular coordinates to graph the impedance of a circuit, what does the vertical axis represent?
A. Resistive component
B. Reactive component
C. The sum of the reactive and resistive components
D. The difference between the resistive and reactive components

## Slide 92: E5C11 What do the two numbers that are used to define a point on a graph using rectangular coordinates represent?
A. The magnitude and phase of the point
B. The sine and cosine values
C. The coordinate values along the horizontal and vertical axes
D. The tangent and cotangent values

## Slide 93: E5C11 What do the two numbers that are used to define a point on a graph using rectangular coordinates represent?
A. The magnitude and phase of the point
B. The sine and cosine values
C. The coordinate values along the horizontal and vertical axes
D. The tangent and cotangent values

## Slide 94: E5C12 If you plot the impedance of a circuit using the rectangular coordinate system and find the impedance point falls on the right side of the graph on the horizontal axis, what do you know about the circuit?
A. It has to be a direct current circuit
B. It contains resistance and capacitive reactance
C. It contains resistance and inductive reactance
D. It is equivalent to a pure resistance

## Slide 95: E5C12 If you plot the impedance of a circuit using the rectangular coordinate system and find the impedance point falls on the right side of the graph on the horizontal axis, what do you know about the circuit?
A. It has to be a direct current circuit
B. It contains resistance and capacitive reactance
C. It contains resistance and inductive reactance
D. It is equivalent to a pure resistance

## Slide 96: E5C13 What coordinate system is often used to display the resistive, inductive, and/or capacitive reactance components of an impedance?
A. Maidenhead grid
B. Faraday grid
C. Elliptical coordinates
D. Rectangular coordinates

## Slide 97: E5C13 What coordinate system is often used to display the resistive, inductive, and/or capacitive reactance components of an impedance?
A. Maidenhead grid
B. Faraday grid
C. Elliptical coordinates
D. Rectangular coordinates

## Slide 98: E5C14 What coordinate system is often used to display the phase angle of a circuit containing resistance, inductive and/or capacitive reactance?
A. Maidenhead grid
B. Faraday grid
C. Elliptical coordinates
D. Polar coordinates

## Slide 99: E5C14 What coordinate system is often used to display the phase angle of a circuit containing resistance, inductive and/or capacitive reactance?
A. Maidenhead grid
B. Faraday grid
C. Elliptical coordinates
D. Polar coordinates

## Slide 100: Rectangular Coordinates
Reactance positive ?
Inductive
Reactance negative ?
Capacitive
Reactance
= L - C

## Slide 101: E5C14 Which point on Figure E5-2 best represents the impedance of a series circuit consisting of a 400 ohm resistor and a 38 picofarad capacitor at 14 MHz?
A. Point 2
B. Point 4
C. Point 5
D. Point 6

## Slide 102: E5C14 Which point on Figure E5-2 best represents the impedance of a series circuit consisting of a 400 ohm resistor and a 38 picofarad capacitor at 14 MHz?
A. Point 2
B. Point 4
C. Point 5
D. Point 6
XC = 1 / (2 Pi * F * C)
XC = 1 / (6.28 * 14 MHz * 38pf
XC = 300 ohm

## Slide 103: E5C15 Which point in Figure E5-2 best represents the impedance of a series circuit consisting of a 300 ohm resistor and an 18 microhenry inductor at 3.505 MHz?
A. Point 1
B. Point 3
C. Point 7
D. Point 8

## Slide 104: E5C15 Which point in Figure E5-2 best represents the impedance of a series circuit consisting of a 300 ohm resistor and an 18 microhenry inductor at 3.505 MHz?
A. Point 1
B. Point 3
C. Point 7
D. Point 8
XL = 2 * Pi * F * L)
XL = 6.28 * 3.505 MHz. * 18µh
XL = 396 ohm

## Slide 105: E5C16 Which point on Figure E5-2 best represents the impedance of a series circuit consisting of a 300 ohm resistor and a 19 picofarad capacitor at 21.200 MHz?
A. Point 1
B. Point 3
C. Point 7
D. Point 8

## Slide 106: E5C16 Which point on Figure E5-2 best represents the impedance of a series circuit consisting of a 300 ohm resistor and a 19 picofarad capacitor at 21.200 MHz?
A. Point 1
B. Point 3
C. Point 7
D. Point 8
XC = 1 / (2 Pi * F * C)
XC = 1 / (6.28 * 21.2 MHz. * 19pf
XC = 395 ohm

## Slide 107: E5C17 Which point on Figure E5-2 best represents the impedance of a series circuit consisting of a 300 ohm resistor, a 0.64-microhenry inductor and an 85-picofarad capacitor at 24.900 MHz?
A. Point 1
B. Point 3
C. Point 5
D. Point 8

## Slide 108: E5C17 Which point on Figure E5-2 best represents the impedance of a series circuit consisting of a 300 ohm resistor, a 0.64-microhenry inductor and an 85-picofarad capacitor at 24.900 MHz?
A. Point 1
B. Point 3
C. Point 5
D. Point 8
XL = 2 * Pi * F * L)
XL = 6.28 * 24.9 MHz. * 85 µh
XL = 100 ohm
XL – XC = 100 – 75 = + 25 ohms
XC = 1 / (2 Pi * F * C)
XC = 1 / (6.28 * 24.9 MHz. * 85 pf
XC = 75 ohm

## Slide 109: E5D AC and RF energy in real circuits
skin effect; electrostatic and electromagnetic fields; reactive power; power factor; electrical length of conductors at UHF and microwave frequencies

## Slide 110: E5D01 What is the result of skin effect?
A. As frequency increases, RF current flows in a thinner layer of the conductor, closer to the surface
B. As frequency decreases, RF current flows in a thinner layer of the conductor, closer to the surface
C. Thermal effects on the surface of the conductor increase the impedance
D. Thermal effects on the surface of the conductor decrease the impedance

## Slide 111: E5D01 What is the result of skin effect?
A. As frequency increases, RF current flows in a thinner layer of the conductor, closer to the surface
B. As frequency decreases, RF current flows in a thinner layer of the conductor, closer to the surface
C. Thermal effects on the surface of the conductor increase the impedance
D. Thermal effects on the surface of the conductor decrease the impedance

## Slide 112: E5D02 Why is it important to keep lead lengths short for components used in circuits for VHF and above?
A. To increase the thermal time constant
B. To avoid unwanted inductive reactance
C. To maintain component lifetime
D. All of these choices are correct

## Slide 113: E5D02 Why is it important to keep lead lengths short for components used in circuits for VHF and above?
A. To increase the thermal time constant
B. To avoid unwanted inductive reactance
C. To maintain component lifetime
D. All of these choices are correct

## Slide 114: E5D03 What is microstrip?
A. Lightweight transmission line made of common zip cord
B. Miniature coax used for low power applications
C. Short lengths of coax mounted on printed circuit boards to minimize time delay between microwave circuits
D. Precision printed circuit conductors above a ground plane that provide constant impedance interconnects at microwave frequencies

## Slide 115: E5D03 What is microstrip?
A. Lightweight transmission line made of common zip cord
B. Miniature coax used for low power applications
C. Short lengths of coax mounted on printed circuit boards to minimize time delay between microwave circuits
D. Precision printed circuit conductors above a ground plane that provide constant impedance interconnects at microwave frequencies

## Slide 116: E5D04 Why are short connections necessary at microwave frequencies?
A. To increase neutralizing resistance
B. To reduce phase shift along the connection
C. Because of ground reflections
D. To reduce noise figure

## Slide 117: E5D04 Why are short connections necessary at microwave frequencies?
A. To increase neutralizing resistance
B. To reduce phase shift along the connection
C. Because of ground reflections
D. To reduce noise figure

## Slide 118: E5D05 Which parasitic characteristic increases with conductor length?
A. Inductance
B. Permeability
C. Permittivity
D. Malleability

## Slide 119: E5D05 Which parasitic characteristic increases with conductor length?
A. Inductance
B. Permeability
C. Permittivity
D. Malleability

## Slide 120: E5D06 In what direction is the magnetic field oriented about a conductor in relation to the direction of electron flow?
A. In the same direction as the current
B. In a direction opposite to the current
C. In all directions; omni-directional
D. In a direction determined by the left-hand rule

## Slide 121: Left Hand Rule
The Left Hand Rule shows what happens when charged particles (such as electrons in a current) enter a
magnetic field. You need to contort your hand in an unnatural position for this rule, illustrated below. As you can
see, if your index finger points in the direction of a magnetic field, and your middle finger, at a 90 degree angle to
your index, points in the direction of the charged particle (as in an electrical current), then your extended thumb
(forming an L with your index) points in the direction of the force exerted upon that particle. This rule is also called
Fleming's Left Hand Rule, after English electronics pioneer John Ambrose Fleming, who came up with it.

## Slide 122: E5D06 In what direction is the magnetic field oriented about a conductor in relation to the direction of electron flow?
A. In the same direction as the current
B. In a direction opposite to the current
C. In all directions; omni-directional
D. In a direction determined by the left-hand rule

## Slide 123: E5D07 What determines the strength of the magnetic field around a conductor?
A. The resistance divided by the current
B. The ratio of the current to the resistance
C. The diameter of the conductor
D. The amount of current flowing through the conductor

## Slide 124: E5D07 What determines the strength of the magnetic field around a conductor?
A. The resistance divided by the current
B. The ratio of the current to the resistance
C. The diameter of the conductor
D. The amount of current flowing through the conductor

## Slide 125: E5D08 What type of energy is stored in an electromagnetic or electrostatic field?
A. Electromechanical energy
B. Potential energy
C. Thermodynamic energy
D. Kinetic energy

## Slide 126: E5D08 What type of energy is stored in an electromagnetic or electrostatic field?
A. Electromechanical energy
B. Potential energy
C. Thermodynamic energy
D. Kinetic energy

## Slide 127: E5D09 What happens to reactive power in an AC circuit that has both ideal inductors and ideal capacitors?
A. It is dissipated as heat in the circuit
B. It is repeatedly exchanged between the associated magnetic and electric fields, but is not dissipated
C. It is dissipated as kinetic energy in the circuit
D. It is dissipated in the formation of inductive and capacitive fields

## Slide 128: E5D09 What happens to reactive power in an AC circuit that has both ideal inductors and ideal capacitors?
A. It is dissipated as heat in the circuit
B. It is repeatedly exchanged between the associated magnetic and electric fields, but is not dissipated
C. It is dissipated as kinetic energy in the circuit
D. It is dissipated in the formation of inductive and capacitive fields

## Slide 129: E5D10 How can the true power be determined in an AC circuit where the voltage and current are out of phase?
A. By multiplying the apparent power times the power factor
B. By dividing the reactive power by the power factor
C. By dividing the apparent power by the power factor
D. By multiplying the reactive power times the power factor

## Slide 130: E5D10 How can the true power be determined in an AC circuit where the voltage and current are out of phase?
A. By multiplying the apparent power times the power factor
B. By dividing the reactive power by the power factor
C. By dividing the apparent power by the power factor
D. By multiplying the reactive power times the power factor

## Slide 131: E5D11 What is the power factor of an R-L circuit having a 60 degree phase angle between the voltage and the current?
A. 1.414
B. 0.866
C. 0.5
D. 1.73

## Slide 132: E5D11 What is the power factor of an R-L circuit having a 60 degree phase angle between the voltage and the current?
A. 1.414
B. 0.866
C. 0.5
D. 1.73
Power Factor = cosine of angle
Cosine 60 degrees = 0.5

## Slide 133: E5D12 How many watts are consumed in a circuit having a power factor of 0.2 if the input is 100-VAC at 4 amperes?
A. 400 watts
B. 80 watts
C. 2000 watts
D. 50 watts

## Slide 134: E5D12 How many watts are consumed in a circuit having a power factor of 0.2 if the input is 100-VAC at 4 amperes?
A. 400 watts
B. 80 watts
C. 2000 watts
D. 50 watts
P = 100 * 4 = 400 watts
400 watts * 0.2 = 80 watts

## Slide 135: E5D13 How much power is consumed in a circuit consisting of a 100 ohm resistor in series with a 100 ohm inductive reactance drawing 1 ampere?
A. 70.7 Watts
B. 100 Watts
C. 141.4 Watts
D. 200 Watts

## Slide 136: E5D13 How much power is consumed in a circuit consisting of a 100 ohm resistor in series with a 100 ohm inductive reactance drawing 1 ampere?
A. 70.7 Watts
B. 100 Watts
C. 141.4 Watts
D. 200 Watts
P = I ² * R = 1*1 * 100
P = 100 watts

## Slide 137: E5D14 What is reactive power?
A. Wattless, nonproductive power
B. Power consumed in wire resistance in an inductor
C. Power lost because of capacitor leakage
D. Power consumed in circuit Q

## Slide 138: E5D14 What is reactive power?
A. Wattless, nonproductive power
B. Power consumed in wire resistance in an inductor
C. Power lost because of capacitor leakage
D. Power consumed in circuit Q

## Slide 139: E5D15 What is the power factor of an R-L circuit having a 45 degree phase angle between the voltage and the current?
A. 0.866
B. 1.0
C. 0.5
D. 0.707

## Slide 140: E5D15 What is the power factor of an R-L circuit having a 45 degree phase angle between the voltage and the current?
A. 0.866
B. 1.0
C. 0.5
D. 0.707
Power Factor = cosine of angle
Cosine 45 degrees = 0.707

## Slide 141: E5D16 What is the power factor of an R-L circuit having a 30 degree phase angle between the voltage and the current?
A. 1.73
B. 0.5
C. 0.866
D. 0.577

## Slide 142: E5D16 What is the power factor of an R-L circuit having a 30 degree phase angle between the voltage and the current?
A. 1.73
B. 0.5
C. 0.866
D. 0.577
Power Factor = cosine of angle
Cosine 30 degrees = 0.866

## Slide 143: E5D17 How many watts are consumed in a circuit having a power factor of 0.6 if the input is 200VAC at 5 amperes?
A. 200 watts
B. 1000 watts
C. 1600 watts
D. 600 watts

## Slide 144: E5D17 How many watts are consumed in a circuit having a power factor of 0.6 if the input is 200VAC at 5 amperes?
A. 200 watts
B. 1000 watts
C. 1600 watts
D. 600 watts
P = 200 * 5 = 1,000 watts
1,000 watts * 0.6 = 600 watts

## Slide 145: E5D18 How many watts are consumed in a circuit having a power factor of 0.71 if the apparent power is 500VA?
A. 704 W
B. 355 W
C. 252 W
D. 1.42 mW

## Slide 146: E5D18 How many watts are consumed in a circuit having a power factor of 0.71 if the apparent power is 500VA?
A. 704 W
B. 355 W
C. 252 W
D. 1.42 mW
P = VA * PF
P = 500 VA * 0.71 = 355 W

## Slide 147: End of SUBELEMENT E5
ELECTRICAL PRINCIPLES