## Slide 1: SUBELEMENT G4 AMATEUR RADIO PRACTICES [5 Exam Questions - 5 groups]
Notes: Subelement G4 Amateur Radio Practices. General Training Slides for 2015 Question Pool Good through June 30, 2019 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM, Howard Schultz, W7HS.
<number>

## Slide 2
G4A – Station Operation and set up
G4B - Test and monitoring equipment; two-tone test
G4C - Interference with consumer electronics; grounding; DSP
G4D - Speech processors; S meters; sideband operation near band edges
G4E - HF mobile radio installations; emergency and battery powered operation
<number>
Radio Practices

## Slide 3: G4A – Station Operation and set up
<number>
Radio Practices

## Slide 4: G4A01 - What is the purpose of the "notch filter" found on many HF transceivers?
A. To restrict the transmitter voice bandwidth
B. To reduce interference from carriers in the receiver passband
C. To eliminate receiver interference from impulse noise sources
D. To enhance the reception of a specific frequency on a crowded band
<number>
Radio Practices

## Slide 5: G4A01 - What is the purpose of the "notch filter" found on many HF transceivers?
A. To restrict the transmitter voice bandwidth
B. To reduce interference from carriers in the receiver passband
C. To eliminate receiver interference from impulse noise sources
D. To enhance the reception of a specific frequency on a crowded band
<number>
Radio Practices

## Slide 6: G4A02 - What is one advantage of selecting the opposite or "reverse" sideband when receiving CW signals on a typical HF transceiver?
A. Interference from impulse noise will be eliminated
B. More stations can be accommodated within a given signal passband
C. It may be possible to reduce or eliminate interference from other signals
D. Accidental out of band operation can be prevented
<number>
Radio Practices

## Slide 7: G4A02 - What is one advantage of selecting the opposite or "reverse" sideband when receiving CW signals on a typical HF transceiver?
A. Interference from impulse noise will be eliminated
B. More stations can be accommodated within a given signal passband
C. It may be possible to reduce or eliminate interference from other signals
D. Accidental out of band operation can be prevented
<number>
Radio Practices

## Slide 8: G4A03 - What is normally meant by operating a transceiver in "split" mode?
A. The radio is operating at half power
B. The transceiver is operating from an external power source
C. The transceiver is set to different transmit and receive frequencies
D. The transmitter is emitting an SSB signal, as opposed to DSB operation
<number>
Radio Practices

## Slide 9: G4A03 - What is normally meant by operating a transceiver in "split" mode?
A. The radio is operating at half power
B. The transceiver is operating from an external power source
C. The transceiver is set to different transmit and receive frequencies
D. The transmitter is emitting an SSB signal, as opposed to DSB operation
<number>
Radio Practices

## Slide 10: G4A04 - What reading on the plate current meter of a vacuum tube RF power amplifier indicates correct adjustment of the plate tuning control?
A. A pronounced peak
B. A pronounced dip
C. No change will be observed
D. A slow, rhythmic oscillation
<number>
Radio Practices

## Slide 11: G4A04 - What reading on the plate current meter of a vacuum tube RF power amplifier indicates correct adjustment of the plate tuning control?
A. A pronounced peak
B. A pronounced dip
C. No change will be observed
D. A slow, rhythmic oscillation
<number>
Radio Practices

## Slide 12: G4A05 - What is a reason to use Automatic Level Control ( ALC ) with an RF power amplifier?
A. To balance the transmitter audio frequency response
B. To reduce harmonic radiation
C. To reduce distortion due to excessive drive
D. To increase overall efficiency
<number>
Radio Practices

## Slide 13: G4A05 - What is a reason to use Automatic Level Control ( ALC ) with an RF power amplifier?
A. To balance the transmitter audio frequency response
B. To reduce harmonic radiation
C. To reduce distortion due to excessive drive
D. To increase overall efficiency
<number>
Radio Practices

## Slide 14: G4A06 - What type of device is often used to match transmitter output impedance to an impedance not equal to 50 ohms?
A. Balanced modulator
B. SWR Bridge
C. Antenna coupler or antenna tuner
D. Q Multiplier
<number>
Radio Practices

## Slide 15: G4A06 - What type of device is often used to match transmitter output impedance to an impedance not equal to 50 ohms?
A. Balanced modulator
B. SWR Bridge
C. Antenna coupler or antenna tuner
D. Q Multiplier
<number>
Radio Practices

## Slide 16: G4A07 - What condition can lead to permanent damage to a solid-state RF power amplifier?
A. Insufficient drive power
B. Low input SWR
C. Shorting the input signal to ground
D. Excessive drive power
<number>
Radio Practices

## Slide 17: G4A07 - What condition can lead to permanent damage to a solid-state RF power amplifier?
A. Insufficient drive power
B. Low input SWR
C. Shorting the input signal to ground
D. Excessive drive power
<number>
Radio Practices

## Slide 18: G4A08 - What is the correct adjustment for the load or coupling control of a vacuum tube RF power amplifier?
A. Minimum SWR on the antenna
B. Minimum plate current without exceeding maximum allowable grid current
C. Highest plate voltage while minimizing grid current
D. Maximum power output without exceeding maximum allowable plate current
<number>
Radio Practices

## Slide 19: G4A08 - What is the correct adjustment for the load or coupling control of a vacuum tube RF power amplifier?
A. Minimum SWR on the antenna
B. Minimum plate current without exceeding maximum allowable grid current
C. Highest plate voltage while minimizing grid current
D. Maximum power output without exceeding maximum allowable plate current
<number>
Radio Practices

## Slide 20: G4A09 - Why is a time delay sometimes included in a transmitter keying circuit?
A. To prevent stations from interfering with one another
B. To allow the transmitter power regulators to charge properly
C. To allow time for transmit-receive changeover operations to complete properly before RF output is allowed
D. To allow time for a warning signal to be sent to other stations
<number>
Radio Practices

## Slide 21: G4A09 - Why is a time delay sometimes included in a transmitter keying circuit?
A. To prevent stations from interfering with one another
B. To allow the transmitter power regulators to charge properly
C. To allow time for transmit-receive changeover operations to complete properly before RF output is allowed
D. To allow time for a warning signal to be sent to other stations
<number>
Radio Practices

## Slide 22: G4A10 - What is the purpose of an electronic keyer?
A. Automatic transmit/receive switching
B. Automatic generation of strings of dots and dashes for CW operation
C. VOX operation
D. Computer interface for PSK and RTTY operation
<number>
Radio Practices

## Slide 23: G4A10 - What is the purpose of an electronic keyer?
A. Automatic transmit/receive switching
B. Automatic generation of strings of dots and dashes for CW operation
C. VOX operation
D. Computer interface for PSK and RTTY operation
<number>
Radio Practices

## Slide 24: G4A11 - Which of the following is a use for the IF shift control on a receiver?
A. To avoid interference from stations very close to the receive frequency
B. To change frequency rapidly
C. To permit listening on a different frequency from that on which you are transmitting
D. To tune in stations that are slightly off frequency without changing your transmit frequency
<number>
Radio Practices

## Slide 25: G4A11 - Which of the following is a use for the IF shift control on a receiver?
A. To avoid interference from stations very close to the receive frequency
B. To change frequency rapidly
C. To permit listening on a different frequency from that on which you are transmitting
D. To tune in stations that are slightly off frequency without changing your transmit frequency
<number>
Radio Practices

## Slide 26: G4A12 - Which of the following is a common use for the dual VFO feature on a transceiver?
A. To allow transmitting on two frequencies at once
B. To permit full duplex operation, that is transmitting and receiving at the same time
C. To permit monitoring of two different frequencies
D. To facilitate computer interface
<number>
Radio Practices

## Slide 27: G4A12 - Which of the following is a common use for the dual VFO feature on a transceiver?
A. To allow transmitting on two frequencies at once
B. To permit full duplex operation, that is transmitting and receiving at the same time
C. To permit monitoring of two different frequencies
D. To facilitate computer interface
<number>
Radio Practices

## Slide 28: G4A13 - What is one reason to use the attenuator function that is present on many HF transceivers?
A. To reduce signal overload due to strong incoming signals
B. To reduce the transmitter power when driving a linear amplifier
C. To reduce power consumption when operating from batteries
D. To slow down received CW signals for better copy
<number>
Radio Practices

## Slide 29: G4A13 - What is one reason to use the attenuator function that is present on many HF transceivers?
A. To reduce signal overload due to strong incoming signals
B. To reduce the transmitter power when driving a linear amplifier
C. To reduce power consumption when operating from batteries
D. To slow down received CW signals for better copy
<number>
Radio Practices

## Slide 30: G4A14 - What is likely to happen if a transceiver’s ALC system is not set properly when transmitting AFSK signals with the radio using single sideband mode?
A. ALC will invert the modulation of the AFSK mode
B. Improper action of ALC distorts the signal and can cause spurious emissions
C. When using digital modes, too much ALC activity can cause the transmitter to overheat
D. All of these choices are correct
<number>
Radio Practices

## Slide 31: G4A14 - What is likely to happen if a transceiver’s ALC system is not set properly when transmitting AFSK signals with the radio using single sideband mode?
A. ALC will invert the modulation of the AFSK mode
B. Improper action of ALC distorts the signal and can cause spurious emissions
C. When using digital modes, too much ALC activity can cause the transmitter to overheat
D. All of these choices are correct
<number>
Radio Practices

## Slide 32: G4A15 - Which of the following can be a symptom of transmitted RF being picked up by an audio cable carrying AFSK data signals between a computer and a transceiver?
A. The VOX circuit does not un-key the transmitter
B. The transmitter signal is distorted
C. Frequent connection timeouts
D. All of these choices are correct
<number>
Radio Practices

## Slide 33: G4A15 - Which of the following can be a symptom of transmitted RF being picked up by an audio cable carrying AFSK data signals between a computer and a transceiver?
A. The VOX circuit does not un-key the transmitter
B. The transmitter signal is distorted
C. Frequent connection timeouts
D. All of these choices are correct
<number>
Radio Practices

## Slide 34: G4B - Test and monitoring equipment; two-tone test
<number>
Radio Practices

## Slide 35: Oscilloscope
<number>
Amateur Radio Practices
Notes: <number>
<number>
This is a current model Tektronix oscilloscope. It has four signal inputs along the lower right edge and can display the waveforms from those inputs. There are three main sections to the right of the screen; vertical, horizontal and trigger. The horizontal and vertical controls adjust how the waveform appears on the screen by adjusting the horizontal and vertical amplifiers. The trigger controls allow the oscilloscope to synchronize to external events.
Newer oscilloscopes are digital and can record data to the floppy seen here on the left or send to other external devices. By connecting the RF output of a transmitter (through appropriate connections) to the vertical input of the scope, the quality of a transmitted signal can be seen on the display.

## Slide 36: Audio Distortion
<number>
Amateur Radio Practices
Notes: <number>
<number>
Two tone audio tests are used on an oscilloscope to test proper linearity. The pure tones fed in will give you a stable picture on the scope if the amplifier is properly adjusted. The lower image shows a signal with some noise that it also overdriven (overmodulated) and is clipping or flattopping. Any two audio tones may be used, but they must be within the transmitter audio passband, and should not be harmonically related.
Speech Processors are used to keep input audio close to a perfect level for 100% modulation. If they are not adjusted properly, they can cause the distortion seen here. Overdriving causes very distorted audio and no additional power output.

## Slide 37: Field Strength Meter
<number>
Amateur Radio Practices
Notes: <number>
<number>
Here are two digital Field Strength Meter models. Some SWR meters and frequency counters can also be used as field strength meters. Field Strength Meters are used to test the density of an RF field. This allows testing of antenna patterns and ambient RF levels at repeater and home sites to insure safe levels.

## Slide 38: G4B01 - What item of test equipment contains horizontal and vertical channel amplifiers?
A. An ohmmeter
B. A signal generator
C. An ammeter
D. An oscilloscope
<number>
Radio Practices

## Slide 39: G4B01 - What item of test equipment contains horizontal and vertical channel amplifiers?
A. An ohmmeter
B. A signal generator
C. An ammeter
D. An oscilloscope
<number>
Radio Practices

## Slide 40: G4B02 - Which of the following is an advantage of an oscilloscope versus a digital voltmeter?
A. An oscilloscope uses less power
B. Complex impedances can be easily measured
C. Input impedance is much lower
D. Complex waveforms can be measured
<number>
Radio Practices

## Slide 41: G4B02 - Which of the following is an advantage of an oscilloscope versus a digital voltmeter?
A. An oscilloscope uses less power
B. Complex impedances can be easily measured
C. Input impedance is much lower
D. Complex waveforms can be measured
<number>
Radio Practices

## Slide 42: G4B03 - Which of the following is the best instrument to use when checking the keying waveform of a CW transmitter?
A. An oscilloscope
B. A field strength meter
C. A sidetone monitor
D. A wavemeter
<number>
Radio Practices

## Slide 43: G4B03 - Which of the following is the best instrument to use when checking the keying waveform of a CW transmitter?
A. An oscilloscope
B. A field strength meter
C. A sidetone monitor
D. A wavemeter
<number>
Radio Practices

## Slide 44: G4B04 - What signal source is connected to the vertical input of an oscilloscope when checking the RF envelope pattern of a transmitted signal?
A. The local oscillator of the transmitter
B. An external RF oscillator
C. The transmitter balanced mixer output
D. The attenuated RF output of the transmitter
<number>
Radio Practices

## Slide 45: G4B04 - What signal source is connected to the vertical input of an oscilloscope when checking the RF envelope pattern of a transmitted signal?
A. The local oscillator of the transmitter
B. An external RF oscillator
C. The transmitter balanced mixer output
D. The attenuated RF output of the transmitter
<number>
Radio Practices

## Slide 46: G4B05 - Why is high input impedance desirable for a voltmeter?
A. It improves the frequency response
B. It decreases battery consumption in the meter
C. It improves the resolution of the readings
D. It decreases the loading on circuits being measured
<number>
Radio Practices

## Slide 47: G4B05 - Why is high input impedance desirable for a voltmeter?
A. It improves the frequency response
B. It decreases battery consumption in the meter
C. It improves the resolution of the readings
D. It decreases the loading on circuits being measured
<number>
Radio Practices

## Slide 48: G4B06 - What is an advantage of a digital voltmeter as compared to an analog voltmeter?
A. Better for measuring computer circuits
B. Better for RF measurements
C. Better precision for most uses
D. Faster response
<number>
Radio Practices

## Slide 49: G4B06 - What is an advantage of a digital voltmeter as compared to an analog voltmeter?
A. Better for measuring computer circuits
B. Better for RF measurements
C. Better precision for most uses
D. Faster response
<number>
Radio Practices

## Slide 50: G4B07 - What signals are used to conduct a two-tone test?
A. Two audio signals of the same frequency shifted 90 degrees
B. Two non-harmonically related audio signals
C. Two swept frequency tones
D. Two audio frequency range square wave signals of equal amplitude
<number>
Radio Practices

## Slide 51: G4B07 - What signals are used to conduct a two-tone test?
A. Two audio signals of the same frequency shifted 90 degrees
B. Two non-harmonically related audio signals
C. Two swept frequency tones
D. Two audio frequency range square wave signals of equal amplitude
<number>
Radio Practices

## Slide 52: G4B08 - Which of the following instruments may be used to monitor relative RF output when making antenna and transmitter adjustments?
A. A field strength meter
B. An antenna noise bridge
C. A multimeter
D. A Q meter
<number>
Radio Practices

## Slide 53: G4B08 - Which of the following instruments may be used to monitor relative RF output when making antenna and transmitter adjustments?
A. A field strength meter
B. An antenna noise bridge
C. A multimeter
D. A Q meter
<number>
Radio Practices

## Slide 54: G4B09 - Which of the following can be determined with a field strength meter?
A. The radiation resistance of an antenna
B. The radiation pattern of an antenna
C. The presence and amount of phase distortion of a transmitter
D. The presence and amount of amplitude distortion of a transmitter
<number>
Radio Practices

## Slide 55: G4B09 - Which of the following can be determined with a field strength meter?
A. The radiation resistance of an antenna
B. The radiation pattern of an antenna
C. The presence and amount of phase distortion of a transmitter
D. The presence and amount of amplitude distortion of a transmitter
<number>
Radio Practices

## Slide 56: G4B10 - Which of the following can be determined with a directional wattmeter?
A. Standing wave ratio
B. Antenna front-to-back ratio
C. RF interference
D. Radio wave propagation
<number>
Radio Practices

## Slide 57: G4B10 - Which of the following can be determined with a directional wattmeter?
A. Standing wave ratio
B. Antenna front-to-back ratio
C. RF interference
D. Radio wave propagation
<number>
Radio Practices

## Slide 58: G4B11 - Which of the following must be connected to an antenna analyzer when it is being used for SWR measurements?
A. Receiver
B. Transmitter
C. Antenna and feed line
D. All of these choices are correct
<number>
Radio Practices

## Slide 59: G4B11 - Which of the following must be connected to an antenna analyzer when it is being used for SWR measurements?
A. Receiver
B. Transmitter
C. Antenna and feed line
D. All of these choices are correct
<number>
Radio Practices

## Slide 60: G4B12 - What problem can occur when making measurements on an antenna system with an antenna analyzer
A. Permanent damage to the analyzer may occur if it is operated into a high SWR
B. Strong signals from nearby transmitters can affect the accuracy of measurements
C. The analyzer can be damaged if measurements outside the ham bands are attempted
D. Connecting the analyzer to an antenna can cause it to absorb harmonics
<number>
Radio Practices

## Slide 61: G4B12 - What problem can occur when making measurements on an antenna system with an antenna analyzer
A. Permanent damage to the analyzer may occur if it is operated into a high SWR
B. Strong signals from nearby transmitters can affect the accuracy of measurements
C. The analyzer can be damaged if measurements outside the ham bands are attempted
D. Connecting the analyzer to an antenna can cause it to absorb harmonics
<number>
Radio Practices

## Slide 62: G4B13 - What is a use for an antenna analyzer other than measuring the SWR of an antenna system?
A. Measuring the front to back ratio of an antenna
B. Measuring the turns ratio of a power transformer
C. Determining the impedance of an unknown or unmarked coaxial cable
D. Determining the gain of a directional antenna
<number>
Radio Practices

## Slide 63: G4B13 - What is a use for an antenna analyzer other than measuring the SWR of an antenna system?
A. Measuring the front to back ratio of an antenna
B. Measuring the turns ratio of a power transformer
C. Determining the impedance of an unknown or unmarked coaxial cable
D. Determining the gain of a directional antenna
<number>
Radio Practices

## Slide 64: G4B14 - What is an instance in which the use of an instrument with analog readout may be preferred over an instrument with a digital readout?
A. When testing logic circuits
B. When high precision is desired
C. When measuring the frequency of an oscillator
D. When adjusting tuned circuits
<number>
Radio Practices

## Slide 65: G4B14 - What is an instance in which the use of an instrument with analog readout may be preferred over an instrument with a digital readout?
A. When testing logic circuits
B. When high precision is desired
C. When measuring the frequency of an oscillator
D. When adjusting tuned circuits
<number>
Radio Practices

## Slide 66: G4B15 - What type of transmitter performance does a two-tone test analyze?
A. Linearity
B. Percentage of suppression of carrier and undesired sideband for SSB
C. Percentage of frequency modulation
D. Percentage of carrier phase shift
<number>
Radio Practices

## Slide 67: G4B15 - What type of transmitter performance does a two-tone test analyze?
A. Linearity
B. Percentage of suppression of carrier and undesired sideband for SSB
C. Percentage of frequency modulation
D. Percentage of carrier phase shift
<number>
Radio Practices

## Slide 68: G4C - Interference with consumer electronics; grounding; DSP
<number>
Radio Practices

## Slide 69: G4C01 - Which of the following might be useful in reducing RF interference to audio frequency devices?
A. Bypass inductor
B. Bypass capacitor
C. Forward-biased diode
D. Reverse-biased diode
<number>
Radio Practices

## Slide 70: G4C01 - Which of the following might be useful in reducing RF interference to audio frequency devices?
A. Bypass inductor
B. Bypass capacitor
C. Forward-biased diode
D. Reverse-biased diode
<number>
Radio Practices

## Slide 71: G4C02 - Which of the following could be a cause of interference covering a wide range of frequencies?
A. Not using a balun or line isolator to feed balanced antennas
B. Lack of rectification of the transmitter's signal in power conductors
C. Arcing at a poor electrical connection
D. Using a balun to feed an unbalanced antenna
<number>
Radio Practices

## Slide 72: G4C02 - Which of the following could be a cause of interference covering a wide range of frequencies?
A. Not using a balun or line isolator to feed balanced antennas
B. Lack of rectification of the transmitter's signal in power conductors
C. Arcing at a poor electrical connection
D. Using a balun to feed an unbalanced antenna
<number>
Radio Practices

## Slide 73: G4C03 - What sound is heard from an audio device or telephone if there is interference from a nearby single sideband phone transmitter?
A. A steady hum whenever the transmitter is on the air
B. On-and-off humming or clicking
C. Distorted speech
D. Clearly audible speech
<number>
Radio Practices

## Slide 74: G4C03 - What sound is heard from an audio device or telephone if there is interference from a nearby single sideband phone transmitter?
A. A steady hum whenever the transmitter is on the air
B. On-and-off humming or clicking
C. Distorted speech
D. Clearly audible speech
<number>
Radio Practices

## Slide 75: G4C04 - What is the effect on an audio device or telephone system if there is interference from a nearby CW transmitter?
A. On-and-off humming or clicking
B. A CW signal at a nearly pure audio frequency
C. A chirpy CW signal
D. Severely distorted audio
<number>
Radio Practices

## Slide 76: G4C04 - What is the effect on an audio device or telephone system if there is interference from a nearby CW transmitter?
A. On-and-off humming or clicking
B. A CW signal at a nearly pure audio frequency
C. A chirpy CW signal
D. Severely distorted audio
<number>
Radio Practices

## Slide 77: G4C05 - What might be the problem if you receive an RF burn when touching your equipment while transmitting on an HF band, assuming the equipment is connected to a ground rod?
A. Flat braid rather than round wire has been used for the ground wire
B. Insulated wire has been used for the ground wire
C. The ground rod is resonant
D. The ground wire has high impedance on that frequency
<number>
Radio Practices

## Slide 78: G4C05 - What might be the problem if you receive an RF burn when touching your equipment while transmitting on an HF band, assuming the equipment is connected to a ground rod?
A. Flat braid rather than round wire has been used for the ground wire
B. Insulated wire has been used for the ground wire
C. The ground rod is resonant
D. The ground wire has high impedance on that frequency
<number>
Radio Practices

## Slide 79: G4C06 - What effect can be caused by a resonant ground connection?
A. Overheating of ground straps
B. Corrosion of the ground rod
C. High RF voltages on the enclosures of station equipment
D. A ground loop
<number>
Radio Practices

## Slide 80: G4C06 - What effect can be caused by a resonant ground connection?
A. Overheating of ground straps
B. Corrosion of the ground rod
C. High RF voltages on the enclosures of station equipment
D. A ground loop
<number>
Radio Practices

## Slide 81: G4C07 - What is one good way to avoid unwanted effects of stray RF energy in an amateur station?
A. Connect all equipment grounds together
B. Install an RF filter in series with the ground wire
C. Use a ground loop for best conductivity
D. Install a few ferrite beads on the ground wire where it connects to your station
<number>
Radio Practices

## Slide 82: Station Grounding
<number>
Amateur Radio Practices
Notes: <number>
<number>
For a proper RF ground, it’s important to use a heavy gauge copper (not aluminum) braid or foil and keep the run length to a minimum. Standard wire, even heavy gauge, or long runs can cause your ground lead to act as an antenna and resonate. A good ground will reduce RFI to other equipment, minimize the risk of shock and reduce electrical interference. At a minimum a ground rod should be 8 feet long. This can be difficult to achieve in some locations and multiple shorter rods tied together can be used.

## Slide 83: G4C07 - What is one good way to avoid unwanted effects of stray RF energy in an amateur station?
A. Connect all equipment grounds together
B. Install an RF filter in series with the ground wire
C. Use a ground loop for best conductivity
D. Install a few ferrite beads on the ground wire where it connects to your station
<number>
Radio Practices

## Slide 84: G4C08 - Which of the following would reduce RF interference caused by common-mode current on an audio cable?
A. Placing a ferrite choke around the cable
B. Adding series capacitors to the conductors
C. Adding shunt inductors to the conductors
D. Adding an additional insulating jacket to the cable
<number>
Radio Practices

## Slide 85: G4C08 - Which of the following would reduce RF interference caused by common-mode current on an audio cable?
A. Placing a ferrite choke around the cable
B. Adding series capacitors to the conductors
C. Adding shunt inductors to the conductors
D. Adding an additional insulating jacket to the cable
<number>
Radio Practices

## Slide 86: G4C09 - How can a ground loop be avoided?
A. Connect all ground conductors in series
B. Connect the AC neutral conductor to the ground wire
C. Avoid using lock washers and star washers when making ground connections
D. Connect all ground conductors to a single point
<number>
Radio Practices

## Slide 87: G4C09 - How can a ground loop be avoided?
A. Connect all ground conductors in series
B. Connect the AC neutral conductor to the ground wire
C. Avoid using lock washers and star washers when making ground connections
D. Connect all ground conductors to a single point
<number>
Radio Practices

## Slide 88: G4C10 - What could be a symptom of a ground loop somewhere in your station?
A. You receive reports of "hum" on your station's transmitted signal
B. The SWR reading for one or more antennas is suddenly very high
C. An item of station equipment starts to draw excessive amounts of current
D. You receive reports of harmonic interference from your station
<number>
Radio Practices

## Slide 89: G4C10 - What could be a symptom of a ground loop somewhere in your station?
A. You receive reports of "hum" on your station's transmitted signal
B. The SWR reading for one or more antennas is suddenly very high
C. An item of station equipment starts to draw excessive amounts of current
D. You receive reports of harmonic interference from your station
<number>
Radio Practices

## Slide 90: G4C11 - Which of the following is a function of a digital signal processor?
A. To provide adequate grounding
B. To remove noise from received signals
C. To increase antenna gain
D. To increase antenna bandwidth
<number>
Radio Practices

## Slide 91: G4C11 - Which of the following is a function of a digital signal processor?
A. To provide adequate grounding
B. To remove noise from received signals
C. To increase antenna gain
D. To increase antenna bandwidth
<number>
Radio Practices

## Slide 92: G4C12 - Which of the following is an advantage of a receiver DSP IF filter as compared to an analog filter?
A. A wide range of filter bandwidths and shapes can be created
B. Fewer digital components are required
C. Mixing products are greatly reduced
D. The DSP filter is much more effective at VHF frequencies
<number>
Radio Practices

## Slide 93: G4C12 - Which of the following is an advantage of a receiver DSP IF filter as compared to an analog filter?
A. A wide range of filter bandwidths and shapes can be created
B. Fewer digital components are required
C. Mixing products are greatly reduced
D. The DSP filter is much more effective at VHF frequencies
<number>
Radio Practices

## Slide 94: G4C13 - Which of the following can perform automatic notching of interfering carriers?
A. Bandpass tuning
B. A Digital Signal Processor (DSP) filter
C. Balanced mixing
D. A noise limiter
<number>
Radio Practices

## Slide 95: G4C13 - Which of the following can perform automatic notching of interfering carriers?
A. Bandpass tuning
B. A Digital Signal Processor (DSP) filter
C. Balanced mixing
D. A noise limiter
<number>
Radio Practices

## Slide 96: G4D - Speech processors; S meters; sideband operation near band edges
<number>
Radio Practices

## Slide 97: G4D01 - What is the purpose of a speech processor as used in a modern transceiver?
A. Increase the intelligibility of transmitted phone signals during poor conditions
B. Increase transmitter bass response for more natural sounding SSB signals
C. Prevent distortion of voice signals
D. Decrease high-frequency voice output to prevent out of band operation
<number>
Radio Practices

## Slide 98: G4D01 - What is the purpose of a speech processor as used in a modern transceiver?
A. Increase the intelligibility of transmitted phone signals during poor conditions
B. Increase transmitter bass response for more natural sounding SSB signals
C. Prevent distortion of voice signals
D. Decrease high-frequency voice output to prevent out of band operation
<number>
Radio Practices

## Slide 99: G4D02 - Which of the following describes how a speech processor affects a transmitted single sideband phone signal?
A. It increases peak power
B. It increases average power
C. It reduces harmonic distortion
D. It reduces intermodulation distortion
<number>
Radio Practices

## Slide 100: G4D02 - Which of the following describes how a speech processor affects a transmitted single sideband phone signal?
A. It increases peak power
B. It increases average power
C. It reduces harmonic distortion
D. It reduces intermodulation distortion
<number>
Radio Practices

## Slide 101: G4D03 - Which of the following can be the result of an incorrectly adjusted speech processor?
A. Distorted speech
B. Splatter
C. Excessive background pickup
D. All of these choices are correct
<number>
Radio Practices

## Slide 102: G4D03 - Which of the following can be the result of an incorrectly adjusted speech processor?
A. Distorted speech
B. Splatter
C. Excessive background pickup
D. All of these choices are correct
<number>
Radio Practices

## Slide 103: G4D04 - What does an S meter measure?
A. Conductance
B. Impedance
C. Received signal strength
D. Transmitter power output
<number>
Radio Practices

## Slide 104: G4D04 - What does an S meter measure?
A. Conductance
B. Impedance
C. Received signal strength
D. Transmitter power output
<number>
Radio Practices

## Slide 105: G4D05 - How does a signal that reads 20 dB over S9 compare to one that reads S9 on a receiver, assuming a properly calibrated S meter?
A. It is 10 times less powerful
B. It is 20 times less powerful
C. It is 20 times more powerful
D. It is 100 times more powerful
<number>
Radio Practices

## Slide 106: G4D05 - How does a signal that reads 20 dB over S9 compare to one that reads S9 on a receiver, assuming a properly calibrated S meter?
A. It is 10 times less powerful
B. It is 20 times less powerful
C. It is 20 times more powerful
D. It is 100 times more powerful
<number>
Radio Practices

## Slide 107: G4D06 - Where is an S meter found?
A. In a receiver
B. In an SWR bridge
C. In a transmitter
D. In a conductance bridge
<number>
Radio Practices

## Slide 108: G4D06 - Where is an S meter found?
A. In a receiver
B. In an SWR bridge
C. In a transmitter
D. In a conductance bridge
<number>
Radio Practices

## Slide 109: G4D07 - How much must the power output of a transmitter be raised to change the S meter reading on a distant receiver from S8 to S9?
A. Approximately 1.5 times
B. Approximately 2 times
C. Approximately 4 times
D. Approximately 8 times
<number>
Radio Practices

## Slide 110: G4D07 - How much must the power output of a transmitter be raised to change the S meter reading on a distant receiver from S8 to S9?
A. Approximately 1.5 times
B. Approximately 2 times
C. Approximately 4 times
D. Approximately 8 times
<number>
Radio Practices

## Slide 111: G4D08 - What frequency range is occupied by a 3 kHz LSB signal when the displayed carrier frequency is set to 7.178 MHz?
A. 7.178 to 7.181 MHz
B. 7.178 to 7.184 MHz
C. 7.175 to 7.178 MHz
D. 7.1765 to 7.1795 MHz
<number>
Radio Practices

## Slide 112: G4D08 - What frequency range is occupied by a 3 kHz LSB signal when the displayed carrier frequency is set to 7.178 MHz?
A. 7.178 to 7.181 MHz
B. 7.178 to 7.184 MHz
C. 7.175 to 7.178 MHz
D. 7.1765 to 7.1795 MHz
<number>
Radio Practices

## Slide 113: G4D09 - What frequency range is occupied by a 3 kHz USB signal with the displayed carrier frequency set to 14.347 MHz?
A. 14.347 to 14.647 MHz
B. 14.347 to 14.350 MHz
C. 14.344 to 14.347 MHz
D. 14.3455 to 14.3485 MHz
<number>
Radio Practices

## Slide 114: G4D09 - What frequency range is occupied by a 3 kHz USB signal with the displayed carrier frequency set to 14.347 MHz?
A. 14.347 to 14.647 MHz
B. 14.347 to 14.350 MHz
C. 14.344 to 14.347 MHz
D. 14.3455 to 14.3485 MHz
<number>
Radio Practices

## Slide 115: G4D10 - How close to the lower edge of the 40-meter General Class phone segment should your displayed carrier frequency be when using 3 kHz wide LSB?
A. At least 3 kHz above the edge of the segment
B. At least 3 kHz below the edge of the segment
C. Your displayed carrier frequency may be set at the edge of the segment
D. At least 1 kHz above the edge of the segment
<number>
Radio Practices

## Slide 116: G4D10 - How close to the lower edge of the 40-meter General Class phone segment should your displayed carrier frequency be when using 3 kHz wide LSB?
A. At least 3 kHz above the edge of the segment
B. At least 3 kHz below the edge of the segment
C. Your displayed carrier frequency may be set at the edge of the segment
D. At least 1 kHz above the edge of the segment
<number>
Radio Practices

## Slide 117: G4D11 - How close to the upper edge of the 20-meter General Class band should your displayed carrier frequency be when using 3 kHz wide USB?
A. At least 3 kHz above the edge of the band
B. At least 3 kHz below the edge of the band
C. Your displayed carrier frequency may be set at the edge of the band
D. At least 1 kHz below the edge of the segment
<number>
Radio Practices

## Slide 118: G4D11 - How close to the upper edge of the 20-meter General Class band should your displayed carrier frequency be when using 3 kHz wide USB?
A. At least 3 kHz above the edge of the band
B. At least 3 kHz below the edge of the band
C. Your displayed carrier frequency may be set at the edge of the band
D. At least 1 kHz below the edge of the segment
<number>
Radio Practices

## Slide 119: G4E - HF mobile radio installations; emergency and battery powered operation
<number>
Radio Practices

## Slide 120: G4E01 - What is the purpose of a capacitance hat on a mobile antenna?
A. To increase the power handling capacity of a whip antenna
B. To allow automatic band changing
C. To electrically lengthen a physically short antenna
D. To allow remote tuning
<number>
Radio Practices

## Slide 121: G4E01 - What is the purpose of a capacitance hat on a mobile antenna?
A. To increase the power handling capacity of a whip antenna
B. To allow automatic band changing
C. To electrically lengthen a physically short antenna
D. To allow remote tuning
<number>
Radio Practices

## Slide 122
<number>
Radio Practices
Capacitance Hat

## Slide 123: G4E02 - What is the purpose of a corona ball on a HF mobile antenna?
A. To narrow the operating bandwidth of the antenna
B. To increase the "Q" of the antenna
C. To reduce the chance of damage if the antenna should strike an object
D. To reduce high voltage discharge from the tip of the antenna
<number>
Radio Practices

## Slide 124: G4E02 - What is the purpose of a corona ball on a HF mobile antenna?
A. To narrow the operating bandwidth of the antenna
B. To increase the "Q" of the antenna
C. To reduce the chance of damage if the antenna should strike an object
D. To reduce high voltage discharge from the tip of the antenna
<number>
Radio Practices

## Slide 125: G4E03 - Which of the following direct, fused power connections would be the best for a 100 watt HF mobile installation?
A. To the battery using heavy gauge wire
B. To the alternator or generator using heavy gauge wire
C. To the battery using resistor wire
D. To the alternator or generator using resistor wire
<number>
Radio Practices

## Slide 126: G4E03 - Which of the following direct, fused power connections would be the best for a 100 watt HF mobile installation?
A. To the battery using heavy gauge wire
B. To the alternator or generator using heavy gauge wire
C. To the battery using resistor wire
D. To the alternator or generator using resistor wire
<number>
Radio Practices

## Slide 127: G4E04 - Why is it best NOT to draw the DC power for a 100 watt HF transceiver from a vehicle’s auxiliary power socket?
A. The socket is not wired with an RF-shielded power cable
B. The socket's wiring may be inadequate for the current drawn by the transceiver
C. The DC polarity of the socket is reversed from the polarity of modern HF transceivers
D. Drawing more than 50 watts from this socket could cause the engine to overheat
<number>
Radio Practices

## Slide 128: G4E04 - Why is it best NOT to draw the DC power for a 100 watt HF transceiver from a vehicle’s auxiliary power socket?
A. The socket is not wired with an RF-shielded power cable
B. The socket's wiring may be inadequate for the current drawn by the transceiver
C. The DC polarity of the socket is reversed from the polarity of modern HF transceivers
D. Drawing more than 50 watts from this socket could cause the engine to overheat
<number>
Radio Practices

## Slide 129: G4E05 - Which of the following most limits the effectiveness of an HF mobile transceiver operating in the 75-meter band?
A. "Picket Fencing" signal variation
B. The wire gauge of the DC power line to the transceiver
C. The antenna system
D. FCC rules limiting mobile output power on the 75-meter band
<number>
Radio Practices

## Slide 130: G4E05 - Which of the following most limits the effectiveness of an HF mobile transceiver operating in the 75-meter band?
A. "Picket Fencing" signal variation
B. The wire gauge of the DC power line to the transceiver
C. The antenna system
D. FCC rules limiting mobile output power on the 75-meter band
<number>
Radio Practices

## Slide 131: G4E06 - What is one disadvantage of using a shortened mobile antenna as opposed to a full size antenna?
A. Short antennas are more likely to cause distortion of transmitted signals
B. Short antennas can only receive circularly polarized signals
C. Operating bandwidth may be very limited
D. Harmonic radiation may increase
<number>
Radio Practices

## Slide 132: G4E06 - What is one disadvantage of using a shortened mobile antenna as opposed to a full size antenna?
A. Short antennas are more likely to cause distortion of transmitted signals
B. Short antennas can only receive circularly polarized signals
C. Operating bandwidth may be very limited
D. Harmonic radiation may increase
<number>
Radio Practices

## Slide 133: G4E07 - Which of the following may cause interference to be heard in the receiver of an HF radio installed in a recent model vehicle?
A. The battery charging system
B. The fuel delivery system
C. The vehicle control computer
D. All of these choices are correct
<number>
Radio Practices

## Slide 134: G4E07 - Which of the following may cause interference to be heard in the receiver of an HF radio installed in a recent model vehicle?
A. The battery charging system
B. The fuel delivery system
C. The vehicle control computer
D. All of these choices are correct
<number>
Radio Practices

## Slide 135: G4E08 - What is the name of the process by which sunlight is changed directly into electricity?
A. Photovoltaic conversion
B. Photon emission
C. Photosynthesis
D. Photon decomposition
<number>
Radio Practices

## Slide 136: G4E08 - What is the name of the process by which sunlight is changed directly into electricity?
A. Photovoltaic conversion
B. Photon emission
C. Photosynthesis
D. Photon decomposition
<number>
Radio Practices

## Slide 137: G4E09 - What is the approximate open-circuit voltage from a fully illuminated silicon photovoltaic cell?
A. 0.02 VDC
B. 0.5 VDC
C. 0.2 VDC
D. 1.38 VDC
<number>
Radio Practices

## Slide 138: G4E09 - What is the approximate open-circuit voltage from a fully illuminated silicon photovoltaic cell?
A. 0.02 VDC
B. 0.5 VDC
C. 0.2 VDC
D. 1.38 VDC
<number>
Radio Practices

## Slide 139: G4E10 - What is the reason that a series diode is connected between a solar panel and a storage battery that is being charged by the panel?
A. The diode serves to regulate the charging voltage to prevent overcharge
B. The diode prevents self-discharge of the battery though the panel during times of low or no illumination
C. The diode limits the current flowing from the panel to a safe value
D. The diode greatly increases the efficiency during times of high illumination
<number>
Radio Practices

## Slide 140: G4E10 - What is the reason that a series diode is connected between a solar panel and a storage battery that is being charged by the panel?
A. The diode serves to regulate the charging voltage to prevent overcharge
B. The diode prevents self-discharge of the battery though the panel during times of low or no illumination
C. The diode limits the current flowing from the panel to a safe value
D. The diode greatly increases the efficiency during times of high illumination
<number>
Radio Practices

## Slide 141: G4E11 - Which of the following is a disadvantage of using wind as the primary source of power for an emergency station?
A. The conversion efficiency from mechanical energy to electrical energy is less than 2 percent
B. The voltage and current ratings of such systems are not compatible with amateur equipment
C. A large energy storage system is needed to supply power when the wind is not blowing
D. All of these choices are correct
<number>
Radio Practices

## Slide 142: G4E11 - Which of the following is a disadvantage of using wind as the primary source of power for an emergency station?
A. The conversion efficiency from mechanical energy to electrical energy is less than 2 percent
B. The voltage and current ratings of such systems are not compatible with amateur equipment
C. A large energy storage system is needed to supply power when the wind is not blowing
D. All of these choices are correct
<number>
Radio Practices

## Slide 143: End of SUBELEMENT G4 AMATEUR RADIO PRACTICES