## Slide 1: SUBELEMENT G10 ELECTRICAL AND RF SAFETY [2 Exam Questions–2 Groups]
G0 - RF Safety
<number>
Notes: Subelement G10 Electrical and RF Safety. General Training Slides for 2015 Question Pool Good through June 30, 2019 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM, Howard Schultz, W7HS.
<number>

## Slide 2: SUBELEMENT G10 ELECTRICAL AND RF SAFETY [2 Exam Questions–2 Groups]
G10A - RF safety principles, rules and guidelines; routine station evaluation
G10B - Safety in the ham shack; electrical shock and treatment, safety grounding, fusing, interlocks, wiring, antenna and tower safety
Notes: <number>

## Slide 3: G0A - RF safety principles, rules and guidelines; routine station evaluation
<number>
Elec. & RF Safety

## Slide 4
G0 - RF Safety
<number>
Band (Wavelength) | Transmitter Power (W)
160 m | 500
75 m | 500
80 m | 500
40 m | 500
30 m | 425
20 m | 225
17 m | 125
15 m | 100
12 m | 75
10 m | 50
6 - 1.23 m | 50
70 cm | 70
33 cm | 150
23 cm | 200
13 cm and up | 250
Power Thresholds for Routine Evaluation
Notes: Notice that power levels that trigger a station evaluation vary with frequency
<number>

## Slide 5: Duty Cycle
G0 - RF Safety
<number>
Mode | Duty Cycle
CW Morse telegraphy | 40%
SSB voice | 20%
SSB voice, heavy speech processing | 50%
SSB AFSK | 100%
SSB SSTV | 100%
FM voice or data | 100%
FSK | 100%
AM voice, 50% modulation | 50%
AM voice, 100% modulation | 30%
Duty cycle refers to both the transmit vs. receive time and the average power level during transmission. Because CW has gaps between symbols the average power is less than 100%. SSB power output varies with modulation. FM is full power regardless of modulation.

## Slide 6: Time Averaged Exposure Calculations
G0 - RF Safety
<number>
Notes: <number>
The vertical axis is power level, with time on the horizontal axis. The shaded areas in the diagrams above represent RF exposure. As power or duty cycle is decreased, exposure time can be increased and maintain a comparable exposure level. Time, field strength, frequency and specific absorption rate (SAR) are critical factors to consider. The body is most sensitive to VHF frequencies (30-300 MHZ). The eyes are particularly sensitive to energy at 1270MHz which can cause cataracts.

## Slide 7: G0A01 - What is one way that RF energy can affect human body tissue?
A. It heats body tissue
B. It causes radiation poisoning
C. It causes the blood count to reach a dangerously low level
D. It cools body tissue
<number>
Elec. & RF Safety

## Slide 8: G0A01 - What is one way that RF energy can affect human body tissue?
A. It heats body tissue
B. It causes radiation poisoning
C. It causes the blood count to reach a dangerously low level
D. It cools body tissue
<number>
Elec. & RF Safety

## Slide 9: G0A02 - Which of the following properties is important in estimating whether an RF signal exceeds the maximum permissible exposure ( MPE ) ?
A. Its duty cycle
B. Its frequency
C. Its power density
D. All of these choices are correct
<number>
Elec. & RF Safety

## Slide 10: G0A02 - Which of the following properties is important in estimating whether an RF signal exceeds the maximum permissible exposure ( MPE ) ?
A. Its duty cycle
B. Its frequency
C. Its power density
D. All of these choices are correct
<number>
Elec. & RF Safety

## Slide 11: G0A03 - How can you determine that your station complies with FCC RF exposure regulations?
A. By calculation based on FCC OET Bulletin 65
B. By calculation based on computer modeling
C. By measurement of field strength using calibrated equipment
D. All of these choices are correct
<number>
Elec. & RF Safety

## Slide 12: G0A03 - How can you determine that your station complies with FCC RF exposure regulations?
A. By calculation based on FCC OET Bulletin 65
B. By calculation based on computer modeling
C. By measurement of field strength using calibrated equipment
D. All of these choices are correct
<number>
Elec. & RF Safety

## Slide 13: G0A04 - What does "time averaging" mean in reference to RF radiation exposure?
A. The average amount of power developed by the transmitter over a specific 24 hour period
B. The average time it takes RF radiation to have any long-term effect on the body
C. The total time of the exposure
D. The total RF exposure averaged over a certain time
<number>
Elec. & RF Safety

## Slide 14: G0A04 - What does "time averaging" mean in reference to RF radiation exposure?
A. The average amount of power developed by the transmitter over a specific 24 hour period
B. The average time it takes RF radiation to have any long-term effect on the body
C. The total time of the exposure
D. The total RF exposure averaged over a certain time
<number>
Elec. & RF Safety

## Slide 15: G0A05 - What must you do if an evaluation of your station shows RF energy radiated from your station exceeds permissible limits?
A. Take action to prevent human exposure to the excessive RF fields
B. File an Environmental Impact Statement (EIS-97) with the FCC
C. Secure written permission from your neighbors to operate above the controlled MPE limits
D. All of these choices are correct
<number>
Elec. & RF Safety

## Slide 16: G0A05 - What must you do if an evaluation of your station shows RF energy radiated from your station exceeds permissible limits?
A. Take action to prevent human exposure to the excessive RF fields
B. File an Environmental Impact Statement (EIS-97) with the FCC
C. Secure written permission from your neighbors to operate above the controlled MPE limits
D. All of these choices are correct
<number>
Elec. & RF Safety

## Slide 17: G0A06 - What precaution should be taken when installing a ground-mounted antenna?
A. It should not be installed higher than you can reach
B. It should not be installed in a wet area
C. It should limited to 10 feet in height
D. It should be installed such that it is protected against unauthorized access
<number>
Elec. & RF Safety

## Slide 18: G0A06 - What precaution should be taken when installing a ground-mounted antenna?
A. It should not be installed higher than you can reach
B. It should not be installed in a wet area
C. It should limited to 10 feet in height
D. It should be installed such that it is protected against unauthorized access
<number>
Elec. & RF Safety

## Slide 19: G0A07 - What effect does transmitter duty cycle have when evaluating RF exposure?
A. A lower transmitter duty cycle permits greater short-term exposure levels
B. A higher transmitter duty cycle permits greater short-term exposure levels
C. Low duty cycle transmitters are exempt from RF exposure evaluation requirements
D. High duty cycle transmitters are exempt from RF exposure requirements
<number>
Elec. & RF Safety

## Slide 20: G0A07 - What effect does transmitter duty cycle have when evaluating RF exposure?
A. A lower transmitter duty cycle permits greater short-term exposure levels
B. A higher transmitter duty cycle permits greater short-term exposure levels
C. Low duty cycle transmitters are exempt from RF exposure evaluation requirements
D. High duty cycle transmitters are exempt from RF exposure requirements
<number>
Elec. & RF Safety

## Slide 21: G0A08 - Which of the following steps must an amateur operator take to ensure compliance with RF safety regulations when transmitter power exceeds levels specified in FCC Part 97.13?
A. Post a copy of FCC Part 97.13 in the station
B. Post a copy of OET Bulletin 65 in the station
C. Perform a routine RF exposure evaluation
D. All of these choices are correct
<number>
Elec. & RF Safety

## Slide 22: G0A08 - Which of the following steps must an amateur operator take to ensure compliance with RF safety regulations when transmitter power exceeds levels specified in FCC Part 97.13?
A. Post a copy of FCC Part 97.13 in the station
B. Post a copy of OET Bulletin 65 in the station
C. Perform a routine RF exposure evaluation
D. All of these choices are correct
<number>
Elec. & RF Safety

## Slide 23: G0A09 - What type of instrument can be used to accurately measure an RF field?
A. A receiver with an S meter
B. A calibrated field strength meter with a calibrated antenna
C. An SWR meter with a peak-reading function
D. An oscilloscope with a high-stability crystal marker generator
<number>
Elec. & RF Safety

## Slide 24: G0A09 - What type of instrument can be used to accurately measure an RF field?
A. A receiver with an S meter
B. A calibrated field strength meter with a calibrated antenna
C. An SWR meter with a peak-reading function
D. An oscilloscope with a high-stability crystal marker generator
<number>
Elec. & RF Safety

## Slide 25: Field Strength Meter
Amateur Radio Practices
<number>
Here are two digital Field Strength Meter models. Some SWR meters and frequency counters can also be used as field strength meters.
Field Strength Meters are used to test the density of an RF field when near the transmitter (near field). This can help determine the radiation pattern of an antenna and locate a nearby transmitter.
Notes: <number>
<number>
Here are two digital Field Strength Meter models. Some SWR meters and frequency counters can also be used as field strength meters. Field Strength Meters are used to test the density of an RF field. This allows testing of antenna patterns and ambient RF levels at repeater and home sites to insure safe levels.

## Slide 26: G0A10 - What is one thing that can be done if evaluation shows that a neighbor might receive more than the allowable limit of RF exposure from the main lobe of a directional antenna?
A. Change to a non-polarized antenna with higher gain
B. Post a warning sign that is clearly visible to the neighbor
C. Use an antenna with a higher front-to-back ratio
D. Take precautions to ensure that the antenna cannot be pointed in their direction
G0 - RF Safety
<number>

## Slide 27: G0A10 - What is one thing that can be done if evaluation shows that a neighbor might receive more than the allowable limit of RF exposure from the main lobe of a directional antenna?
A. Change to a non-polarized antenna with higher gain
B. Post a warning sign that is clearly visible to the neighbor
C. Use an antenna with a higher front-to-back ratio
D. Take precautions to ensure that the antenna cannot be pointed in their direction
G0 - RF Safety
<number>

## Slide 28: G0A11 - What precaution should you take if you install an indoor transmitting antenna?
A. Locate the antenna close to your operating position to minimize feed line radiation
B. Position the antenna along the edge of a wall to reduce parasitic radiation
C. Make sure that MPE limits are not exceeded in occupied areas
D. Make sure the antenna is properly shielded
G0 - RF Safety
<number>

## Slide 29: G0A11 - What precaution should you take if you install an indoor transmitting antenna?
A. Locate the antenna close to your operating position to minimize feed line radiation
B. Position the antenna along the edge of a wall to reduce parasitic radiation
C. Make sure that MPE limits are not exceeded in occupied areas
D. Make sure the antenna is properly shielded
G0 - RF Safety
<number>

## Slide 30: G0A12 - What precaution should you take whenever you make adjustments or repairs to an antenna?
A. Ensure that you and the antenna structure are grounded
B. Turn off the transmitter and disconnect the feed line
C. Wear a radiation badge
D. All of these choices are correct
G0 - RF Safety
<number>

## Slide 31: G0A12 - What precaution should you take whenever you make adjustments or repairs to an antenna?
A. Ensure that you and the antenna structure are grounded
B. Turn off the transmitter and disconnect the feed line
C. Wear a radiation badge
D. All of these choices are correct
G0 - RF Safety
<number>

## Slide 32: G0B - Safety in the ham shack: electrical shock and treatment, safety grounding, fusing, interlocks, wiring, antenna and tower safety
G0 - RF Safety
<number>

## Slide 33: 240 Volt House Power
G0 - RF Safety
<number>
Wire Color | Use
Red | Hot
Black | Hot
White | Common
Bare or Green | Ground
Notes: <number>
Homes in the US are generally supplied with 240 volts. This is split into two 120 volt halves to supply outlets and lights throughout the house. There are two places that are commonly wired with 240: a dryer and range. This is a range plug. Some larger appliances such as air compressors and large amplifiers also require 240 volts to allow for the use of smaller wire to support their current draw.
Note the Red, Black, White and bare wire. Red and Black are the two “hot leads”. The white is “common” or “neutral” and the bare wire is the ground. Hot leads must always be fuse or breaker protected.

## Slide 34: AWG Wire Gauges vs. Current Capacity
G0 - RF Safety
Continuous-Duty
Current Capacity (Amps)
AWG Single Bundled
Gauge Wire Wire
8 73 46
10 55 33
12 41 23
14 32 17
16 22 13
18 16 10
<number>
Notes: <number>
This shows various wire sizes and their maximum current capacity. Single conductor wire has a higher capacity the multiconductor bundled wire because it has less ability to heat up (melt through) its jacket. The important point here is the two common wire sizes in household wiring are 12 and 14 gauge. They receive 20 amp and 15 amp fuses or circuit breakers respectively. The table above shows their maximum capacity in a multiconductor cable is just over this amount – not enough headroom to support the next larger fuse or breaker.

## Slide 35: AWG Wire Gauges vs. Current Capacity
G0 - RF Safety
<number>

## Slide 36: G0B01 - Which wire or wires in a four-conductor connection should be attached to fuses or circuit breakers in a device operated from a 240 VAC single phase source?
A. Only the two wires carrying voltage
B. Only the neutral wire
C. Only the ground wire
D. All wires
G0 - RF Safety
<number>

## Slide 37: G0B01 - Which wire or wires in a four-conductor connection should be attached to fuses or circuit breakers in a device operated from a 240 VAC single phase source?
A. Only the two wires carrying voltage
B. Only the neutral wire
C. Only the ground wire
D. All wires
G0 - RF Safety
<number>

## Slide 38: G0B02 - What is the minimum wire size that may be safely used for a circuit that draws up to 20 amperes of continuous current?
A. AWG number 20
B. AWG number 16
C. AWG number 12
D. AWG number 8
G0 - RF Safety
<number>

## Slide 39: G0B02 - What is the minimum wire size that may be safely used for a circuit that draws up to 20 amperes of continuous current?
A. AWG number 20
B. AWG number 16
C. AWG number 12
D. AWG number 8
G0 - RF Safety
<number>

## Slide 40: G0B03 - Which size of fuse or circuit breaker would be appropriate to use with a circuit that uses AWG number 14 wiring?
A. 100 amperes
B. 60 amperes
C. 30 amperes
D. 15 amperes
G0 - RF Safety
<number>

## Slide 41: G0B03 - Which size of fuse or circuit breaker would be appropriate to use with a circuit that uses AWG number 14 wiring?
A. 100 amperes
B. 60 amperes
C. 30 amperes
D. 15 amperes
G0 - RF Safety
<number>

## Slide 42: G0B04 - Which of the following is a primary reason for not placing a gasoline-fueled generator inside an occupied area?
A. Danger of carbon monoxide poisoning
B. Danger of engine over torque
C. Lack of oxygen for adequate combustion
D. Lack of nitrogen for adequate combustion
G0 - RF Safety
<number>

## Slide 43: G0B04 - Which of the following is a primary reason for not placing a gasoline-fueled generator inside an occupied area?
A. Danger of carbon monoxide poisoning
B. Danger of engine over torque
C. Lack of oxygen for adequate combustion
D. Lack of nitrogen for adequate combustion
G0 - RF Safety
<number>

## Slide 44: G0B05 - Which of the following conditions will cause a Ground Fault Circuit Interrupter (GFCI) to disconnect the 120 or 240 Volt AC line power to a device?
A. Current flowing from one or more of the voltage-carrying wires to the neutral wire
B. Current flowing from one or more of the voltage-carrying wires directly to ground
C. Overvoltage on the voltage-carrying wires
D. All of these choices are correct
G0 - RF Safety
<number>

## Slide 45: G0B05 - Which of the following conditions will cause a Ground Fault Circuit Interrupter (GFCI) to disconnect the 120 or 240 Volt AC line power to a device?
A. Current flowing from one or more of the voltage-carrying wires to the neutral wire
B. Current flowing from one or more of the voltage-carrying wires directly to ground
C. Overvoltage on the voltage-carrying wires
D. All of these choices are correct
G0 - RF Safety
<number>

## Slide 46: G0B06 - Why must the metal enclosure of every item of station equipment be grounded?
A. It prevents a blown fuse in the event of an internal short circuit
B. It prevents signal overload
C. It ensures that the neutral wire is grounded
D. It ensures that hazardous voltages cannot appear on the chassis
G0 - RF Safety
<number>

## Slide 47: G0B06 - Why must the metal enclosure of every item of station equipment be grounded?
A. It prevents a blown fuse in the event of an internal short circuit
B. It prevents signal overload
C. It ensures that the neutral wire is grounded
D. It ensures that hazardous voltages cannot appear on the chassis
G0 - RF Safety
<number>

## Slide 48: G0B07 - Which of these choices should be observed when climbing a tower using a safety belt or harness?
A. Never lean back and rely on the belt alone to support your weight
B. Confirm that the belt is rated for the weight of the climber and that it is within its allowable service life
C. Ensure that all heavy tools are securely fastened to the belt D-ring
D. All of these choices are correct
G0 - RF Safety
<number>

## Slide 49: G0B07 - Which of these choices should be observed when climbing a tower using a safety belt or harness?
A. Never lean back and rely on the belt alone to support your weight
B. Confirm that the belt is rated for the weight of the climber and that it is within its allowable service life
C. Ensure that all heavy tools are securely fastened to the belt D-ring
D. All of these choices are correct
G0 - RF Safety
<number>
Notes: <number>

## Slide 50: G0B08 - What should be done by any person preparing to climb a tower that supports electrically powered devices?
A. Notify the electric company that a person will be working on the tower
B. Make sure all circuits that supply power to the tower are locked out and tagged
C. Unground the base of the tower
D. All of these choices are correct
G0 - RF Safety
<number>

## Slide 51: G0B08 - What should be done by any person preparing to climb a tower that supports electrically powered devices?
A. Notify the electric company that a person will be working on the tower
B. Make sure all circuits that supply power to the tower are locked out and tagged
C. Unground the base of the tower
D. All of these choices are correct
G0 - RF Safety
<number>

## Slide 52: G0B09 - Why should soldered joints not be used with the wires that connect the base of a tower to a system of ground rods?
A. The resistance of solder is too high
B. Solder flux will prevent a low conductivity connection
C. Solder has too high a dielectric constant to provide adequate lightning protection
D. A soldered joint will likely be destroyed by the heat of a lightning strike
G0 - RF Safety
<number>

## Slide 53: G0B09 - Why should soldered joints not be used with the wires that connect the base of a tower to a system of ground rods?
A. The resistance of solder is too high
B. Solder flux will prevent a low conductivity connection
C. Solder has too high a dielectric constant to provide adequate lightning protection
D. A soldered joint will likely be destroyed by the heat of a lightning strike
G0 - RF Safety
<number>

## Slide 54: G0B10 - Which of the following is a danger from lead-tin solder?
A. Lead can contaminate food if hands are not washed carefully after handling the solder
B. High voltages can cause lead-tin solder to disintegrate suddenly
C. Tin in the solder can "cold flow" causing shorts in the circuit
D. RF energy can convert the lead into a poisonous gas
G0 - RF Safety
<number>

## Slide 55: G0B10 - Which of the following is a danger from lead-tin solder?
A. Lead can contaminate food if hands are not washed carefully after handling the solder
B. High voltages can cause lead-tin solder to disintegrate suddenly
C. Tin in the solder can "cold flow" causing shorts in the circuit
D. RF energy can convert the lead into a poisonous gas
G0 - RF Safety
<number>

## Slide 56: G0B11 - Which of the following is good practice for lightning protection grounds?
A. They must be bonded to all buried water and gas lines
B. Bends in ground wires must be made as close as possible to a right angle
C. Lightning grounds must be connected to all ungrounded wiring
D. They must be bonded together with all other grounds
G0 - RF Safety
<number>

## Slide 57: G0B11 - Which of the following is good practice for lightning protection grounds?
A. They must be bonded to all buried water and gas lines
B. Bends in ground wires must be made as close as possible to a right angle
C. Lightning grounds must be connected to all ungrounded wiring
D. They must be bonded together with all other grounds
G0 - RF Safety
<number>

## Slide 58: G0B12 - What is the purpose of a power supply interlock?
A. To prevent unauthorized changes to the circuit that would void the manufacturer’s warranty
B. To shut down the unit if it becomes too hot
C. To ensure that dangerous voltages are removed if the cabinet is opened
D. To shut off the power supply if too much voltage is produced
G0 - RF Safety
<number>

## Slide 59: G0B12 - What is the purpose of a power supply interlock?
A. To prevent unauthorized changes to the circuit that would void the manufacturer’s warranty
B. To shut down the unit if it becomes too hot
C. To ensure that dangerous voltages are removed if the cabinet is opened
D. To shut off the power supply if too much voltage is produced
G0 - RF Safety
<number>

## Slide 60: G0B13 - What must you do when powering your house from an emergency generator?
A. Disconnect the incoming utility power feed
B. Insure that the generator is not grounded
C. Insure that all lightning grounds are disconnected
D. All of these choices are correct
G0 - RF Safety
<number>

## Slide 61: G0B13 - What must you do when powering your house from an emergency generator?
A. Disconnect the incoming utility power feed
B. Insure that the generator is not grounded
C. Insure that all lightning grounds are disconnected
D. All of these choices are correct
G0 - RF Safety
<number>

## Slide 62: G0B14 - Which of the following is covered by the National Electrical Code?
A. Acceptable bandwidth limits
B. Acceptable modulation limits
C. Electrical safety inside the ham shack
D. RF exposure limits of the human body
G0 - RF Safety
<number>

## Slide 63: G0B14 - Which of the following is covered by the National Electrical Code?
A. Acceptable bandwidth limits
B. Acceptable modulation limits
C. Electrical safety inside the ham shack
D. RF exposure limits of the human body
G0 - RF Safety
<number>

## Slide 64: G0B15 - Which of the following is true of an emergency generator installation?
A. The generator should be located in a well-ventilated area
B. The generator must be insulated from ground
C. Fuel should be stored near the generator for rapid refueling in case of an emergency
D. All of these choices are correct
G0 - RF Safety
<number>

## Slide 65: G0B15 - Which of the following is true of an emergency generator installation?
A. The generator should be located in a well-ventilated area
B. The generator must be insulated from ground
C. Fuel should be stored near the generator for rapid refueling in case of an emergency
D. All of these choices are correct
G0 - RF Safety
<number>

## Slide 66: End Of SUBELEMENT G10 ELECTRICAL AND RF SAFETY