## Slide 1: SUBELEMENT G2 OPERATING PROCEDURES [5 Exam Questions - 5 Groups]
Operating Procedures
<number>
Notes: Subelement G2 Operating Procedures. General Training Slides for 2015 Question Pool Good through June 30, 2019 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM, Howard Schultz, W7HS.
Subelement G1 FCC Rules. Technician Training Slides for 2015 Question Pool Good through June 30, 2019 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM, Howard Schultz, W7HS.
<number>

## Slide 2: SUBELEMENT G2 - OPERATING PROCEDURES [5 Exam Questions - 5 Groups]
G2A - Phone operating procedures; USB/LSB conventions; procedural signals; breaking into a contact; VOX operation
G2B - Operating courtesy; band plans; emergencies, including drills and emergency communications
G2C - CW operating procedures and procedural signals; Q signals and common abbreviations; full break in
G2D - Amateur Auxiliary; minimizing interference; HF operations
G2E - Digital operating; procedures, procedural signals and common abbreviations
Notes: Subelement G2 Operating Procedures. General Training Slides for 2015 Question Pool Good through June 30, 2019 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM, Howard Schultz, W7HS.
Subelement G1 FCC Rules. Technician Training Slides for 2015 Question Pool Good through June 30, 2019 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM, Howard Schultz, W7HS.
<number>

## Slide 3: G2A - Phone operating procedures; USB/LSB conventions; procedural signals; breaking into a contact; VOX operation
<number>
Operating Procudures

## Slide 4: Amplitude Modulation Spectral Plot
<number>
Notes: <number>
This is the appearance of an AM signal on a spectrum scope. There is a carrier in the center that uses power but contains no information (it can be used for tuning). Each of the two sidebands (upper and lower) are identical but inverted. HF amateur communications are generally on a single sideband (SSB) by suppressing the carrier and opposite sideband. This is more efficient by using less bandwidth and power is not wasted transmitting a dead carrier and duplicate sideband. By convention hams use upper sideband (USB) on bands above 10 MHz and lower sideband (LSB) on bands below 10 MHz.
Because of radio design simplicity, the convention has been to use lower sideband (LSB) below 14 MHz and upper sideband (USB) above 14 MHz.

## Slide 5: Amplitude Modulation Spectrum Analyzer View
Operating Procedures
<number>
An unmodulated RF
carrier requires narrow
bandwidth
Modulation of the carrier
creates sidebands. This
requires more bandwidth.
Transmitter power is spread across this bandwidth

## Slide 6: AM and SSB Spectrum Analyzer View
Operating Procedures
<number>
The carrier contains no
audio information.
The sidebands contain
duplicate audio information
By filtering out the carrier and one sideband,
we save spectrum and concentrate our RF
energy into a narrower bandwidth. SSB is
therefore more efficient.

## Slide 7: VOX – Voice Operation
<number>
Notes: <number>
Voice Operated (VOX) headsets and speaker/mikes are available. These permit hands-free operation by detecting the voice of the user and automatically activating the push-to-talk (PTT). Most of these unit offer a way to switch to manual operation to eliminate falsing (inadvertent transmissions) in a noisy environment. They also generally offer some means to control the sensitivity (gain) of the VOX circuitry. Better units include VOX delay to eliminate falsing on pulse noises and anti-VOX to prevent received audio from activating the transmitter.

## Slide 8: G2A01 - Which sideband is most commonly used for voice communications on frequencies of 14 MHz or higher?
A. Upper sideband
B. Lower sideband
C. Vestigial sideband
D. Double sideband
Operating Procedures
<number>

## Slide 9: G2A01 - Which sideband is most commonly used for voice communications on frequencies of 14 MHz or higher?
A. Upper sideband
B. Lower sideband
C. Vestigial sideband
D. Double sideband
Operating Procedures
<number>

## Slide 10: G2A02 - Which of the following modes is most commonly used for voice communications on the 160-meter, 75-meter, and 40-meter bands?
A. Upper sideband
B. Lower sideband
C. Vestigial sideband
D. Double sideband
Operating Procedures
<number>

## Slide 11: G2A02 - Which of the following modes is most commonly used for voice communications on the 160-meter, 75-meter, and 40-meter bands?
A. Upper sideband
B. Lower sideband
C. Vestigial sideband
D. Double sideband
Operating Procedures
<number>

## Slide 12: G2A03 - Which of the following is most commonly used for SSB voice communications in the VHF and UHF bands?
A. Upper sideband
B. Lower sideband
C. Vestigial sideband
D. Double sideband
Operating Procedures
<number>

## Slide 13: G2A03 - Which of the following is most commonly used for SSB voice communications in the VHF and UHF bands?
A. Upper sideband
B. Lower sideband
C. Vestigial sideband
D. Double sideband
Operating Procedures
<number>

## Slide 14: G2A04 - Which mode is most commonly used for voice communications on the 17-meter and 12-meter bands?
A. Upper sideband
B. Lower sideband
C. Vestigial sideband
D. Double sideband
Operating Procedures
<number>

## Slide 15: G2A04 - Which mode is most commonly used for voice communications on the 17-meter and 12-meter bands?
A. Upper sideband
B. Lower sideband
C. Vestigial sideband
D. Double sideband
Operating Procedures
<number>

## Slide 16: G2A05 - Which mode of voice communication is most commonly used on the HF amateur bands?
A. Frequency modulation
B. Double sideband
C. Single sideband
D. Phase modulation
Operating Procedures
<number>

## Slide 17: G2A05 - Which mode of voice communication is most commonly used on the HF amateur bands?
A. Frequency modulation
B. Double sideband
C. Single sideband
D. Phase modulation
Operating Procedures
<number>

## Slide 18: G2A06 - Which of the following is an advantage when using single sideband as compared to other analog voice modes on the HF amateur bands?
A. Very high fidelity voice modulation
B. Less bandwidth used and greater power efficiency
C. Ease of tuning on receive and immunity to impulse noise
D. Less subject to interference from atmospheric static crashes
Operating Procedures
<number>

## Slide 19: G2A06 - Which of the following is an advantage when using single sideband as compared to other analog voice modes on the HF amateur bands?
A. Very high fidelity voice modulation
B. Less bandwidth used and greater power efficiency
C. Ease of tuning on receive and immunity to impulse noise
D. Less subject to interference from atmospheric static crashes
Operating Procedures
<number>

## Slide 20: G2A07 - Which of the following statements is true of the single sideband voice mode?
A. Only one sideband and the carrier are transmitted; the other sideband is suppressed
B. Only one sideband is transmitted; the other sideband and carrier are suppressed
C. SSB is the only voice mode that is authorized on the 20-meter, 15-meter, and 10-meter amateur bands
D. SSB is the only voice mode that is authorized on the 160-meter, 75-meter and 40-meter amateur bands
Operating Procedures
<number>

## Slide 21: G2A07 - Which of the following statements is true of the single sideband voice mode?
A. Only one sideband and the carrier are transmitted; the other sideband is suppressed
B. Only one sideband is transmitted; the other sideband and carrier are suppressed
C. SSB is the only voice mode that is authorized on the 20-meter, 15-meter, and 10-meter amateur bands
D. SSB is the only voice mode that is authorized on the 160-meter, 75-meter and 40-meter amateur bands
Operating Procedures
<number>

## Slide 22: G2A08 - Which of the following is a recommended way to break into a contact when using phone?
A. Say "QRZ" several times followed by your call sign
B. Say your call sign during a break between transmissions by the other stations
C. Say "Break Break Break" and wait for a response
D. Say "CQ" followed by the call sign of either station
Operating Procedures
<number>

## Slide 23: G2A08 - Which of the following is a recommended way to break into a contact when using phone?
A. Say "QRZ" several times followed by your call sign
B. Say your call sign during a break between transmissions by the other stations
C. Say "Break Break Break" and wait for a response
D. Say "CQ" followed by the call sign of either station
Operating Procedures
<number>

## Slide 24: G2A09 - Why do most amateur stations use lower sideband on the 160-meter, 75-meter and 40-meter bands?
A. Lower sideband is more efficient than upper sideband at these frequencies
B. Lower sideband is the only sideband legal on these frequency bands
C. Because it is fully compatible with an AM detector
D. Current amateur practice is to use lower sideband on these frequency bands
Operating Procedures
<number>

## Slide 25: G2A09 - Why do most amateur stations use lower sideband on the 160-meter, 75-meter and 40-meter bands?
A. Lower sideband is more efficient than upper sideband at these frequencies
B. Lower sideband is the only sideband legal on these frequency bands
C. Because it is fully compatible with an AM detector
D. Current amateur practice is to use lower sideband on these frequency bands
Operating Procedures
<number>

## Slide 26: G2A10 - Which of the following statements is true of voice VOX operation versus PTT operation?
A. The received signal is more natural sounding
B. It allows "hands free" operation
C. It occupies less bandwidth
D. It provides more power output
Operating Procedures
<number>

## Slide 27: G2A10 - Which of the following statements is true of voice VOX operation versus PTT operation?
A. The received signal is more natural sounding
B. It allows "hands free" operation
C. It occupies less bandwidth
D. It provides more power output
Operating Procedures
<number>

## Slide 28: G2A11 - What does the expression "CQ DX" usually indicate?
A. A general call for any station
B. The caller is listening for a station in Germany
C. The caller is looking for any station outside their own country
D. A distress call
Operating Procedures
<number>

## Slide 29: G2A11 - What does the expression "CQ DX" usually indicate?
A. A general call for any station
B. The caller is listening for a station in Germany
C. The caller is looking for any station outside their own country
D. A distress call
Operating Procedures
<number>

## Slide 30: G2B - Operating courtesy; band plans; emergencies, including drills and emergency communications
Operating Procedures
<number>

## Slide 31: G2B01 - Which of the following is true concerning access to frequencies in non-emergency situations?
A. Nets always have priority
B. QSOs in progress always have priority
C. Except during FCC declared emergencies, no one has priority access to frequencies
D. Contest operations must always yield to non-contest use of frequencies
Operating Procedures
<number>

## Slide 32: G2B01 - Which of the following is true concerning access to frequencies in non-emergency situations?
A. Nets always have priority
B. QSOs in progress always have priority
C. Except during FCC declared emergencies, no one has priority access to frequencies
D. Contest operations must always yield to non-contest use of frequencies
Operating Procedures
<number>

## Slide 33: G2B02 - What is the first thing you should do if you are communicating with another amateur station and hear a station in distress break in?
A. Continue your communication because you were on the frequency first
B. Acknowledge the station in distress and determine what assistance may be needed
C. Change to a different frequency
D. Immediately cease all transmissions
Operating Procedures
<number>

## Slide 34: G2B02 - What is the first thing you should do if you are communicating with another amateur station and hear a station in distress break in?
A. Continue your communication because you were on the frequency first
B. Acknowledge the station in distress and determine what assistance may be needed
C. Change to a different frequency
D. Immediately cease all transmissions
Operating Procedures
<number>

## Slide 35: G2B03 - If propagation changes during your contact and you notice increasing interference from other activity on the same frequency, what should you do?
A. Tell the interfering stations to change frequency
B. Report the interference to your local Amateur Auxiliary Coordinator
C. As a common courtesy, move your contact to another frequency
D. Increase power to overcome interference
Operating Procedures
<number>

## Slide 36: G2B03 - If propagation changes during your contact and you notice increasing interference from other activity on the same frequency, what should you do?
A. Tell the interfering stations to change frequency
B. Report the interference to your local Amateur Auxiliary Coordinator
C. As a common courtesy, move your contact to another frequency
D. Increase power to overcome interference
Operating Procedures
<number>

## Slide 37: G2B04 - When selecting a CW transmitting frequency, what minimum separation should be used to minimize interference to stations on adjacent frequencies?
A. 5 to 50 Hz
B. 150 to 500 Hz
C. 1 to 3 kHz
D. 3 to 6 kHz
Operating Procedures
<number>

## Slide 38: G2B04 - When selecting a CW transmitting frequency, what minimum separation should be used to minimize interference to stations on adjacent frequencies?
A. 5 to 50 Hz
B. 150 to 500 Hz
C. 1 to 3 kHz
D. 3 to 6 kHz
Operating Procedures
<number>

## Slide 39: G2B05 - What is the customary minimum frequency separation between SSB signals under normal conditions?
A. Between 150 and 500 Hz
B. Approximately 3 kHz
C. Approximately 6 kHz
D. Approximately 10 kHz
Operating Procedures
<number>

## Slide 40: G2B05 - What is the customary minimum frequency separation between SSB signals under normal conditions?
A. Between 150 and 500 Hz
B. Approximately 3 kHz
C. Approximately 6 kHz
D. Approximately 10 kHz
Operating Procedures
<number>

## Slide 41: G2B06 - What is a practical way to avoid harmful interference on an apparently clear frequency before calling CQ on CW or phone?
A. Send "QRL?" on CW, followed by your call sign; or, if using phone, ask if the frequency is in use, followed by your call sign
B. Listen for 2 minutes before calling CQ
C. Send the letter "V" in Morse code several times and listen for a response or say "test" several times and listen for a response
D. Send "QSY" on CW or if using phone, announce "the frequency is in use", then give your call and listen for a response
Operating Procedures
<number>

## Slide 42: G2B06 - What is a practical way to avoid harmful interference on an apparently clear frequency before calling CQ on CW or phone?
A. Send "QRL?" on CW, followed by your call sign; or, if using phone, ask if the frequency is in use, followed by your call sign
B. Listen for 2 minutes before calling CQ
C. Send the letter "V" in Morse code several times and listen for a response or say "test" several times and listen for a response
D. Send "QSY" on CW or if using phone, announce "the frequency is in use", then give your call and listen for a response
Operating Procedures
<number>

## Slide 43: G2B07 - Which of the following complies with good amateur practice when choosing a frequency on which to initiate a call?
A. Check to see if the channel is assigned to another station
B. Identify your station by transmitting your call sign at least 3 times
C. Follow the voluntary band plan for the operating mode you intend to use
D. All of these choices are correct
Operating Procedures
<number>

## Slide 44: G2B07 - Which of the following complies with good amateur practice when choosing a frequency on which to initiate a call?
A. Check to see if the channel is assigned to another station
B. Identify your station by transmitting your call sign at least 3 times
C. Follow the voluntary band plan for the operating mode you intend to use
D. All of these choices are correct
Operating Procedures
<number>

## Slide 45: CW Prosigns
DX – Distant station (outside the country)
CQ – Calling any station
AR – "+" over, end of message
K – go, invite any station to transmit
KN – "(" go only, invite a specific station to transmit
BK – invite receiving station to transmit
AS – please stand by
SK – end of contact (sent before call)
CL – going off the air (clear)
<number>

## Slide 46: G2B08 - What is the "DX window" in a voluntary band plan?
A. A portion of the band that should not be used for contacts between stations within the 48 contiguous United States
B. An FCC rule that prohibits contacts between stations within the United States and possessions in that portion of the band
C. An FCC rule that allows only digital contacts in that portion of the band
D. A portion of the band that has been voluntarily set aside for digital contacts only
Operating Procedures
<number>

## Slide 47
Operating Procedures
<number>

## Slide 48: G2B08 - What is the "DX window" in a voluntary band plan?
A. A portion of the band that should not be used for contacts between stations within the 48 contiguous United States
B. An FCC rule that prohibits contacts between stations within the United States and possessions in that portion of the band
C. An FCC rule that allows only digital contacts in that portion of the band
D. A portion of the band that has been voluntarily set aside for digital contacts only
Operating Procedures
<number>

## Slide 49: G2B09 - Who may be the control operator of an amateur station transmitting in RACES to assist relief operations during a disaster?
A. Only a person holding an FCC issued amateur operator license
B. Only a RACES net control operator
C. A person holding an FCC issued amateur operator license or an appropriate government official
D. Any control operator when normal communication systems are operational
Operating Procedures
<number>

## Slide 50: G2B09 - Who may be the control operator of an amateur station transmitting in RACES to assist relief operations during a disaster?
A. Only a person holding an FCC issued amateur operator license
B. Only a RACES net control operator
C. A person holding an FCC issued amateur operator license or an appropriate government official
D. Any control operator when normal communication systems are operational
Operating Procedures
<number>

## Slide 51: G2B10 - When may the FCC restrict normal frequency operations of amateur stations participating in RACES?
A. When they declare a temporary state of communication emergency
B. When they seize your equipment for use in disaster communications
C. Only when all amateur stations are instructed to stop transmitting
D. When the President’s War Emergency Powers have been invoked
Operating Procedures
<number>

## Slide 52: G2B10 - When may the FCC restrict normal frequency operations of amateur stations participating in RACES?
A. When they declare a temporary state of communication emergency
B. When they seize your equipment for use in disaster communications
C. Only when all amateur stations are instructed to stop transmitting
D. When the President’s War Emergency Powers have been invoked
Operating Procedures
<number>

## Slide 53: G2B11 - What frequency should be used to send a distress call?
A. Whichever frequency has the best chance of communicating the distress message
B. Only frequencies authorized for RACES or ARES stations
C. Only frequencies that are within your operating privileges
D. Only frequencies used by police, fire or emergency medical services
Operating Procedures
<number>

## Slide 54: G2B11 - What frequency should be used to send a distress call?
A. Whichever frequency has the best chance of communicating the distress message
B. Only frequencies authorized for RACES or ARES stations
C. Only frequencies that are within your operating privileges
D. Only frequencies used by police, fire or emergency medical services
Operating Procedures
<number>

## Slide 55: G2B12 - When is an amateur station allowed to use any means at its disposal to assist another station in distress?
A. Only when transmitting in RACES
B. At any time when transmitting in an organized net
C. At any time during an actual emergency
D. Only on authorized HF frequencies
Operating Procedures
<number>

## Slide 56: G2B12 - When is an amateur station allowed to use any means at its disposal to assist another station in distress?
A. Only when transmitting in RACES
B. At any time when transmitting in an organized net
C. At any time during an actual emergency
D. Only on authorized HF frequencies
Operating Procedures
<number>

## Slide 57: G2C - CW operating procedures and procedural signals; Q signals and common abbreviations: full break in
Operating Procedures
<number>

## Slide 58: Q Signals
<number>
QRM | Man-made noise | QRN | Atmospheric noise
QSY | Change frequency | QTH | Current/home location
QSB | Atmospheric fading | QSL | Confirmation of report
QSK | Full break-in keying | QRV | Ready to receive
QRS | Send more slowly | QRQ | Send more quickly

## Slide 59: G2C01 - Which of the following describes full break-in telegraphy ( QSK ) ?
A. Breaking stations send the Morse code prosign BK
B. Automatic keyers are used to send Morse code instead of hand keys
C. An operator must activate a manual send/receive switch before and after every transmission
D. Transmitting stations can receive between code characters and elements
Operating Procedures
<number>

## Slide 60: G2C01 - Which of the following describes full break-in telegraphy ( QSK ) ?
A. Breaking stations send the Morse code prosign BK
B. Automatic keyers are used to send Morse code instead of hand keys
C. An operator must activate a manual send/receive switch before and after every transmission
D. Transmitting stations can receive between code characters and elements
Operating Procedures
<number>

## Slide 61: G2C02 - What should you do if a CW station sends "QRS“ ?
A. Send slower
B. Change frequency
C. Increase your power
D. Repeat everything twice
Operating Procedures
<number>

## Slide 62: G2C02 - What should you do if a CW station sends "QRS“ ?
A. Send slower
B. Change frequency
C. Increase your power
D. Repeat everything twice
Operating Procedures
<number>

## Slide 63: G2C03 - What does it mean when a CW operator sends "KN" at the end of a transmission?
A. Listening for novice stations
B. Operating full break-in
C. Listening only for a specific station or stations
D. Closing station now
Operating Procedures
<number>

## Slide 64: G2C03 - What does it mean when a CW operator sends "KN" at the end of a transmission?
A. Listening for novice stations
B. Operating full break-in
C. Listening only for a specific station or stations
D. Closing station now
Operating Procedures
<number>

## Slide 65: G2C04 - What does the Q signal "QRL“ mean?
A. "Will you keep the frequency clear?"
B. "Are you operating full break-in" or "Can you operate full break-in?"
C. "Are you listening only for a specific station?"
D. "Are you busy?", or "Is this frequency in use?"
Operating Procedures
<number>

## Slide 66: G2C04 - What does the Q signal "QRL“ mean?
A. "Will you keep the frequency clear?"
B. "Are you operating full break-in" or "Can you operate full break-in?"
C. "Are you listening only for a specific station?"
D. "Are you busy?", or "Is this frequency in use?"
Operating Procedures
<number>

## Slide 67: G2C05 - What is the best speed to use when answering a CQ in Morse code?
A. The fastest speed at which you are comfortable copying
B. The speed at which the CQ was sent
C. A slow speed until contact is established
D. At the standard calling speed of 5 wpm
Operating Procedures
<number>

## Slide 68: G2C05 - What is the best speed to use when answering a CQ in Morse code?
A. The fastest speed at which you are comfortable copying
B. The speed at which the CQ was sent
C. A slow speed until contact is established
D. At the standard calling speed of 5 wpm
Operating Procedures
<number>

## Slide 69: G2C06 - What does the term "zero beat" mean in CW operation?
A. Matching the speed of the transmitting station
B. Operating split to avoid interference on frequency
C. Sending without error
D. Matching your transmit frequency to the frequency of a received signal.
Operating Procedures
<number>

## Slide 70: G2C06 - What does the term "zero beat" mean in CW operation?
A. Matching the speed of the transmitting station
B. Operating split to avoid interference on frequency
C. Sending without error
D. Matching your transmit frequency to the frequency of a received signal.
Operating Procedures
<number>

## Slide 71: G2C07 - When sending CW, what does a "C" mean when added to the RST report?
A. Chirpy or unstable signal
B. Report was read from an S meter rather than estimated
C. 100 percent copy
D. Key clicks
Operating Procedures
<number>

## Slide 72: G2C07 - When sending CW, what does a "C" mean when added to the RST report?
A. Chirpy or unstable signal
B. Report was read from an S meter rather than estimated
C. 100 percent copy
D. Key clicks
Operating Procedures
<number>

## Slide 73: G2C08 - What prosign is sent to indicate the end of a formal message when using CW?
A. SK
B. BK
C. AR
D. KN
Operating Procedures
<number>

## Slide 74: G2C08 - What prosign is sent to indicate the end of a formal message when using CW?
A. SK
B. BK
C. AR
D. KN
Operating Procedures
<number>

## Slide 75: G2C09 - What does the Q signal "QSL" mean?
A. Send slower
B. We have already confirmed by card
C. I acknowledge receipt
D. We have worked before
Operating Procedures
<number>

## Slide 76: G2C09 - What does the Q signal "QSL" mean?
A. Send slower
B. We have already confirmed by card
C. I acknowledge receipt
D. We have worked before
Operating Procedures
<number>

## Slide 77: G2C10 - What does the Q signal "QRN" mean?
A. Send more slowly
B. I am troubled by static
C. Zero beat my signal
D. Stop sending
Operating Procedures
<number>

## Slide 78: G2C10 - What does the Q signal "QRN" mean?
A. Send more slowly
B. I am troubled by static
C. Zero beat my signal
D. Stop sending
Operating Procedures
<number>

## Slide 79: G2C11 - What does the Q signal "QRV" mean?
A. You are sending too fast
B. There is interference on the frequency
C. I am quitting for the day
D. I am ready to receive messages
Operating Procedures
<number>

## Slide 80: G2C11 - What does the Q signal "QRV" mean?
A. You are sending too fast
B. There is interference on the frequency
C. I am quitting for the day
D. I am ready to receive messages
Operating Procedures
<number>

## Slide 81: G2D - Amateur Auxiliary; minimizing interference; HF operations
Operating Procedures
<number>

## Slide 82: G2D01 - What is the Amateur Auxiliary to the FCC?
A. Amateur volunteers who are formally enlisted to monitor the airwaves for rules violations
B. Amateur volunteers who conduct amateur licensing examinations
C. Amateur volunteers who conduct frequency coordination for amateur VHF repeaters
D. Amateur volunteers who use their station equipment to help civil defense organizations in times of emergency
Operating Procedures
<number>

## Slide 83: G2D01 - What is the Amateur Auxiliary to the FCC?
A. Amateur volunteers who are formally enlisted to monitor the airwaves for rules violations
B. Amateur volunteers who conduct amateur licensing examinations
C. Amateur volunteers who conduct frequency coordination for amateur VHF repeaters
D. Amateur volunteers who use their station equipment to help civil defense organizations in times of emergency
Operating Procedures
<number>

## Slide 84: G2D02 - Which of the following are objectives of the Amateur Auxiliary?
A. To conduct efficient and orderly amateur licensing examinations
B. To encourage self-regulation and compliance with the rules by radio amateur operators
C. To coordinate repeaters for efficient and orderly spectrum usage
D. To provide emergency and public safety communications
Operating Procedures
<number>

## Slide 85: G2D02 - Which of the following are objectives of the Amateur Auxiliary?
A. To conduct efficient and orderly amateur licensing examinations
B. To encourage self-regulation and compliance with the rules by radio amateur operators
C. To coordinate repeaters for efficient and orderly spectrum usage
D. To provide emergency and public safety communications
Operating Procedures
<number>

## Slide 86: G2D03 - What skills learned during hidden transmitter hunts are of help to the Amateur Auxiliary?
A. Identification of out of band operation
B. Direction finding used to locate stations violating FCC Rules
C. Identification of different call signs
D. Hunters have an opportunity to transmit on non-amateur frequencies
Operating Procedures
<number>

## Slide 87: G2D03 - What skills learned during hidden transmitter hunts are of help to the Amateur Auxiliary?
A. Identification of out of band operation
B. Direction finding used to locate stations violating FCC Rules
C. Identification of different call signs
D. Hunters have an opportunity to transmit on non-amateur frequencies
Operating Procedures
<number>

## Slide 88: Azmuthal Map Projection
<number>
Notes: <number>
An Azmuthal map is a map projection centered on a particular location, used to determine the shortest path between points on the surface of the earth. From this map, centered on Seattle, it can be seen that San Diego is 165 degrees, Hawaii about 230 degrees and Anchorage, AK will be about 325 degrees for the shortest path. These bearings will likely be different than those from a standard Mercator projection because they account for the earth’s curvature.
It is often possible to hear your own voice echo when transmitting. This is from a signal propagating all the way around the world via “long path”. This “long path” signal will be from exactly the opposite bearing (180 degrees different) and because one path may have daylight, where the other doesn’t, it is often possible to make a long path contact when short path doesn’t work.

## Slide 89: G2D04 - Which of the following describes an azimuthal projection map?
A. A map that shows accurate land masses
B. A map that shows true bearings and distances from a particular location
C. A map that shows the angle at which an amateur satellite crosses the equator
D. A map that shows the number of degrees longitude that an amateur satellite appears to move westward at the equator with each orbit
Operating Procedures
<number>

## Slide 90: G2D04 - Which of the following describes an azimuthal projection map?
A. A map that shows accurate land masses
B. A map that shows true bearings and distances from a particular location
C. A map that shows the angle at which an amateur satellite crosses the equator
D. A map that shows the number of degrees longitude that an amateur satellite appears to move westward at the equator with each orbit
Operating Procedures
<number>

## Slide 91: G2D05 - When is it permissible to communicate with amateur stations in countries outside the areas administered by the Federal Communications Commission?
A. Only when the foreign country has a formal third party agreement filed with the FCC
B. When the contact is with amateurs in any country except those whose administrations have notified the ITU that they object to such communications
C. When the contact is with amateurs in any country as long as the communication is conducted in English
D. Only when the foreign country is a member of the International Amateur Radio Union
Operating Procedures
<number>

## Slide 92: G2D05 - When is it permissible to communicate with amateur stations in countries outside the areas administered by the Federal Communications Commission?
A. Only when the foreign country has a formal third party agreement filed with the FCC
B. When the contact is with amateurs in any country except those whose administrations have notified the ITU that they object to such communications
C. When the contact is with amateurs in any country as long as the communication is conducted in English
D. Only when the foreign country is a member of the International Amateur Radio Union
Operating Procedures
<number>

## Slide 93: G2D06 - How is a directional antenna pointed when making a "long-path" contact with another station?
A. Toward the rising Sun
B. Along the gray line
C. 180 degrees from its short-path heading
D. Toward the north
Operating Procedures
<number>

## Slide 94: G2D06 - How is a directional antenna pointed when making a "long-path" contact with another station?
A. Toward the rising Sun
B. Along the gray line
C. 180 degrees from its short-path heading
D. Toward the north
Operating Procedures
<number>

## Slide 95: G2D07 - Which of the following is required by the FCC rules when operating in the 60-meter band?
A. If you are using other than a dipole antenna, you must keep a record of the gain of your antenna
B. You must keep a record of the date, time, frequency, power level and stations worked
C. You must keep a record of all third party traffic
D. You must keep a record of the manufacturer of your equipment and the antenna used
Operating Procedures
<number>

## Slide 96: G2D07 - Which of the following is required by the FCC rules when operating in the 60-meter band?
A. If you are using other than a dipole antenna, you must keep a record of the gain of your antenna
B. You must keep a record of the date, time, frequency, power level and stations worked
C. You must keep a record of all third party traffic
D. You must keep a record of the manufacturer of your equipment and the antenna used
Operating Procedures
<number>

## Slide 97: Station Log Examples
<number>

## Slide 98: G2D08 - What is a reason why many amateurs keep a station log?
A. The ITU requires a log of all international contacts
B. The ITU requires a log of all international third party traffic
C. The log provides evidence of operation needed to renew a license without retest
D. To help with a reply if the FCC requests information
Operating Procedures
<number>

## Slide 99: G2D08 - What is a reason why many amateurs keep a station log?
A. The ITU requires a log of all international contacts
B. The ITU requires a log of all international third party traffic
C. The log provides evidence of operation needed to renew a license without retest
D. To help with a reply if the FCC requests information
Operating Procedures
<number>

## Slide 100: G2D09 - What information is traditionally contained in a station log?
A. Date and time of contact
B. Band and/or frequency of the contact
C. Call sign of station contacted and the signal report given
D. All of these choices are correct
Operating Procedures
<number>

## Slide 101: G2D09 - What information is traditionally contained in a station log?
A. Date and time of contact
B. Band and/or frequency of the contact
C. Call sign of station contacted and the signal report given
D. All of these choices are correct
Operating Procedures
<number>

## Slide 102: G2D10 - What is QRP operation?
A. Remote piloted model control
B. Low power transmit operation
C. Transmission using Quick Response Protocol
D. Traffic relay procedure net operation
Operating Procedures
<number>

## Slide 103: G2D10 - What is QRP operation?
A. Remote piloted model control
B. Low power transmit operation
C. Transmission using Quick Response Protocol
D. Traffic relay procedure net operation
Operating Procedures
<number>

## Slide 104: G2D11 - Which HF antenna would be the best to use for minimizing interference?
A. A quarter-wave vertical antenna
B. An isotropic antenna
C. A directional antenna
D. An omnidirectional antenna
Operating Procedures
<number>

## Slide 105: G2D11 - Which HF antenna would be the best to use for minimizing interference?
A. A quarter-wave vertical antenna
B. An isotropic antenna
C. A directional antenna
D. An omnidirectional antenna
Operating Procedures
<number>

## Slide 106: G2E - Digital operating: procedures, procedural signals and common abbreviations
Operating Procedures
<number>

## Slide 107: G2E01 - Which mode is normally used when sending an RTTY signal via AFSK with an SSB transmitter?
A. USB
B. DSB
C. CW
D. LSB
Operating Procedures
<number>

## Slide 108: G2E01 - Which mode is normally used when sending an RTTY signal via AFSK with an SSB transmitter?
A. USB
B. DSB
C. CW
D. LSB
Operating Procedures
<number>

## Slide 109: G2E02 - How can a PACTOR modem or controller be used to determine if the channel is in use by other PACTOR stations?
A. Unplug the data connector temporarily and see if the channel-busy indication is turned off B. Put the modem or controller in a mode which allows monitoring communications without a connection C. Transmit UI packets several times and wait to see if there is a response from another PACTOR station D. Send the message: "Is this frequency in use?"
Operating Procedures
<number>

## Slide 110: G2E02 - How can a PACTOR modem or controller be used to determine if the channel is in use by other PACTOR stations?
A. Unplug the data connector temporarily and see if the channel-busy indication is turned off B. Put the modem or controller in a mode which allows monitoring communications without a connection C. Transmit UI packets several times and wait to see if there is a response from another PACTOR station D. Send the message: "Is this frequency in use?"
Operating Procedures
<number>

## Slide 111: G2E03 - What symptoms may result from other signals interfering with a PACTOR or WINMOR transmission?
A. Frequent retries or timeouts
B. Long pauses in message transmission
C. Failure to establish a connection between stations
D. All of these choices are correct
Operating Procedures
<number>

## Slide 112: G2E03 - What symptoms may result from other signals interfering with a PACTOR or WINMOR transmission?
A. Frequent retries or timeouts
B. Long pauses in message transmission
C. Failure to establish a connection between stations
D. All of these choices are correct
Operating Procedures
<number>

## Slide 113: G2E04 - What segment of the 20-meter band is most often used for digital transmissions?
A. 14.000 - 14.050 MHz
B. 14.070 - 14.100 MHz
C. 14.150 - 14.225 MHz
D. 14.275 - 14.350 MHz
Operating Procedures
<number>

## Slide 114: G2E04 - What segment of the 20-meter band is most often used for digital transmissions?
A. 14.000 - 14.050 MHz
B. 14.070 - 14.100 MHz
C. 14.150 - 14.225 MHz
D. 14.275 - 14.350 MHz
Operating Procedures
<number>

## Slide 115: G2E06 - What is the most common frequency shift for RTTY emissions in the amateur HF bands?
A. 85 Hz
B. 170 Hz
C. 425 Hz
D. 850 Hz
Operating Procedures
<number>

## Slide 116: G2E06 - What is the most common frequency shift for RTTY emissions in the amateur HF bands?
A. 85 Hz
B. 170 Hz
C. 425 Hz
D. 850 Hz
Operating Procedures
<number>

## Slide 117: G2E07 - What segment of the 80-meter band is most commonly used for digital transmissions?
A. 3570 – 3600 kHz
B. 3500 – 3525 kHz
C. 3700 – 3750 kHz
D. 3775 – 3825 kHz
Operating Procedures
<number>

## Slide 118: G2E07 - What segment of the 80-meter band is most commonly used for digital transmissions?
A. 3570 – 3600 kHz
B. 3500 – 3525 kHz
C. 3700 – 3750 kHz
D. 3775 – 3825 kHz
Operating Procedures
<number>

## Slide 119: G2E08 - In what segment of the 20-meter band are most PSK31 operations commonly found?
A. At the bottom of the slow-scan TV segment, near 14.230 MHz
B. At the top of the SSB phone segment, near 14.325 MHz
C. In the middle of the CW segment, near 14.100 MHz
D. Below the RTTY segment, near 14.070 MHz
Operating Procedures
<number>

## Slide 120: G2E08 - In what segment of the 20-meter band are most PSK31 operations commonly found?
A. At the bottom of the slow-scan TV segment, near 14.230 MHz
B. At the top of the SSB phone segment, near 14.325 MHz
C. In the middle of the CW segment, near 14.100 MHz
D. Below the RTTY segment, near 14.070 MHz
Operating Procedures
<number>

## Slide 121: G2E09 - How do you join a contact between two stations using the PACTOR protocol?
A. Send broadcast packets containing your call sign while in MONITOR mode B. Transmit a steady carrier until the PACTOR protocol times out and disconnects C. Joining an existing contact is not possible, PACTOR connections are limited to two stations D. Send a NAK response continuously so that the sending station has to pause.
Operating Procedures
<number>

## Slide 122: G2E09 - How do you join a contact between two stations using the PACTOR protocol?
A. Send broadcast packets containing your call sign while in MONITOR mode B. Transmit a steady carrier until the PACTOR protocol times out and disconnects C. Joining an existing contact is not possible, PACTOR connections are limited to two stations D. Send a NAK response continuously so that the sending station has to pause.
Operating Procedures
<number>

## Slide 123: G2E10 - Which of the following is a way to establish contact with a digital messaging system gateway station?
A. Long Path propagation
B. Backscatter propagation
C. Insufficient modulation
D. Overmodulation
Operating Procedures
<number>

## Slide 124: G2E10 - Which of the following is a way to establish contact with a digital messaging system gateway station?
A. Long Path propagation
B. Backscatter propagation
C. Insufficient modulation
D. Overmodulation
Operating Procedures
<number>

## Slide 125: Digital Waterfall Example’s
Operating Procedures
<number>

## Slide 126: G2E11 - What is indicated on a waterfall display by one or more vertical lines adjacent to a PSK31 signal?
A. Long Path propagation
B. Backscatter propagation
C. Insufficient modulation
D. Overmodulation
Operating Procedures
<number>

## Slide 127: G2E11 - What is indicated on a waterfall display by one or more vertical lines adjacent to a PSK31 signal?
A. Long Path propagation
B. Backscatter propagation
C. Insufficient modulation
D. Overmodulation
Operating Procedures
<number>

## Slide 128: G2E12 - Which of the following describes a waterfall display?
A. Frequency is horizontal, signal strength is vertical, time is intensity
B. Frequency is vertical, signal strength is intensity, time is horizontal
C. Frequency is horizontal, signal strength is intensity, time is vertical
D. Frequency is vertical, signal strength is horizontal, time is intensity
Operating Procedures
<number>

## Slide 129: G2E12 - Which of the following describes a waterfall display?
A. Frequency is horizontal, signal strength is vertical, time is intensity
B. Frequency is vertical, signal strength is intensity, time is horizontal
C. Frequency is horizontal, signal strength is intensity, time is vertical
D. Frequency is vertical, signal strength is horizontal, time is intensity
Operating Procedures
<number>

## Slide 130: G2E13 - Which communication system sometimes uses the Internet to transfer messages?
A. Winlink
B. RTTY
C. ARES
D. Skywarn
Operating Procedures
<number>

## Slide 131: G2E13 - Which communication system sometimes uses the Internet to transfer messages?
A. Winlink
B. RTTY
C. ARES
D. Skywarn
Operating Procedures
<number>

## Slide 132: G2E14 - What could be wrong if you cannot decode an RTTY or other FSK signal even though it is apparently tuned in properly?
A. The mark and space frequencies may be reversed B. You may have selected the wrong baud rate C. You may be listening on the wrong sideband
D. All of these choices are correct
Operating Procedures
<number>

## Slide 133: G2E14 - What could be wrong if you cannot decode an RTTY or other FSK signal even though it is apparently tuned in properly?
A. The mark and space frequencies may be reversed B. You may have selected the wrong baud rate C. You may be listening on the wrong sideband
D. All of these choices are correct
Operating Procedures
<number>

## Slide 134: G2E15 - What is the standard sideband used to generate a JT65 or JT9 digital signal when using AFSK in any amateur band?
A. LSB
B. USB
C. DSB
D. SSB
Operating Procedures
<number>

## Slide 135: G2E15 - What is the standard sideband used to generate a JT65 or JT9 digital signal when using AFSK in any amateur band?
A. LSB
B. USB
C. DSB
D. SSB
Operating Procedures
<number>

## Slide 136: End of SUBELEMENT G2 OPERATING PROCEDURES
Operating Procedures
<number>