## Slide 1: SUBELEMENT G8 SIGNALS AND EMISSIONS [3 Exam Questions–3 Groups]
Signals & Emissions
<number>
Notes: Subelement G8 Signals and Emissions. General Training Slides for 2015 Question Pool Good through June 30, 2019 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM, Howard Schultz, W7HS.
<number>

## Slide 2: SUBELEMENT G8 SIGNALS AND EMISSIONS [3 Exam Questions–3 Groups]
G8A - Carriers and modulation; AM; FM; single sideband; modulation envelope; digital modulation; over modulation
G8B - Frequency mixing; multiplication; bandwidths of various modes; deviation
G8C – Digital emission modes

## Slide 3: Amplitude Modulation Oscilloscope View
Signals and Emissions
<number>
An unmodulated RF
carrier wave
A carrier wave amplitude
modulated (AM) with a simple audio tone
Notes: <number>
Note the identical sidebands. They peak and dip together.

## Slide 4: Amplitude Modulation Spectrum Analyzer View
Signals and Emissions
<number>
An unmodulated RF
carrier requires narrow
bandwidth
Modulation of the carrier
creates sidebands. This
requires more bandwidth.
Transmitter power is spread across this bandwidth

## Slide 5: AM and SSB Spectrum Analyzer View
Signals and Emissions
<number>
The carrier contains no
audio information.
The sidebands contain
duplicate audio information
By filtering out the carrier and one sideband,
we save spectrum and concentrate our RF
energy into a narrower bandwidth. SSB is
therefore more efficient.

## Slide 6: Frequency Modulation
Signals and Emissions
<number>
Unmodulated carrier, full power at all times
Waveform of modulating signal
Modulated carrier with frequency deviation and constant amplitude
“Over modulation” called “over deviation” on FM, causes the signal to become wider and potentially cause adjacent channel interference

## Slide 7: G8A01 - How is an FSK signal generated?
A. By keying an FM transmitter with a sub-audible tone
B. By changing an oscillator’s frequency directly with a digital control signal
C. By using a transceiver’s computer data interface protocol to change frequencies
D. By reconfiguring the CW keying input to act as a tone generator
<number>
Signals & Emmisions

## Slide 8: G8A01 - How is an FSK signal generated?
A. By keying an FM transmitter with a sub-audible tone
B. By changing an oscillator’s frequency directly with a digital control signal
C. By using a transceiver’s computer data interface protocol to change frequencies
D. By reconfiguring the CW keying input to act as a tone generator
<number>
Signals & Emmisions

## Slide 9: G8A02 - What is the name of the process that changes the phase angle of an RF wave to convey information?
A. Phase convolution
B. Phase modulation
C. Angle convolution
D. Radian inversion
<number>
Signals & Emmisions

## Slide 10: G8A02 - What is the name of the process that changes the phase angle of an RF wave to convey information?
A. Phase convolution
B. Phase modulation
C. Angle convolution
D. Radian inversion
<number>
Signals & Emmisions

## Slide 11: G8A03 - What is the name of the process that changes the instantaneous frequency of an RF wave to convey information?
A. Frequency convolution
B. Frequency transformation
C. Frequency conversion
D. Frequency modulation
<number>
Signals & Emmisions

## Slide 12: G8A03 - What is the name of the process that changes the instantaneous frequency of an RF wave to convey information?
A. Frequency convolution
B. Frequency transformation
C. Frequency conversion
D. Frequency modulation
<number>
Signals & Emmisions

## Slide 13: G8A04 - What emission is produced by a reactance modulator connected to a transmitter RF amplifier stage?
A. Multiplex modulation
B. Phase modulation
C. Amplitude modulation
D. Pulse modulation
<number>
Signals & Emmisions

## Slide 14: G8A04 - What emission is produced by a reactance modulator connected to a transmitter RF amplifier stage?
A. Multiplex modulation
B. Phase modulation
C. Amplitude modulation
D. Pulse modulation
<number>
Signals & Emmisions

## Slide 15: G8A05 - What type of modulation varies the instantaneous power level of the RF signal?
A. Frequency shift keying
B. Phase modulation
C. Frequency modulation
D. Amplitude modulation
<number>
Signals & Emmisions

## Slide 16: G8A05 - What type of modulation varies the instantaneous power level of the RF signal?
A. Frequency shift keying
B. Phase modulation
C. Frequency modulation
D. Amplitude modulation
<number>
Signals & Emmisions

## Slide 17: G8A06 - What is one advantage of carrier suppression in a single sideband phone transmission versus full carrier amplitude modulation?
A. Audio fidelity is improved
B. Greater modulation percentage is obtainable with lower distortion
C. Available transmitter power can be used more effectively
D. Simpler receiving equipment can be used
<number>
Signals & Emmisions

## Slide 18: G8A06 - What is one advantage of carrier suppression in a single sideband phone transmission versus full carrier amplitude modulation?
A. Audio fidelity is improved
B. Greater modulation percentage is obtainable with lower distortion
C. Available transmitter power can be used more effectively
D. Simpler receiving equipment can be used
<number>
Signals & Emmisions

## Slide 19: G8A07 - Which of the following phone emissions uses the narrowest bandwidth?
A. Single sideband
B. Double sideband
C. Phase modulation
D. Frequency modulation
<number>
Signals & Emmisions

## Slide 20: G8A07 - Which of the following phone emissions uses the narrowest bandwidth?
A. Single sideband
B. Double sideband
C. Phase modulation
D. Frequency modulation
<number>
Signals & Emmisions

## Slide 21: G8A08 - Which of the following is an effect of overmodulation?
A. Insufficient audio
B. Insufficient bandwidth
C. Frequency drift
D. Excessive bandwidth
<number>
Signals & Emmisions

## Slide 22: G8A08 - Which of the following is an effect of overmodulation?
A. Insufficient audio
B. Insufficient bandwidth
C. Frequency drift
D. Excessive bandwidth
<number>
Signals & Emmisions
Excessive
Proper
Oscilloscope View

## Slide 23: G8A09 - What control is typically adjusted for proper ALC setting on an amateur single sideband transceiver?
A. The RF clipping level
B. Transmit audio or microphone gain
C. Antenna inductance or capacitance
D. Attenuator level
<number>
Signals & Emmisions

## Slide 24: G8A09 - What control is typically adjusted for proper ALC setting on an amateur single sideband transceiver?
A. The RF clipping level
B. Transmit audio or microphone gain
C. Antenna inductance or capacitance
D. Attenuator level
<number>
Signals & Emmisions

## Slide 25: G8A10 - What is meant by the term flat-topping when referring to a single sideband phone transmission?
A. Signal distortion caused by insufficient collector current
B. The transmitter's automatic level control (ALC) is properly adjusted
C. Signal distortion caused by excessive drive
D. The transmitter's carrier is properly suppressed
<number>
Signals & Emmisions

## Slide 26: G8A10 - What is meant by the term flat-topping when referring to a single sideband phone transmission?
A. Signal distortion caused by insufficient collector current
B. The transmitter's automatic level control (ALC) is properly adjusted
C. Signal distortion caused by excessive drive
D. The transmitter's carrier is properly suppressed
<number>
Signals & Emmisions

## Slide 27: G8A11 - What is the modulation envelope of an AM signal?
A. The waveform created by connecting the peak values of the modulated signal
B. The carrier frequency that contains the signal
C. Spurious signals that envelop nearby frequencies
D. The bandwidth of the modulated signal
<number>
Signals & Emmisions

## Slide 28: G8A11 - What is the modulation envelope of an AM signal?
A. The waveform created by connecting the peak values of the modulated signal
B. The carrier frequency that contains the signal
C. Spurious signals that envelop nearby frequencies
D. The bandwidth of the modulated signal
<number>
Signals & Emmisions

## Slide 29: G8B - Frequency mixing; multiplication; bandwidths of various modes; deviation; duty cycle
<number>
Signals & Emmisions

## Slide 30: G8B01 - What receiver stage combines a 14.250 MHz input signal with a 13.795 MHz oscillator signal to produce a 455 kHz intermediate frequency ( IF ) signal?
A. Mixer
B. BFO
C. VFO
D. Discriminator
<number>
Signals & Emmisions

## Slide 31: G8B01 - What receiver stage combines a 14.250 MHz input signal with a 13.795 MHz oscillator signal to produce a 455 kHz intermediate frequency ( IF ) signal?
A. Mixer
B. BFO
C. VFO
D. Discriminator
<number>
Signals & Emmisions

## Slide 32: G8B02 - If a receiver mixes a 13.800 MHz VFO with a 14.255 MHz received signal to produce a 455 kHz intermediate frequency ( IF ) signal, what type of interference will a 13.345 MHz signal produce in the receiver?
A. Quadrature noise
B. Image response
C. Mixer interference
D. Intermediate interference
<number>
Signals & Emmisions

## Slide 33: G8B02 - If a receiver mixes a 13.800 MHz VFO with a 14.255 MHz received signal to produce a 455 kHz intermediate frequency ( IF ) signal, what type of interference will a 13.345 MHz signal produce in the receiver?
A. Quadrature noise
B. Image response
C. Mixer interference
D. Intermediate interference
<number>
Signals & Emmisions
Received Signal Image
14,255 MHz
- 13,800 VFO 13,800 VFO
455 kHz - 13,345 MHz
455 kHz

## Slide 34: G8B03 - What is another term for the mixing of two RF signals?
A. Heterodyning
B. Synthesizing
C. Cancellation
D. Phase inverting
<number>
Signals & Emmisions

## Slide 35: G8B03 - What is another term for the mixing of two RF signals?
A. Heterodyning
B. Synthesizing
C. Cancellation
D. Phase inverting
<number>
Signals & Emmisions

## Slide 36: G8B04 - What is the stage in a VHF FM transmitter that generates a harmonic of a lower frequency signal to reach the desired operating frequency?
A. Mixer
B. Reactance modulator
C. Pre-emphasis network
D. Multiplier
<number>
Signals & Emmisions

## Slide 37: G8B04 - What is the stage in a VHF FM transmitter that generates a harmonic of a lower frequency signal to reach the desired operating frequency?
A. Mixer
B. Reactance modulator
C. Pre-emphasis network
D. Multiplier
<number>
Signals & Emmisions

## Slide 38: G8B05 - What is the approximate bandwidth of a PACTOR3 or WINMOR signal at maximum data rate?
A. 31.5 Hz
B. 500 Hz
C. 1800 Hz
D. 2300 Hz
<number>
Signals & Emmisions

## Slide 39: G8B05 - What is the approximate bandwidth of a PACTOR3 or WINMOR signal at maximum data rate?
A. 31.5 Hz
B. 500 Hz
C. 1800 Hz
D. 2300 Hz
<number>
Signals & Emmisions

## Slide 40: G8B06 - What is the total bandwidth of an FM phone transmission having 5 kHz deviation and 3 kHz modulating frequency?
A. 3 kHz
B. 5 kHz
C. 8 kHz
D. 16 kHz
<number>
Signals & Emmisions

## Slide 41: G8B06 - What is the total bandwidth of an FM phone transmission having 5 kHz deviation and 3 kHz modulating frequency?
A. 3 kHz
B. 5 kHz
C. 8 kHz
D. 16 kHz
<number>
Signals & Emmisions
(Deviation + Modulating Freq) * 2 (5kHz + 3kHz) * 2 = 16kHz

## Slide 42: G8B07 - What is the frequency deviation for a 12.21 MHz reactance modulated oscillator in a 5 kHz deviation, 146.52 MHz FM phone transmitter?
A. 101.75 Hz
B. 416.7 Hz
C. 5 kHz
D. 60 kHz
<number>
Signals & Emmisions

## Slide 43: G8B07 - What is the frequency deviation for a 12.21 MHz reactance modulated oscillator in a 5 kHz deviation, 146.52 MHz FM phone transmitter?
A. 101.75 Hz
B. 416.7 Hz
C. 5 kHz
D. 60 kHz
<number>
Signals & Emissions
146.52 / 12.21 = 12 times
5,000 / 12 = 416.67 Hz

## Slide 44: Duty Cycle
<number>
Mode | Duty Cycle
CW Morse telegraphy | 40%
SSB voice | 20%
SSB voice, heavy speech processing | 50%
SSB AFSK | 100%
SSB SSTV | 100%
FM voice or data | 100%
FSK | 100%
AM voice, 50% modulation | 50%
AM voice, 100% modulation | 30%
Duty cycle refers to both the transmit vs. receive time and the average power level during transmission. Because CW has gaps between symbols the average power is less than 100%. SSB power output varies with modulation. FM is full power regardless of modulation.
Signals & Emissions
Notes: <number>

## Slide 45: G8B08 - Why is it important to know the duty cycle of the mode you are using when transmitting?
A. To aid in tuning your transmitter
B. Some modes have high duty cycles which could exceed the transmitter's average power rating.
C. To allow time for the other station to break in during a transmission
D. All of these choices are correct
<number>
Signals & Emmisions

## Slide 46: G8B08 - Why is it important to know the duty cycle of the mode you are using when transmitting?
A. To aid in tuning your transmitter
B. Some modes have high duty cycles which could exceed the transmitter's average power rating.
C. To allow time for the other station to break in during a transmission
D. All of these choices are correct
<number>
Signals & Emmisions

## Slide 47: G8B09 - Why is it good to match receiver bandwidth to the bandwidth of the operating mode?
A. It is required by FCC rules
B. It minimizes power consumption in the receiver
C. It improves impedance matching of the antenna
D. It results in the best signal to noise ratio
<number>
Signals & Emissions

## Slide 48: G8B09 - Why is it good to match receiver bandwidth to the bandwidth of the operating mode?
A. It is required by FCC rules
B. It minimizes power consumption in the receiver
C. It improves impedance matching of the antenna
D. It results in the best signal to noise ratio
<number>
Signals & Emissions

## Slide 49: G8B10 - What is the relationship between transmitted symbol rate and bandwidth?
A. Symbol rate and bandwidth are not related
B. Higher symbol rates require wider bandwidth
C. Lower symbol rates require wider bandwidth
D. Bandwidth is always half the symbol rate
<number>
Signals & Emissions

## Slide 50: G8B10 - What is the relationship between transmitted symbol rate and bandwidth?
A. Symbol rate and bandwidth are not related
B. Higher symbol rates require wider bandwidth
C. Lower symbol rates require wider bandwidth
D. Bandwidth is always half the symbol rate
<number>
Signals & Emissions

## Slide 51: G8C – Digital emission modes
<number>
Signals & Emissions

## Slide 52: What is digital communication?
Voice
CW
Digital
1, 0, 1, 1, 1, 0 , …
Yada
Yada
Yada
Tone ON
Tone OFF
Tones

## Slide 53: Types of Digital Modes
<number>
Signals & Emissions

## Slide 54: PSK31
The Undisputed King!
“Phase Shift Keying” is the the most popular of the newer digital modes.
Wealth of information on the web regarding BPSK (Binary PSK) and QPSK (Quadrature PSK)
Because bandwidth only 31Hz, many signals can fit into the same bandwidth occupied by an SSB signal (2.4kHz approx.).
Quite common to see 15 or more signals on a 2.5kHz waterfall display.
Debuted in 1999
Most popular HF digital mode
Heard near: 3.580, 7.070, 14.070, 21.070 MHz

## Slide 55: RTTY
One of the oldest HF digital modes—Hams began using it immediately after WW II.
Most popular contest and DX mode.
Heard near: 7.040, 14.090, 21.090 MHz
Been around for many, many years and is still just as popular.
Years ago the only way to get on RTTY was to use a mechanical terminal unit such as the Creed 7 series, which were big, noisy and messy.
Today virtually all RTTY is done by the computer/soundcard combination.
Hams use 45 baud (the speed) with 170Hz shift (between mark and space).
Commercial stations use 50 or 100 baud with shifts of 425 or even 850Hz.
Most software caters for differing speeds and shifts.
Unlike most digital modes, RTTY is transmitted on LSB.

## Slide 56: PACTOR
HF mailboxes use PACTOR to forward messages to users.
Lots of bad press recently, mainly due to the actions of a few inconsiderate operators who are apparently causing interference deliberately to existing users of the digital sub bands.
Because it uses error correction, it can take quite a time to send a message particularly over a less than perfect path—but the transmitting station will keep trying until the message is received perfectly.
Developed in 1991
Three versions: 1, 2 and 3
PACTOR 2 and 3 are the most popular today
Error-free burst mode
Used primarily to exchange data, such as in the Winlink 2000 system.
400 Hz bandwidth … ~ 2x 100 baud PSK

## Slide 57: MFSK16
Introduced in 2000 by IZ8BLY
Uses 16 tones
Good performance in poor signal conditions
Heard near 14.080 MHz
Usual variant is MFSK 16, but other types such as MFSK 8.
MFSK is sideband dependent … must have receiver set to the correct sideband in order to decode it properly.
Tuning is quite critical, although AFC helps somewhat.
Top image is of an MFSK16 signal and the lower image is of an MFSK32 signal (which is nearly 500Hz wide, twice as wide as an MFSK16 signal).

## Slide 58: Hellschreiber
Oldest digital mode; created in 1929
Fax-type mode where text is “painted” on the screen for direct reading—not decoded by software.
Heard between 14.075 and 14.080 MHz
Your eyes do the filtering!
Decoded text displayed on a ‘ticker tape’ display.
Very distinctive ‘grating’ sound and is a narrow band mode.
Even weak signals can be decoded as your eye/brain combination can ‘fill in the blanks’ where the signal fades.

## Slide 59: Packet
Declining popularity, but still heard
Used for message forwarding, APRS and some “live” keyboard-to-keyboard QSOs.
HF forwarding heard near 14.095 MHz
APRS near 10.150 MHz
Live QSOs at 14.105 MHz
HF mailboxes etc. use packet to forward messages to users.
Usual data rate on HF is 300 baud, with 1200 and 9600 baud being common place at VHF and UHF.
Picture shows a mailbox/BBS in Turkey negotiating with a BBS in the UK.
Short burst at the bottom of the picture is header and callsign information.
Longer burst is the actual data.
Packet BBS/mailboxes can be heard chirping around 14.1MHz.

## Slide 60: Olivia
New HF digital mode introduced in 2005
Selectable bandwidth
Heard between 14.105 and 14.109 MHz
Extremely resistant to fading and QRM.
Can get full copy on stations that are barely audible … even ones that fade down to almost zero seem to still print well.
Has different variants each having a different bandwidth (from 500Hz to 2kHz) and different number of tones.
Can be very slow (2-3 characters per second) but a slow contact is better than none at all!
To avoid interference to other stations is it usual to start an Olivia transmission on a full kHz (i.e. 14.108.0 rather than 14.108.3 for instance).
8 tones over a 250Hz bandwidth

## Slide 61: ALE
Automatic Link Establishment
Automatically determines the best band for communication between two stations.
Will alert operators when path is determined
Now finding more use in amateur circles, thanks to the efforts of the writers of some of the multimode decoders, such as MultiPSK.
When running correctly, can initiate and establish connections between two stations without human intervention (hence the ‘Automatic’ part.)

## Slide 62: JT65
Developed originally as part of the WSJT weak signal modes software package by Joe K1JT.
Can also be decoded by other packages, such as MultiPSK.
Has found a use on HF and can be found around 14.076MHz and 21.076MHz amongst others.
Signals that are virtually inaudible can give perfect copy so its performance is excellent on the noisy HF bands.
Transfer rate is slow, as are most modes that excel in low signal decoding.

## Slide 63: G8C01 - Which of the following digital modes is designed to operate at extremely low signal strength on the HF bands?
A. FSK441 and Hellschreiber
B. JT9 and JT65
C. Clover
D. RTTY
<number>
Signals & Emissions

## Slide 64: G8C01 - Which of the following digital modes is designed to operate at extremely low signal strength on the HF bands?
A. FSK441 and Hellschreiber
B. JT9 and JT65
C. Clover
D. RTTY
<number>
Signals & Emissions

## Slide 65: G8C02 - How many data bits are sent in a single PSK31 character?
A. The number varies
B. 5
C. 7
D. 8
<number>
Signals & Emissions

## Slide 66: G8C02 - How many data bits are sent in a single PSK31 character?
A. The number varies
B. 5
C. 7
D. 8
<number>
Signals & Emissions

## Slide 67: G8C03 - What part of a data packet contains the routing and handling information?
A. Directory
B. Preamble
C. Header
D. Footer
<number>
Signals & Emissions

## Slide 68: G8C03 - What part of a data packet contains the routing and handling information?
A. Directory
B. Preamble
C. Header
D. Footer
<number>
Signals & Emissions

## Slide 69: G8C04 - Which of the following describes Baudot code?
A. A 7-bit code with start, stop and parity bits
B. A code using error detection and correction
C. A 5-bit code with additional start and stop bits
D. A code using SELCAL and LISTEN
<number>
Signals & Emissions

## Slide 70: G8C04 - Which of the following describes Baudot code?
A. A 7-bit code with start, stop and parity bits
B. A code using error detection and correction
C. A 5-bit code with additional start and stop bits
D. A code using SELCAL and LISTEN
<number>
Signals & Emissions

## Slide 71: G8C05 - In the PACTOR protocol, what is meant by an NAK response to a transmitted packet?
A. The receiver is requesting the packet be retransmitted
B. The receiver is reporting the packet was received without error
C. The receiver is busy decoding the packet
D. The entire file has been received correctly
<number>
Signals & Emissions

## Slide 72: G8C05 - In the PACTOR protocol, what is meant by an NAK response to a transmitted packet?
A. The receiver is requesting the packet be retransmitted
B. The receiver is reporting the packet was received without error
C. The receiver is busy decoding the packet
D. The entire file has been received correctly
<number>
Signals & Emissions

## Slide 73: G8C06 - What action results from a failure to exchange information due to excessive transmission attempts when using PACTOR or WINMOR?
A. The checksum overflows
B. The connection is dropped
C. Packets will be routed incorrectly
D. Encoding reverts to the default character set
<number>
Signals & Emissions

## Slide 74: G8C06 - What action results from a failure to exchange information due to excessive transmission attempts when using PACTOR or WINMOR?
A. The checksum overflows
B. The connection is dropped
C. Packets will be routed incorrectly
D. Encoding reverts to the default character set
<number>
Signals & Emissions

## Slide 75: G8C07 - How does the receiving station respond to an ARQ data mode packet containing errors?
A. It terminates the contact
B. It requests the packet be retransmitted
C. It sends the packet back to the transmitting station
D. It requests a change in transmitting protocol
<number>
Signals & Emissions

## Slide 76: G8C07 - How does the receiving station respond to an ARQ data mode packet containing errors?
A. It terminates the contact
B. It requests the packet be retransmitted
C. It sends the packet back to the transmitting station
D. It requests a change in transmitting protocol
<number>
Signals & Emissions

## Slide 77: G8C08 - Which of the following statements is true about PSK31 ?
A. Upper case letters make the signal stronger
B. Upper case letters use longer Varicode signals and thus slow down transmission
C. Varicode Error Correction is used to ensure accurate message reception
D. Higher power is needed as compared to RTTY for similar error rates
<number>
Signals & Emissions

## Slide 78: G8C08 - Which of the following statements is true about PSK31 ?
A. Upper case letters make the signal stronger
B. Upper case letters use longer Varicode signals and thus slow down transmission
C. Varicode Error Correction is used to ensure accurate message reception
D. Higher power is needed as compared to RTTY for similar error rates
<number>
Signals & Emissions

## Slide 79: G8C09 - What does the number 31 represent in "PSK31"?
A. The approximate transmitted symbol rate
B. The version of the PSK protocol
C. The year in which PSK31 was invented
D. The number of characters that can be represented by PSK31
<number>
Signals & Emissions

## Slide 80: G8C09 - What does the number 31 represent in "PSK31"?
A. The approximate transmitted symbol rate
B. The version of the PSK protocol
C. The year in which PSK31 was invented
D. The number of characters that can be represented by PSK31
<number>
Signals & Emissions

## Slide 81: G8C10 - How does forward error correction ( FEC ) allow the receiver to correct errors in received data packets?
A. By controlling transmitter output power for optimum signal strength
B. By using the varicode character set
C. By transmitting redundant information with the data
D. By using a parity bit with each character
<number>
Signals & Emissions

## Slide 82: G8C10 - How does forward error correction ( FEC ) allow the receiver to correct errors in received data packets?
A. By controlling transmitter output power for optimum signal strength
B. By using the varicode character set
C. By transmitting redundant information with the data
D. By using a parity bit with each character
<number>
Signals & Emissions

## Slide 83: G8C11 - How are the two separate frequencies of a Frequency Shift Keyed ( FSK ) signal identified?
A. Dot and Dash
B. On and Off
C. High and Low
D. Mark and Space
<number>
Signals & Emissions

## Slide 84: G8C11 - How are the two separate frequencies of a Frequency Shift Keyed ( FSK ) signal identified?
A. Dot and Dash
B. On and Off
C. High and Low
D. Mark and Space
<number>
Signals & Emissions

## Slide 85: G8C12 - Which type of code is used for sending characters in a PSK31 signal?
A. Varicode
B. Viterbi
C. Volumetric
D. Binary
<number>
Signals & Emissions

## Slide 86: G8C12 - Which type of code is used for sending characters in a PSK31 signal?
A. Varicode
B. Viterbi
C. Volumetric
D. Binary
<number>
Signals & Emissions

## Slide 87: End Of SUBELEMENT G8 SIGNALS AND EMISSIONS