## Slide 1: SUBELEMENT G5 ELECTRICAL PRINCIPLES [3 Exam Questions – 3 Groups]
Notes: Subelement G5 Electrical Principles. General Training Slides for 2015 Question Pool Good through June 30, 2019 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM, Howard Schultz, W7HS.
<number>

## Slide 2: SUBELEMENT G5 ELECTRICAL PRINCIPLES [3 Exam Questions–3 Groups]
G5A - Reactance; inductance; capacitance; impedance; impedance matching
G5B - The Decibel; current and voltage dividers; electrical power calculations; sine wave root-mean-square (RMS) values; PEP calculations
G5C – Resistors, capacitors, and inductors in series and parallel; transformers
<number>
Electrical Principles 2010

## Slide 3: Resonate Circuit
<number>
Elec. Princip.

## Slide 4: G5A01 - What is impedance?
A. The electric charge stored by a capacitor
B. The inverse of resistance
C. The opposition to the flow of current in an AC circuit
D. The force of repulsion between two similar electric fields
<number>
Elec. Princip.

## Slide 5: G5A01 - What is impedance?
A. The electric charge stored by a capacitor
B. The inverse of resistance
C. The opposition to the flow of current in an AC circuit
D. The force of repulsion between two similar electric fields
<number>
Elec. Princip.

## Slide 6: G5A02 - What is reactance?
A. Opposition to the flow of direct current caused by resistance
B. Opposition to the flow of alternating current caused by capacitance or inductance
C. A property of ideal resistors in AC circuits
D. A large spark produced at switch contacts when an inductor is de-energized
<number>
Elec. Princip.

## Slide 7: G5A02 - What is reactance?
A. Opposition to the flow of direct current caused by resistance
B. Opposition to the flow of alternating current caused by capacitance or inductance
C. A property of ideal resistors in AC circuits
D. A large spark produced at switch contacts when an inductor is de-energized
<number>
Elec. Princip.

## Slide 8: G5A03 - Which of the following causes opposition to the flow of alternating current in an inductor?
A. Conductance
B. Reluctance
C. Admittance
D. Reactance
<number>
Elec. Princip.

## Slide 9: G5A03 - Which of the following causes opposition to the flow of alternating current in an inductor?
A. Conductance
B. Reluctance
C. Admittance
D. Reactance
<number>
Elec. Princip.

## Slide 10: G5A04 - Which of the following causes opposition to the flow of alternating current in a capacitor?
A. Conductance
B. Reluctance
C. Reactance
D. Admittance
<number>
Elec. Princip.

## Slide 11: G5A04 - Which of the following causes opposition to the flow of alternating current in a capacitor?
A. Conductance
B. Reluctance
C. Reactance
D. Admittance
<number>
Elec. Princip.

## Slide 12: G5A05 - How does an inductor react to AC?
A. As the frequency of the applied AC increases, the reactance decreases
B. As the amplitude of the applied AC increases, the reactance increases
C. As the amplitude of the applied AC increases, the reactance decreases
D. As the frequency of the applied AC increases, the reactance increases
<number>
Elec. Princip.

## Slide 13: G5A05 - How does an inductor react to AC?
A. As the frequency of the applied AC increases, the reactance decreases
B. As the amplitude of the applied AC increases, the reactance increases
C. As the amplitude of the applied AC increases, the reactance decreases
D. As the frequency of the applied AC increases, the reactance increases
<number>
Elec. Princip.

## Slide 14: G5A06 - How does a capacitor react to AC?
A. As the frequency of the applied AC increases, the reactance decreases
B. As the frequency of the applied AC increases, the reactance increases
C. As the amplitude of the applied AC increases, the reactance increases
D. As the amplitude of the applied AC increases, the reactance decreases
<number>
Elec. Princip.

## Slide 15: G5A06 - How does a capacitor react to AC?
A. As the frequency of the applied AC increases, the reactance decreases
B. As the frequency of the applied AC increases, the reactance increases
C. As the amplitude of the applied AC increases, the reactance increases
D. As the amplitude of the applied AC increases, the reactance decreases
<number>
Elec. Princip.

## Slide 16: G5A07 - What happens when the impedance of an electrical load is equal to the output impedance of a power source, assuming both impedances are resistive?
A. The source delivers minimum power to the load
B. The electrical load is shorted
C. No current can flow through the circuit
D. The source can deliver maximum power to the load
<number>
Elec. Princip.

## Slide 17: G5A07 - What happens when the impedance of an electrical load is equal to the output impedance of a power source, assuming both impedances are resistive?
A. The source delivers minimum power to the load
B. The electrical load is shorted
C. No current can flow through the circuit
D. The source can deliver maximum power to the load
<number>
Elec. Princip.

## Slide 18: G5A08 - Why is impedance matching important?
A. So the source can deliver maximum power to the load
B. So the load will draw minimum power from the source
C. To ensure that there is less resistance than reactance in the circuit
D. To ensure that the resistance and reactance in the circuit are equal
<number>
Elec. Princip.

## Slide 19: G5A08 - Why is impedance matching important?
A. So the source can deliver maximum power to the load
B. So the load will draw minimum power from the source
C. To ensure that there is less resistance than reactance in the circuit
D. To ensure that the resistance and reactance in the circuit are equal
<number>
Elec. Princip.

## Slide 20
<number>
Elec. Princip.
Ohm’s Law and Power Calculations
E=Voltage (Volts)
I=Current (Amps)
R=Resistance (Ohms)
P=Power (Watts)
E
I
R
P
I
E

## Slide 21: Ohm’s Law and Power Calculations Unit Circles
Electrical Principles 2015
<number>
V
O
A
W
A
V
V=Voltage (Volts)
O=Resistance (Ohms)
A=Current (Amps)
W=Power (Watts)
To solve for a value, cover it with your finger and solve the remaining formula
Voice Of America – VOLTAGE CIRCLE W A V - WATTAGE CIRCLE
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 22: Ohm’s Law and Power Calculations Unit Circles
Electrical Principles 2015
<number>
V
O
A
W
A
V
V=Voltage (Volts)
O=Resistance (Ohms)
A=Current (Amps)
W=Power (Watts)
To solve for a value, cover it with your finger and solve the remaining formula
Voice Of America – VOLTAGE W A V - WATTAGE CIRCLE CIRCLE
E
R I
P
I E
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 23: G5A09 - What unit is used to measure reactance?
A. Farad
B. Ohm
C. Ampere
D. Siemens
<number>
Elec. Princip.

## Slide 24: G5A09 - What unit is used to measure reactance?
A. Farad
B. Ohm
C. Ampere
D. Siemens
<number>
Elec. Princip.

## Slide 25: G5A10 - What unit is used to measure impedance?
A. Volt
B. Ohm
C. Ampere
D. Watt
<number>
Elec. Princip.

## Slide 26: G5A10 - What unit is used to measure impedance?
A. Volt
B. Ohm
C. Ampere
D. Watt
<number>
Elec. Princip.

## Slide 27: G5A11 - Which of the following describes one method of impedance matching between two AC circuits?
A. Insert an LC network between the two circuits
B. Reduce the power output of the first circuit
C. Increase the power output of the first circuit
D. Insert a circulator between the two circuits
<number>
Elec. Princip.

## Slide 28: G5A11 - Which of the following describes one method of impedance matching between two AC circuits?
A. Insert an LC network between the two circuits
B. Reduce the power output of the first circuit
C. Increase the power output of the first circuit
D. Insert a circulator between the two circuits
<number>
Elec. Princip.

## Slide 29: G5A12 - What is one reason to use an impedance matching transformer?
A. To minimize transmitter power output
B. To maximize the transfer of power
C. To reduce power supply ripple
D. To minimize radiation resistance
<number>
Elec. Princip.

## Slide 30: G5A12 - What is one reason to use an impedance matching transformer?
A. To minimize transmitter power output
B. To maximize the transfer of power
C. To reduce power supply ripple
D. To minimize radiation resistance
<number>
Elec. Princip.

## Slide 31: G5A13 - Which of the following devices can be used for impedance matching at radio frequencies?
A. A transformer
B. A Pi-network
C. A length of transmission line
D. All of these choices are correct
<number>
Elec. Princip.

## Slide 32: G5A13 - Which of the following devices can be used for impedance matching at radio frequencies?
A. A transformer
B. A Pi-network
C. A length of transmission line
D. All of these choices are correct
<number>
Elec. Princip.

## Slide 33: G5B - The Decibel; current and voltage dividers; electrical power calculations; sine wave root-mean-square ( RMS ) values; PEP calculations
<number>
Elec. Princip.

## Slide 34
<number>
Elec. Princip.
Decibel Multipliers

## Slide 35: G5B01 - What dB change represents a two-times increase or decrease in power?
A. Approximately 2 dB
B. Approximately 3 dB
C. Approximately 6 dB
D. Approximately 12 dB
<number>
Elec. Princip.

## Slide 36: G5B01 - What dB change represents a two-times increase or decrease in power?
A. Approximately 2 dB
B. Approximately 3 dB
C. Approximately 6 dB
D. Approximately 12 dB
<number>
Elec. Princip.

## Slide 37
<number>
Elec. Princip.
RMS, Peak and Peak to Peak Voltages

## Slide 38: G5B02 - How does the total current relate to the individual currents in each branch of a purely resistive parallel circuit?
A. It equals the average of each branch current
B. It decreases as more parallel branches are added to the circuit
C. It equals the sum of the currents through each branch
D. It is the sum of the reciprocal of each individual voltage drop
<number>
Elec. Princip.

## Slide 39: G5B02 - How does the total current relate to the individual currents in each branch of a purely resistive parallel circuit?
A. It equals the average of each branch current
B. It decreases as more parallel branches are added to the circuit
C. It equals the sum of the currents through each branch
D. It is the sum of the reciprocal of each individual voltage drop
<number>
Elec. Princip.

## Slide 40: G5B03 - How many watts of electrical power are used if 400 VDC is supplied to an 800 ohm load?
A. 0.5 watts
B. 200 watts
C. 400 watts
D. 3200 watts
<number>
Elec. Princip.

## Slide 41: G5B03 How many WATTS of electrical power are used if 400 VDC is supplied to an 800-ohm load?
Electrical Principles 2010
<number>
V
O
A
W?
A
V
V=Voltage (Volts)
O=Resistance (Ohms)
A=Current (Amps)
W=Power (Watts)
1. What are you looking for? Watts
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 42: G5B03 How many watts of electrical power are used if 400 VDC is supplied to an 800-ohm load?
Electrical Principles 2010
<number>
V
400 V
O
800 Ω
A
W ?
A
V
400 V
V=Voltage (Volts)
O=Resistance (Ohms)
A=Current (Amps)
W=Power (Watts)
2. What do you know? Put it on the circles
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 43: G5B03 How many watts of electrical power are used if 400 VDC is supplied to an 800-ohm load?
Radio and Electronic Fundamentals
<number>
400 V
A
800 Ohms
STEP 3 - Find A
A = V / O
A = 400V / 800Ω = 0.5A
3. Solve the Ohms Law Circle
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 44: G5B03 How many watts of electrical power are used if 400 VDC is supplied to an 800-ohm load?
Radio and Electronic Fundamentals
<number>
W
0.5 A
400 V
STEP 4 - Find W
W = A x V
W = 0.5 A x 400 V = 200 W
4. Moves the Amps value to the Watts Circle
Solve the Watts Circles
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 45: G5B03 - How many watts of electrical power are used if 400 VDC is supplied to an 800 ohm load?
A. 0.5 watts
B. 200 watts
C. 400 watts
D. 3200 watts
<number>
Elec. Princip.
P
I
E
E=Voltage (Volts)
I=Current (Amps)
R=Resistance (Ohms)
P=Power (Watts)
E
I
R
400 VDC
400 VDC
800 Ω

## Slide 46: G5B04 - How many watts of electrical power are used by a 12 VDC light bulb that draws 0.2 amperes?
A. 2.4 watts
B. 24 watts
C. 6 watts
D. 60 watts
<number>
Elec. Princip.

## Slide 47: G5B04 How many WATTS of electrical power are used by a 12-VDC light bulb that draws 0.2 amperes?
Electrical Principles 2010
<number>
W ?
A
V
W = A x V
1. What are you looking for? Watts
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 48: G5B04 How many watts of electrical power are used by a 12-VDC light bulb that draws 0.2 amperes?
Electrical Principles 2010
<number>
W ?
0.2 A
12 V
W = A x V
2. What do you know? Put it on the circles
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 49: G5B04 How many watts of electrical power are used by a 12-VDC light bulb that draws 0.2 amperes?
Electrical Principles 2010
<number>
W
0.2 A
12 V
W = A x V
W = 0.2 A x 12 V = 2.4 W
3. Solve for Watts
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 50: G5B04 - How many watts of electrical power are used by a 12 VDC light bulb that draws 0.2 amperes?
A. 2.4 watts
B. 24 watts
C. 6 watts
D. 60 watts
<number>
Elec. Princip.
P
I
E
E=Voltage (Volts)
I=Current (Amps)
R=Resistance (Ohms)
P=Power (Watts)
E
I
R
12 VDC
12 VDC
0.2 amps
0.2 amps

## Slide 51: G5B05 - How many watts are dissipated when a current of 7.0 milliamperes flows through 1.25 kilohms resistance?
A. Approximately 61 milliwatts
B. Approximately 61 watts
C. Approximately 11 milliwatts
D. Approximately 11 watts
<number>
Elec. Princip.

## Slide 52: G5B05 How many WATTS are dissipated when a current of 7.0 milliamperes flows through 1.25 kilohms?
Electrical Principles 2010
<number>
V
O
A
W?
A
V
V=Voltage (Volts)
O=Resistance (Ohms)
A=Current (Amps)
W=Power (Watts)
1. What are you looking for? Watts
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 53: G5B05 How many watts are dissipated when a current of 7.0 milliamperes flows through 1.25 kilohms?
Electrical Principles 2010
<number>
V?
1250 Ω
0.007 A
W ?
0.007 A
V
1.25 kilo ohms = 1250 Ohms
7 mili Amps = 0.007 Amps
2. What do you know? Put it on the circles.
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 54: G5B05 How many watts are dissipated when a current of 7.0 milliamperes flows through 1.25 kilohms?
Electrical Principles 2010
<number>
V ?
O
1,250 Ohms
A
0.007 Amps
STEP 3 - Find V
V = O x A
V = 1,250Ω X 0.007 amps
V = 8.750
3. Find the voltage from the Ohns Law circle
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 55: G5B05 How many watts are dissipated when a current of 7.0 milliamperes flows through 1.25 kilohms?
Radio and Electronic Fundamentals
<number>
W
0.007 A
8.750 V
STEP 4 - Find W
W = A x V
W = 0.007 A x 8.75 V =
0.06125 W or 61.25 mW
4. Moves the Voltage to the Watts Circle
Solve the Watts Circles
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 56: G5B05 - How many watts are dissipated when a current of 7.0 milliamperes flows through 1.25 kilohms resistance?
A. Approximately 61 milliwatts
B. Approximately 61 watts
C. Approximately 11 milliwatts
D. Approximately 11 watts
<number>
Elec. Princip.

## Slide 57: G5B06 - What is the output PEP from a transmitter if an oscilloscope measures 200 volts peak-to-peak across a 50 ohm dummy load connected to the transmitter output?
A. 1.4 watts
B. 100 watts
C. 353.5 watts
D. 400 watts
<number>
Elec. Princip.

## Slide 58: G5B06 What is the output PEP from a transmitter if an oscilloscope measures 200 volts peak-to-peak across a 50-ohm dummy load connected to the transmitter output?
Electrical Principles 2010
<number>
V rms
O
A
W?
A
V
V=Voltage (Volts)
O=Resistance (Ohms)
A=Current (Amps)
W=Power (Watts)
PEP is Peek Envelope Power
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 59: G5B06 What is the output PEP from a transmitter if an oscilloscope measures 200 volts peak-to-peak across a 50-ohm dummy load connected to the transmitter output?
Electrical Principles 2010
<number>
V rms ?
O
A
W?
A
V
V=Voltage (Volts)
O=Resistance (Ohms)
A=Current (Amps)
W=Power (Watts)
You have Peak-to-Peak voltage
You need rms
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 60: G5B06 What is the output PEP from a transmitter if an oscilloscope measures 200 Volts peak-to-peak across a 50-ohm dummy load connected to the transmitter output?
Electrical Principles 2010
<number>
V rms ?
50 Ohms
A
W?
A
V
V=Voltage (Volts)
O=Resistance (Ohms)
A=Current (Amps)
W=Power (Watts)
200 V p to p
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 61: G5B06 What is the output PEP from a transmitter if an oscilloscope measures 200 volts peak-to-peak across a 50-ohm dummy load connected to the transmitter output?
Radio and Electronic Fundamentals
<number>
V rms
O
A
STEP 1 - Find RMS Volts
200 V pp / 2 = 100 V peak
100 V peak X 0.707
= 70.7 V rms
1. Change P-to-P to rms volatage
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 62: G5B06 What is the output PEP from a transmitter if an oscilloscope measures 200 volts peak-to-peak across a 50-ohm dummy load connected to the transmitter output?
Radio and Electronic Fundamentals
<number>
70.7 V rms
50 Ohms
A
STEP 2 - Find Amps
A = V / O
A = 70.7 V / 50 Ω
= 1.414 A
2. Use rms voltage and solve for amps
from Ohms Law Circle
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 63: G5B06 What is the output PEP from a transmitter if an oscilloscope measures 200 volts peak-to-peak across a 50-ohm dummy load connected to the transmitter output?
Radio and Electronic Fundamentals
<number>
W
1.414 A
70.7 V rms
STEP 3 find W
W = A x V
W = 1.414 A x 70.7 V rms
= 100 W
3. Move amps into Watts Circle and solve for Watts
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 64: G5B06 - What is the output PEP from a transmitter if an oscilloscope measures 200 volts peak-to-peak across a 50 ohm dummy load connected to the transmitter output?
A. 1.4 watts
B. 100 watts
C. 353.5 watts
D. 400 watts
<number>
Elec. Princip.

## Slide 65: G5B07 - What value of an AC signal produces the same power dissipation in a resistor as a DC voltage of the same value?
A. The peak-to-peak value
B. The peak value
C. The RMS value
D. The reciprocal of the RMS value
<number>
Elec. Princip.

## Slide 66: G5B07 - What value of an AC signal produces the same power dissipation in a resistor as a DC voltage of the same value?
A. The peak-to-peak value
B. The peak value
C. The RMS value
D. The reciprocal of the RMS value
<number>
Elec. Princip.

## Slide 67: G5B08 - What is the peak-to-peak voltage of a sine wave that has an RMS voltage of 120 volts?
A. 84.8 volts
B. 169.7 volts
C. 240.0 volts
D. 338.4 volts
<number>
Elec. Princip.

## Slide 68: G5B08 - What is the peak-to-peak voltage of a sine wave that has an RMS voltage of 120 volts?
A. 84.8 volts
B. 169.7 volts
C. 240.0 volts
D. 338.4 volts
<number>
Elec. Princip.
STEP 1
120 Vrms / 0.7 = 169.7 Vp
STEP 2
169.7 X 2 = 338.4 Vpp

## Slide 69: G5B09 - What is the RMS voltage of a sine wave with a value of 17 volts peak?
A. 8.5 volts
B. 12 volts
C. 24 volts
D. 34 volts
<number>
Elec. Princip.

## Slide 70: G5B09 - What is the RMS voltage of a sine wave with a value of 17 volts peak?
A. 8.5 volts
B. 12 volts
C. 24 volts
D. 34 volts
<number>
Elec. Princip.
17 Vp X 0.7 = 11.9 Vrms

## Slide 71: G5B10 - What percentage of power loss would result from a transmission line loss of 1 dB?
A. 10.9 percent
B. 12.2 percent
C. 20.5 percent
D. 25.9 percent
<number>
Elec. Princip.

## Slide 72: G5B10 - What percentage of power loss would result from a transmission line loss of 1 dB?
A. 10.9 percent
B. 12.2 percent
C. 20.5 percent
D. 25.9 percent
<number>
Elec. Princip.

## Slide 73: G5B11 - What is the ratio of peak envelope power to average power for an unmodulated carrier?
A. 0.707
B. 1.00
C. 1.414
D. 2.00
<number>
Elec. Princip.

## Slide 74: G5B11 - What is the ratio of peak envelope power to average power for an unmodulated carrier?
A. 0.707
B. 1.00
C. 1.414
D. 2.00
<number>
Elec. Princip.

## Slide 75: G5B12 - What would be the RMS voltage across a 50 ohm dummy load dissipating 1200 watts?
A. 173 volts
B. 245 volts
C. 346 volts
D. 692 volts
<number>
Elec. Princip.

## Slide 76: G5B12 What would be the RMS voltage across a 50-ohm dummy load dissipating 1200 watts?
Electrical Principles 2010
<number>
V?
O
A?
W
A?
V?
V=Voltage (Volts)
O=Resistance (Ohms)
A=Current (Amps)
W=Power (Watts)
Law and Power Calculations - Unit Circles
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 77: G5B12 What would be the RMS voltage across a 50-ohm dummy load dissipating 1200 watts? `
Electrical Principles 2010
<number>
V
O
A
W
V?
Replace A
With V/O
▬▬▬▬►
Voice Of America – VOLTAGE CIRCLE W A V - WATTAGE CIRCLE
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 78: G5B12 What would be the RMS voltage across a 50-ohm dummy load dissipating 1200 watts?
Electrical Principles 2010
<number>
O x W
V
50 Ω x 1200 W
V ?
W A V - WATTAGE CIRCLE
↑
V
O x W
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 79: G5B12 What would be the RMS voltage across a 50-ohm dummy load dissipating 1200 watts?
Electrical Principles 2010
<number>
50 Ω x 1200 W
V
50 Ω x 1200 W
V ²
W A V - WATTAGE CIRCLE
↑
V
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 80: G5B12 What would be the RMS voltage across a 50-ohm dummy load dissipating 1200 watts?
Electrical Principles
<number>
  A. 173 volts
B. 245 volts
  C. 346 volts
  D. 692 volts
V ² = 1200 Watts x 50 Ohms
V ² = 60,000
V = square root 60,000
V = √ 60.000
V = 245 Volts

## Slide 81: G5B12 - What would be the RMS voltage across a 50 ohm dummy load dissipating 1200 watts?
A. 173 volts
B. 245 volts
C. 346 volts
D. 692 volts
<number>
Elec. Princip.
V = square root (W x Ω)
V = √ (1200 x 50)
V = √ 60.000
V = 245 Volts

## Slide 82: G5B13 - What is the output PEP of an unmodulated carrier if an average reading wattmeter connected to the transmitter output indicates 1060 watts?
A. 530 watts
B. 1060 watts
C. 1500 watts
D. 2120 watts
<number>
Elec. Princip.

## Slide 83: G5B13 - What is the output PEP of an unmodulated carrier if an average reading wattmeter connected to the transmitter output indicates 1060 watts?
A. 530 watts
B. 1060 watts
C. 1500 watts
D. 2120 watts
<number>
Elec. Princip.

## Slide 84: G5B14 - What is the output PEP from a transmitter if an oscilloscope measures 500 volts peak-to-peak across a 50 ohm resistive load connected to the transmitter output?
A. 8.75 watts
B. 625 watts
C. 2500 watts
D. 5000 watts
<number>
Elec. Princip.

## Slide 85: G5B14 What is the output PEP from a transmitter if an oscilloscope measures 500 volts peak-to-peak across a 50-ohm resistor connected to the transmitter output?
Electrical Principles 2010
<number>
V rms
O
A
W?
A
V
V=Voltage (Volts)
O=Resistance (Ohms)
A=Current (Amps)
W=Power (Watts)
You are looking for Wattage
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 86: G5B14 What is the output PEP from a transmitter if an oscilloscope measures 500 volts peak-to-peak across a 50-ohm resistor connected to the transmitter output?
Electrical Principles 2010
<number>
V rms ?
O
A
W?
A
V rms
V=Voltage (Volts)
O=Resistance (Ohms)
A=Current (Amps)
W=Power (Watts)
You need V rms
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 87: RMS, Peak and Peak to Peak Voltages
Electrical Principles
<number>
Electrical Principles
<number>
Notes: <number>
<number>
There are three key voltage measurements, RMS (Vrms), Peak (Vpk) and Peak to Peak (Vpp). The Peak voltage is relative to ground. RMS or Root Mean Square is more of an “average” voltage over the duration of the AC cycle. RMS voltage is calculated by multiplying 0.707 times the peak voltage. The Peak to Peak voltage measures from the peak of the positive swing to the peak of the negative swing.
The 120 volt AC line voltage in the wall is a peak value. That means the RMS voltage is 85 volts and Peak to Peak is 240 volts.

## Slide 88: G5B14 What is the output PEP from a transmitter if an oscilloscope measures 500 volts peak-to-peak across a 50-ohm resistor connected to the transmitter output?
Radio and Electronic Fundamentals
<number>
V rms
O
A
STEP 1 - Find RMS Volts
500 V pp / 2 = 250 V peak
250 V peak X 0.707
= 176.75 V rms
1. Change P-to-P to rms volatage
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 89: G5B14 What is the output PEP from a transmitter if an oscilloscope measures 500 volts peak-to-peak across a 50-ohm resistor connected to the transmitter output?
Radio and Electronic Fundamentals
<number>
176.75 V rms
50 Ohms
A
STEP 2 - Find Amps
A = V / O
A = 176.75 V rms / 50 Ω
= 3.535 A
2. Put V rms in to Ohm Circle and find Amps
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 90: G5B14 What is the output PEP from a transmitter if an oscilloscope measures 500 volts peak-to-peak across a 50-ohm resistor connected to the transmitter output?
Radio and Electronic Fundamentals
<number>
W
3.535 A
176.75 V rms
STEP 3 find W
W = A x V
W = 3.535 A x 176.75 V rms
= 624.811 W
3. Put amps into Watts Circle and solve for Watts
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 91: G5B14 - What is the output PEP from a transmitter if an oscilloscope measures 500 volts peak-to-peak across a 50 ohm resistive load connected to the transmitter output?
A. 8.75 watts
B. 625 watts
C. 2500 watts
D. 5000 watts
<number>
Elec. Princip.

## Slide 92: G5C – Resistors, capacitors, and inductors in series and parallel; transformers
<number>
Elec. Princip.

## Slide 93: G5C01 - What causes a voltage to appear across the secondary winding of a transformer when an AC voltage source is connected across its primary winding?
A. Capacitive coupling
B. Displacement current coupling
C. Mutual inductance
D. Mutual capacitance
<number>
Elec. Princip.

## Slide 94: G5C01 - What causes a voltage to appear across the secondary winding of a transformer when an AC voltage source is connected across its primary winding?
A. Capacitive coupling
B. Displacement current coupling
C. Mutual inductance
D. Mutual capacitance
<number>
Elec. Princip.

## Slide 95: G5C02 - What happens if you reverse the primary and secondary windings of a 4:1 voltage step down transformer?
A. The secondary voltage becomes 4 times the primary voltage
B. The transformer no longer functions as it is a unidirectional device
C. Additional resistance must be added in series with the primary to prevent overload
D. Additional resistance must be added in parallel with the secondary to prevent overload
<number>
Elec. Princip.

## Slide 96: G5C02 - What happens if you reverse the primary and secondary windings of a 4:1 voltage step down transformer?
A. The secondary voltage becomes 4 times the primary voltage
B. The transformer no longer functions as it is a unidirectional device
C. Additional resistance must be added in series with the primary to prevent overload
D. Additional resistance must be added in parallel with the secondary to prevent overload
<number>
Elec. Princip.

## Slide 97: G5C03 - Which of the following components should be added to an existing resistor to increase the resistance?
A. A resistor in parallel
B. A resistor in series
C. A capacitor in series
D. A capacitor in parallel
<number>
Elec. Princip.

## Slide 98: G5C03 - Which of the following components should be added to an existing resistor to increase the resistance?
A. A resistor in parallel
B. A resistor in series
C. A capacitor in series
D. A capacitor in parallel
<number>
Elec. Princip.

## Slide 99: G5C04 - What is the total resistance of three 100 ohm resistors in parallel?
A. 0.30 ohms
B. 0.33 ohms
C. 33.3 ohms
D. 300 ohms
<number>
Elec. Princip.

## Slide 100: G5C04 - What is the total resistance of three 100 ohm resistors in parallel?
A. 0.30 ohms
B. 0.33 ohms
C. 33.3 ohms
D. 300 ohms
<number>
Elec. Princip.
100 / 3 = 33.3 Ω

## Slide 101: G5C05 - If three equal value resistors in series produce 450 ohms, what is the value of each resistor?
A. 1500 ohms
B. 90 ohms
C. 150 ohms
D. 175 ohms
<number>
Elec. Princip.

## Slide 102: G5C05 - If three equal value resistors in series produce 450 ohms, what is the value of each resistor?
A. 1500 ohms
B. 90 ohms
C. 150 ohms
D. 175 ohms
<number>
Elec. Princip.
450 / 3 = 150 Ω

## Slide 103: G5C06 - What is the RMS voltage across a 500-turn secondary winding in a transformer if the 2250-turn primary is connected to 120 VAC?
A. 2370 volts
B. 540 volts
C. 26.7 volts
D. 5.9 volts
<number>
Elec. Princip.

## Slide 104: G5C06 - What is the RMS voltage across a 500-turn secondary winding in a transformer if the 2250-turn primary is connected to 120 VAC?
A. 2370 volts
B. 540 volts
C. 26.7 volts
D. 5.9 volts
<number>
Elec. Princip.
Voltage ratio = Turn Ratio
500 / 2250 x 120 V =
26.66 Vac

## Slide 105: G5C07 - What is the turns ratio of a transformer used to match an audio amplifier having 600 ohm output impedance to a speaker having 4 ohm impedance?
A. 12.2 to 1
B. 24.4 to 1
C. 150 to 1
D. 300 to 1
<number>
Elec. Princip.

## Slide 106: G5C07 - What is the turns ratio of a transformer used to match an audio amplifier having 600 ohm output impedance to a speaker having 4 ohm impedance?
A. 12.2 to 1
B. 24.4 to 1
C. 150 to 1
D. 300 to 1
<number>
Elec. Princip.
Turn ratio = ( 600 / 4)
150 = 12.2 to 1

## Slide 107: G5C08 - What is the equivalent capacitance of two 5.0 nanofarad capacitors and one 750 picofarad capacitor connected in parallel?
A. 576.9 nanofarads
B. 1733 picofarads
C. 3583 picofarads
D. 10.750 nanofarads
<number>
Elec. Princip.

## Slide 108: G5C08 - What is the equivalent capacitance of two 5.0 nanofarad capacitors and one 750 picofarad capacitor connected in parallel?
A. 576.9 nanofarads
B. 1733 picofarads
C. 3583 picofarads
D. 10.750 nanofarads
<number>
Elec. Princip.
Add capacitance in Parallel
5 nf = 5,000 pf
5,000 pf
750 pf
10,750 pf

## Slide 109: G5C09 - What is the capacitance of three 100 microfarad capacitors connected in series?
A. 0.30 microfarads
B. 0.33 microfarads
C. 33.3 microfarads
D. 300 microfarads
<number>
Elec. Princip.

## Slide 110: G5C09 - What is the capacitance of three 100 microfarad capacitors connected in series?
A. 0.30 microfarads
B. 0.33 microfarads
C. 33.3 microfarads
D. 300 microfarads
<number>
Elec. Princip.
Divide Capacitance in series
100 / 3 = 33.3 mf

## Slide 111: G5C10 - What is the inductance of three 10 millihenry inductors connected in parallel?
A. 0.30 henrys
B. 3.3 henrys
C. 3.3 millihenrys
D. 30 millihenrys
<number>
Elec. Princip.

## Slide 112: G5C10 - What is the inductance of three 10 millihenry inductors connected in parallel?
A. 0.30 henrys
B. 3.3 henrys
C. 3.3 millihenrys
D. 30 millihenrys
<number>
Elec. Princip.
Divide Inductance in parallel
10 / 3 = 3.33 mh

## Slide 113: G5C11 - What is the inductance of a 20 millihenry inductor connected in series with a 50 millihenry inductor?
A. 0.07 millihenrys
B. 14.3 millihenrys
C. 70 millihenrys
D. 1000 millihenrys
<number>
Elec. Princip.

## Slide 114: G5C11 - What is the inductance of a 20 millihenry inductor connected in series with a 50 millihenry inductor?
A. 0.07 millihenrys
B. 14.3 millihenrys
C. 70 millihenrys
D. 1000 millihenrys
<number>
Elec. Princip.
Add Inductprs in series
20 + 50 = 70 mh

## Slide 115: G5C12 - What is the capacitance of a 20 microfarad capacitor connected in series with a 50 microfarad capacitor?
A. 0.07 microfarads
B. 14.3 microfarads
C. 70 microfarads
D. 1000 microfarads
<number>
Elec. Princip.

## Slide 116: G5C12 - What is the capacitance of a 20 microfarad capacitor connected in series with a 50 microfarad capacitor?
A. 0.07 microfarads
B. 14.3 microfarads
C. 70 microfarads
D. 1000 microfarads
<number>
Elec. Princip.
cC1 x C2
C1 + C2
20 x 50 1,000
20 + 50 70
= 14.286 mf

## Slide 117: G5C13 - Which of the following components should be added to a capacitor to increase the capacitance?
A. An inductor in series
B. A resistor in series
C. A capacitor in parallel
D. A capacitor in series
<number>
Elec. Princip.

## Slide 118: G5C13 - Which of the following components should be added to a capacitor to increase the capacitance?
A. An inductor in series
B. A resistor in series
C. A capacitor in parallel
D. A capacitor in series
<number>
Elec. Princip.

## Slide 119: G5C14 - Which of the following components should be added to an inductor to increase the inductance?
A. A capacitor in series
B. A resistor in parallel
C. An inductor in parallel
D. An inductor in series
<number>
Elec. Princip.

## Slide 120: G5C14 - Which of the following components should be added to an inductor to increase the inductance?
A. A capacitor in series
B. A resistor in parallel
C. An inductor in parallel
D. An inductor in series
<number>
Elec. Princip.

## Slide 121: G5C15 - What is the total resistance of a 10 ohm, a 20 ohm, and a 50 ohm resistor connected in parallel?
A. 5.9 ohms
B. 0.17 ohms
C. 10000 ohms
D. 80 ohms
<number>
Elec. Princip.

## Slide 122: G5C15 - What is the total resistance of a 10 ohm, a 20 ohm, and a 50 ohm resistor in parallel?
Electrical Principles
<number>
A. 5.9 ohms
  B. 0.17 ohms
  C. 10000 ohms
  D. 80 ohms
R = 1 .
(1/R1 + 1/R2 + 1/R3)
R = 1 .
(1/10 + 1/20 + 1/50)
R total = 100 / 17 = 5.9 ohms

## Slide 123: G5C16 - Why is the conductor of the primary winding of many voltage step up transformers larger in diameter than the conductor of the secondary winding?
A. To improve the coupling between the primary and secondary
B. To accommodate the higher current of the primary
C. To prevent parasitic oscillations due to resistive losses in the primary
D. To insure that the volume of the primary winding is equal to the volume of the secondary winding
<number>
Elec. Princip.

## Slide 124: G5C16 - Why is the conductor of the primary winding of many voltage step up transformers larger in diameter than the conductor of the secondary winding?
A. To improve the coupling between the primary and secondary
B. To accommodate the higher current of the primary
C. To prevent parasitic oscillations due to resistive losses in the primary
D. To insure that the volume of the primary winding is equal to the volume of the secondary winding
<number>
Elec. Princip.

## Slide 125: G5C17 - What is the value in nanofarads (nF) of a 22,000 pF capacitor?
A. 0.22 nF B. 2.2 nF C. 22 nF D. 220 nF
<number>
Elec. Princip.

## Slide 126: G5C17 - What is the value in nanofarads (nF) of a 22,000 pF capacitor?
A. 0.22 nF B. 2.2 nF C. 22 nF D. 220 nF
<number>
Elec. Princip.
1 pf = 0.000 000 000 001 f
1 nf = 0.000 000 001 f
1 mf = 0.000.001 f
22,000 pf = 22 nf

## Slide 127: G5C18 - What is the value in microfarads of a 4700 nanofarad ( nF ) capacitor?
A. 47 µF B. 0.47 µF C. 47,000 µF D. 4.7 µF
<number>
Elec. Princip.

## Slide 128: G5C18 - What is the value in microfarads of a 4700 nanofarad ( nF ) capacitor?
A. 47 µF B. 0.47 µF C. 47,000 µF D. 4.7 µF
<number>
Elec. Princip.
4,700 nf = 4.700 mf

## Slide 129: End Of SUBELEMENT G5 ELECTRICAL PRINCIPLES