## Slide 1: SUBELEMENT G1 COMMISSION'S RULES [5 Exam Questions-5 Groups]
<number>
FCC Rules
Notes: Subelement G1 FCC Rules. General Training Slides for 2015 Question Pool Good through June 30, 2019 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM, Howard Schultz, W7HS.
<number>

## Slide 2: SUBELEMENT G1 COMMISSION'S RULES [5 Exam Questions-5 Groups]
G1A - General Class control operator frequency privileges; primary and secondary allocations
G1B - Antenna structure limitations; good engineering and good amateur practice; beacon operation; prohibited transmissions; retransmitting radio signals
G1C - Transmitter power regulations; data emission standards
G1D - Volunteer Examiners and Volunteer Examiner Coordinators; temporary identification
G1E – Control categories; repeater regulations; harmful interference; third party rules; ITU regions; automatically controlled digital station
<number>
FCC Rules
Notes: Subelement G1 FCC Rules. General Training Slides for 2015 Question Pool Good through June 30, 2019 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM, Howard Schultz, W7HS.
<number>

## Slide 3: G1A - General Class control operator frequency privileges; primary and secondary allocations
FCC Rules
<number>

## Slide 4: General Band Allocations
10 meters 28000 – 29700 kHz
12 meters 24890 – 24990 kHz
15 meters 21025 – 21200 kHz and 21300 – 21450 kHz
17 meters 18068 – 18168 kHz
20 meters 14025 – 14150 kHz and 14225 – 14350 kHz
30 meters 10100 – 10150 kHz
40 meters 7025 – 7150 kHz and 7225 – 1300 kHz
60 meters 5332, 5348, 5368, 5373, 5405 kHz (USB)
80 meters 3525 – 3750 kHz and 3850 – 4000 kHz
160 meters 1800 – 2000 kHz
FCC Rules
<number>

## Slide 5
FCC Rules
<number>
BAND PLAN

## Slide 6: G1A01 - On which of the following bands is a General Class license holder granted all amateur frequency privileges?
    A. 60, 20, 17, and 12 meters
    B. 160, 80, 40, and 10 meters
    C. 160, 60, 30, 17, 12, and 10 meters
    D. 160, 30, 17, 15, 12, and 10 meters
FCC Rules
<number>

## Slide 7: G1A01 - On which of the following bands is a General Class license holder granted all amateur frequency privileges?
    A. 60, 20, 17, and 12 meters
    B. 160, 80, 40, and 10 meters
    C. 160, 60, 30, 17, 12, and 10 meters
    D. 160, 30, 17, 15, 12, and 10 meters
FCC Rules
<number>
Note: The older HF band: 80, 40, 20, and 15 meters reserve the first 25 kHz for Extra class CW operations.
On these bands, the bottom of the phone band is also reserved for Extra class operators.

## Slide 8: G1A02 - On which of the following bands is phone operation prohibited?
A. 160 meters
B. 30 meters
C. 17 meters
D. 12 meters
FCC Rules
<number>

## Slide 9: G1A02 - On which of the following bands is phone operation prohibited?
A. 160 meters
B. 30 meters
C. 17 meters
D. 12 meters
FCC Rules
<number>

## Slide 10: G1A03 - On which of the following bands is image transmission prohibited?
A. 160 meters
B. 30 meters
C. 20 meters
D. 12 meters
FCC Rules
<number>

## Slide 11: G1A03 - On which of the following bands is image transmission prohibited?
A. 160 meters
B. 30 meters
C. 20 meters
D. 12 meters
FCC Rules
<number>

## Slide 12: G1A04 - Which of the following amateur bands is restricted to communication on only specific channels, rather than frequency ranges?
A. 11 meters
B. 12 meters
C. 30 meters
D. 60 meters
FCC Rules
<number>

## Slide 13: G1A04 - Which of the following amateur bands is restricted to communication on only specific channels, rather than frequency ranges?
A. 11 meters
B. 12 meters
C. 30 meters
D. 60 meters
FCC Rules
<number>

## Slide 14: Frequency Calculations
300 is the Speed of Light in free space
  Radio wave travel at the Speed of Light
  300,000,000 meters per second
  Radio waves moves slower in wire
  Velocity Factor is speed in a material divided by the speed of light i.e. .66
f is frequency in millions (MHz)
  The millions of cycles cancel the millions of meters
  146,520,000 = 146.53 MHz
m is Wave length in Meters or the distance of a full cycle
  How far it takes a wave to complete a complete cycle
  The higher the frequency the lower the meter (shorter)
  The lower the frequency the higher the meters (longer)
<number>
Radio Waves
300
f
m
300 = f x m
300
f
m
Notes: <number>

## Slide 15: G1A05 - Which of the following frequencies is in the General Class portion of the 40 meter band?
A. 7.250 MHz
B. 7.500 MHz
C. 40.200 MHz
D. 40.500 MHz
FCC Rules
<number>

## Slide 16: G1A05 - Which of the following frequencies is in the General Class portion of the 40 meter band?
A. 7.250 MHz
B. 7.500 MHz
C. 40.200 MHz
D. 40.500 MHz
FCC Rules
<number>
300
f
m
300 / 7.250 = 41.379 Meters
↑

## Slide 17: G1A06 - Which of the following frequencies is within the General Class portion of the 75-meter phone band?
A. 1875 kHz
B. 3750 kHz
C. 3900 kHz
D. 4005 kHz
FCC Rules
<number>

## Slide 18: G1A06 - Which of the following frequencies is within the General Class portion of the 75-meter phone band?
A. 1875 kHz
B. 3750 kHz
C. 3900 kHz
D. 4005 kHz
FCC Rules
<number>
300
f
m
300 / 3.900 = 76.923 Meters
↑

## Slide 19: G1A07 - Which of the following frequencies is within the General Class portion of the 20-meter phone band?
A. 14005 kHz
B. 14105 kHz
C. 14305 kHz
D. 14405 kHz
FCC Rules
<number>

## Slide 20: G1A07 - Which of the following frequencies is within the General Class portion of the 20-meter phone band?
A. 14005 kHz
B. 14105 kHz
C. 14305 kHz
D. 14405 kHz
FCC Rules
<number>
300
f
m
300 / 14.305 = 20.97 Meters
↑

## Slide 21: G1A08 - Which of the following frequencies is within the General Class portion of the 80-meter band?
A. 1855 kHz
B. 2560 kHz
C. 3560 kHz
D. 3650 kHz
FCC Rules
<number>

## Slide 22: G1A08 - Which of the following frequencies is within the General Class portion of the 80-meter band?
A. 1855 kHz
B. 2560 kHz
C. 3560 kHz
D. 3650 kHz
FCC Rules
<number>
300
f
m
300 / 3.560 = 41.379 Meters
↑

## Slide 23: G1A09 - Which of the following frequencies is within the General Class portion of the 15-meter band?
A. 14250 kHz
B. 18155 kHz
C. 21300 kHz
D. 24900 kHz
FCC Rules
<number>

## Slide 24: G1A09 - Which of the following frequencies is within the General Class portion of the 15-meter band?
A. 14250 kHz
B. 18155 kHz
C. 21300 kHz
D. 24900 kHz
FCC Rules
<number>
300
f
m
300 / 21.300 = 14.085 Meters
↑

## Slide 25: G1A10 - Which of the following frequencies is available to a control operator holding a General Class license?
A. 28.020 MHz
B. 28.350 MHz
C. 28.550 MHz
D. All of these choices are correct
FCC Rules
<number>

## Slide 26: G1A10 - Which of the following frequencies is available to a control operator holding a General Class license?
A. 28.020 MHz
B. 28.350 MHz
C. 28.550 MHz
D. All of these choices are correct
FCC Rules
<number>
300
f
m
300 / 28.020 = 10.7066 Meters
300 / 28.350 = 10.5820 Meters
300 / 28.550 = 10.5079 Meters
↑
↑
↑
Notes: <number>

## Slide 27: G1A11 - When General Class licensees are not permitted to use the entire voice portion of a particular band, which portion of the voice segment is generally available to them?
A. The lower frequency end
B. The upper frequency end
C. The lower frequency end on frequencies below 7.3 MHz and the upper end on frequencies above 14.150 MHz
D. The upper frequency end on frequencies below 7.3 MHz and the lower end on frequencies above 14.150 MHz
FCC Rules
<number>

## Slide 28: G1A11 - When General Class licensees are not permitted to use the entire voice portion of a particular band, which portion of the voice segment is generally available to them?
A. The lower frequency end
B. The upper frequency end
C. The lower frequency end on frequencies below 7.3 MHz and the upper end on frequencies above 14.150 MHz
D. The upper frequency end on frequencies below 7.3 MHz and the lower end on frequencies above 14.150 MHz
FCC Rules
<number>

## Slide 29: G1A12 - Which of the following applies when the FCC rules designate the Amateur Service as a secondary user on a band?
A. Amateur stations must record the call sign of the primary service station before operating on a frequency assigned to that station
B. Amateur stations are allowed to use the band only during emergencies
C. Amateur stations are allowed to use the band only if they do not cause harmful interference to primary users
D. Amateur stations may only operate during specific hours of the day, while primary users are permitted 24 hour use of the band
FCC Rules
<number>

## Slide 30: G1A12 - Which of the following applies when the FCC rules designate the Amateur Service as a secondary user on a band?
A. Amateur stations must record the call sign of the primary service station before operating on a frequency assigned to that station
B. Amateur stations are allowed to use the band only during emergencies
C. Amateur stations are allowed to use the band only if they do not cause harmful interference to primary users
D. Amateur stations may only operate during specific hours of the day, while primary users are permitted 24 hour use of the band
FCC Rules
<number>

## Slide 31: G1A13 - What is the appropriate action if, when operating on either the 30- or 60- meter bands, a station in the primary service interferes with your contact?
A. Notify the FCCs regional Engineer in Charge of the interference
B. Increase your transmitter's power to overcome the interference
C. Attempt to contact the station and request that it stop the interference
D. Move to a clear frequency or stop transmitting
FCC Rules
<number>

## Slide 32: G1A13 - What is the appropriate action if, when operating on either the 30- or 60- meter bands, a station in the primary service interferes with your contact?
A. Notify the FCCs regional Engineer in Charge of the interference
B. Increase your transmitter's power to overcome the interference
C. Attempt to contact the station and request that it stop the interference
D. Move to a clear frequency or stop transmitting
FCC Rules
<number>

## Slide 33: G1A14 - In what ITU region is operation in the 7.175 to 7.300 MHz band permitted for a control operator holding an FCC issued General Class license?
A. Region 1
B. Region 2
C. Region 3
D. All three regions
FCC Rules
<number>

## Slide 34: G1A14 - In what ITU region is operation in the 7.175 to 7.300 MHz band permitted for a control operator holding an FCC issued General Class license?
A. Region 1
B. Region 2
C. Region 3
D. All three regions
FCC Rules
<number>

## Slide 35: G1B - Antenna structure limitations; good engineering and good amateur practice; beacon operation; prohibited transmissions; retransmitting radio signals
FCC Rules
<number>

## Slide 36: G1B01 - What is the maximum height above ground to which an antenna structure may be erected without requiring notification to the FAA and registration with the FCC, provided it is not at or near a public use airport?
A. 50 feet
B. 100 feet
C. 200 feet
D. 300 feet
FCC Rules
<number>

## Slide 37: Amateur Radio Towers Near a Public Airport
Distances from runway and height permitted. 200 feet maximum is the only info needed.

## Slide 38: G1B01 - What is the maximum height above ground to which an antenna structure may be erected without requiring notification to the FAA and registration with the FCC, provided it is not at or near a public use airport?
A. 50 feet
B. 100 feet
C. 200 feet
D. 300 feet
FCC Rules
<number>

## Slide 39: G1B02 - With which of the following conditions must beacon stations comply?
A. A beacon station may not use automatic control
B. The frequency must be coordinated with the National Beacon Organization
C. The frequency must be posted on the Internet or published in a national periodical
D. There must be no more than one beacon signal transmitting in the same band from the same station location
FCC Rules
<number>

## Slide 40: G1B02 - With which of the following conditions must beacon stations comply?
A. A beacon station may not use automatic control
B. The frequency must be coordinated with the National Beacon Organization
C. The frequency must be posted on the Internet or published in a national periodical
D. There must be no more than one beacon signal transmitting in the same band from the same station location
FCC Rules
<number>

## Slide 41: G1B03 - Which of the following is a purpose of a beacon station as identified in the FCC rules?
A. Observation of propagation and reception
B. Automatic identification of repeaters
C. Transmission of bulletins of general interest to Amateur Radio licensees
D. Identifying net frequencies
FCC Rules
<number>

## Slide 42: G1B03 - Which of the following is a purpose of a beacon station as identified in the FCC rules?
A. Observation of propagation and reception
B. Automatic identification of repeaters
C. Transmission of bulletins of general interest to Amateur Radio licensees
D. Identifying net frequencies
FCC Rules
<number>

## Slide 43: G1B04 - Which of the following must be true before amateur stations may provide communications to broadcasters for dissemination to the public?
A. The communications must directly relate to the immediate safety of human life or protection of property and there must be no other means of communication reasonably available before or at the time of the event
B. The communications must be approved by a local emergency preparedness official and conducted on officially designated frequencies
C. The FCC must have declared a state of emergency
D. All of these choices are correct
FCC Rules
<number>

## Slide 44: G1B04 - Which of the following must be true before amateur stations may provide communications to broadcasters for dissemination to the public?
A. The communications must directly relate to the immediate safety of human life or protection of property and there must be no other means of communication reasonably available before or at the time of the event
B. The communications must be approved by a local emergency preparedness official and conducted on officially designated frequencies
C. The FCC must have declared a state of emergency
D. All of these choices are correct
FCC Rules
<number>

## Slide 45: G1B05 - When may music be transmitted by an amateur station?
When may music be transmitted by an amateur station?
A. At any time, as long as it produces no spurious emissions
B. When it is unintentionally transmitted from the background at the transmitter
C. When it is transmitted on frequencies above 1215 MHz
D. When it is an incidental part of a manned space craft retransmission
FCC Rules
<number>

## Slide 46: G1B05 - When may music be transmitted by an amateur station?
When may music be transmitted by an amateur station?
A. At any time, as long as it produces no spurious emissions
B. When it is unintentionally transmitted from the background at the transmitter
C. When it is transmitted on frequencies above 1215 MHz
D. When it is an incidental part of a manned space craft retransmission
FCC Rules
<number>

## Slide 47: G1B06 - When is an amateur station permitted to transmit secret codes?
A. During a declared communications emergency
B. To control a space station
C. Only when the information is of a routine, personal nature
D. Only with Special Temporary Authorization from the FCC
FCC Rules
<number>

## Slide 48: G1B06 - When is an amateur station permitted to transmit secret codes?
A. During a declared communications emergency
B. To control a space station
C. Only when the information is of a routine, personal nature
D. Only with Special Temporary Authorization from the FCC
FCC Rules
<number>

## Slide 49: G1B07 - What are the restrictions on the use of abbreviations or procedural signals in the Amateur Service?
A. Only "Q" signals are permitted
B. They may be used if they do not obscure the meaning of a message
C. They are not permitted
D. Only "10 codes" are permitted
FCC Rules
<number>

## Slide 50: G1B07 - What are the restrictions on the use of abbreviations or procedural signals in the Amateur Service?
A. Only "Q" signals are permitted
B. They may be used if they do not obscure the meaning of a message
C. They are not permitted
D. Only "10 codes" are permitted
FCC Rules
<number>

## Slide 51: G1B08 - When choosing a transmitting frequency, what should you do to comply with good amateur practice?
A. Insure that the frequency and mode selected are within your license class privileges
B. Follow generally accepted band plans agreed to by the Amateur Radio community.
C. Monitor the frequency before transmitting
D. All of these choices are correct
FCC Rules
<number>

## Slide 52: G1B08 - When choosing a transmitting frequency, what should you do to comply with good amateur practice?
A. Insure that the frequency and mode selected are within your license class privileges
B. Follow generally accepted band plans agreed to by the Amateur Radio community.
C. Monitor the frequency before transmitting
D. All of these choices are correct
FCC Rules
<number>

## Slide 53: G1B09 - When may an amateur station transmit communications in which the licensee or control operator has a pecuniary ( monetary ) interest?
A. When other amateurs are being notified of the sale of apparatus normally used in an amateur station and such activity is not done on a regular basis
B. Only when there is no other means of communications readily available
C. When other amateurs are being notified of the sale of any item with a monetary value less than $200 and such activity is not done on a regular basis
D. Never
FCC Rules
<number>

## Slide 54: G1B09 - When may an amateur station transmit communications in which the licensee or control operator has a pecuniary ( monetary ) interest?
A. When other amateurs are being notified of the sale of apparatus normally used in an amateur station and such activity is not done on a regular basis
B. Only when there is no other means of communications readily available
C. When other amateurs are being notified of the sale of any item with a monetary value less than $200 and such activity is not done on a regular basis
D. Never
FCC Rules
<number>

## Slide 55: G1B10 - What is the power limit for beacon stations?
A. 10 watts PEP output
B. 20 watts PEP output
C. 100 watts PEP output
D. 200 watts PEP output
FCC Rules
<number>

## Slide 56: G1B10 - What is the power limit for beacon stations?
A. 10 watts PEP output
B. 20 watts PEP output
C. 100 watts PEP output
D. 200 watts PEP output
FCC Rules
<number>

## Slide 57: G1B11 - How does the FCC require an amateur station to be operated in all respects not specifically covered by the Part 97 rules?
A. In conformance with the rules of the IARU
B. In conformance with Amateur Radio custom
C. In conformance with good engineering and good amateur practice
D. All of these choices are correct
FCC Rules
<number>

## Slide 58: G1B11 - How does the FCC require an amateur station to be operated in all respects not specifically covered by the Part 97 rules?
A. In conformance with the rules of the IARU
B. In conformance with Amateur Radio custom
C. In conformance with good engineering and good amateur practice
D. All of these choices are correct
FCC Rules
<number>

## Slide 59: G1B12 - Who or what determines "good engineering and good amateur practice" as applied to the operation of an amateur station in all respects not covered by the Part 97 rules?
A. The FCC
B. The Control Operator
C. The IEEE
D. The ITU
FCC Rules
<number>

## Slide 60: G1B12 - Who or what determines "good engineering and good amateur practice" as applied to the operation of an amateur station in all respects not covered by the Part 97 rules?
A. The FCC
B. The Control Operator
C. The IEEE
D. The ITU
FCC Rules
<number>

## Slide 61: G1C - Transmitter power regulations; data emission standards
FCC Rules
<number>

## Slide 62: Maximum Power Levels
<number>
Maximum 1500 watts PEP!
Exceptions - 200 watts PEP maximum
  On 30 meters
  Novice/Tech+ sub bands
    80 meters (3675-3725 kHz)
    40 meters (7100-7150 kHz)
    15 meters (21100-21200 kHz)
FCC Rules
Notes: <number>
Amateurs are allowed 1500 watts PEP with a few exceptions. These limitations also apply to Advanced and Extra class licensees. There is a level playing field on these frequencies.

## Slide 63: Maximum Allowable Data Symbol Rates
<number>
Below 10 meters (28 MHz) 300 baud
10 Meter band 1200 baud
6 and 2 meters 19.6 kilobaud Maximum 20Khz
1.25m and 70cm 56 kilobaud
FCC Rules

## Slide 64: G1C01 - What is the maximum transmitting power an amateur station may use on 10.140 MHz?
A. 200 watts PEP output
B. 1000 watts PEP output
C. 1500 watts PEP output
D. 2000 watts PEP output
Commission's Rules
<number>

## Slide 65: G1C01 - What is the maximum transmitting power an amateur station may use on 10.140 MHz?
A. 200 watts PEP output
B. 1000 watts PEP output
C. 1500 watts PEP output
D. 2000 watts PEP output
Commission's Rules
<number>
300
f
m

## Slide 66: G1C02 - What is the maximum transmitting power an amateur station may use on the 12-meter band?
A. 50 watts PEP output
B. 200 watts PEP output
C. 1500 watts PEP output
D. An effective radiated power equivalent to 100 watts from a half-wave dipole
Commission's Rules
<number>

## Slide 67: G1C02 - What is the maximum transmitting power an amateur station may use on the 12-meter band?
A. 50 watts PEP output
B. 200 watts PEP output
C. 1500 watts PEP output
D. An effective radiated power equivalent to 100 watts from a half-wave dipole
Commission's Rules
<number>

## Slide 68: G1C03 - What is the maximum bandwidth permitted by FCC rules for Amateur Radio stations transmitting on USB frequencies in the 60-meter band?
A. 2.8 kHz
B. 5.6 kHz
C. 1.8 kHz
D. 3 kHz
Commission's Rules
<number>

## Slide 69: G1C03 - What is the maximum bandwidth permitted by FCC rules for Amateur Radio stations transmitting on USB frequencies in the 60-meter band?
A. 2.8 kHz
B. 5.6 kHz
C. 1.8 kHz
D. 3 kHz
Commission's Rules
<number>

## Slide 70: G1C04 - Which of the following limitations apply to transmitter power on every amateur band?
A. Only the minimum power necessary to carry out the desired communications should be used
B. Power must be limited to 200 watts when transmitting between 14.100 MHz and 14.150 MHz
C. Power should be limited as necessary to avoid interference to another radio service on the frequency
D. Effective radiated power cannot exceed 1500 watts
Commission's Rules
<number>

## Slide 71: G1C04 - Which of the following limitations apply to transmitter power on every amateur band?
A. Only the minimum power necessary to carry out the desired communications should be used
B. Power must be limited to 200 watts when transmitting between 14.100 MHz and 14.150 MHz
C. Power should be limited as necessary to avoid interference to another radio service on the frequency
D. Effective radiated power cannot exceed 1500 watts
Commission's Rules
<number>

## Slide 72: G1C05 - Which of the following is a limitation on transmitter power on the 28 MHz band for a General Class control operator?
A. 100 watts PEP output
B. 1000 watts PEP output
C. 1500 watts PEP output
D. 2000 watts PEP output
Commission's Rules
<number>

## Slide 73: G1C05 - Which of the following is a limitation on transmitter power on the 28 MHz band for a General Class control operator?
A. 100 watts PEP output
B. 1000 watts PEP output
C. 1500 watts PEP output
D. 2000 watts PEP output
Commission's Rules
<number>

## Slide 74: G1C06 - Which of the following is a limitation on transmitter power on the 1.8 MHz band?
A. 200 watts PEP output
B. 1000 watts PEP output
C. 1200 watts PEP output
D. 1500 watts PEP output
Commission's Rules
<number>

## Slide 75: G1C06 - Which of the following is a limitation on transmitter power on the 1.8 MHz band?
A. 200 watts PEP output
B. 1000 watts PEP output
C. 1200 watts PEP output
D. 1500 watts PEP output
Commission's Rules
<number>

## Slide 76: G1C07 - What is the maximum symbol rate permitted for RTTY or data emission transmission on the 20-meter band?
A. 56 kilobaud
B. 19.6 kilobaud
C. 1200 baud
D. 300 baud
Commission's Rules
<number>

## Slide 77: G1C07 - What is the maximum symbol rate permitted for RTTY or data emission transmission on the 20-meter band?
A. 56 kilobaud
B. 19.6 kilobaud
C. 1200 baud
D. 300 baud
Commission's Rules
<number>

## Slide 78: G1C08 - What is the maximum symbol rate permitted for RTTY or data emission transmitted at frequencies below 28 MHz?
A. 56 kilobaud
B. 19.6 kilobaud
C. 1200 baud
D. 300 baud
Commission's Rules
<number>

## Slide 79: G1C08 - What is the maximum symbol rate permitted for RTTY or data emission transmitted at frequencies below 28 MHz?
A. 56 kilobaud
B. 19.6 kilobaud
C. 1200 baud
D. 300 baud
Commission's Rules
<number>

## Slide 80: G1C09 - What is the maximum symbol rate permitted for RTTY or data emission transmitted on the 1.25-meter and 70-centimeter bands?
A. 56 kilobaud
B. 19.6 kilobaud
C. 1200 baud
D. 300 baud
Commission's Rules
<number>

## Slide 81: G1C09 - What is the maximum symbol rate permitted for RTTY or data emission transmitted on the 1.25-meter and 70-centimeter bands?
A. 56 kilobaud
B. 19.6 kilobaud
C. 1200 baud
D. 300 baud
Commission's Rules
<number>

## Slide 82: G1C10 - What is the maximum symbol rate permitted for RTTY or data emission transmissions on the 10-meter band?
A. 56 kilobaud
B. 19.6 kilobaud
C. 1200 baud
D. 300 baud
Commission's Rules
<number>

## Slide 83: G1C10 - What is the maximum symbol rate permitted for RTTY or data emission transmissions on the 10-meter band?
A. 56 kilobaud
B. 19.6 kilobaud
C. 1200 baud
D. 300 baud
Commission's Rules
<number>

## Slide 84: G1C11 - What is the maximum symbol rate permitted for RTTY or data emission transmissions on the 2-meter band?
A. 56 kilobaud
B. 19.6 kilobaud
C. 1200 baud
D. 300 baud
Commission's Rules
<number>

## Slide 85: G1C11 - What is the maximum symbol rate permitted for RTTY or data emission transmissions on the 2-meter band?
A. 56 kilobaud
B. 19.6 kilobaud
C. 1200 baud
D. 300 baud
Commission's Rules
<number>

## Slide 86: G1D - Volunteer Examiners and Volunteer Examiner Coordinators; temporary identification
Commission's Rules
<number>

## Slide 87: VE Exam Eligibility
<number>
Exam Element General Advanced Extra
2 – Technician written X X X
3 – General written X X
4 – Extra written X
General licensees can only administer Technician exams
Advanced can administer Technician and General exams
Extra licensees can administer all exams
Notes: <number>
General class licensees with VE (Volunteer Examiner) credentials are eligible to administer element 2 (Technician written) exams. The older Advanced class licensees can also administer element 3 (General written) exams. Extra class licensees can administer any exam with proper VE credentials from a VEC (Volunteer Examiner Coordinator).
There are still certain rules that must be followed when giving exams. They must be scheduled in advance, open to the public, overseen by 3 VEC-certified VEs, etc.

## Slide 88: Certificate of Successful Completion (CSCE)
<number>
Notes: <number>
Since anyone studying for the General exam likely already has a callsign, a General class CSCE offers immediate General class privileges. Until the new license appears in the mail (or General class is shown on the FCC database), the new spectrum may be used by simply adding /AG to the existing callsign in CW or saying the callsign and “temporary AG” or “slash AG”.

## Slide 89: Certificate of Successful Completion (CSCE)
Commission's Rules
<number>
Notes: <number>
Since anyone studying for the General exam likely already has a callsign, a General class CSCE offers immediate General class privileges. Until the new license appears in the mail (or General class is shown on the FCC database), the new spectrum may be used by simply adding /AG to the existing callsign in CW or saying the callsign and “temporary AG” or “slash AG”.

## Slide 90: G1D01 - Who may receive credit for the elements represented by an expired amateur radio license?
A. Any person who can demonstrate that they once held a FCC issued General, Advanced, or Amateur Extra class license that was not revoked by the FCC
B. Anyone who held a FCC issued amateur radio license has been expired for not less than 5 years and not more than 15 years
C. Any person that previously held an amateur license issued by another country, but only if that country has a current reciprocal licensing agreement with the FCC
D. Only persons who once held a FCC Issued Novice, Technician, or Technician Plus license
Commission's Rules
<number>

## Slide 91: G1D01 - Who may receive credit for the elements represented by an expired amateur radio license?
A. Any person who can demonstrate that they once held a FCC issued General, Advanced, or Amateur Extra class license that was not revoked by the FCC
B. Anyone who held a FCC issued amateur radio license has been expired for not less than 5 years and not more than 15 years
C. Any person that previously held an amateur license issued by another country, but only if that country has a current reciprocal licensing agreement with the FCC
D. Only persons who once held a FCC Issued Novice, Technician, or Technician Plus license
Commission's Rules
<number>

## Slide 92: G1D02 - What license examinations may you administer when you are an accredited VE holding a General Class operator license?
A. General and Technician
B. General only
C. Technician only
D. Extra, General and Technician
Commission's Rules
<number>

## Slide 93: G1D02 - What license examinations may you administer when you are an accredited VE holding a General Class operator license?
A. General and Technician
B. General only
C. Technician only
D. Extra, General and Technician
Commission's Rules
<number>

## Slide 94: G1D03 - On which of the following band segments may you operate if you are a Technician Class operator and have a CSCE for General Class privileges?
A. Only the Technician band segments until your upgrade is posted in the FCC database
B. Only on the Technician band segments until your license arrives in the mail
C. On any General or Technician Class band segment
D. On any General or Technician Class band segment except 30-meters and 60-meters
FCC Rules
<number>

## Slide 95: G1D03 - On which of the following band segments may you operate if you are a Technician Class operator and have a CSCE for General Class privileges?
A. Only the Technician band segments until your upgrade is posted in the FCC database
B. Only on the Technician band segments until your license arrives in the mail
C. On any General or Technician Class band segment
D. On any General or Technician Class band segment except 30-meters and 60-meters
FCC Rules
<number>

## Slide 96: G1D04 - Which of the following is a requirement for administering a Technician Class license examination?
A. At least three General Class or higher VEs must observe the examination
B. At least two General Class or higher VEs must be present
C. At least two General Class or higher VEs must be present, but only one need be Extra Class
D. At least three VEs of Technician Class or higher must observe the examination
FCC Rules
<number>

## Slide 97: G1D04 - Which of the following is a requirement for administering a Technician Class license examination?
A. At least three General Class or higher VEs must observe the examination
B. At least two General Class or higher VEs must be present
C. At least two General Class or higher VEs must be present, but only one need be Extra Class
D. At least three VEs of Technician Class or higher must observe the examination
FCC Rules
<number>

## Slide 98: G1D05 - Which of the following must a person have before they can be an administering VE for a Technician Class license examination?
A. Notification to the FCC that you want to give an examination
B. Receipt of a CSCE for General Class
C. Possession of a properly obtained telegraphy license
D. An FCC General Class or higher license and VEC accreditation
FCC Rules
<number>

## Slide 99: G1D05 - Which of the following must a person have before they can be an administering VE for a Technician Class license examination?
A. Notification to the FCC that you want to give an examination
B. Receipt of a CSCE for General Class
C. Possession of a properly obtained telegraphy license
D. An FCC General Class or higher license and VEC accreditation
FCC Rules
<number>

## Slide 100: G1D06 - When must you add the special identifier "AG" after your call sign if you are a Technician Class licensee and have a CSCE for General Class operator privileges, but the FCC has not yet posted your upgrade on its website ?
A. Whenever you operate using General Class frequency privileges
B. Whenever you operate on any amateur frequency
C. Whenever you operate using Technician frequency privileges
D. A special identifier is not required as long as your General Class license application has been filed with the FCC
FCC Rules
<number>

## Slide 101: G1D06 - When must you add the special identifier "AG" after your call sign if you are a Technician Class licensee and have a CSCE for General Class operator privileges, but the FCC has not yet posted your upgrade on its website ?
A. Whenever you operate using General Class frequency privileges
B. Whenever you operate on any amateur frequency
C. Whenever you operate using Technician frequency privileges
D. A special identifier is not required as long as your General Class license application has been filed with the FCC
FCC Rules
<number>

## Slide 102: G1D07 - Volunteer Examiners are accredited by what organization?
A. The Federal Communications Commission
B. The Universal Licensing System
C. A Volunteer Examiner Coordinator
D. The Wireless Telecommunications Bureau
FCC Rules
<number>

## Slide 103: G1D07 - Volunteer Examiners are accredited by what organization?
A. The Federal Communications Commission
B. The Universal Licensing System
C. A Volunteer Examiner Coordinator
D. The Wireless Telecommunications Bureau
FCC Rules
<number>

## Slide 104: G1D08 - Which of the following criteria must be met for a non-U.S. citizen to be an accredited Volunteer Examiner?
A. The person must be a resident of the U.S. for a minimum of 5 years
B. The person must hold an FCC granted Amateur Radio license of General Class or above
C. The person’s home citizenship must be in ITU region 2
D. None of these choices is correct; a non-U.S. citizen cannot be a Volunteer Examiner
FCC Rules
<number>

## Slide 105: G1D08 - Which of the following criteria must be met for a non-U.S. citizen to be an accredited Volunteer Examiner?
A. The person must be a resident of the U.S. for a minimum of 5 years
B. The person must hold an FCC granted Amateur Radio license of General Class or above
C. The person’s home citizenship must be in ITU region 2
D. None of these choices is correct; a non-U.S. citizen cannot be a Volunteer Examiner
FCC Rules
<number>

## Slide 106: G1D09 - How long is a Certificate of Successful Completion of Examination ( CSCE ) valid for exam element credit?
A. 30 days
B. 180 days
C. 365 days
D. For as long as your current license is valid
FCC Rules
<number>

## Slide 107: G1D09 - How long is a Certificate of Successful Completion of Examination ( CSCE ) valid for exam element credit?
A. 30 days
B. 180 days
C. 365 days
D. For as long as your current license is valid
FCC Rules
<number>

## Slide 108: G1D10 - What is the minimum age that one must be to qualify as an accredited Volunteer Examiner?
A. 12 years
B. 18 years
C. 21 years
D. There is no age limit
FCC Rules
<number>

## Slide 109: G1D10 - What is the minimum age that one must be to qualify as an accredited Volunteer Examiner?
A. 12 years
B. 18 years
C. 21 years
D. There is no age limit
FCC Rules
<number>

## Slide 110: G1D11 - If a person has an expired FCC issued amateur radio license of General Class or higher, what is required before they can receive a new license?
A. They must have a letter from the FCC showing they once held an amateur or commercial license
B. There are no requirements other than being able to show a copy of the expired license
C. The applicant must be able to produce a copy of a page from a call book published in the USA showing his or her name and address
D. The applicant must pass the current element 2 exam
FCC Rules
<number>

## Slide 111: G1D11 - If a person has an expired FCC issued amateur radio license of General Class or higher, what is required before they can receive a new license?
A. They must have a letter from the FCC showing they once held an amateur or commercial license
B. There are no requirements other than being able to show a copy of the expired license
C. The applicant must be able to produce a copy of a page from a call book published in the USA showing his or her name and address
D. The applicant must pass the current element 2 exam
FCC Rules
<number>

## Slide 112: G1E – Control categories; repeater regulations; harmful interference; third party rules; ITU regions; automatically controlled digital station
FCC Rules
<number>

## Slide 113: G1E01 - Which of the following would disqualify a third party from participating in stating a message over an amateur station?
A. The third party’s amateur license has been revoked and not reinstated
B. The third party is not a U.S. citizen
C. The third party is a licensed amateur
D. The third party is speaking in a language other than English
FCC Rules
<number>

## Slide 114: G1E01 - Which of the following would disqualify a third party from participating in stating a message over an amateur station?
A. The third party’s amateur license has been revoked and not reinstated
B. The third party is not a U.S. citizen
C. The third party is a licensed amateur
D. The third party is speaking in a language other than English
FCC Rules
<number>

## Slide 115: G1E02 - When may a 10-meter repeater retransmit the 2-meter signal from a station having a Technician Class control operator?
A. Under no circumstances
B. Only if the station on 10-meters is operating under a Special Temporary Authorization allowing such retransmission
C. Only during an FCC declared general state of communications emergency
D. Only if the 10-meter repeater control operator holds at least a General Class license
FCC Rules
<number>

## Slide 116: G1E02 - When may a 10-meter repeater retransmit the 2-meter signal from a station having a Technician Class control operator?
A. Under no circumstances
B. Only if the station on 10-meters is operating under a Special Temporary Authorization allowing such retransmission
C. Only during an FCC declared general state of communications emergency
D. Only if the 10-meter repeater control operator holds at least a General Class license
FCC Rules
<number>

## Slide 117: G1E03 - What is required to conduct communications with a digital station operating under automatic control outside the automatic control band segments?
A. The station initiating the contact must be under local or remote control
B. The interrogating transmission must be made by another automatically controlled station
C. No third part traffic maybe be transmitted
D. The control operator of the interrogating station must hold an Extra
Class license
FCC Rules
<number>

## Slide 118: G1E03 - What is required to conduct communications with a digital station operating under automatic control outside the automatic control band segments?
A. The station initiating the contact must be under local or remote control
B. The interrogating transmission must be made by another automatically controlled station
C. No third part traffic maybe be transmitted
D. The control operator of the interrogating station must hold an Extra
Class license
FCC Rules
<number>

## Slide 119: G1E04 - Which of the following conditions require a licensed Amateur Radio operator to take specific steps to avoid harmful interference to other users or facilities?
A. When operating within one mile of an FCC Monitoring Station
B. When using a band where the Amateur Service is secondary
C. When a station is transmitting spread spectrum emissions
D. All of these choices are correct
FCC Rules
<number>

## Slide 120: G1E04 - Which of the following conditions require a licensed Amateur Radio operator to take specific steps to avoid harmful interference to other users or facilities?
A. When operating within one mile of an FCC Monitoring Station
B. When using a band where the Amateur Service is secondary
C. When a station is transmitting spread spectrum emissions
D. All of these choices are correct
FCC Rules
<number>

## Slide 121: G1E05 - What types of messages for a third party in another country may be transmitted by an amateur station?
A. Any message, as long as the amateur operator is not paid
B. Only messages for other licensed amateurs
C. Only messages relating to Amateur Radio or remarks of a personal character, or messages relating to emergencies or disaster relief
D. Any messages, as long as the text of the message is recorded in the station log
FCC Rules
<number>

## Slide 122: G1E05 - What types of messages for a third party in another country may be transmitted by an amateur station?
A. Any message, as long as the amateur operator is not paid
B. Only messages for other licensed amateurs
C. Only messages relating to Amateur Radio or remarks of a personal character, or messages relating to emergencies or disaster relief
D. Any messages, as long as the text of the message is recorded in the station log
FCC Rules
<number>

## Slide 123: G1E06 - Which of the following applies in the event of interference between a coordinated repeater and an uncoordinated repeater?
A. The licensee of the uncoordinated repeater has primary responsibility to resolve the interference
B. The licensee of the coordinated repeater has primary responsibility to resolve the interference
C. Both repeater licensees share equal responsibility to resolve the interference
D. The frequency coordinator bears primary responsibility to resolve the interference
FCC Rules
<number>

## Slide 124: G1E06 - Which of the following applies in the event of interference between a coordinated repeater and an uncoordinated repeater?
A. The licensee of the uncoordinated repeater has primary responsibility to resolve the interference
B. The licensee of the coordinated repeater has primary responsibility to resolve the interference
C. Both repeater licensees share equal responsibility to resolve the interference
D. The frequency coordinator bears primary responsibility to resolve the interference
FCC Rules
<number>

## Slide 125: US Amateurs May Handle Third-Party Traffic With:
<number>
FCC Rules
V2 | Antigua/Barbuda
LO-LW | Argentina
VK | Australia
V3 | Belize
CP | Bolivia
E7 | Bosnia-Herzegovina
PP-PY | Brazil
VE, VO, VY | Canada
CA-CE | Chile
HJ-HK | Colombia
D6 | Comoros (Federal Islamic Republic of)
TI, TE | Costa Rica
CM, CO | Cuba
HI | Dominican Republic
J7 | Dominica
HC-HD | Ecuador
YS | El Salvador
C5 | Gambia, The
9G | Ghana
J3 | Grenada
TG | Guatemala
8R | Guyana
HH | Haiti
HQ-HR | Honduras
4X, 4Z | Israel
6Y | Jamaica
JY | Jordan
EL | Liberia
V7 | Marshall Islands
XA-XI | Mexico
V6 | Micronesia, Federated States of
YN | Nicaragua
HO-HP | Panama
ZP | Paraguay
OA-OC | Peru
DU-DZ | Philippines
VR6 | Pitcairn Island*
V4 | St. Kitts/Nevis
J6 | St. Lucia
J8 | St. Vincent and the Grenadines
9L | Sierra Leone
ZR-ZU | South Africa
3DA | Swaziland
9Y-9Z | Trinidad/Tobago
TA-TC | Turkey
GB | United Kingdom
CV-CX | Uruguay
YV-YY | Venezuela
4U1ITU | ITU - Geneva
4U1VIC | VIC - Vienna
http://www.arrl.org/third-party-operating-agreements

## Slide 126: G1E07 - With which foreign countries is third party traffic prohibited, except for messages directly involving emergencies or disaster relief communications?
A. Countries in ITU Region 2
B. Countries in ITU Region 1
C. Every foreign country, unless there is a third party agreement in effect with that country
D. Any country which is not a member of the International Amateur Radio Union (IARU)
FCC Rules
<number>

## Slide 127: G1E07 - With which foreign countries is third party traffic prohibited, except for messages directly involving emergencies or disaster relief communications?
A. Countries in ITU Region 2
B. Countries in ITU Region 1
C. Every foreign country, unless there is a third party agreement in effect with that country
D. Any country which is not a member of the International Amateur Radio Union (IARU)
FCC Rules
<number>

## Slide 128: G1E08 - Which of the following is a requirement for a non-licensed person to communicate with a foreign Amateur Radio station from a station with an FCC-granted license at which an FCC licensed control operator is present?
A. Information must be exchanged in English
B. The foreign amateur station must be in a country with which the United States has a third party agreement
C. The control operator must have at least a General Class license
D. All of these choices are correct
FCC Rules
<number>

## Slide 129: G1E08 - Which of the following is a requirement for a non-licensed person to communicate with a foreign Amateur Radio station from a station with an FCC-granted license at which an FCC licensed control operator is present?
A. Information must be exchanged in English
B. The foreign amateur station must be in a country with which the United States has a third party agreement
C. The control operator must have at least a General Class license
D. All of these choices are correct
FCC Rules
<number>

## Slide 130: G1E09 - What language must be used when identifying your station if you are using a language other than English in making a contact using phone emission?
A. The language being used for the contact
B. Any language recognized by the United Nations
C. English only
D. English, Spanish, French, or German
FCC Rules
<number>

## Slide 131: G1E09 - What language must be used when identifying your station if you are using a language other than English in making a contact using phone emission?
A. The language being used for the contact
B. Any language recognized by the United Nations
C. English only
D. English, Spanish, French, or German
FCC Rules
<number>

## Slide 132: G1E10 - What portion of the 10-meter band is available for repeater use?
A. The entire band
B. The portion between 28.1 MHz and 28.2 MHz
C. The portion between 28.3 MHz and 28.5 MHz
D. The portion above 29.6 MHz
FCC Rules
<number>

## Slide 133: G1E10 - What portion of the 10-meter band is available for repeater use?
A. The entire band
B. The portion between 28.1 MHz and 28.2 MHz
C. The portion between 28.3 MHz and 28.5 MHz
D. The portion above 29.6 MHz
FCC Rules
<number>

## Slide 134: G1E11 - Which of the following is the FCC term for an unattended digital station that transfers messages to and from the Internet?
A. Locally controlled station
B. Robotically controlled station
C. Automatically controlled digital station
D. Fail-safe digital station
FCC Rules
<number>

## Slide 135: G1E11 - Which of the following is the FCC term for an unattended digital station that transfers messages to and from the Internet?
A. Locally controlled station
B. Robotically controlled station
C. Automatically controlled digital station
D. Fail-safe digital station
FCC Rules
<number>

## Slide 136: G1E12 - Under what circumstances are messages that are sent via digital modes exempt from Part 97 third party rules that apply to other modes of communication?
A. Under no circumstances
B. When messages are encrypted
C. When messages are not encrypted
D. When under automatic control
FCC Rules
<number>

## Slide 137: G1E12 - Under what circumstances are messages that are sent via digital modes exempt from Part 97 third party rules that apply to other modes of communication?
A. Under no circumstances
B. When messages are encrypted
C. When messages are not encrypted
D. When under automatic control
FCC Rules
<number>

## Slide 138: G1E13 - On what bands may automatically controlled stations transmitting RTTY or data emissions communicate with other automatically controlled digital stations?
A. On any band segment where digital operation is permitted
B. Anywhere in the non-phone segments of the 10-meter or shorter wavelength bands
C. Only in the non-phone Extra Class segments of the bands
D. Anywhere in the 1.25 meter or shorter wavelength bands, and in specified segments of the 80-meter through 2-meter bands
FCC Rules
<number>

## Slide 139: G1E13 - On what bands may automatically controlled stations transmitting RTTY or data emissions communicate with other automatically controlled digital stations?
A. On any band segment where digital operation is permitted
B. Anywhere in the non-phone segments of the 10-meter or shorter wavelength bands
C. Only in the non-phone Extra Class segments of the bands
D. Anywhere in the 1.25 meter or shorter wavelength bands, and in specified segments of the 80-meter through 2-meter bands
FCC Rules
<number>

## Slide 140: END OF SUBELEMENT G1 COMMISSION'S RULES [5 Exam Questions-5 Groups]
FCC Rules
<number>