## Slide 1: SUBELEMENT G7 PRACTICAL CIRCUITS [3 Exam Questions–3 Groups]
G7 - Practical Circuits
<number>
Notes: Subelement G7 Practical Circuits. General Training Slides for 2015 Question Pool Good through June 30, 2019 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM, Howard Schultz, W7HS.
<number>

## Slide 2: SUBELEMENT G7 PRACTICAL CIRCUITS [3 Exam Questions–3 Groups]
G7A Power supplies; and schematic symbols
G7C - Receivers and transmitters; filters, oscillators

## Slide 3: Half Wave Power Supply
<number>
Practical Circuits

## Slide 4: Regulated Power Supply
The transformer converts 120 volt AC line voltage to 12.6 volts AC.
The bridge rectifier feeds pulsed DC into the large capacitor which filters the power to DC. The 7812 voltage regulator takes the DC input and creates a stable 12 volt DC output. The final capacitor removes any ripple from the regulator and stabilizes the output.
<number>
Practical Circuits

## Slide 5: G7A01 - What useful feature does a power supply bleeder resistor provide?
A. It acts as a fuse for excess voltage
B. It ensures that the filter capacitors are discharged when power is removed
C. It removes shock hazards from the induction coils
D. It eliminates ground loop current
<number>
Practical Circuits

## Slide 6: G7A01 - What useful feature does a power supply bleeder resistor provide?
A. It acts as a fuse for excess voltage
B. It ensures that the filter capacitors are discharged when power is removed
C. It removes shock hazards from the induction coils
D. It eliminates ground loop current
<number>
Practical Circuits

## Slide 7: G7A02 - Which of the following components are used in a power supply filter network?
A. Diodes
B. Transformers and transducers
C. Quartz crystals
D. Capacitors and inductors
<number>
Practical Circuits

## Slide 8: G7A02 - Which of the following components are used in a power supply filter network?
A. Diodes
B. Transformers and transducers
C. Quartz crystals
D. Capacitors and inductors
<number>
Practical Circuits

## Slide 9: G7A03 - What is the peak-inverse-voltage across the rectifiers in a full-wave bridge power supply?
A. One-quarter the normal output voltage of the power supply
B. Half the normal output voltage of the power supply
C. Double the normal peak output voltage of the power supply
D. Equal to the normal peak output voltage of the power supply
<number>
Practical Circuits

## Slide 10: G7A03 - What is the peak-inverse-voltage across the rectifiers in a full-wave bridge power supply?
A. One-quarter the normal output voltage of the power supply
B. Half the normal output voltage of the power supply
C. Double the normal peak output voltage of the power supply
D. Equal to the normal peak output voltage of the power supply
<number>
Practical Circuits

## Slide 11: G7A04 - What is the peak-inverse-voltage across the rectifier in a half-wave power supply?
A. One-half the normal peak output voltage of the power supply
B. One-half the normal output voltage of the power supply
C. Equal to the normal output voltage of the power supply
D. Two times the normal peak output voltage of the power supply
<number>
Practical Circuits

## Slide 12: G7A04 - What is the peak-inverse-voltage across the rectifier in a half-wave power supply?
A. One-half the normal peak output voltage of the power supply
B. One-half the normal output voltage of the power supply
C. Equal to the normal output voltage of the power supply
D. Two times the normal peak output voltage of the power supply
<number>
Practical Circuits

## Slide 13: G7A05 - What portion of the AC cycle is converted to DC by a half-wave rectifier?
A. 90 degrees
B. 180 degrees
C. 270 degrees
D. 360 degrees
<number>
Practical Circuits

## Slide 14: G7A05 - What portion of the AC cycle is converted to DC by a half-wave rectifier?
A. 90 degrees
B. 180 degrees
C. 270 degrees
D. 360 degrees
<number>
Practical Circuits

## Slide 15: G7A06 - What portion of the AC cycle is converted to DC by a full-wave rectifier?
A. 90 degrees
B. 180 degrees
C. 270 degrees
D. 360 degrees
<number>
Practical Circuits

## Slide 16: G7A06 - What portion of the AC cycle is converted to DC by a full-wave rectifier?
A. 90 degrees
B. 180 degrees
C. 270 degrees
D. 360 degrees
<number>
Practical Circuits

## Slide 17: G7A07 - What is the output waveform of an unfiltered full-wave rectifier connected to a resistive load?
A. A series of DC pulses at twice the frequency of the AC input
B. A series of DC pulses at the same frequency as the AC input
C. A sine wave at half the frequency of the AC input
D. A steady DC voltage
<number>
Practical Circuits

## Slide 18: G7A07 - What is the output waveform of an unfiltered full-wave rectifier connected to a resistive load?
A. A series of DC pulses at twice the frequency of the AC input
B. A series of DC pulses at the same frequency as the AC input
C. A sine wave at half the frequency of the AC input
D. A steady DC voltage
<number>
Practical Circuits

## Slide 19: G7A08 - Which of the following is an advantage of a switchmode power supply as compared to a linear power supply?
A. Faster switching time makes higher output voltage possible
B. Fewer circuit components are required
C. High frequency operation allows the use of smaller components
D. All of these choices are correct
<number>
Practical Circuits

## Slide 20: G7A08 - Which of the following is an advantage of a switchmode power supply as compared to a linear power supply?
A. Faster switching time makes higher output voltage possible
B. Fewer circuit components are required
C. High frequency operation allows the use of smaller components
D. All of these choices are correct
<number>
Practical Circuits

## Slide 21: G7A09 - Which symbol in figure G7-1 represents a field effect transistor?
A. Symbol 2
B. Symbol 5
C. Symbol 1
D. Symbol 4
<number>
Practical Circuits

## Slide 22: G7A09 - Which symbol in figure G7-1 represents a field effect transistor?
A. Symbol 2
B. Symbol 5
C. Symbol 1
D. Symbol 4
<number>
Practical Circuits

## Slide 23: G7A10 - Which symbol in figure G7-1 represents a Zener diode?
A. Symbol 4
B. Symbol 1
C. Symbol 11
D. Symbol 5
<number>
Practical Circuits

## Slide 24: G7A10 - Which symbol in figure G7-1 represents a Zener diode?
A. Symbol 4
B. Symbol 1
C. Symbol 11
D. Symbol 5
<number>
Practical Circuits

## Slide 25: G7A11 - Which symbol in figure G7-1 represents an NPN junction transistor?
A. Symbol 1
B. Symbol 2
C. Symbol 7
D. Symbol 11
<number>
Practical Circuits

## Slide 26: G7A11 - Which symbol in figure G7-1 represents an NPN junction transistor?
A. Symbol 1
B. Symbol 2
C. Symbol 7
D. Symbol 11
<number>
Practical Circuits

## Slide 27: G7A12 - Which symbol in Figure G7-1 represents a multiple-winding transformer?
A. Symbol 4
B. Symbol 7
C. Symbol 6
D. Symbol 1
<number>
Practical Circuits

## Slide 28: G7A12 - Which symbol in Figure G7-1 represents a multiple-winding transformer?
A. Symbol 4
B. Symbol 7
C. Symbol 6
D. Symbol 1
<number>
Practical Circuits

## Slide 29: G7A13 - Which symbol in Figure G7-1 represents a tapped inductor?
A. Symbol 7
B. Symbol 11
C. Symbol 6
D. Symbol 1
<number>
Practical Circuits

## Slide 30: G7A13 - Which symbol in Figure G7-1 represents a tapped inductor?
A. Symbol 7
B. Symbol 11
C. Symbol 6
D. Symbol 1
<number>
Practical Circuits

## Slide 31: G7B - Digital circuits; amplifiers and oscillators
<number>
Practical Circuits

## Slide 32: G7B01 - Complex digital circuitry can often be replaced by what type of integrated circuit?
A. Microcontroller
B. Charge-coupled device
C. Phase detector
D. Window comparator
<number>
Practical Circuits

## Slide 33: G7B01 - Complex digital circuitry can often be replaced by what type of integrated circuit?
A. Microcontroller
B. Charge-coupled device
C. Phase detector
D. Window comparator
<number>
Practical Circuits

## Slide 34: Digital Circuits
<number>
Practical Circuits
A | B | Q
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A | B | Q
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
AND
NAND
A | B | Q
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
OR
NOR
A and B are inputs to the gates with Q being the output value.
Notice the NAND and NOR gates are exactly the opposite of their counterparts. The AND or OR function is performed and the result is inverted or NOTed.

## Slide 35: G7B02 - Which of the following is an advantage of using the binary system when processing digital signals?
A. Binary "ones" and "zeros" are easy to represent by an "on" or "off" state
B. The binary number system is most accurate
C. Binary numbers are more compatible with analog circuitry
D. All of these choices are correct
<number>
Practical Circuits

## Slide 36: G7B02 - Which of the following is an advantage of using the binary system when processing digital signals?
A. Binary "ones" and "zeros" are easy to represent by an "on" or "off" state
B. The binary number system is most accurate
C. Binary numbers are more compatible with analog circuitry
D. All of these choices are correct
<number>
Practical Circuits

## Slide 37: G7B03 - Which of the following describes the function of a two input AND gate?
A. Output is high when either or both inputs are low
B. Output is high only when both inputs are high
C. Output is low when either or both inputs are high
D. Output is low only when both inputs are high
<number>
Practical Circuits

## Slide 38: G7B03 - Which of the following describes the function of a two input AND gate?
A. Output is high when either or both inputs are low
B. Output is high only when both inputs are high
C. Output is low when either or both inputs are high
D. Output is low only when both inputs are high
<number>
Practical Circuits

## Slide 39: G7B04 - Which of the following describes the function of a two input NOR gate?
A. Output is high when either or both inputs are low
B. Output is high only when both inputs are high
C. Output is low when either or both inputs are high
D. Output is low only when both inputs are high
<number>
Practical Circuits

## Slide 40: G7B04 - Which of the following describes the function of a two input NOR gate?
A. Output is high when either or both inputs are low
B. Output is high only when both inputs are high
C. Output is low when either or both inputs are high
D. Output is low only when both inputs are high
<number>
Practical Circuits

## Slide 41: G7B05 - How many states does a 3-bit binary counter have?
A. 3
B. 6
C. 8
D. 16
<number>
Practical Circuits

## Slide 42: G7B05 - How many states does a 3-bit binary counter have?
A. 3
B. 6
C. 8
D. 16
<number>
Practical Circuits
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
3 bit = 2 ³ = 8

## Slide 43: G7B06 - What is a shift register?
A. A clocked array of circuits that passes data in steps along the array
B. An array of operational amplifiers used for tri-state arithmetic operations
C. A digital mixer
D. An analog mixer
<number>
Practical Circuits

## Slide 44: G7B06 - What is a shift register?
A. A clocked array of circuits that passes data in steps along the array
B. An array of operational amplifiers used for tri-state arithmetic operations
C. A digital mixer
D. An analog mixer
<number>
Practical Circuits

## Slide 45: G7B07 - What are the basic components of virtually all sine wave oscillators?
A. An amplifier and a divider
B. A frequency multiplier and a mixer
C. A circulator and a filter operating in a feed-forward loop
D. A filter and an amplifier operating in a feedback loop
<number>
Practical Circuits

## Slide 46: G7B07 - What are the basic components of virtually all sine wave oscillators?
A. An amplifier and a divider
B. A frequency multiplier and a mixer
C. A circulator and a filter operating in a feed-forward loop
D. A filter and an amplifier operating in a feedback loop
<number>
Practical Circuits

## Slide 47: G7B08 - How is the efficiency of an RF power amplifier determined?
A. Divide the DC input power by the DC output power
B. Divide the RF output power by the DC input power
C. Multiply the RF input power by the reciprocal of the RF output power
D. Add the RF input power to the DC output power
<number>
Practical Circuits

## Slide 48: G7B08 - How is the efficiency of an RF power amplifier determined?
A. Divide the DC input power by the DC output power
B. Divide the RF output power by the DC input power
C. Multiply the RF input power by the reciprocal of the RF output power
D. Add the RF input power to the DC output power
<number>
Practical Circuits

## Slide 49: G7B09 - What determines the frequency of an LC oscillator?
A. The number of stages in the counter
B. The number of stages in the divider
C. The inductance and capacitance in the tank circuit
D. The time delay of the lag circuit
<number>
Practical Circuits

## Slide 50: G7B09 - What determines the frequency of an LC oscillator?
A. The number of stages in the counter
B. The number of stages in the divider
C. The inductance and capacitance in the tank circuit
D. The time delay of the lag circuit
<number>
Practical Circuits

## Slide 51: Amplifier classes
<number>
Practical Circuits
Class A
Class B
Class C
Class AB
Linear
Bias current
Low efficiency
High distortion
Better efficiency
Linear
Better efficiency
More complex
Non-Linear
High efficiency

## Slide 52: G7B10 - Which of the following is a characteristic of a Class A amplifier?
A. Low standby power
B. High Efficiency
C. No need for bias
D. Low distortion
<number>
Practical Circuits

## Slide 53: G7B10 - Which of the following is a characteristic of a Class A amplifier?
A. Low standby power
B. High Efficiency
C. No need for bias
D. Low distortion
<number>
Practical Circuits
Class A

## Slide 54: G7B11 - For which of the following modes is a Class C power stage appropriate for amplifying a modulated signal?
A. SSB
B. CW
C. AM
D. All of these choices are correct
G7 - Practical Circuits
<number>

## Slide 55: G7B11 - For which of the following modes is a Class C power stage appropriate for amplifying a modulated signal?
A. SSB
B. CW
C. AM
D. All of these choices are correct
G7 - Practical Circuits
<number>

## Slide 56: G7B12 - Which of these classes of amplifiers has the highest efficiency?
A. Class A
B. Class B
C. Class AB
D. Class C
<number>
Practical Circuits

## Slide 57: G7B12 - Which of these classes of amplifiers has the highest efficiency?
A. Class A
B. Class B
C. Class AB
D. Class C
<number>
Practical Circuits
Class C
Non-Linear
High efficiency

## Slide 58: G7B13 - What is the reason for neutralizing the final amplifier stage of a transmitter?
A. To limit the modulation index
B. To eliminate self-oscillations
C. To cut off the final amplifier during standby periods
D. To keep the carrier on frequency
<number>
Practical Circuits

## Slide 59: G7B13 - What is the reason for neutralizing the final amplifier stage of a transmitter?
A. To limit the modulation index
B. To eliminate self-oscillations
C. To cut off the final amplifier during standby periods
D. To keep the carrier on frequency
<number>
Practical Circuits

## Slide 60: G7B14 - Which of the following describes a linear amplifier?
A. Any RF power amplifier used in conjunction with an amateur transceiver
B. An amplifier in which the output preserves the input waveform
C. A Class C high efficiency amplifier
D. An amplifier used as a frequency multiplier
<number>
Practical Circuits

## Slide 61: G7B14 - Which of the following describes a linear amplifier?
A. Any RF power amplifier used in conjunction with an amateur transceiver
B. An amplifier in which the output preserves the input waveform
C. A Class C high efficiency amplifier
D. An amplifier used as a frequency multiplier
<number>
Practical Circuits

## Slide 62: G7C - Receivers and transmitters; filters, oscillators
<number>
Practical Circuits

## Slide 63: Simple Single-Sideband Phone Transmitter
Practical Circuits
<number>
Speech Amp
Balanced Modulator
Filter
Filter
Mixer
Linear RF Amp
Carrier Oscillator
Heterodyne Oscillator
The microphone audio is modulated into AM by mixing with the carrier oscillator in the balanced modulator. The filter removes the unwanted products before mixing again to create the signal on the desired frequency. That final signal is amplified and sent to the antenna.
Notes: The audio comes in the microphone and is modulated into AM by mixing with the carrier oscillator in the balanced modulator. The filter removes the unwanted products before mixing again to create the signal on the desired frequency. That final signal is amplified and sent to the antenna.
<number>

## Slide 64: G7C01 - Which of the following is used to process signals from the balanced modulator then send them to the mixer in some single sideband phone transmitters?
A. Carrier oscillator
B. Filter
C. IF amplifier
D. RF amplifier
<number>
Practical Circuits

## Slide 65: G7C01 - Which of the following is used to process signals from the balanced modulator then send them to the mixer in some single sideband phone transmitters?
A. Carrier oscillator
B. Filter
C. IF amplifier
D. RF amplifier
<number>
Practical Circuits
Speech Amp
Balanced Modulator
Filter
Mixer
Linear RF Amp
Carrier Oscillator
Heterodyne Oscillator
Filter

## Slide 66: G7C02 - Which circuit is used to combine signals from the carrier oscillator and speech amplifier then send the result to the filter in some single sideband phone transmitters?
A. Discriminator
B. Detector
C. IF amplifier
D. Balanced modulator
<number>
Practical Circuits

## Slide 67: G7C02 - Which circuit is used to combine signals from the carrier oscillator and speech amplifier then send the result to the filter in some single sideband phone transmitters?
A. Discriminator
B. Detector
C. IF amplifier
D. Balanced modulator
<number>
Practical Circuits
Speech Amp
Balanced Modulator
Filter
Mixer
Linear RF Amp
Carrier Oscillator
Heterodyne Oscillator
Filter

## Slide 68: G7C03 - What circuit is used to process signals from the RF amplifier and local oscillator then send the result to the IF filter in a superheterodyne receiver?
A. Balanced modulator
B. IF amplifier
C. Mixer
D. Detector
<number>
Practical Circuits

## Slide 69: G7C03 - What circuit is used to process signals from the RF amplifier and local oscillator then send the result to the IF filter in a superheterodyne receiver?
A. Balanced modulator
B. IF amplifier
C. Mixer
D. Detector
<number>
Practical Circuits
RF preamp
Mixer
IF Filter
Product Detector
AF Amp
Local Oscillator
BFO
Beat Freq. Osc.
Superhet receiver is basically a transmitter in reverse

## Slide 70: G7C04 - What circuit is used to combine signals from the IF amplifier and BFO and send the result to the AF amplifier in some single sideband receivers?
A. RF oscillator
B. IF filter
C. Balanced modulator
D. Product detector
<number>
Practical Circuits

## Slide 71: G7C04 - What circuit is used to combine signals from the IF amplifier and BFO and send the result to the AF amplifier in some single sideband receivers?
A. RF oscillator
B. IF filter
C. Balanced modulator
D. Product detector
<number>
Practical Circuits
RF preamp
Mixer
IF Filter
Product Detector
AF Amp
Local Oscillator
BFO

## Slide 72: G7C05 - Which of the following is an advantage of a transceiver controlled by a direct digital synthesizer ( DDS ) ?
A. Wide tuning range and no need for band switching
B. Relatively high power output
C. Relatively low power consumption
D. Variable frequency with the stability of a crystal oscillator
<number>
Practical Circuits

## Slide 73: G7C05 - Which of the following is an advantage of a transceiver controlled by a direct digital synthesizer ( DDS ) ?
A. Wide tuning range and no need for band switching
B. Relatively high power output
C. Relatively low power consumption
D. Variable frequency with the stability of a crystal oscillator
<number>
Practical Circuits

## Slide 74: G7C06 - What should be the impedance of a low-pass filter as compared to the impedance of the transmission line into which it is inserted?
A. Substantially higher
B. About the same
C. Substantially lower
D. Twice the transmission line impedance
<number>
Practical Circuits

## Slide 75: G7C06 - What should be the impedance of a low-pass filter as compared to the impedance of the transmission line into which it is inserted?
A. Substantially higher
B. About the same
C. Substantially lower
D. Twice the transmission line impedance
<number>
Practical Circuits

## Slide 76: G7C07 - What is the simplest combination of stages that implement a superheterodyne receiver?
A. RF amplifier, detector, audio amplifier
B. RF amplifier, mixer, IF discriminator
C. HF oscillator, mixer, detector
D. HF oscillator, prescaler, audio amplifier
<number>
Practical Circuits

## Slide 77: G7C07 - What is the simplest combination of stages that implement a superheterodyne receiver?
A. RF amplifier, detector, audio amplifier
B. RF amplifier, mixer, IF discriminator
C. HF oscillator, mixer, detector
D. HF oscillator, prescaler, audio amplifier
<number>
Practical Circuits

## Slide 78: G7C08 - What type of circuit is used in many FM receivers to convert signals coming from the IF amplifier to audio?
A. Product detector
B. Phase inverter
C. Mixer
D. Discriminator
<number>
Practical Circuits

## Slide 79: G7C08 - What type of circuit is used in many FM receivers to convert signals coming from the IF amplifier to audio?
A. Product detector
B. Phase inverter
C. Mixer
D. Discriminator
<number>
Practical Circuits

## Slide 80: G7C09 - Which of the following is needed for a Digital Signal Processor IF filter?
A. An analog to digital converter
B. A digital to analog converter
C. A digital processor chip
D. All of the these choices are correct
<number>
Practical Circuits

## Slide 81: G7C09 - Which of the following is needed for a Digital Signal Processor IF filter?
A. An analog to digital converter
B. A digital to analog converter
C. A digital processor chip
D. All of the these choices are correct
<number>
Practical Circuits

## Slide 82: G7C10 - How is Digital Signal Processor filtering accomplished?
A. By using direct signal phasing
B. By converting the signal from analog to digital and using digital processing
C. By differential spurious phasing
D. By converting the signal from digital to analog and taking the difference of mixing products
<number>
Practical Circuits

## Slide 83: G7C10 - How is Digital Signal Processor filtering accomplished?
A. By using direct signal phasing
B. By converting the signal from analog to digital and using digital processing
C. By differential spurious phasing
D. By converting the signal from digital to analog and taking the difference of mixing products
<number>
Practical Circuits

## Slide 84: G7C11 - What is meant by the term "software defined radio" ( SDR ) ?
A. A radio in which most major signal processing functions are performed by software
B. A radio that provides computer interface for automatic logging of band and frequency
C. A radio that uses crystal filters designed using software
D. A computer model that can simulate performance of a radio to aid in the design process
<number>
Practical Circuits

## Slide 85: G7C11 - What is meant by the term "software defined radio" ( SDR ) ?
A. A radio in which most major signal processing functions are performed by software
B. A radio that provides computer interface for automatic logging of band and frequency
C. A radio that uses crystal filters designed using software
D. A computer model that can simulate performance of a radio to aid in the design process
<number>
Practical Circuits

## Slide 86: End of SUBELEMENT G7 PRACTICAL CIRCUITS