## Slide 1: SUBELEMENT T1 – COMMISSION’S Rules,
Descriptions and definitions for the Amateur Radio Service, operator and station license responsibilities.
[6 Exam Questions - 6 Groups]
Notes: Subelement T1 COMMISSION’S Rules. Technician Training Slides for 2022 Question Pool Good through June 30, 2026 Assembled by Western Washington Ham Training Team, Daniel Stevens KL7WM.

## Slide 2: FCC Rules
T1A - Purpose and permissible use of the Amateur Radio Service; Operator/primary station license grant; Meanings of basic terms used in FCC rules; Interference; RACES rules; Phonetics; Frequency Coordinator
T1B - Frequency allocations; Emission modes; Spectrum sharing; Transmissions near band edges; Contacting the International Space Station; Power output
T1C - Licensing: classes, sequential and vanity call sign systems, places where the Amateur Radio Service is regulated by the FCC, name and address on FCC license database, term, renewal, grace period, maintaining mailing address; International communications
T1D - Authorized and prohibited transmissions: communications with other countries, music, exchange of information with other services, indecent language, compensation for operating, retransmission of other amateur signals, encryption, sale of equipment, unidentified transmissions, one-way transmission
T1E - Control operator: eligibility, designating, privileges, duties, location, required; Control point; Control types: automatic, remote
T1F - Station identification; Repeaters; Third party communications; Club stations; FCC inspection

## Slide 3: Certificate of Successful Completion (CSCE)

## Slide 4: FCC Part 97
  Title 47 governs all Telecommunications in the US
    There are 301 parts (Part 0-332)
  Part 97 applies to Amateur Radio
  Copies available at:
  http://www.arrl.org/FandES/field/regulations/rules-g.html http://www.fcc.gov

## Slide 5: FCC Universal License System
  Online License Service http://wireless.fcc.gov/uls/
  Tracks all FCC License Applications and Licensees
  When your license shows up here, you’re legal 

## Slide 6: Definitions
Regulatory Body – FCC rules are defined in Part 97
Amateur Service – A radio communication service, carried out by authorized individuals without pecuniary interest
Amateur Operator – A person granted a license for amateur service
Amateur Station – A station licensed for Amateur Service
Amateur Space Station – An amateur station over 50KM high
Unidentified Communications – Communications from an unidentified source
Interference – Unwanted signals that disrupt other communications

## Slide 7: Five Fundamental Purposes of Ham Radio
  1. Recognition and enhancement of the value of the amateur service to the public as a voluntary noncommercial communication service, particularly with respect to providing emergency communications.
  2. Continuation and extension of the amateur’s proven ability to contribute to the advancement of the radio art.
  3. Encouragement and improvement of the amateur service through rules which provide for advancing skills in both the communications and technical phases of the art.
  4. Expansion of the existing reservoir within the amateur radio service of trained operators, technicians, and electronics experts.
  5. Continuation and extension of the amateur’s unique ability to enhance international goodwill.

## Slide 8: Section T1A
Amateur Radio Service: purpose and permissible use of the Amateur Radio Service, operator/primary station license grant; Meanings of basic terms used in FCC rules; Interference; RACES rules; Phonetics; Frequency Coordinator

## Slide 9: T1A01 - Which of the following is part of the Basis and Purpose of the Amateur Radio Service?
A. Providing personal radio communications for as many citizens as possible
B. Providing communications for international non-profit organizations
C. Advancing skills in the technical and communication phases of the radio art
D. All of these choices are correct

## Slide 10: T1A01 - Which of the following is part of the Basis and Purpose of the Amateur Radio Service?
A. Providing personal radio communications for as many citizens as possible
B. Providing communications for international non-profit organizations
C. Advancing skills in the technical and communication phases of the radio art
D. All of these choices are correct

## Slide 11: T1A02 - Which agency regulates and enforces the rules for the Amateur Radio Service in the United States?
A. FEMA
B. Homrland Security
C. The FCC
D. All these choices are correct

## Slide 12: T1A02 - Which agency regulates and enforces the rules for the Amateur Radio Service in the United States?
A. FEMA
B. Homeland Security
C. The FCC
D. Al;l these choices are correct

## Slide 13: T1A03 What do the FCC rules state regarding the use of a phonetic alphabet for station identification in the Amateur Radio Service?
A. It is required when transmitting emergency messages
B. It is encouraged
C. It is required when in contact with foreign stations
D. Al the choices are correct

## Slide 14: T1A03 What do the FCC rules state regarding the use of a phonetic alphabet for station identification in the Amateur Radio Service?
A. It is required when transmitting emergency messages
B. It is encouraged
C. It is required when in contact with foreign stations
D. All thre choices are correct

## Slide 15: T1A04 How many operator/primary station license grants may be held by any one person?
A. One
B. No more than two
C. One for each band on which the person plans to operate
D. One for each permanent station location from which the person plans to operate

## Slide 16: T1A04 How many operator/primary station license grants may be held by any one person?
A. One
B. No more than two
C. One for each band on which the person plans to operate
D. One for each permanent station location from which the person plans to operate

## Slide 17: T1A05 What proves that the FCC has issued an operator/primary license grant?
A printed copy of the certificate of successful completion of examination
An email notification from the NCVEC granting the license.
The license appears in the FCC ULS database.
All these choices are correct.

## Slide 18: T1A05 What proves that the FCC has issued an operator/primary license grant?
A printed copy of the certificate of successful completion of examination
An email notification from the NCVEC granting the license.
The license appears in the FCC ULS database.
All these choices are correct.

## Slide 19: T1A06 What is the FCC Part 97 definition of a beacon?
A. A government transmitter marking the amateur radio band edges
B. A bulletin sent by the FCC to announce a national emergency
C. A continuous transmission of weather information authorized in the amateur bands by the National Weather Service
D .An amateur station transmitting communications for the purposes of observing propagation or related experimental activities

## Slide 20: T1A06 What is the FCC Part 97 definition of a beacon?
A. A government transmitter marking the amateur radio band edges
B. A bulletin sent by the FCC to announce a national emergency
C. A continuous transmission of weather information authorized in the amateur bands by the National Weather Service
D .An amateur station transmitting communications for the purposes of observing propagation or related experimental activities

## Slide 21: T1A07 What is the FCC Part 97 definition of a space station?
A. Any satellite orbiting the earth
B. A manned satellite orbiting the earth
C. An amateur station located more than 50 km above the Earth's surface
D. An amateur station using amateur radio satellites for relay of signals

## Slide 22: T1A07 What is the FCC Part 97 definition of a space station?
A. Any satellite orbiting the earth
B. A manned satellite orbiting the earth
C. An amateur station located more than 50 km above the Earth's surface
D. An amateur station using amateur radio satellites for relay of signals

## Slide 23: T1A08 - Which of the following entities recommends transmit/receive channels and other parameters for auxiliary and repeater stations?
A. Frequency Spectrum Manager appointed by the FCC
B. Volunteer Frequency Coordinator recognized by local amateurs
C. FCC Regional Field Office
D. International Telecommunications Union

## Slide 24: T1A08 - Which of the following entities recommends transmit/receive channels and other parameters for auxiliary and repeater stations?
A. Frequency Spectrum Manager appointed by the FCC
B. Volunteer Frequency Coordinator recognized by local amateurs
C. FCC Regional Field Office
D. International Telecommunications Union

## Slide 25: T1A09 - Who selects a Frequency Coordinator?
A. The FCC Office of Spectrum Management and Coordination Policy
B. The local chapter of the Office of National Council of Independent Frequency Coordinators
C. Amateur operators in a local or regional area whose stations are eligible to be repeater or auxiliary stations
D. FCC Regional Field Office

## Slide 26: T1A09 - Who selects a Frequency Coordinator?
A. The FCC Office of Spectrum Management and Coordination Policy
B. The local chapter of the Office of National Council of Independent Frequency Coordinators
C. Amateur operators in a local or regional area whose stations are eligible to be repeater or auxiliary stations
D. FCC Regional Field Office

## Slide 27
Local Frequency Coordinators help organize repeater activities within a region to minimize interference issues
The Western Washington Amateur Relay Association (WWARA) covers Western Washington and has repeater lists and the local band plan
http://www.WWARA.org
WWARA PO BOX 31521 SEATTLE WA 98103-1521

## Slide 28: T1A10 What is the Radio Amateur Civil Emergency Service (RACES)?
A. A radio service using amateur frequencies for emergency management or civil defense communications
B. A radio service using amateur stations for emergency management or civil defense communications
C. An emergency service using amateur operators certified by a civil defense organization as being enrolled in that organization
D. All of these choices are correct

## Slide 29: T1A10 What is the Radio Amateur Civil Emergency Service (RACES)?
A. A radio service using amateur frequencies for emergency management or civil defense communications
B. A radio service using amateur stations for emergency management or civil defense communications
C. An emergency service using amateur operators certified by a civil defense organization as being enrolled in that organization
D. All of these choices are correct

## Slide 30: T1A11 - When is willful interference to other amateur radio stations permitted?
A. To stop another amateur station that is breaking the FCC rules.
B. At no time
C. When making short test transmissions
D. At any time. Stations in the Amateur Radio Service are not protected from willful interference

## Slide 31: T1A11 - When is willful interference to other amateur radio stations permitted?
A. To stop another amateur station that is breaking the FCC rules.
B. At no time
C. When making short test transmissions
D. At any time. Stations in the Amateur Radio Service are not protected from willful interference

## Slide 32: Section T1B
Frequency allocations; ITU; emission modes; restricted sub-bands; spectrum sharing; transmissions near band edges; contacting the International Space Station; power output

## Slide 33: International Telecommunication Union (ITU) Regions

## Slide 34: Wavelength vs Frequency
The distance a radio wave travels in one cycle is called wavelength
The number of cycles per second is frequency
The maximum displacement of wave from reference value is amplitude
One Wavelength
Time
V+
V-
0V
Amplitude
One Cycle
½ Wave
¼ wave

## Slide 35: Frequency to Wavelength Conversion
To convert from frequency to wavelength in meters:
Wavelength = 300/Freq (MHz)
Frequency and wavelength are inversely proportional – as one increases, the other decreases
Longer (wavelength) – Lower (frequency)

## Slide 36: Frequency Calculations
300
f
m
300,000,000
Frequency
Wave length meters
300 is the speed of light 300,000,000 meters per second
F is frequency in MHz
M is Wave Length distance in meters of a full cycle at this frequency
To solve for a value, cover it with your finger and solve the remaining formula
Radio Waves 2014

## Slide 37: Frequency Calculations
300 is the Speed of Light in free space
  Radio wave travel at the Speed of Light
  300,000,000 meters per second
  Radio waves moves slower in wire
  Velocity Factor is speed in a material divided by the speed of light i.e. .66
f is frequency in millions (MHz)
  The millions of cycles cancel the millions of meters 146,520,000 = 146.53 MHz
m is Wave length in Meters or the distance of a full cycle
  How far it takes a wave to complete a complete cycle
  The higher the frequency the lower the meter (shorter)
  The lower the frequency the higher the meters (longer)
300
m
f
300 = m x f

## Slide 39: Technician HF Privileges
Notes
This information does not appear in the Technician exam
Technician Licensees may use up to 1500 watts PEP
Technician + HF Licensees may use up to 1500 watts PEP and 200 watts PEP on the HF bands

## Slide 40: FCC Line A

## Slide 41: Metric Units of Measure
Gigahertz | 1,000,000,000
Megahertz | 1,000,000
Kilohertz | 1,000
Hertz | 1
Ampere | 1
Milliampere | 0.001
Microampere | 0.000001
Nanoampere | 0.000000001
Millions
Thousands
Hundreds
Tens
Tenths
Thousandths
Hundredths
Millionths
LARGER than
SMALLER than 1
1
109 106 103 102 101 100 10-1 10-2 10-3 10-6 10-9 10-12
G M k h da d c m µ n p
giga mega kilo hecto deca 0 deci centi milli micro nano pico

## Slide 42: T1B01 Which of the following frequency ranges are available for phone operation by Technician licensees?
A. 28.050 MHz to 28.150 MHz
B. 28.100 MHz to 28.300 MHz
C. 28.300 MHz to 28.500 MHz
D. 28.500 MHz to 28.600 MHz

## Slide 43: T1B01 Which of the following frequency ranges are available for phone operation by Technician licensees?
A. 28.050 MHz to 28.150 MHz
B. 28.100 MHz to 28.300 MHz
C. 28.300 MHz to 28.500 MHz
D. 28.500 MHz to 28.600 MHz

## Slide 44: T1B02 Which amateurs may contact the International Space Station (ISS) on VHF?
A. Any amateur holding a General class or higher license..
B. Any amateur holding a Technician or higher-class license
C. Any amateur holding a General class or higher license who has applied for and received approval from NSSA
D. Any amateur holding a Technician class or higher licenser who has applied for and received approval from NSSA

## Slide 45: T1B02 Which amateurs may contact the International Space Station (ISS) on VHF?
A. Any amateur holding a General class or higher license..
B. Any amateur holding a Technician or higher-class license
C. Any amateur holding a General class or higher license who has applied for and received approval from NSSA
D. Any amateur holding a Technician class or higher licenser who has applied for and received approval from NSSA

## Slide 46: T1B03 - Which frequency is in the 6 meter band?
A. 49.00 MHz
B. 52.525 MHz
C. 28.50 MHz
D. 222.15 MHz

## Slide 47: T1B03 - Which frequency is in the 6 meter band?
A. 49.00 MHz
B. 52.525 MHz
C. 28.50 MHz
D. 222.15 MHz
300
6m
f
f = 50 MHz
6m Band 50 to 54 MHz
What are you looking for?
What do you have?

## Slide 48: T1B04 - Which amateur band includes 146.52 MHz?
A. 6 meter
B. 20 meter
C. 70 centimeters
D. 2 meter

## Slide 49: T1B04 - Which amateur band includes 146.52 MHz?
A. 6 meters
B. 20 meters
C. 70 centimeters
D. 2 meters
300
m
146.52
m = 300 / 146.52
m = 2.0475
2 meter band
What are you looking for?
What do you have?

## Slide 50: T1B05 How may amateur use the 219 to 220 MHz segment of the 1.25 meter band?
A. Spread spectrum only
B. Fast-scan television only
C. Emergency traffic only
D. Fixed digital message forwarding systems only
~~

## Slide 51: T1B05 How may amateur use the 219 to 220 MHz segment of the 1.25 meter band?
A. Spread spectrum only
B. Fast-scan television only
C. Emergency traffic only
D. Fixed digital message forwarding systems only
~~
219 through 220 is not on many band charts

## Slide 52: Technician HF Privileges

## Slide 53: T1B06 On which HF bands does a Technician class operator have phone privileges?
A. None
B. 10 meter band only
C. 80 meter, 40 meter, 15 meter and 10 meter bands
D. 30 meter band only

## Slide 54: T1B06 On which HF bands does a Technician class operator have phone privileges?
A. None
B. 10 meter band only
C. 80 meter, 40 meter, 15 meter and 10 meter bands
D. 30 meter band only

## Slide 55: T1B07 Which of the following VHF/UHF band segments are limited to CW only?
A. 50.0 MHz to 50.1 MHz and 144.0 MHz to 144.1 MHz
B. 219 MHz to 220 MHz and 420.0 MHz to 420.1 MHz
C. 902.0 MHz to 902.1 MHZ
D. All of these choices are correct

## Slide 56: T1B07 Which of the following VHF/UHF band segments are limited to CW only?
A. 50.0 MHz to 50.1 MHz and 144.0 MHz to 144.1 MHz
B. 219 MHz to 220 MHz and 420.0 MHz to 420.1 MHz
C. 902.0 MHz to 902.1 MHZ
D. All of these choices are correct

## Slide 57: T1B08 How are US amateurs restricted in segmernts of bands where the Amateur Radio Service is secondary?
A. U.S. amateurs may find non-amateur stations in the bands, and must avoid interfering with them
B. U.S. amateurs must give foreign amateur stations priority in those segments
C. International communications are not permitted in those segments
D. Digital transmissions are not permitted in those segments

## Slide 58: T1B08 How are US amateurs restricted in segmernts of bands where the Amateur Radio Service is secondary?
A. U.S. amateurs may find non-amateur stations in the bands, and must avoid interfering with them
B. U.S. amateurs must give foreign amateur stations priority in those segments
C. International communications are not permitted in those segments
D. Digital transmissions are not permitted in those segments

## Slide 59: T1B09 - Why should you not set your transmit frequency to be exactly at the edge of an amateur band or sub-band?
A. To allow for calibration error in the transmitter frequency display
B. So that modulation sidebands do not extend beyond the band edge
C. To allow for transmitter frequency drift
D. All of these choices are correct

## Slide 60: T1B09 - Why should you not set your transmit frequency to be exactly at the edge of an amateur band or sub-band?
A. To allow for calibration error in the transmitter frequency display
B. So that modulation sidebands do not extend beyond the band edge
C. To allow for transmitter frequency drift
D. All of these choices are correct

## Slide 61: T1B10 Where may SSB phone be used in amateur bands above 50 MHz?
A. Only in sub-bands allocated to General class or higher licenses
B. Only on repeaters
C. In at least some segment of all these bands
D. On any band if the power is limited to 25 watts.

## Slide 62: T1B10 Where may SSB phone be used in amateur bands above 50 MHz?
A. Only in sub-bands allocated to General class or higher licenses
B. Only on repeaters
C. In at least some segment of all these bands
D. On any band if the power is limited to 25 watts.

## Slide 63: T1B11 What is the maximum peak envelope power output for Technician class operators in their HF band segments?
A. 200 watts
B. 100 watts
C. 50 watts
D. 10 watts

## Slide 64: T1B11 What is the maximum peak envelope power output for Technician class operators in their HF band segments?
A. 200 watts
B. 100 watts
C. 50 watts
D. 10 watts

## Slide 65: T1B12 Except for some specific restrictions, what is the maximum peak envelope power output for Technician class operators using frequencies above 30 MHz?
A. 50 watts
B. 100 watts
C. 500 watts
D. 1500 watts

## Slide 66: T1B12 Except for some specific restrictions, what is the maximum peak envelope power output for Technician class operators using frequencies above 30 MHz?
A. 50 watts
B. 100 watts
C. 500 watts
D. 1500 watts

## Slide 67: Section T1C
Licensing: classes, sequential and vanity call sign systems, places where the Amateur Radio Service is regulated by the FCC, name and address on FCC license database, term, renewal, grace period, maintaining mailing address; International communications

## Slide 68: ITU Regions

## Slide 69
Callsign Groups
All valid US Callsigns start with
A, K, N or W and contain a digit 0-9
Group A | 1x2, 2x1 W1AW, KU7M
Group B | 2x2 KK7LK
Group C | 1x3 N7WSU
Group D | 2x3 KB7PJM

## Slide 70: US Call Districts

## Slide 71: Other Call Sign Categories
Vanity Call Sign
  Custom call sign chosen by you
  Can be any valid callsign available to your license class
Club Call Sign
  Call sign for your club
  Can be any valid callsign available to the trustee
Special Event Call Sign
  1x1 – N8D
  Valid only for the duration of the event
  Available to any amateur licensee

## Slide 72: FCC Amateur License

## Slide 73: T1C01 For which license classes are new licenses currently available from the FCC?
A. Novice, Technician, General, Advanced
B. Technician, Technician Plus, General, Advanced
C. Novice, Technician Plus, General, Advanced
D. Technician, General, Amateur Extra

## Slide 74: T1C01 For which license classes are new licenses currently available from the FCC?
A. Novice, Technician, General, Advanced
B. Technician, Technician Plus, General, Advanced
C. Novice, Technician Plus, General, Advanced
D. Technician, General, Amateur Extra

## Slide 75: T1C02 Who may select a desired call sign under the vanity call sign rules?
A. Only a licensed amateur with a General or Amateur Extra class license
B. Only a licensed amateur with an Amateur Extra class license
C. Only a licensed amateur who has been licensed continuously for more than 10 years
D. Any licensed amateur

## Slide 76: T1C02 Who may select a desired call sign under the vanity call sign rules?
A. Only a licensed amateur with a General or Amateur Extra class license
B. Only a licensed amateur with an Amateur Extra class license
C. Only a licensed amateur who has been licensed continuously for more than 10 years
D. Any licensed amateur

## Slide 77: T1C03 What types of international communications is an FCC-licensed amateur radio station permitted to make?
A. Communications incidental to the purposes of the Amateur Radio Service and remarks of a personal character
B. Communications incidental to conducting business or remarks of a personal nature
C. Only communications incidental to contest exchanges, all other communications are prohibited
D. Any communications that would be permitted by an international broadcast station

## Slide 78: T1C03 What types of international communications is an FCC-licensed amateur radio station permitted to make?
A. Communications incidental to the purposes of the Amateur Radio Service and remarks of a personal character
B. Communications incidental to conducting business or remarks of a personal nature
C. Only communications incidental to contest exchanges, all other communications are prohibited
D. Any communications that would be permitted by an international broadcast station

## Slide 79: T1C04 – What may happen if the FCC is unable to reach you by email?
Fine and suspension of operator license
Revocation of the station license or suspension of the operator license
Revocation of access to the license record in the FCC system
Nothing, there is no such requirement

## Slide 80: T1C04 – What may happen if the FCC is unable to reach you by email?
Fine and suspension of operator license
Revocation of the station license or suspension of the operator license
Revocation of access to the license record in the FCC system
Nothing, there is no such requirement

## Slide 81: T1C05 Which of the following is a valid Technician call sign format?
A. KF1XXX
B. KA1X
C. W1XX
D. All of these choices are correct

## Slide 82: T1C05 Which of the following is a valid Technician call sign format?
A. KF1XXX
B. KA1X
C. W1XX
D. All of these choices are correct

## Slide 83: T1C06 From which of the following locations may an FCC-licensed amateur station transmit?
A. From within any country that belongs to the International Telecommunications Union
B. From within any country that is a member of the United Nations
C. From anywhere within in International Telecommunication Union (ITU) Regions 2 and 3
D. From any vessel or craft located in international waters and documented or registered in the United States

## Slide 84: T1C06 From which of the following locations may an FCC-licensed amateur station transmit?
A. From within any country that belongs to the International Telecommunications Union
B. From within any country that is a member of the United Nations
C. From anywhere within in International Telecommunication Union (ITU) Regions 2 and 3
D. From any vessel or craft located in international waters and documented or registered in the United States

## Slide 85: T1C07 – Which of the following can result in revocation of the station license or suspension of the operator license?
A. Failure to inform the FCC of any changes in the amateur station following performance of an RF safety. Environmental evaluation
B. Failure to provide and maintain a correct email address with the FCC
C. Failure to obtain FCC type acceptance prior to using a home-built transmitter
D. Failure to have a copy of your license available at your station

## Slide 86: T1C07 – Which of the following can result in revocation of the station license or suspension of the operator license?
A. Failure to inform the FCC of any changes in the amateur station following performance of an RF safety. Environmental evaluation
B. Failure to provide and maintain a correct email address with the FCC
C. Failure to obtain FCC type acceptance prior to using a home-built transmitter
D. Failure to have a copy of your license available at your station

## Slide 87: T1C08 - What is the normal term for an FCC-issued primary amateur radio license?
A. Five years
B. Life
C. Ten years
D. Twenty years

## Slide 88: T1C08 - What is the normal term for an FCC-issued primary amateur radio license?
A. Five years
B. Life
C. Ten years
D. Twenty years

## Slide 89: T1C09 - What is the grace period for renewal if an amateur license expires?
A. Two years
B. Three years
C. Five years
D. Ten years

## Slide 90: T1C09 - What is the grace period for renewal if an amateur license expires?
A. Two years
B. Three years
C. Five years
D. Ten years

## Slide 91: T1C10 - How soon after passing the examination for your first amateur radio license may you transmit on the amateur radio bands?
A. Immediately on receiving your Certificate of Successful Completion of Examination (CSCE)
B. As soon as your operator/ststion license grant appears on the ARRL website
C. As soon as your operator/station license grant appears in the FCC’s license database
D. As soon as you receive your license in the mail from the FCC

## Slide 92: T1C10 - How soon after passing the examination for your first amateur radio license may you transmit on the amateur radio bands?
A. Immediately on receiving your Certificate of Successful Completion of Examination (CSCE)
B. As soon as your operator/ststion license grant appears on the ARRL website
C. As soon as your operator/station license grant appears in the FCC’s license database
D. As soon as you receive your license in the mail from the FCC

## Slide 93: T1C11 - If your license has expired and is still within the allowable grace period, may you continue to transmit on the amateur radio bands?
A. Yes, for up to to years
B. Yes, as soon as you apply for a renewal
C. Yes, for up to one year
D. No, you must wait until the license has been renewed

## Slide 94: T1C11 - If your license has expired and is still within the allowable grace period, may you continue to transmit on the amateur radio bands?
A. Yes, for up to to years
B. Yes, as soon as you apply for a renewal
C. Yes, for up to one year
D. No, you must wait until the license has been renewed

## Slide 95: Section T1D Authorized and prohibited transmission: communications with other countries; music; exchange of information with other services; indecent language; compensation for operating; retransmission of other amateur signals; encription; sale of equipment; unidentified transmissions; one-way transmission

## Slide 96: T1D01 - With which countries are FCC-licensed amateur radio stations prohibited from exchanging communications?
A. Any country whose administration has notified the International Telecommunication Union (ITU) that it objects to such communications
B. Any country whose administration has notified the American Radio Relay League (ARRL) that it objects to such communications
C. Any country banned from such communication by the International Amateur Radio Union (IARU)
D. Any country banned from making such communication by the American Radio Relay League (ARRL)

## Slide 97: T1D01 - With which countries are FCC-licensed amateur radio stations prohibited from exchanging communications?
A. Any country whose administration has notified the International Telecommunication Union (ITU) that it objects to such communications
B. Any country whose administration has notified the American Radio Relay League (ARRL) that it objects to such communications
C. Any country banned from such communication by the International Amateur Radio Union (IARU)
D. Any country banned from making such communication by the American Radio Relay League (ARRL)

## Slide 98: T1D02 Under which of the following circumstances are one-way transmissions by amateur station prohibited?
In all circumstances
Broadcasting
International Morse Code Practice
Telecommand or transmissions of telemetry

## Slide 99: T1D02 Under which of the following circumstances are one-way transmissions by amateur station prohibited?
In all circumstances
Broadcasting
International Morse Code Practice
Telecommand or transmissions of telemetry

## Slide 100: T1D03 When is it permissible to transmit messages encoded to hide their meaning?
A. Only during contests
B. Only when transmitting cxwetrrain approved digital codes
C. Only when transmitting control commands to space stations or radio control craft
D. Never

## Slide 101: T1D03 When is it permissible to transmit messages encoded to hide their meaning?
A. Only during contests
B. Only when transmitting cxwetrrain approved digital codes
C. Only when transmitting control commands to space stations or radio control craft
D. Never

## Slide 102: T1D04 Under what conditions is an amateur station authorized to transmit music using a phone emission?
A. When incidental to an authorized retransmission of manned spacecraft communications
B. When the music produces no spurious emissions
C. When transmissions are limited to less than three minutes per hour
D When the music is transmitted above 1280 MHz

## Slide 103: T1D04 Under what conditions is an amateur station authorized to transmit music using a phone emission?
A. When incidental to an authorized retransmission of manned spacecraft communications
B. When the music produces no spurious emissions
C. When transmissions are limited to less than three minutes per hour
D When the music is transmitted above 1280 MHz

## Slide 104: T1D05 When may amateur radio operators use their stations to notify other amateurs of the availability of equipment for sale or trade?
Never
When the equipment is not the personal property of either the station licensee, or the control; operator, or their close relatives.
When no profit is made on the sale.
When selling amateur equipment and not on a regular basis

## Slide 105: T1D05 When may amateur radio operators use their stations to notify other amateurs of the availability of equipment for sale or trade?
Never
When the equipment is not the personal property of either the station licensee, or the control; operator, or their close relatives.
When no profit is made on the sale.
When selling amateur equipment and not on a regular basis

## Slide 106: T1D06 - What, if any, are the restrictions concerning transmission of language that may be considered indecent or obscene?
A. The FCC maintains a list of words that are not permitted to be used on amateur frequencies
B. Any such language is prohibited
C. The ITU maintains a list of words that are not permitted to be used on amateur frequencies
D. There is no such prohibition

## Slide 107: T1D06 - What, if any, are the restrictions concerning transmission of language that may be considered indecent or obscene?
A. The FCC maintains a list of words that are not permitted to be used on amateur frequencies
B. Any such language is prohibited
C. The ITU maintains a list of words that are not permitted to be used on amateur frequencies
D. There is no such prohibition

## Slide 108: Station Control
Control Operator
Licensed amateur responsible for proper station operation
Control Point
The point at which the Control Operator function is performed
Local - Control operator has hands on control point
Remote – Control operator uses a link: phone, Internet, or Skype
Automatic Control - Using a Repeater

## Slide 109: T1D07 - What types of amateur stations can automatically retransmit the signals of other amateur stations?
A. Auxiliary, beacon, or Earth stations
B. Earth, repeater, or space stations
C. Beacon, repeater, or space stations
D. Auxiliary, repeater, or space stations

## Slide 110: T1D07 - What types of amateur stations can automatically retransmit the signals of other amateur stations?
A. Auxiliary, beacon, or Earth stations
B. Earth, repeater, or space stations
C. Beacon, repeater, or space stations
D Auxiliary, repeater, or space stations

## Slide 111: T1D08 In which of the following circumstances may the control operator of an amateur station receive compensation for operating that station?
A. When the communication is related to the sale of amateur equipment by the control operator's employer
B. When the communication is incidental to classroom instruction at an educational institution
C. When the communication is made to obtain emergency information for a local broadcast station
D. All of these choices are correct

## Slide 112: T1D08 In which of the following circumstances may the control operator of an amateur station receive compensation for operating that station?
A. When the communication is related to the sale of amateur equipment by the control operator's employer
B. When the communication is incidental to classroom instruction at an educational institution
C. When the communication is made to obtain emergency information for a local broadcast station
D. All of these choices are correct

## Slide 113: T1D09 When may amateur stations transmit information in support of broadcasting, program production, or news gathering, assuming no other means is available?
A. When such communications are directly related to the immediate safety of human life or protection of property
B. When broadcasting communications to or from the space shuttle
C. When noncommercial programming is gathered and supplied exclusively to the National Public Radio network
D. Never

## Slide 114: T1D09 When may amateur stations transmit information in support of broadcasting, program production, or news gathering, assuming no other means is available?
A. When such communications are directly related to the immediate safety of human life or protection of property
B. When broadcasting communications to or from the space shuttle
C. When noncommercial programming is gathered and supplied exclusively to the National Public Radio network
D. Never

## Slide 115: T1D10 How does the FCC define broadcasting for the Amateur Radio Service?
A. Two-way transmissions by amateur stations
B. Any transmission made by the licensed station
C. Transmission of messages directed only to amateur operators
D. Transmissions intended for reception by the general public

## Slide 116: T1D10 How does the FCC define broadcasting for the Amateur Radio Service?
A. Two-way transmissions by amateur stations
B. Any transmission made by the licensed station
C. Transmission of messages directed only to amateur operators
D. Transmissions intended for reception by the general public

## Slide 117: T1D11 When may an amateur station transmit without identifying on the air?
A. When the transmissions are of a brief nature to make station adjustments
B. When the transmissions are unmodulated
C. When the transmitted power level is below 1 watt
D. When transmitting signals to control model craft

## Slide 118: T1D11 When may an amateur station transmit without identifying on the air?
A. When the transmissions are of a brief nature to make station adjustments
B. When the transmissions are unmodulated
C. When the transmitted power level is below 1 watt
D. When transmitting signals to control model craft

## Slide 119: Section T1E Control operator: eligibility, designating, privileges, duties, location, required; Control point; Control types: automatic, remote

## Slide 120: T1E01 - When is an amateur station permitted to transmit without a control operator?
A. When using automatic control, such as in the case of a repeater
B. When the station licensee is away and another licensed amateur is using the station
C. When the transmitting station is an auxiliary station
D. Never

## Slide 121: T1E01 - When is an amateur station permitted to transmit without a control operator?
A. When using automatic control, such as in the case of a repeater
B. When the station licensee is away and another licensed amateur is using the station
C. When the transmitting station is an auxiliary station
D. Never

## Slide 122: T1E02 Who may be the control operator of a station communicating through an amateur satellite or space station?
A. Only an Amateur Extra Class operator
B. A General class or higher licensee who has a satellite operator certification
C. Only an Amateur Extra Class operator who is also an AMSAT member
D. Any amateur whose license privileges allow them to transmit on the satellite uplink frequency

## Slide 123: T1E02 Who may be the control operator of a station communicating through an amateur satellite or space station?
A. Only an Amateur Extra Class operator
B. A General class or higher licensee who has a satellite operator certification
C. Only an Amateur Extra Class operator who is also an AMSAT member
D. Any amateur whose license privileges allow them to transmit on the satellite uplink frequency

## Slide 124: T1E03 - Who must designate the station control operator?
A. The station licensee
B. The FCC
C. The frequency coordinator
D. Any licensed operator

## Slide 125: T1E03 - Who must designate the station control operator?
A. The station licensee
B. The FCC
C. The frequency coordinator
D. Any licensed operator

## Slide 126: T1E04 What determines the transmitting privileges of an amateur station?
A. The frequency authorized by the frequency coordinator
B. The frequencies printed on the license grant
C. The highest class of operator license held by anyone on the premises
D. The class of operator license held by the control operator

## Slide 127: T1E04 What determines the transmitting privileges of an amateur station?
A. The frequency authorized by the frequency coordinator
B. The frequencies printed on the license grant
C. The highest class of operator license held by anyone on the premises
D. The class of operator license held by the control operator

## Slide 128: T1E05 - What is an amateur station’s control point?
A. The location of the station’s transmitting antenna
B. The location of the station transmitting apparatus
C. The location at which the control operator function is performed
D. The mailing address of the station licensee

## Slide 129: T1E05 - What is an amateur station’s control point?
A. The location of the station’s transmitting antenna
B. The location of the station transmitting apparatus
C. The location at which the control operator function is performed
D. The mailing address of the station licensee

## Slide 130: T1E06 When, under normal circumstances, may a Technician class licensee be the control operator of a station operating in an Amateur Extra class band segment?
A. At no time
B. When designated as the control operator by an Amateur extra Class licensee
C. As part of a multi-operator contest team
D. When using a club station whose trustee holds an Amateur Extra class licensee

## Slide 131: T1E06 When, under normal circumstances, may a Technician class licensee be the control operator of a station operating in an Amateur Extra class band segment?
A. At no time
B. When designated as the control operator by an Amateur extra Class licensee
C. As part of a multi-operator contest team
D. When using a club station whose trustee holds an Amateur Extra class licensee

## Slide 132: T1E07 - When the control operator is not the station licensee, who is responsible for the proper operation of the station?
A. All licensed amateurs who are present at the operation
B. Only the station licensee
C. Only the control operator
D. The control operator and the station licensee are equally responsible

## Slide 133: T1E07 - When the control operator is not the station licensee, who is responsible for the proper operation of the station?
A. All licensed amateurs who are present at the operation
B. Only the station licensee
C. Only the control operator
D. The control operator and the station licensee are equally responsible

## Slide 134: T1E08 - Which of the following is an example of automatic control?
A. Repeater operation
B. Controlling the station over the Internet
C. Using a computer or other device to send CW automatically
D. Using a computer or other device to identify automatically

## Slide 135: T1E08 - Which of the following is an example of automatic control?
A. Repeater operation
B. Controlling the station over the Internet
C. Using a computer or other device to send CW automatically
D. Using a computer or other device to identify automatically

## Slide 136: T1E09 Which of the following are required for remote control operation?
A. The control operator must be at the control point
B. A control operator is required at all times
C. The control operator indirectly manipulates the controls
D. All these choices are correct

## Slide 137: T1E09 Which of the following are required for remote control operation?
A. The control operator must be at the control point
B. A control operator is required at all times
C. The control operator indirectly manipulates the controls
D. All these choices are correct

## Slide 138: T1E10 - Which of the following is an example of remote control as defined in Part 97?
A. Repeater operation
B. Operating the station over the Internet
C. Controlling a model aircraft, boat or car by amateur radio
D. All of these choices are correct

## Slide 139: T1E10 - Which of the following is an example of remote control as defined in Part 97?
A. Repeater operation
B. Operating the station over the Internet
C. Controlling a model aircraft, boat or car by amateur radio
D. All of these choices are correct

## Slide 140: T1E11 - Who does the FCC presume to be the control operator of an amateur station, unless documentation to the contrary is in the station records?
A. The station custodian
B. The third party participant
C. The person operating the station equipment
D. The station licensee

## Slide 141: T1E11 - Who does the FCC presume to be the control operator of an amateur station, unless documentation to the contrary is in the station records?
A. The station custodian
B. The third party participant
C. The person operating the station equipment
D. The station licensee

## Slide 142: Section T1F Station identification; repeaters; third-party communications; club stations; FCC inspection

## Slide 143: T1F01 When must the station and its records be available for FCC inspection?
A. At any time ten days after notification by the FCC of such an inspection
B. At any time upon request by an FCC representative
C. At any time after written notification by the FCC of such inspection
D. Only when presented with a valid warrant by an FCC official or government agent

## Slide 144: T1F01 When must the station and its records be available for FCC inspection?
A. At any time ten days after notification by the FCC of such an inspection
B. At any time upon request by an FCC representative
C. At any time after written notification by the FCC of such inspection
D. Only when presented with a valid warrant by an FCC official or government agent

## Slide 145: T1F02 How often must you identify with your FCC assigned call sign when using tactical call signs such as “Race Headquarters”?
A. Never, the tactical call is sufficient
B. Once during every hour
C. At the end of each communication and every ten minutes during a communication
D. At the end of every transmission

## Slide 146: T1F02 How often must you identify with your FCC assigned call sign when using tactical call signs such as “Race Headquarters”?
A. Never, the tactical call is sufficient
B. Once during every hour
C. At the end of each communication and every ten minutes during a communication
D. At the end of every transmission

## Slide 147: T1F03 - When are you required to transmit its assigned call sign?
A. At the beginning of each contact, and every 10 minutes thereafter
B. At least once during each transmission
C. At least every 15 minutes during and at the end of a communication
D. At least every 10 minutes during and at the end of a communication

## Slide 148: T1F03 - When are you required to transmit its assigned call sign?
A. At the beginning of each contact, and every 10 minutes thereafter
B. At least once during each transmission
C. At least every 15 minutes during and at the end of a communication
D. At least every 10 minutes during and at the end of a communication

## Slide 149: T1F04 - What language may you use for identification when operating in a phone sub-band?
A. Any language recognized by the United Nations
B. Any language recognized by the ITU
C. The English language
D. English, French, or Spanish

## Slide 150: T1F04 - What language may you use for identification when operating in a phone sub-band?
A. Any language recognized by the United Nations
B. Any language recognized by the ITU
C. The English language
D. English, French, or Spanish

## Slide 151: T1F05 - What method of call sign identification is required for a station transmitting phone signals?
A. Send the call sign followed by the indicator RPT
B. Send the call sign using CW or phone emission
C. Send the call sign followed by the indicator R
D. Send the call sign using only phone emission

## Slide 152: T1F05 - What method of call sign identification is required for a station transmitting phone signals?
A. Send the call sign followed by the indicator RPT
B. Send the call sign using CW or phone emission
C. Send the call sign followed by the indicator R
D. Send the call sign using only phone emission

## Slide 153: T1F06 - Which of the following self-assigned indicator are acceptable when using a phone transmission?
A. KL7CC stroke W3
B. KL7CC slant W3
C. KL7CC slash W3
D. All of these choices are correct

## Slide 154: T1F06 - Which of the following self-assigned indicator are acceptable when using a phone transmission?
A. KL7CC stroke W3
B. KL7CC slant W3
C. KL7CC slash W3
D. All of these choices are correct

## Slide 155: T1F07 - Which of the following restrictions apply when a non-licensed person is allowed to speak to a foreign station using a station under the control of a licensed amateur operator?
A. The person must be a U.S. citizen
B. The foreign station must be one with which the U.S. has a third party agreement
C. The licensed control operator must do the station identification
D. All of these choices are correct

## Slide 156: T1F07 - Which of the following restrictions apply when a non-licensed person is allowed to speak to a foreign station using a station under the control of a licensed amateur operator?
A. The person must be a U.S. citizen
B. The foreign station must be one with which the U.S. has a third party agreement
C. The licensed control operator must do the station identification
D. All of these choices are correct

## Slide 157: US Amateurs May Handle Third-Party Traffic With:
V2 | Antigua/Barbuda
LO-LW | Argentina
VK | Australia
V3 | Belize
CP | Bolivia
E7 | Bosnia-Herzegovina
PP-PY | Brazil
VE, VO, VY | Canada
CA-CE | Chile
HJ-HK | Colombia
D6 | Comoros (Federal Islamic Republic of)
TI, TE | Costa Rica
CM, CO | Cuba
HI | Dominican Republic
J7 | Dominica
HC-HD | Ecuador
YS | El Salvador
C5 | Gambia, The
9G | Ghana
J3 | Grenada
TG | Guatemala
8R | Guyana
HH | Haiti
HQ-HR | Honduras
4X, 4Z | Israel
6Y | Jamaica
JY | Jordan
EL | Liberia
V7 | Marshall Islands
XA-XI | Mexico
V6 | Micronesia, Federated States of
YN | Nicaragua
HO-HP | Panama
ZP | Paraguay
OA-OC | Peru
DU-DZ | Philippines
VR6 | Pitcairn Island*
V4 | St. Kitts/Nevis
J6 | St. Lucia
J8 | St. Vincent and the Grenadines
9L | Sierra Leone
ZR-ZU | South Africa
3DA | Swaziland
9Y-9Z | Trinidad/Tobago
TA-TC | Turkey
GB | United Kingdom
CV-CX | Uruguay
YV-YY | Venezuela
4U1ITU | ITU - Geneva
4U1VIC | VIC - Vienna
http://www.arrl.org/third-party-operating-agreements

## Slide 158: T1F08 What is the definition of third party communications?
A. A message from a control operator to another amateur station control operator on behalf of another person
B. Amateur radio communications where three stations are in communications with one another
C. Operation when the transmitting equipment is licensed to a person other than the control operator
D. Temporary authorization for an unlicensed person to transmit on the amateur bands for technical experiments

## Slide 159: T1F08 What is the definition of third party communications?
A. A message from a control operator to another amateur station control operator on behalf of another person
B. Amateur radio communications where three stations are in communications with one another
C. Operation when the transmitting equipment is licensed to a person other than the control operator
D. Temporary authorization for an unlicensed person to transmit on the amateur bands for technical experiments

## Slide 160: T1F09 - What type of amateur station simultaneously retransmits the signal of another amateur station on a different channel or channels?
A. Beacon station
B. Earth station
C. Repeater station
D. Message forwarding station

## Slide 161: T1F09 - What type of amateur station simultaneously retransmits the signal of another amateur station on a different channel or channels?
A. Beacon station
B. Earth station
C. Repeater station
D. Message forwarding station

## Slide 162: T1F10 - Who is accountable should a repeater inadvertently retransmit communications that violate the FCC rules?
A. The control operator of the originating station
B. The control operator of the repeater
C. The owner of the repeater
D. Both the originating station and the repeater owner

## Slide 163: T1F10 - Who is accountable should a repeater inadvertently retransmit communications that violate the FCC rules?
A. The control operator of the originating station
B. The control operator of the repeater
C. The owner of the repeater
D. Both the originating station and the repeater owner

## Slide 164: T1F11 Which of the following is a requirement for the issuance of a club station license grant?
A. The trustee must have an Amateur Extra class operator license grant
B. The club must have at least four members
C. The club must be registered with the American Radio Relay League
D. All of these choices are correct

## Slide 165: T1F11 Which of the following is a requirement for the issuance of a club station license grant?
A. The trustee must have an Amateur Extra class operator license grant
B. The club must have at least four members
C. The club must be registered with the American Radio Relay League
D. All of these choices are correct

## Slide 166: End of SUBELEMENT T1 – FCC Rules,