## Slide 1: SUBELEMENT T5
Electrical principles: math for electronics; electronic principles; Ohm’s Law
[4 Exam Questions - 4 Groups]
Notes: Subelement T5 FCC Electrical Principles. Technician Training Slides for 2022 Question Pool Good through June 30, 2026 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM.

## Slide 2
T5A – Current and voltage: terminology and units; conductors and insolators, alternating and direct current
T5B - Math for electronics: conversion of electrical units; decibels
T5C – Capacitance and inductance terminology and units: Radio frequency definition and units; Impedance definition and units; Calculating power
T5D – Ohm’s Law: Series and parallel circuits

## Slide 3
Electrical Principles 2010
3
Conductors and Insulators
In a conductor, electric current can flow freely, in an insulator it cannot. Simply stated, most metals are good electrical conductors, most nonmetals are not. Metals are also generally good heat conductors while nonmetals are not.
Conductors – Copper, Silver, Gold, Aluminum, Platinum, Steel, …
Insulators – Glass, Wood, Rubber, Air, Plastic …
Note: Salt water is a
conductor, and so are you!
Cu
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
Neighboring electrons are repulsed by the motion of electrons, creating a chain reaction that propagates through the material at nearly the speed of light.
Cross- section of copper wire
Copper’s valence electrons move freely throughout the solid copper metal
Copper and other metals have a weak hold on their outer or “valence” electrons. Atoms of insulating materials have a tight grip on their outer electrons.

## Slide 4
Voltage, Current, Resistance
+
-
Voltage
Current
Resistance (Load)
You need a circuit for electricity to flow
Components of a circuit: Source, Conductors, Load, Sink (Ground)
Notes: 4
Voltage is also called Electromotive Force and is an electrical “pressure”. Current is a measure of the flow of electrons (volume) from the negative to positive poles. The load presents resistance to the flow of electrons. Voltage is measured across the positive and negative poles (in parallel) to measure the difference in “pressure”. To measure the electron flow, the meter must be placed in-line (in series) with the flow.
Direct Current (DC) is a constant voltage source that causes current to flow in only one direction and has a positive and negative pole – like a battery. Alternating Current is what is available in the wall and the constantly changing polarity causes current to alternate directions.

## Slide 5
Units of Measure
Power | Watt
Resistance | Ohm
Voltage | Volt
Current | Ampere
Frequency | Hertz
Inductance | Henry (AC ohms)
Capactance | Farad (AC ohms)

## Slide 6: T5A01 - Electrical current is measured in which of the following units?
A. Volts
B. Watts
C. Ohms
D. Amperes

## Slide 7: T5A01 - Electrical current is measured in which of the following units?
A. Volts
B. Watts
C. Ohms
D. Amperes

## Slide 8: T5A02 - Electrical power is measured in which of the following units?
A. Volts
B. Watts
C. Ohms
D. Amperes

## Slide 9: T5A02 - Electrical power is measured in which of the following units?
A. Volts
B. Watts
C. Ohms
D. Amperes

## Slide 10: T5A03 - What is the name for the flow of electrons in an electric circuit?
A. Voltage
B. Resistance
C. Capacitance
D. Current

## Slide 11: T5A03 - What is the name for the flow of electrons in an electric circuit?
A. Voltage
B. Resistance
C. Capacitance
D. Current

## Slide 12: T5A04 - What are the units of electrical resistance?
A. Siemens
B. Mhos
C. Ohms
D. Coulombs

## Slide 13: T5A04 - What are the units of electrical resistance?
A. Siemens
B. Mhos
C. Ohms
D. Coulombs

## Slide 14: T5A05 What is the electrical term for the force that causes electron flow?
A. Voltage
B. Ampere-hours
C. Capacitance
D. Inductance

## Slide 15: T5A05 What is the electrical term for the force that causes electron flow?
A. Voltage
B. Ampere-hours
C. Capacitance
D. Inductance

## Slide 16: T5A06 – What is the unit of frequency?
A. Hertz
B. Henry
C. Farad
D. Tesla

## Slide 17: T5A06 – What is the unit of frequency?
A. Hertz
B. Henry
C. Farad
D. Tesla

## Slide 18
Conductors and Insulators
In a conductor, electric current can flow freely, in an insulator it cannot. Simply stated, most metals are good electrical conductors, most nonmetals are not. Metals are also generally good heat conductors while nonmetals are not.
Conductors – Copper, Silver, Gold, Aluminum, Platinum, Steel, …
Insulators – Glass, Wood, Rubber, Air, Plastic …
Note: Salt water is a
conductor, and so are you!
Cu
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
Neighboring electrons are repulsed by the motion of electrons, creating a chain reaction that propagates through the material at nearly the speed of light.
Cross- section of copper wire
Copper’s valence electrons move freely throughout the solid copper metal
Copper and other metals have a weak hold on their outer or “valence” electrons. Atoms of insulating materials have a tight grip on their outer electrons.

## Slide 19: T5A07 – Why are metals generally good conductors of electricity?
A. They have relative high density
B. They have many free electrons
C. They have many free protons
D. All these choices are correct

## Slide 20: T5A07 – Why are metals generally good conductors of electricity?
A. They have relative high density
B. They have many free electrons
C. They have many free protons
D. All these choices are correct

## Slide 21: T5A08 - Which of the following is a good electrical insulator?
A. Copper
B. Glass
C. Aluminum
D. Mercury

## Slide 22: T5A08 - Which of the following is a good electrical insulator?
A. Copper
B. Glass
C. Aluminum
D. Mercury

## Slide 23
Direct Current Alternating Current
DC
Current flows in one direction only
  Examples:
    Battery Operated Devices
    Cars
AC
Current flows in both directions, voltage and current very with time
  Example: House Wiring
DC
AC
AC

## Slide 24: T5A09 – Which of the following describes alternating current?
A. Current that alternates between a positive direction and zero
B. Current that alternates between a negative direction and zero
C. Current that alternates between positive and negative directions
D. All these answers are correct

## Slide 25: T5A09 – Which of the following describes alternating current?
A. Current that alternates between a positive direction and zero
B. Current that alternates between a negative direction and zero
C. Current that alternates between positive and negative directions
D. All these answers are correct

## Slide 26: T5A10 - Which term describes the rate at which electrical energy is used?
A. Resistance
B. Current
C. Power
D. Voltage

## Slide 27: T5A10 - Which term describes the rate at which electrical energy is used?
A. Resistance
B. Current
C. Power
D. Voltage

## Slide 28: T5A11 – What type of current flow is opposed by resistance?
A. Direct current
B. Alternating current
C. RF current
D. Al these choices are correct

## Slide 29: T5A11 – What type of current flow is opposed by resistance?
A. Direct current
B. Alternating current
C. RF current
D. Al these choices are correct

## Slide 30: T5A12 - What describes the number of times per second that an alternating current makes a complete cycle?
A. Pulse rate
B. Speed
C. Wavelength
D. Frequency

## Slide 31: T5A12 - What describes the number of times per second that an alternating current makes a complete cycle?
A. Pulse rate
B. Speed
C. Wavelength
D. Frequency

## Slide 32: T5B - Math for electronics
conversion of electrical units; decibels;

## Slide 33
System of Metric Units
giga G 109 1,000,000,000.0 f
Mega M 106 1,000,000.0 f Ω
kilo K 103 1,000.0 f Ω kV kW
basic unit 100 1.0 f Ω V W
milli m 10-3 mh mV 0.001
Micro µ 10-6 µh µV µf 0.000 001
nano n 10-9 0.000 000 001
pico p 10-12 picofarads 0.000 000 000 001
Ω
Ω

## Slide 34
109 106 103 102 101 100 10-1 10-2 10-3 10-6 10-9 10-12
G M k h da d c m µ n p
giga mega kilo hecto deca 0 deci centi milli micro nano pico
Metric Units of Measure
Gigahertz | 1,000,000,000
Megahertz | 1,000,000
Kilohertz | 1,000
Hertz | 1
Ampere | 1
Milliampere | 0.001
Microampere | 0.000001
Nanoampere | 0.000000001
Billions
Millions
Thousands
Hundreds
Tens
Tenths
Thousandths
Hundredths
Millionths
Trillionths
Billionths
LARGER than
SMALLER than 1
1
Notes: 34
Note the shift in decimal places. This is standard metric notation. 1 Gigahertz is 1 Billion Hertz and a Nanoampere is 1 Billionth of an Ampere.

## Slide 35: T5B01 - How many milliamperes is 1.5 amperes?
A. 15 milliamperes
B. 150 milliamperes
C. 1,500 milliamperes
D. 15,000 milliamperes

## Slide 36: T5B01 - How many milliamperes is 1.5 amperes?
A. 15 milliamperes
B. 150 milliamperes
C. 1,500 milliamperes
D. 15,000 milliamperes
Ampere | 1
Milliampere | 0.001
Microampere | 0.000 001
Nanoampere | 0.000 000 001

## Slide 37: T5B02 - What is another way to specify a radio signal frequency of 1,500,000 hertz?
A. 1500 kHz
B. 1500 MHz
C. 15 GHz
D. 150 kHz

## Slide 38: T5B02 - What is another way to specify a radio signal frequency of 1,500,000 hertz?
A. 1500 kHz
B. 1500 MHz
C. 15 GHz
D. 150 kHz
Gigahertz | 1,000,000,000
Megahertz | 1,000,000
Kilohertz | 1,000
Hertz | 1

## Slide 39: T5B03 – Which is equal to one kilovolt?
A. One one-thousandth of a volt
B. One hundred volts
C. One thousand volts
D. One million volts

## Slide 40: T5B03 – Which is equal to one kilovolt?
A. One one-thousandth of a volt
B. One hundred volts
C. One thousand volts
D. One million volts
MegaVolts | 1,000,000
KiloVolts | 1,000
Volts | 1

## Slide 41: T5B04 – Which is equal to one microvolt?
A. One one-millionth of a volt
B. One million volts
C. One thousand kilovolts
D. One one-thousandth of a volt

## Slide 42: T5B04 – Which is equal to one microvolt?
A. One one-millionth of a volt
B. One million volts
C. One thousand kilovolts
D. One one-thousandth of a volt
Volts | 1
MilliVolts | 0.001
MicroVolts | 0.000 001

## Slide 43: T5B05 - Which is equal to 500 milliwatts?
A. 0.02 watts
B. 0.5 watts
C. 5 watts
D. 50 watts

## Slide 44: T5B05 - Which is equal to 500 milliwatts?
A. 0.02 watts
B. 0.5 watts
C. 5 watts
D. 50 watts
Watts | 1
Milliwatts | 0.001
Microwatts | 0.000 001

## Slide 45: T5B06 – Which is equal to 3000-milliampere?
A. 0.003 amperes
B. 0.3 amperes
C. 3,000,000 amperes
D. 3 amperes

## Slide 46: T5B06 – Which is equal to 3000-milliampere?
A. 0.003 amperes
B. 0.3 amperes
C. 3,000,000 amperes
D. 3 amperes
Ampere | 1
Milliampere | 0.001
Microampere | 0.000 001
Nanoampere | 0.000 000 001

## Slide 47: T5B07 – Which is equal to 3.525 MHz?
A. 0.003525 kHz
B. 35.25 kHz
C. 3525 kHz
D. 3,525,000 kHz

## Slide 48: T5B07 – Which is equal to 3.525 MHz?
A. 0.003525 kHz
B. 35.25 kHz
C. 3525 kHz
D. 3,525,000 kHz
Gigahertz | 1,000,000,000
Megahertz | 1,000,000
Kilohertz | 1,000
Hertz | 1

## Slide 49: T5B08 – Which is equal to 1,000,000 picofarads?
A. 0.001 microfarads
B. 1 microfarad
C. 1000 microfarads
D. 1,000,000,000 microfarads

## Slide 50: T5B08 – Which is equal to 1,000,000 picofarads?
A. 0.001 microfarads
B. 1 microfarad
C. 1000 microfarads
D. 1,000,000,000 microfarads
Farad | 1
Millifarad | 0.001
Microfarad | 0.000 001
Picofarad | 0.000 000 000 001

## Slide 51
51
Decibel Multipliers
10 TIMES
4 TIMES
2 TIMES
3 db
6 db
10 db
Power Increase
Notes: 51
51
The Decibel scale is logarithmic. 3dB represents a 2-fold increase in power, 6dB is 4 fold, 10dB is 10-fold, 20dB is 100-fold. The S-Unit scale on a receiver meter is not an absolute scale and can vary from radio to radio. Although these meters are not calibrated, they can be useful for verifying antenna performance. One “S-Unit” represents a 4-fold change in power or 6dB.

## Slide 52: T5B09 – Which decibel value most closely represents a power increase from 5 watts to 10 watts?
A. 2 dB
B. 3 dB
C. 5 dB
D. 10 dB

## Slide 53: T5B09 – Which decibel value most closely represents a power increase from 5 watts to 10 watts?
A. 2 dB
B. 3 dB
C. 5 dB
D. 10 dB
3 db = 2 X
2 X 5 watts = 10 watts

## Slide 54: T5B10 – Which decibel value most closely represents a power decrease from 12 watts to 3 watts?
A. -1 dB
B. -3 dB
C. -6 dB
D. -9 dB

## Slide 55: T5B10 – Which decibel value most closely represents a power decrease from 12 watts to 3 watts?
A. -1 dB
B. -3 dB
C. -6 dB
D. -9 dB
12 W / 2 = 6 W = -3 db
6 W / 2 = 3 W = + -3 db
- 6 db

## Slide 56: T5B11 – Which decibel value re[resents a power increase from 20 watts to 200 watts?
A. 10 dB
B. 12 dB
C. 18 dB
D. 28 dB

## Slide 57: T5B11 – Which decibel value re[resents a power increase from 20 watts to 200 watts?
A. 10 dB
B. 12 dB
C. 18 dB
D. 28 dB
200 Watts / 20 Watts = 10 db
10 deci bel = 1 bel

## Slide 58: T5B12 - Which is equal to 28400 kHz?
A. 28.400 kHz
B. 2.800 MHz
C. 284.00 MHz
D. 28.400 MHz

## Slide 59: T5B12 - Which is equal to 28400 kHz?
A. 28.400 kHz
B. 2.800 MHz
C. 284.00 MHz
D. 28.400 MHz
Gigahertz | 1,000,000,000
Megahertz | 1,000,000
Kilohertz | 1,000
Hertz | 1

## Slide 60: T5B13 – Which is equal to 2425 MHz?
A. 0.002425 GHZ
B. 24.25 GHz
C. 2.425 GHz
D. 2425 GHz

## Slide 61: T5B13 – Which is equal to 2425 MHz?
A. 0.002425 GHZ
B. 24.25 GHz
C. 2.425 GHz
D. 2425 GHz
Gigahertz | 1,000,000,000
Megahertz | 1,000,000
Kilohertz | 1,000
Hertz | 1

## Slide 62: T5C – Capacitance and Inductance terminology and units
Radio frequency definition and units; Impedance definition and units; Calculating power

## Slide 63: T5C01 – What describes the ability to store energy in an electric field?
A. Inductance
B. Resistance
C. Tolerance
D. Capacitance

## Slide 64: T5C01 – What describes the ability to store energy in an electric field?
A. Inductance
B. Resistance
C. Tolerance
D. Capacitance

## Slide 65: T5C02 - What is the basic unit of capacitance?
A. The farad
B. The ohm
C. The volt
D. The henry

## Slide 66: T5C02 - What is the basic unit of capacitance?
A. The farad
B. The ohm
C. The volt
D. The henry

## Slide 67: T5C03 - What describes the ability to store energy in a magnetic field?
A. Admittance
B. Capacitance
C. Resistance
D. Inductance

## Slide 68: T5C03 - What describes the ability to store energy in a magnetic field?
A. Admittance
B. Capacitance
C. Resistance
D. Inductance

## Slide 69: T5C04 - What is the unit of inductance?
A. The coulomb
B. The farad
C. The henry
D. The ohm

## Slide 70: T5C04 - What is the unit of inductance?
A. The coulomb
B. The farad
C. The henry
D. The ohm

## Slide 71: T5C05 - What is the unit of inductance?
A. The volt
B. The ampere
C. The coulomb
D. The ohm

## Slide 72: T5C05 - What is the unit of inductance?
A. The volt
B. The ampere
C. The coulomb
D. The ohm

## Slide 73: T5C06 - What does the abbreviation “RF” mean?
A. Radio frequency signals of all types
B. The resonant frequency of a tuned circuit
C. The real frequency transmitted as opposed to the apparent frequency
D. Reflective force in antenna transmission lines

## Slide 74: T5C06 - What does the abbreviation “RF” refer to?
A. Radio frequency signals of all types
B. The resonant frequency of a tuned circuit
C. The real frequency transmitted as opposed to the apparent frequency
D. Reflective force in antenna transmission lines

## Slide 75: T5C07 – What is the abbreviation for megahertz?
MH
mh
Mhz
MHz

## Slide 76: T5C07 – What is the abbreviation for megahertz?
MH
mh
Mhz
MHz

## Slide 77
77
Watts Law Voltage, Current and Power
Potential – Electromotive Force
  Electromotive Force (E)
  Units – Volts
  Unit Symbol V – 10V
  Measured across (parallel to load)
Current – Electron flow
  Current (I)
  Units – Amps, Amperes
  Unit Symbol A – 0.1A
  Measured through (inline with load)
Power (P)
  Watts
  Units – Watts
  Unit Symbol W – 60W
P
I
E
P = I x E
Notes: 77
Potential – Voltage or Electromotive force
Units are Volts named after Count Alessandro Giuseppe Antonio Anastasio Volta (Italian Inventor), invented the baterry.
Flow – Current, measured in amps, named after André-Marie Ampère (French) scientist and mathematician. I is used as the abbreviation because it referred to the Intensity of the current.
Power – Measured in Watts, named after James Watt (Scottish/British) inventor

## Slide 78
78
Power, Current, and Voltage Power Unit Circle WAV
Potential – Electromotive Force
  Electromotive Force (E)
  Units – Volts (V)
  Unit Symbol V – 10V
  Measured across (parallel to load)
Current – Electron flow
  Current (I)
  Unites – Amps, Amperes (A)
  Unit Symbol A – 0.1A
  Measured through (inline with load)
Power (P)
  Watts
  Units – Watts (W)
  Unit Symbol W – 60W
W
A
V
W = A x V
P = I x E
P
I E
Notes: 78
Potential – Voltage or Electromotive force
Units are Volts named after Count Alessandro Giuseppe Antonio Anastasio Volta (Italian Inventor), invented the baterry.
Flow – Current, measured in amps, named after André-Marie Ampère (French) scientist and mathematician. I is used as the abbreviation because it referred to the Intensity of the current.
Power – Measured in Watts, named after James Watt (Scottish/British) inventor

## Slide 79: T5C08 - What is the formula used to calculate electrical power (P) in a DC circuit?
P = I x E
B. P = E / I
C. P = E - I
D. P = I + E

## Slide 80: T5C08 - What is the formula used to calculate electrical power (P) in a DC circuit?
A. P = I x E
B. P = E / I
C. P = E - I
D. P = I + E
P
I
E
W = A x V
P = I x E
w
A
V

## Slide 81: T5C09 - How much power is delivered by a voltage of 13.8 volts DC and a current of 10 amperes?
A. 138 watts
B. 0.7 watts
C. 23.8 watts
D. 3.8 watts

## Slide 82: T5C09 - How much power is delivered by a voltage of 13.8 volts DC and a current of 10 amperes?
A. 138 watts
B. 0.7 watts
C. 23.8 watts
D. 3.8 watts
W?
A
V
What are you looking For?

## Slide 83
83
W ?
A
10 Amps
V
13.8 Volts
W = A x V
What info do you have?
T5C09 - How much power is delivered by a voltage of 13.8 volts DC and a current of 10 amperes?
Notes: 83
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 84
Electrical Principles 2014
84
W
A
10 A
V
13.8 V
W = A x V
W = 10 A x 13.8 V = 138 W
T5C09 How much power is delivered by a voltage of 13.8 volts DC and a current of 10 amperes?
Notes: 84
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 85: T5C09 - How much power is delivered by a voltage of 13.8 volts DC and a current of 10 amperes?
A. 138 watts
B. 0.7 watts
C. 23.8 watts
D. 3.8 watts

## Slide 86
T5C10 - How much power is delivered by a voltage of 12 volts DC and the current of 2.5 amperes?
  A. 4.8 watts
  B. 30 watts
  C. 14.5 watts
  D. 0.208 watts
Electrical Principles 2014
86

## Slide 87
Electrical Principles 2014
87
T5C10 - How much power is delivered by a voltage of 12 volts DC and the current of 2.5 amperes?
W ?
A
V
W = A x V
What are you looking For?
Notes: 87
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 88
Electrical Principles 2014
88
T5C10 - How much power is delivered by a voltage of 12 volts DC and the current of 2.5 amperes?
W ?
2.5 A
12 V
W = A x V
What info do you have?
Notes: 88
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 89
Electrical Principles 2014
89
T5C10 - How much power is delivered by a voltage of 12 volts DC and the current of 2.5 amperes?
W
2.5 A
12 V
W = A x V
W = 2.5 A x 12 V = 30 W
Notes: 89
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 90
T5C10 - How much power is delivered by a voltage of 12 volts DC and the current of 2.5 amperes?
  A. 4.8 watts
  B. 30 watts
  C. 14.5 watts
  D. 0.208 watts
Electrical Principles 2014
90

## Slide 91
T5C11 – How much current is required to deliver 120 watts at a voltage of 12 volts DC?
  A. 0.1 amperes
  B. 10 amperes
  C. 12 amperes
  D. 132 amperes
Electrical Principles 2014
91

## Slide 92
Electrical Principles 2014
92
T5C11 – How much current is required to deliver 120 watts at a voltage of 12 volts DC?
W
A ?
V
A = W / V
What are you looking For?
Notes: 92
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 93
Electrical Principles 2014
93
T5C11 – How much current is required to deliver 120 watts at a voltage of 12 volts DC?
W 120 W
A ?
V 12VDC
A = W / V
What info do you have?
Notes: 93
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 94
Electrical Principles 2014
94
T5C11 – How much current is required to deliver 120 watts at a voltage of 12 volts DC?
120 W
A
12 V
A = W / V
A = 120 W / 12 VDC = 10 A
Notes: 94
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 95
T5C11 – How much current is required to deliver 120 watts at a voltage of 12 volts DC?
  A. 0.1 amperes
B. 10 amperes
  C. 12 amperes
  D. 132 amperes
Electrical Principles 2014
95

## Slide 96: T5C12 - What is impedance?
A. The opposition to AC current flow
B. It is the inverse of resistance
C. The Q or Quality Factor of a component
D. The power handling capability of a component

## Slide 97: T5C12 - What is impedance?
A. The opposition to AC current flow
B. It is the inverse of resistance
C. The Q or Quality Factor of a component
D. The power handling capability of a component

## Slide 98: T5C13 - What is the abbreviation for kilohertz?
A. KHZ
B. khz
C. khZ
D. kHz

## Slide 99: T5C13 - What is the abbreviation for kilohertz?
A. KHz
B. khz
C. khZ
D. kHz

## Slide 100: T5D – Ohm’s Law
Series and parallel circuits

## Slide 102
102
Ohms Law Voltage, Current and Resistance
Potential – Electromotive Force
  Electromotive Force (E)
  Units – Volts
  Unit Symbol V – 10V
  Measured across (parallel to load)
Current – Electron flow
  Current (I)
  Units – Amps, Amperes
  Unit Symbol A – 0.1A
  Measured through (inline with load)
Resistance (R)
  Ohms (R)
  Units – Ohms
  Unit Symbol  – 60 
E
I
R
E = I x R
Notes: 102
Potential – Voltage or Electromotive force
Units are Volts named after Count Alessandro Giuseppe Antonio Anastasio Volta (Italian Inventor), invented the baterry.
Flow – Current, measured in amps, named after André-Marie Ampère (French) scientist and mathematician. I is used as the abbreviation because it referred to the Intensity of the current.
Power – Measured in Watts, named after James Watt (Scottish/British) inventor

## Slide 103
103
Ohms Law - Unit Circle Voltage, Current and Resistance
Potential – Electromotive Force
  Electromotive Force (V)
  Units – Volts
  Unit Symbol V – 10V
  Measured across (parallel to load)
Current – Electron flow
  Current (A)
  Units – Amps, Amperes
  Unit Symbol A – 0.1A
  Measured through (inline with load)
Resistance (R)
  Ohms (O)
  Units – Ohms
  Unit Symbol  – 60 
V
O
A
V = O x A
E
R I
Voice Of America
VOLTAGE CIRCLE
Notes: 103
Potential – Voltage or Electromotive force
Units are Volts named after Count Alessandro Giuseppe Antonio Anastasio Volta (Italian Inventor), invented the baterry.
Flow – Current, measured in amps, named after André-Marie Ampère (French) scientist and mathematician. I is used as the abbreviation because it referred to the Intensity of the current.
Power – Measured in Watts, named after James Watt (Scottish/British) inventor

## Slide 104
104
Ohm’s Law and Power Calculations
E
I
R
P
I
E
E=Voltage (Volts)
I=Current (Amps)
R=Resistance (Ohms)
* Ω is the symbol for ohms
P=Power (Watts)
To solve for a value, cover it with your finger and solve the remaining formula
Notes: 104
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 105
Electrical Principles 2010
105
Ohm’s Law and Power Calculations Unit Circles
V
O
A
W
A
V
V=Voltage (Volts)
O=Resistance (Ohms)
A=Current (Amps)
W=Power (Watts)
To solve for a value, cover it with your finger and solve the remaining formula
Voice Of America – VOLTAGE CIRCLE W A V - WATTAGE CIRCLE
Notes: 105
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 106: T5D01 - What formula is used to calculate current in a circuit?
I = E x R
I = E / R
I = E + R
I = E - R

## Slide 107: T5D01 - What formula is used to calculate current in a circuit?
I = E x R
I = E / R
I = E + R
I = E - R
E
I?
R
E = I x R
I = E / R
A = V / O
A?
O
V

## Slide 108: T5D02 - What formula is used to calculate voltage in a circuit?
E = I x R
E = I / R
E = I + R
E = I - R

## Slide 109: T5D02 - What formula is used to calculate voltage in a circuit?
E = I x R
E = I / R
E = I + R
E = I - R
E?
I
R
E = I x R
V = A x O
A
O
V?

## Slide 110: T5D03 – What formula is used to calculate resistance in a circuit?
R = E x I
R = E / I
R = E + I
R = E - I

## Slide 111: T5D03 – What formula is used to calculate resistance in a circuit?
R = E x I
R = E / I
R = E + I
R = E - I
E
I
R?
E = I x R
R = E / I
O = V / A
A
O?
V

## Slide 112: T5D04 - What is the resistance of a circuit in which a current of 3 amperes flows when connected to 90 volts?
A. 3 ohms
B. 30 ohms
C. 93 ohms
D. 270 ohms

## Slide 113
113
V
O ?
A
O = V / A
What are you looking For?
T5D04 - What is the resistance of a circuit in which a current of 3 amperes flows when connected to 90 volts?
Notes: 113
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 114
114
90 V
O ?
3 Amps
O = V / A
What info do you have?
T5D04 - What is the resistance of a circuit in which a current of 3 amperes flows when connected to 90 volts?
Notes: 114
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 115
115
90 V
O
3 A
O = V / A
O = 90 V / 3 A = 30 Ω
T5D04 - What is the resistance of a circuit in which a current of 3 amperes flows when connected to 90 volts?
Notes: 115
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 116
116
T5D04 - What is the resistance of a circuit in which a current of 3 amperes flows when connected to 90 volts?
A. 3 ohms
B. 30 ohms
C. 93 ohms
D. 270 ohms

## Slide 117
T5D05 - What is the resistance in a circuit for which the applied voltage is 12 volts and the current flow is 1.5 amperes?
  A. 18 ohms
  B. 0.125 ohms
  C. 8 ohms
  D. 13.5 ohms
117

## Slide 118
118
T5D05 - What is the resistance in a circuit for which the applied voltage is 12 volts and the current flow is 1.5 amperes?
V
O ?
A
O = V / A
What are you looking For?
Notes: 118
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 119
119
T5D05 - What is the resistance in a circuit for which the applied voltage is 12 volts and the current flow is 1.5 amperes?
12 V
O ?
1.5 A
O = V / A
What info do you have?
Notes: 119
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 120
120
T5D05 - What is the resistance in a circuit for which the applied voltage is 12 volts and the current flow is 1.5 amperes?
12 V
O
1.5 A
O = V / A
O = 12 V / 1.5 A = 8 Ω
Notes: 120
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 121
T5D05 - What is the resistance in a circuit for which the applied voltage is 12 volts and the current flow is 1.5 amperes?
121
  A. 18 ohms
  B. 0.125 ohms
  C. 8 ohms
  D. 13.5 ohms

## Slide 122
T5D06 - What is the resistance of a circuit that draws 4 amperes from a 12-volt source?
  A. 3 ohms
  B. 16 ohms
  C. 48 ohms
  D. 8 Ohms
122

## Slide 123
123
T5D06 - What is the resistance of a circuit that draws 4 amperes from a 12-volt source?
V
O ?
A
O = V / A
What are you looking For?
Notes: 123
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 124
124
T5D06 - What is the resistance of a circuit that draws 4 amperes from a 12-volt source?
V 12 Volts
O ?
A 4 Amps
O = V / A
What info do you have?
Notes: 124
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 125
125
T5D06 - What is the resistance of a circuit that draws 4 amperes from a 12-volt source?
12 V
O
4 A
O = V / A
O = 12 V / 4 A = 3 Ω
Notes: 125
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 126
T5D06 - What is the resistance of a circuit that draws 4 amperes from a 12-volt source?
126
  A. 3 ohms
  B. 16 ohms
  C. 48 ohms
  D. 8 Ohms

## Slide 127
T5D07 - What is the current in a circuit with an applied voltage of 120 volts and a resistance of
80 ohms?
  A. 9600 amperes
  B. 200 amperes
  C. 0.667 amperes
  D. 1.5 amperes
127

## Slide 128
128
V
O
A ?
A = V / O
T5D07 - What is the current in a circuit with an applied voltage of 120 volts and a resistance of
80 ohms?
What are you looking For?
Notes: 128
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 129
129
120 V
O
80 Ohms
A ?
A = V / O
T5D07 - What is the current in a circuit with an applied voltage of 120 volts and a resistance of
80 ohms?
What info do you have?
Notes: 129
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 130
130
120 V
O
80 Ohms
A
A = V / O
A = 120 V / 80 Ω = 1.5 A
T5D07 - What is the current in a circuit with an applied voltage of 120 volts and a resistance of
80 ohms?
Notes: 130
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 131
T5D07 - What is the current in a circuit with an applied voltage of 120 volts and a resistance of 80 ohms?
131
  A. 9600 amperes
  B. 200 amperes
  C. 0.667 amperes
  D. 1.5 amperes

## Slide 132
T5D08 - What is the current through a 100-ohm resistor connected across 200 volts?
  A. 20,000 amperes
  B. 0.5 amperes
  C. 2 amperes
  D. 100 amperes
132

## Slide 133
133
V
O
A ?
A = V / O
T5D08 - What is the current flowing a 100-ohm resistor connected across 200 volts?
What are you looking For?
Notes: 133
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 134
134
200 Volts
100 Ohms
A ?
A = V / O
What info do you have?
T5D08 - What is the current flowing a 100-ohm resistor connected across 200 volts?
Notes: 134
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 135
135
200 V
O
100 Ohms
A
A = V / O
A = 200 V / 100 Ω = 2 A
T5D08 - What is the current flowing a 100-ohm resistor connected across 200 volts?
Notes: 135
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 136
136
T5D08 - What is the current flowing a 100-ohm resistor connected across 200 volts?
  A. 20,000 amperes
  B. 0.5 amperes
  C. 2 amperes
  D. 100 amperes

## Slide 137
T5D09 - What is the current through a 24-ohm resistor connected across 240 volts?
  A. 24,000 amperes
  B. 0.1 amperes
  C. 10 amperes
  D. 216 amperes
137

## Slide 138
138
V
O
A ?
A = V / O
What are you looking For?
T5D09 - What is the current through a 24-ohm resistor connected across 240 volts?
Notes: 138
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 139
139
240 Volts
24 Ohms
A ?
A = V / O
What info do you have?
T5D09 - What is the current through a 24-ohm resistor connected across 240 volts?
Notes: 139
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 140
140
240 V
O
24 Ohms
A
A = V / O
A = 240 V / 24 Ω = 10 A
T5D09 - What is the current through a 24-ohm resistor connected across 240 volts?
Notes: 140
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 141
141
T5D09 - What is the current flowing through a 24-ohm resistor connected across 240 volts?
  A. 24,000 amperes
  B. 0.1 amperes
  C. 10 amperes
  D. 216 amperes

## Slide 142
T5D10 - What is the voltage across a 2-ohm resistor if a current of 0.5 amperes flows through it?
  A. 1 volt
  B. 0.25 volts
  C. 2.5 volts
  D. 1.5 volts
142

## Slide 143
143
V ?
O
A
V = O x A
What are you looking For?
T5D10 - What is the voltage across a 2-ohm resistor if a current of 0.5 amperes flows through it?
Notes: 143
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 144
144
V ?
O
2 Ohms
A
0.5 Amps
V = O x A
What info do you have?
T5D10 - What is the voltage across a 2-ohm resistor if a current of 0.5 amperes flows through it?
Notes: 144
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 145
145
V
O
2 Ohms
A
0.5 Amps
V = O x A
V = 2 Ω x 0.5 A = 1 V
T5D10 - What is the voltage across a 2-ohm resistor if a current of 0.5 amperes flows through it?
Notes: 145
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 146
146
T5D10 - What is the voltage across a 2-ohm resistor if a current of 0.5 amperes flows through it?
  A. 1 volt
  B. 0.25 volts
  C. 2.5 volts
  D. 1.5 volts

## Slide 147
T5D11 - What is the voltage across a 10-ohm resistor if a current of 1 ampere flows through it?
  A. 1 volt
  B. 10 volts
  C. 11 volts
  D. 9 volts
147

## Slide 148
148
V ?
O
A
V = O x A
What are you looking For?
T5D11 - What is the voltage across a 10-ohm resistor if a current of 1 ampere flows through it?
Notes: 148
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 149
149
V ?
10 Ohms
1 Amp
V = O x A
V = 10 Ω x 1 A = 10 V
What info do you have?
T5D11 - What is the voltage across a 10-ohm resistor if a current of 1 ampere flows through it?
Notes: 149
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 150
150
V
O
10 Ohms
A
1 Amp
V = O x A
V= 10 x 1 = 10 V
T5D11 - What is the voltage across a 10-ohm resistor if a current of 1 ampere flows through it?
Notes: 150
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 151
151
T5D11 - What is the voltage across a 10-ohm resistor if a current of 1 ampere flows through it?
  A. 1 volt
  B. 10 volts
  C. 11 volts
  D. 9 volts

## Slide 152
T5D12 - What is the voltage across a 10-ohm resistor if a current of 2 amperes flows through it?
  A. 8 volts
  B. 0.2 volts
  C. 12 volts
  D. 20 volts
152

## Slide 153
153
V ?
O
A
V = O x A
What are you looking For?
T5D12 - What is the voltage across a 10-ohm resistor if a current of 2 amperes flows through it?
Notes: 153
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 154
154
V ?
O
10 Ohms
A
2 Amps
V = O x A
What info do you have?
T5D12 - What is the voltage across a 10-ohm resistor if a current of 2 amperes flows through it?
Notes: 154
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 155
155
V
10 Ohms
2 Amps
V = O x A
V = 10 Ω x 2 A = 20 V
T5D12 - What is the voltage across a 10-ohm resistor if a current of 2 amperes flows through it?
Notes: 155
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 156
156
T5D12 - What is the voltage across a 10-ohm resistor if a current of 2 amperes flows through it?
  A. 8 volts
  B. 0.2 volts
  C. 12 volts
  D. 20 volts

## Slide 157: T5D13 – In which type of circuit is DC current the same through all components?
Series
Parallel
Resonant
Branch

## Slide 158: T5D13 – In which type of circuit is DC current the same through all components?
Series
Parallel
Resonant
Branch

## Slide 159: Current in Series
All the electrons go through the single path
Look at a river flowing under a bridge.
Water flows under the bridge which represents a connection

## Slide 160: T5D14 – In which type of circuit is voltage the same across all components?
Series
Parallel
Resonant
Branch

## Slide 161: T5D14 – In which type of circuit is voltage the same across all components?
Series
Parallel
Resonant
Branch

## Slide 162: Current Parallel
The electrons divide into the different paths

## Slide 163: Voltage is series – Adds up
Add voltage from each segment to get total voltage
10 volts total
2 Volts 3 volts 1 volts 4 volts

## Slide 164: Voltage in Parallel
Voltage is the same is each segment
10 volts 10 Volts 10 Volts
10 Volts

## Slide 165: Raft fishing in Alaska
We were floating a river in wild western Alaska and the river split into three branches.
We chose the largest branch, but the water flowed through trees, that did not let the rafts go between.
12 people and several rafts were worried that we would having to portage, but the branches came back together.
This is a real life example of parallel currents through several branches

## Slide 166: Three branches - Volume Divides Speed same
        2,000 cubic feet at
        5 feet per second
        1,000 cubic feet
        5 feet per second
        3,000 cubic feet
        5 feet per second
Water migrated through the trees
6,000 cubic feet of water
Notes: We were floating a river in wild western Alaska and the river split into three branches. We chose the largest branch, but the water flowed through trees, that did not let the rafts go between. We were worried that we would have to portage, but the branches came back together.

## Slide 167: End of SUBELEMENT T5
Electrical principles: math for electronics; electronic principles; Ohm’s Law