## Slide 1: SUBELEMENT T6
Electronic and Electrical components;
[4 Exam Questions - 4 Groups]
Notes: Subelement T6 Electronic and Electrical Components. Technician Training Slides for 2022 Question Pool Good through June 30, 2026 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM, Howard Schultz, W7HS.

## Slide 2
T6A - Electrical components: fixed and variable resistors; capacitors and inductors; fuses; switches; batteries
T6B – Semiconductors: basic principles and applications of solid state devices; diodes and transistors
T6C - Circuit diagrams: use of schematics, Schematic symbols of basic components
T6D - Component functions: rectifiers, relay, voltage regulators, meters, indicators, integrated circuits, transformers; Resonant circuit; Shielding

## Slide 3: Resistors
Resistors oppose the flow of current in a DC (or AC) circuit). Their values are represented with the colored strips or numbers and will vary slightly with temperature.
A variable resistor is called a potentiometer and is often used for volume controls

## Slide 4: Capacitors
Electrolytic capacitors (polarized)
Ceramic capacitors
Capacitors are conductive plates separated by an insulator and stores energy in an electric field (electrostatically)
Air Variable Capacitor

## Slide 5: Inductors
Inductors are generally coils of wire that store energy in a magnetic field

## Slide 6: Diode
  Electronic one-way “valve”, used e.g. in rectifiers
  Mostly made of Si, Ga
  Different types: PN diodes, Schottky
  Electrodes are called anode and cathode with the cathode indicated by a stripe

## Slide 7: Transistors (Bipolar)
Can be used as an electronic switch or amplifier
Comprised of three layers of semiconductor (PNP, NPN)
Generally have three electrodes (emitter, base, collector)
Field Effect Transistors (FET) have source, drain and gate instead

## Slide 8: Transistors (FET)

## Slide 9: Transformer

## Slide 10: T6A01 - What electrical component opposes the flow of current in a DC circuit?
A. Inductor
B. Resistor
C. Inverter
D. Transformer

## Slide 11: T6A01 - What electrical component opposes the flow of current in a DC circuit?
A. Inductor
B. Resistor
C. Inverter
D. Transformer

## Slide 12: T6A02 - What type of component is often used as an adjustable volume control?
A. Fixed resistor
B. Power resistor
C. Potentiometer
D. Transformer

## Slide 13: T6A02 - What type of component is often used as an adjustable volume control?
A. Fixed resistor
B. Power resistor
C. Potentiometer
D. Transformer

## Slide 14: T6A03 - What electrical parameter is controlled by a potentiometer?
A. Inductance
B. Resistance
C. Capacitance
D. Field strength

## Slide 15: T6A03 - What electrical parameter is controlled by a potentiometer?
A. Inductance
B. Resistance
C. Capacitance
D. Field strength

## Slide 16: T6A04 - What electrical component stores energy in an electric field?
A. Varistor
B. Capacitor
C. Inductor
D. Diode

## Slide 17: T6A04 - What electrical component stores energy in an electric field?
A. Varistor
B. Capacitor
C. Inductor
D. Diode

## Slide 18: T6A05 - What type of electrical component consists of conductive surfaces separated by an insulator?
A. Resistor
B. Potentiometer
C. Oscillator
D. Capacitor

## Slide 19: T6A05 - What type of electrical component consists of conductive surfaces separated by an insulator?
A. Resistor
B. Potentiometer
C. Oscillator
D. Capacitor

## Slide 20: T6A06 - What type of electrical component stores energy in a magnetic field?
A. Varistor
B. Capacitor
C. Inductor
D. Diode

## Slide 21: T6A06 - What type of electrical component stores energy in a magnetic field?
A. Varistor
B. Capacitor
C. Inductor
D. Diode

## Slide 22: T6A07 - What electrical component is typically constructed of a coil of wire?
A. Switch
B. Capacitor
C. Diode
D. Inductor

## Slide 23: T6A07 - What electrical component is typically constructed of a coil of wire?
A. Switch
B. Capacitor
C. Diode
D. Inductor

## Slide 24: T6A08 - What is the function of an SPDT switch?
A. A single circuit if opened or closed
B. Two circuits are opened or closed
C. A single circuit is switched between one of two other circuits
D. Two circuits are each switched between one of two other circuits

## Slide 25: T6A08 - What is the function of an SPDT switch?
A. A single circuit if opened or closed
B. Two circuits are opened or closed
C. A single circuit is switched between one of two other circuits
D. Two circuits are each switched between one of two other circuits

## Slide 26: T6A09 - What electrical component is used to protect other circuit components from current overloads?
A. Fuse
B. Thyrathon
C. Varactor
D. All of these choices are correct

## Slide 27: T6A09 - What electrical component is used to protect other circuit components from current overloads?
A. Fuse
B. Thyrathon
C. Varactor
D. All of these choices are correct

## Slide 28: T6A10 - Which of the following battery chemistries is rechargeable?
A. Nickel-metal hydride
B. Lithium-ion
C. Lead-acid gel-cell
D. All of these choices are correct

## Slide 29: T6A10 - Which of the following battery chemistries is rechargeable?
A. Nickel-metal hydride
B. Lithium-ion
C. Lead-acid gel-cell
D. All of these choices are correct

## Slide 30: T6A11 - Which of the following battery chemistries is not rechargeable?
A. Nickel-cadmium
B. Carbon-zinc
C. Lead-acid
D. Lithium-ion

## Slide 31: T6A11 - Which of the following battery chemistries is not rechargeable?
A. Nickel-cadmium
B. Carbon-zinc
C. Lead-acid
D. Lithium-ion

## Slide 32: T6A12 – What type of switch is represented by component 3 in figure T-2?
A. Single-pole single-throw
B. Single-pole double-throw
C. Double-pole single-throw
D. Double-pole double-throw

## Slide 33: T6A12 – What type of switch is represented by component 3 in figure T-2?
A. Single-pole single-throw
B. Single-pole double-throw
C. Double-pole single-throw
D. Double-pole double-throw

## Slide 34: T6B – Semiconductors:
basic principles and applications of solid state devices; diodes and transistors

## Slide 35: T6B01 - What is true about forward voltage drop in a diode?
A. It is lower in some diode types than is others
B. It is proportional to peak inverse voltage
C. It indicates that the diode is defective
D. It has no impact on the voltage delivered to the load

## Slide 36: T6B01 - What is true about forward voltage drop in a diode?
A. It is lower in some diode types than is others
B. It is proportional to peak inverse voltage
C. It indicates that the diode is defective
D. It has no impact on the voltage delivered to the load

## Slide 37: T6B02 - What electronic component allows current to flow in only one direction?
A. Resistor
B. Fuse
C. Diode
D. Driven Element

## Slide 38: T6B02 - What electronic component allows current to flow in only one direction?
A. Resistor
B. Fuse
C. Diode
D. Driven Element

## Slide 39: T6B03 - Which of these components can be used as an electronic switch or amplifier?
A. Varistor
B. Potentiometer
C. Transistor
D. Thermistor

## Slide 40: T6B03 - Which of these components can be used as an electronic switch or amplifier?
A. Varistor
B. Potentiometer
C. Transistor
D. Thermistor

## Slide 41: T6B04 - Which of the following components can consist of three layers of semiconductor material?
A. Alternator
B. Transistor
C. Triode
D. Pentagrid converter

## Slide 42: T6B04 - Which of the following components can consist of three layers of semiconductor material?
A. Alternator
B. Transistor
C. Triode
D. Pentagrid converter

## Slide 43: T6B05 – What type of transistor has a gate, drain, and source?
A. Varistor
B. Field-effect
C. Telsa-effect
D. Bipolar junction

## Slide 44: T6B05 – What type of transistor has a gate, drain, and source?
A. Varistor
B. Field-effect
C. Telsa-effect
D. Bipolar junction

## Slide 45: T6B06 - How is the cathode lead of a semiconductor diode often marked on the package?
A. With the word cathode
B. With a stripe
C. With the letter C
D. With the letter K

## Slide 46: T6B06 - How is the cathode lead of a semiconductor diode often marked on the package?
A. With the word cathode
B. With a stripe
C. With the letter C
D. With the letter K

## Slide 47: T6B07 - What causes a light-emitting diode ( LED ) to omit light?
A. Forward current
B. Reverse current
C. Capacitively-coupled RF signal
D. Inductively-coupled RF signal

## Slide 48: T6B07 - What causes a light-emitting diode ( LED ) to omit light?
A. Forward current
B. Reverse current
C. Capacitively-coupled RF signal
D. Inductively-coupled RF signal

## Slide 49: T6B08 - What does the abbreviation FET stand for?
A. Frequency Emission Transmitter
B. Fast Electron Transistor
C. Free Electron Transition
D. Field Effect Transistor

## Slide 50: T6B08 - What does the abbreviation FET stand for?
A. Frequency Emission Transmitter
B. Fast Electron Transistor
C. Free Electron Transition
D. Field Effect Transistor

## Slide 51: T6B09 - What are the names of the electrodes of a diode?
A. Plus and minus
B. Source and drain
C. Anode and cathode
D. Gate and base

## Slide 52: T6B09 - What are the names of the electrodes of a diode?
A. Plus and minus
B. Source and drain
C. Anode and cathode
D. Gate and base

## Slide 53: T6B10 Which of the following can provide power gain?
A. Transformer
B. Transistor
C. Reactor
D. Resistor

## Slide 54: T6B10 Which of the following can provide power gain?
A. Transformer
B. Transistor
C. Reactor
D. Resistor

## Slide 55: T6B11 What is the term that describes a device's ability to amplify a signal?
A. Gain
B. Forward resistance
C. Forward voltage drop
D. On resistance

## Slide 56: T6B11 What is the term that describes a device's ability to amplify a signal?
A. Gain
B. Forward resistance
C. Forward voltage drop
D. On resistance

## Slide 57: T6B12 What are the names of the electrodes of a bipolar junction ttransistor?
A. Signal, bias, power
B. Emitter, base, collector
C. Input, output, supply
D. Pole one, pole two, output

## Slide 58: T6B12 What are the names of the electrodes of a bipolar junction ttransistor?
A. Signal, bias, power
B. Emitter, base, collector
C. Input, output, supply
D. Pole one, pole two, output

## Slide 59
T6C - Circuit diagrams; use of schematics, basic structure; Schematic symbols of basic components

## Slide 60: Schematic Symbols
Resistor |  | Capacitor |  | SPST Switch | 
Variable Resistor |  | Lamp |  | LED | 
Transistor |  | Transformer |  | Antenna | 
Battery |  | Variable Inductor |  |  | 

## Slide 61
Other Circuit Information

## Slide 62: T6C01 - What is the name of electrical wiring diagram that uses standard component symbols?
A. Bill of materials
B. Connector pinout
C. Schematic symbols
D. Low charts

## Slide 63: T6C01 - What is the name of electrical wiring diagram that uses standard component symbols?
A. Bill of materials
B. Connector pinout
C. Schematic symbols
D. Low charts

## Slide 64: T6C02 - What is component 1 in figure T1?
A. Resistor
B. Transistor
C. Battery
D. Connector

## Slide 65: T6C02 - What is component 1 in figure T1?
A. Resistor
B. Transistor
C. Battery
D. Connector

## Slide 66: T6C03 - What is component 2 in figure T1?
A. Resistor
B. Transistor
C. Indicator lamp
D. Connector

## Slide 67: T6C03 - What is component 2 in figure T1?
A. Resistor
B. Transistor
C. Indicator lamp
D. Connector

## Slide 68: T6C04 - What is component 3 in figure T1?
A. Resistor
B. Transistor
C. Lamp
D. Ground symbol

## Slide 69: T6C04 - What is component 3 in figure T1?
A. Resistor
B. Transistor
C. Lamp
D. Ground symbol

## Slide 70: T6C05 - What is component 4 in figure T1?
A. Resistor
B. Transistor
C. Ground symbol
D. Battery

## Slide 71: T6C05 - What is component 4 in figure T1?
A. Resistor
B. Transistor
C. Ground symbol
D. Battery

## Slide 72: T6C06 - What is component 6 in figure T2?
A. Resistor
B. Capacitor
C. Regulator IC
D. Transistor

## Slide 73: T6C06 - What is component 6 in figure T2?
A. Resistor
B. Capacitor
C. Regulator IC
D. Transistor

## Slide 74: T6C07 - What is component 8 in figure T2?
A. Resistor
B. Inductor
C. Regulator IC
D. Light emitting diode

## Slide 75: T6C07 - What is component 8 in figure T2?
A. Resistor
B. Inductor
C. Regulator IC
D. Light emitting diode

## Slide 76: T6C08 - What is component 9 in figure T2?
A. Variable capacitor
B. Variable inductor
C. Variable resistor
D. Variable transformer

## Slide 77: T6C08 - What is component 9 in figure T2?
A. Variable capacitor
B. Variable inductor
C. Variable resistor
D. Variable transformer

## Slide 78: T6C09 - What is component 4 in figure T2?
A. Variable inductor
B. Double-pole switch
C. Potentiometer
D. Transformer

## Slide 79: T6C09 - What is component 4 in figure T2?
A. Variable inductor
B. Double-pole switch
C. Potentiometer
D. Transformer

## Slide 80: T6C10 - What is component 3 in figure T3?
A. Connector
B. Meter
C. Variable capacitor
D. Variable inductor

## Slide 81: T6C10 - What is component 3 in figure T3?
A. Connector
B. Meter
C. Variable capacitor
D. Variable inductor

## Slide 82: T6C11 - What is component 4 in figure T3?
A. Antenna
B. Transmitter
C. Dummy load
D. Ground

## Slide 83: T6C11 - What is component 4 in figure T3?
A. Antenna
B. Transmitter
C. Dummy load
D. Ground

## Slide 84: T6C12 – Which of the following is accurately represented in electrical schematics?
A. Wire lengths
B. Physical appearance of components
C. Component connections
D. All these choices are correct

## Slide 85: T6C12 – Which of the following is accurately represented in electrical schematics?
A. Wire lengths
B. Physical appearance of components
C. Component connections
D. All these choices are correct

## Slide 86
Simple AM radio

## Slide 87: T6D - Component functions
rectifiers, relay, voltage regulators, meters, indicators, integrated circuits, transformers; Resonant circuit; Shielding

## Slide 88: T6D01 - Which of the following devices or circuits changes an alternating current into a varying direct current signal?
A. Transformer
B. Rectifier
C. Amplifier
D. Reflector

## Slide 89: T6D01 - Which of the following devices or circuits changes an alternating current into a varying direct current signal?
A. Transformer
B. Rectifier
C. Amplifier
D. Reflector

## Slide 90: T6D02 - What is a relay?
A. A electrically controlled switch
B. A current controlled amplifier
C. An inverting amplifier
D. A pass transistor

## Slide 91: T6D02 - What is a relay?
A. A electrically controlled switch
B. A current controlled amplifier
C. An inverting ampofier
D. A pass transistor

## Slide 92: T6D03 – Which of the following is a reason to use shielded wire?
A. To decrease the resistance of DC power connections
B. To increase the current carrying capability of the wire
C. To prevent coupling of unwanted signals to or from the wire
D. To couple the wire to other siognals

## Slide 93: T6D03 – Which of the following is a reason to use shielded wire?
A. To decrease the resistance of DC power connections
B. To increase the current carrying capability of the wire
C. To prevent coupling of unwanted signals to or from the wire
D. To couple the wire to other siognals

## Slide 94: T6D04 - Which of the following displays an electrical quantity as a numeric value?
A. Potentiometer
B. Transistor
C. Meter
D. Relay

## Slide 95: T6D04 - Which of the following displays an electrical quantity as a numeric value?
A. Potentiometer
B. Transistor
C. Meter
D. Relay

## Slide 96
Receiver VU Meter

## Slide 97: T6D05 - What type of circuit controls the amount of voltage from a power supply?
A. Regulator
B. Oscillator
C. Filter
D. Phase inverter

## Slide 98: T6D05 - What type of circuit controls the amount of voltage from a power supply?
A. Regulator
B. Oscillator
C. Filter
D. Phase inverter

## Slide 99: T6D06 - What component changes 120V AC power to a lower AC voltage for other uses?
A. Variable capacitor
B. Transformer
C. Transistor
D. Diode

## Slide 100: T6D06 - What component changes 120V AC power to a lower AC voltage for other uses?
A. Variable capacitor
B. Transformer
C. Transistor
D. Diode

## Slide 101: T6D07 - Which of the following is commonly used as a visual indicator?
A. LED
B. FET
C. Zener diode
D. Bipolar transistor

## Slide 102: T6D07 - Which of the following is commonly used as a visual indicator?
A. LED
B. FET
C. Zener diode
D. Bipolar transistor

## Slide 103: T6D08 - Which of the following is combined with an inductor to make a tuned circuit?
A. Resistor
B. Zener diode
C. Potentiometer
D. Capacitor

## Slide 104: T6D08 - Which of the following is combined with an inductor to make a tuned circuit?
A. Resistor
B. Zener diode
C. Potentiometer
D. Capacitor

## Slide 105: T6D09 - What is the name of a device that combines several semiconductors and other components into one package?
A. Transducer
B. Multi-pole relay
C. Integrated circuit
D. Transformer

## Slide 106: T6D09 - What is the name of a device that combines several semiconductors and other components into one package?
A. Transducer
B. Multi-pole relay
C. Integrated circuit
D. Transformer

## Slide 107: T6D10 - What is the function of component 2 in Figure T1?
A. Give off light when current flows through it
B. Supply electrical energy
C. Control the flow of current
D. Convert electrical energy into radio waves

## Slide 108: T6D10 - What is the function of component 2 in Figure T1?
A. Give off light when current flows through it
B. Supply electrical energy
C. Control the flow of current
D. Convert electrical energy into radio waves

## Slide 109: T6D11 - What of the following is a resonant or tuned circuit?
A. An inductor and a capacitor in series or parallel
B. A type of voltage regulator
C. A resistor circuit used for reducing standing wave ratio
D. A circuit designed to provide high fidelity audio

## Slide 110: T6D11 - What of the following is a resonant or tuned circuit?
A. An inductor and a capacitor in series or parallel
B. A type of voltage regulator
C. A resistor circuit used for reducing standing wave ratio
D. A circuit designed to provide high fidelity audio

## Slide 111: Vacuum Tubes
Tubes regulate current flow between cathode and plate with a control grid. Their size can also create unwanted capacitances. A screen grid can be added to reduce grid-to-plate capacitance.
Although still used in high power applications (large amplifiers), they have been largely replaced with transistors. The Field Effect Transistor (FET) has characteristics most similar to a tube.

## Slide 112
Vacuum Tubes

## Slide 113: G6A07 Which of the following is a reason not to use wire-wound resistors in an RF circuit?
  A. The resistor's tolerance value would not be adequate for such a circuit
  B. The resistor's inductance could make circuit performance unpredictable
  C. The resistor could overheat
  D. The resistor's internal capacitance would detune the circuit

## Slide 114: G6A07 Which of the following is a reason not to use wire-wound resistors in an RF circuit?
  A. The resistor's tolerance value would not be adequate for such a circuit
  B. The resistor's inductance could make circuit performance unpredictable
  C. The resistor could overheat
  D. The resistor's internal capacitance would detune the circuit

## Slide 115: G6A08 Which of the following describes a thermistor?
  A. A resistor that is resistant to changes in value with temperature variations
  B. A device having a specific change in resistance with temperature variations
  C. A special type of transistor for use at very cold temperatures
  D. A capacitor that changes value with temperature

## Slide 116: G6A08 Which of the following describes a thermistor?
  A. A resistor that is resistant to changes in value with temperature variations
  B. A device having a specific change in resistance with temperature variations
  C. A special type of transistor for use at very cold temperatures
  D. A capacitor that changes value with temperature

## Slide 117: G6A11 Why would it be important to minimize the mutual inductance between two inductors?
  A. To increase the energy transfer between circuits
  B. To reduce unwanted coupling between circuits
  C. To reduce conducted emissions
  D. To increase the self-resonant frequency of the inductors

## Slide 118: G6A11 Why would it be important to minimize the mutual inductance between two inductors?
  A. To increase the energy transfer between circuits
  B. To reduce unwanted coupling between circuits
  C. To reduce conducted emissions
  D. To increase the self-resonant frequency of the inductors

## Slide 119: G6B02 What are two major ratings that must not be exceeded for silicon diode rectifiers?
  A. Peak inverse voltage; average forward current
  B. Average power; average voltage
  C. Capacitive reactance; avalanche voltage
  D. Peak load impedance; peak voltage

## Slide 120: G6B02 What are two major ratings that must not be exceeded for silicon diode rectifiers?
  A. Peak inverse voltage; average forward current
  B. Average power; average voltage
  C. Capacitive reactance; avalanche voltage
  D. Peak load impedance; peak voltage

## Slide 121: Connectors
DE-9 | Serial data | PL-259 | RF, Good to ~150MHz
DIN | Multiconductor audio/control | N | Waterproof RF, Good to ~10GHz
RCA | Audio/ Video | SMA | Small RF, Good to several GHz

## Slide 122: End of SUBELEMENT T6
Electrical components: semiconductors; circuit diagrams; component functions