## Slide 1: SUBELEMENT T7
Practical Circuits
[4 Exam Questions - 4 Groups]
Notes: Subelement T7 Practical Circuits. Technician Training Slides for 2022 Question Pool Good through June 30, 2022 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM, Howard Schultz, W7HS.

## Slide 2
T7A – Station equipment: receivers; transceivers; transmitters amplifiers, receive amplifiers, transverters; Basic radio circuit concepts and terminology; sensitivity, selectivity, mixers, oscillators, PTT, modulations
T7B – Symtoms; causes and cures of common transmitter and receiver problems: overload and overdrive, distortion, interference and consumer electronics, RF feedback
T7C – Antenna and transmission line measurements and troubleshooting: measuring SWR, effects of high SWR, causes of feed ling failures; Basic coaxial cable characteristics; Use of dummy loads when testing
T7D – Using basic test instruments: voltmeter, ammeter, and ohmmeter; Soldering

## Slide 3: Receiver Technology
Current receivers are largely superheterodyne
Superheterodyne receivers convert the receive frequency to lower Intermediate Frequencies (IF) to allow filtering
Multiple conversions makes a more selective receiver
The final stage includes a Detector that extracts the audio from the modulated carrier
A CW/SSB detector is called a Product Detector
An FM detector is called a Discriminator

## Slide 4: T7A01 - Which term describes the ability of a receiver to detect the presence of a signal?
A. Linearity
B. Sensitivity
C. Selectivity
D. Total Harmonic Distortion

## Slide 5: T7A01 - Which term describes the ability of a receiver to detect the presence of a signal?
A. Linearity
B. Sensitivity
C. Selectivity
D. Total Harmonic Distortion

## Slide 6: T7A02 - What is a transceiver?
A. A device that combines a receiver and transmitter
B. A device for matching feed line impedance to 50 ohms
C. A device for automatically sending and decoding Morse code
D. A device for converting receiver and transmitter frequencies to another band

## Slide 7: T7A02 - What is a transceiver?
A. A device that combines a receiver and transmitter
B. A device for matching feed line impedance to 50 ohms
C. A device for automatically sending and decoding Morse code
D. A device for converting receiver and transmitter frequencies to another band

## Slide 8: T7A03 - Which of the following is used to convert a radio signal from one frequency to another?
A. Phase splitter
B. Mixer
C. Inverter
D. Amplifier

## Slide 9: T7A03 - Which of the following is used to convert a radio signal from one frequency to another?
A. Phase splitter
B. Mixer
C. Inverter
D. Amplifier

## Slide 10: T7A04 - Which term describes the ability of a receiver to discriminate between multiple signals?
A. Discrimination ratio
B. Sensitivity
C. Selectivity
D. Harmonic Distortion

## Slide 11: T7A04 - Which term describes the ability of a receiver to discriminate between multiple signals?
A. Discrimination ratio
B. Sensitivity
C. Selectivity
D. Harmonic Distortion

## Slide 12: T7A05 - What is the name of a circuit that generates a signal of a specific frequency?
A. Reactance modulator
B. Product detector
C. Low-pass filter
D. Oscillator

## Slide 13: T7A05 - What is the name of a circuit that generates a signal of a specific frequency?
A. Reactance modulator
B. Product detector
C. Low-pass filter
D. Oscillator

## Slide 14: T7A06 - What device converts the RF input and output of a transceiver to another band?
A. High-pass filter
B. Low-pass filter
C. Transverter
D. Phase converter

## Slide 15: T7A06 - What device converts the RF input and output of a transceiver to another band?
A. High-pass filter
B. Low-pass filter
C. Transverter
D. Phase converter

## Slide 16: T7A07 - What is the function of a transceiver’s “PTT” input?
A. Input for a key used to send CW
B. Switches transceiver from receive to transmit when grounded
Provides a transit tuning tone when grounded
Input for a preamplifier tuning tone

## Slide 17: T7A07 - What is the function of a transceiver’s “PTT” input?
A. Input for a key used to send CW
B. Switches transceiver from receive to transmit when grounded
Provides a transit tuning tone when grounded
Input for a preamplifier tuning tone

## Slide 18: T7A08 - Which of the following describes combining speech with an RF carrier signal?-
A. Impedance matching
B. Oscillation
C. Modulation
D. Low-pass filtering

## Slide 19: T7A08 - Which of the following describes combining speech with an RF carrier signal?-
A. Impedance matching
B. Oscillation
C. Modulation
D. Low-pass filtering

## Slide 20: T7A09 – What is the function of the SSB/CW – FM switch on a VHF power amplifier?
Change the mode of the transmitted signal
Set the amplifier for proper operation in the selected mode
Change the frequency range of the amplifier to operate in the proper segment of the band
Reduce the received signal noise

## Slide 21: T7A09 – What is the function of the SSB/CW – FM switch on a VHF power amplifier?
Change the mode of the transmitted signal
Set the amplifier for proper operation in the selected mode
Change the frequency range of the amplifier to operate in the proper segment of the band
Reduce the received signal noise

## Slide 22: T7A10 - What device increases the transmitted output power from a transceiver?
A. A voltage divider
B. An RF power amplifier
C. An impedance network
D. All of these choices are correct

## Slide 23: T7A10 - What device increases the transmitted output power from a transceiver?
A. A voltage divider
B. An RF power amplifier
C. An impedance network
D. All of these choices are correct

## Slide 24: T7A11 - Where is an RF preamplifier installed?
A. Between the antenna and receiver
B. At the output of the transmitter's power amplifier
C. Between a transmitter and antenna tuner
D. At the output of the receiver audio ampplifier

## Slide 25: T7A11 - Where is an RF preamplifier installed?
A. Between the antenna and receiver
B. At the output of the transmitter's power amplifier
C. Between a transmitter and antenna tuner
D. At the output of the receiver audio ampifier

## Slide 26: T7B – Symptoms:
causes and cures of common transmitter and receiver problems: overload and overdrive, distortion, interference and consumer electronics, RF feedback

## Slide 27: T7B01 - What can you do if you are told your FM handheld or mobile transceiver is over-deviating?
A. Talk louder into the microphone
B. Let the transceiver cool off
C. Change to a higher power level
D. Talk farther away from the microphone

## Slide 28: T7B01 - What can you do if you are told your FM handheld or mobile transceiver is over-deviating?
A. Talk louder into the microphone
B. Let the transceiver cool off
C. Change to a higher power level
D. Talk farther away from the microphone

## Slide 29: T7B02 - What would cause a broadcast AM or FM radio to receive an amateur radio transmission unintentionally?
A. The receiver is unable to reject strong signals outside the AM or FM band
B. The microphone gain of the transmitter is turned up too high
C. The audio amplifier of the transmitter is overloaded
D. The deviation of an FM transmitter is set too low

## Slide 30: T7B02 - What would cause a broadcast AM or FM radio to receive an amateur radio transmission unintentionally?
A. The receiver is unable to reject strong signals outside the AM or FM band
B. The microphone gain of the transmitter is turned up too high
C. The audio amplifier of the transmitter is overloaded
D. The deviation of an FM transmitter is set too low

## Slide 31: T7B03 - Which of the following may be a cause of radio frequency interference?
A. Fundamental overload
B. Harmonics
C. Spurious emissions
D. All of these choices are correct

## Slide 32: T7B03 - Which of the following may be a cause of radio frequency interference?
A. Fundamental overload
B. Harmonics
C. Spurious emissions
D. All of these choices are correct

## Slide 33: T7B04 - Which of the following could you use to cure distorted audio caused by RF current on the shield of a microphone cable?
A. Band-pass filter
B. Low-pass filter
C. Preamplifier
D. Ferrite choke

## Slide 34: T7B04 - Which of the following could you use to cure distorted audio caused by RF current on the shield of a microphone cable?
A. Band-pass filter
B. Low-pass filter
C. Preamplifier
D. Ferrite choke

## Slide 35: T7B05 - How can fundamental overload of a non-amateur radio or TV receiver by an amateur signal be reduced or eliminated?
A. Block the amateur signal with a filter at the antenna input of the affected receiver
B. Block the interfering signal with a filter on the amateur transmitter
C. Switch the transmitter from FM to SSB
D. Switch the transmitter to a narrow-band mode

## Slide 36: T7B05 - How can fundamental overload of a non-amateur radio or TV receiver by an amateur signal be reduced or eliminated?
A. Block the amateur signal with a filter at the antenna input of the affected receiver
B. Block the interfering signal with a filter on the amateur transmitter
C. Switch the transmitter from FM to SSB
D. Switch the transmitter to a narrow-band mode

## Slide 37: T7B06 - Which of the following actions should you take if a neighbor tells you that your station’s transmissions are interfering with their radio or TV reception?
A. Make sure that your station is functioning properly and that it does not cause interference to your own radio or television when it is tuned to the same channel
B. Immediately turn off your transmitter and contact the nearest FCC office for assistance
C. Install a harmonic doubler on the output of your transmitter and tune it until the interference is eliminated
D. All these choices are correct

## Slide 38: T7B06 - Which of the following actions should you take if a neighbor tells you that your station’s transmissions are interfering with their radio or TV reception?
A. Make sure that your station is functioning properly and that it does not cause interference to your own radio or television when it is tuned to the same channel
B. Immediately turn off your transmitter and contact the nearest FCC office for assistance
C. Install a harmonic doubler on the output of your transmitter and tune it until the interference is eliminated
D. All these choices are correct

## Slide 39: T7B07 - Which of the following can reduce overload of a VHF transceiver by a nearby FM broadcast station?
Installing an RF preamplifier
Using double-shielded coaxial cable
Installing bypass capacitors on the microphone cable
Installing a band-reject filter

## Slide 40: T7B07 - Which of the following can reduce overload of a VHF transceiver by a nearby FM broadcast station?
Installing an RF preamplifier
Using double-shielded coaxial cable
Installing bypass capacitors on the microphone cable
Installing a band-reject filter

## Slide 41: T7B08 - What should you do if something in a neighbor’s home is causing harmful interference to your amateur station?
A. Work with your neighbor to identify the offending device
B. Politely inform your neighbor that FCC rules prohibit the use of devices that cause interference
C. Make sure your station meets the standards of good amateur practice
D. All of these choices are correct

## Slide 42: T7B08 - What should you do if something in a neighbor’s home is causing harmful interference to your amateur station?
A. Work with your neighbor to identify the offending device
B. Politely inform your neighbor that FCC rules prohibit the use of devices that cause interference
C. Make sure your station meets the standards of good amateur practice
D. All of these choices are correct

## Slide 43: T7B09 – What should be the first step to resolve non-fiber optic cable TV interference caused by your amateur radio transmission?
A. Add a low-pass filter to the TV antenna input
B. Add a high-pass filter to the TV antenna input
C. Add a preamplifier to the TV antenna input
D. Be sure all TV feed line coaxial connectors are installed properly

## Slide 44: T7B09 – What should be the first step to resolve non-fiber optic cable TV interference caused by your amateur radio transmission?
A. Add a low-pass filter to the TV antenna input
B. Add a high-pass filter to the TV antenna input
C. Add a preamplifier to the TV antenna input
D. Be sure all TV feed line coaxial connectors are installed properly

## Slide 45: T7B10 - What might be the problem if you receive a report that your audio signal through an FM repeater is distorted or unintelligible?
A. Your transmitter may be slightly off frequency
B. Your batteries are running low
C. You could be in a bad location
D. All of these choices are correct

## Slide 46: T7B10 - What might be the problem if you receive a report that your audio signal through an FM repeater is distorted or unintelligible?
A. Your transmitter may be slightly off frequency
B. Your batteries are running low
C. You could be in a bad location
D. All of these choices are correct

## Slide 47: T7B11 - What is a symptom of RF feedback in a transmitter or transceiver?
A. Excessive SWR at the antenna connection
B. The transmitter will not stay on the desired frequency
C. Reports of garbled, distorted, or unintelligible transmissions
D. Frequent blowing of power supply fuses

## Slide 48: T7B11 - What is a symptom of RF feedback in a transmitter or transceiver?
A. Excessive SWR at the antenna connection
B. The transmitter will not stay on the desired frequency
C. Reports of garbled, distorted, or unintelligible transmissions
D. Frequent blowing of power supply fuses

## Slide 49: T7C – Antenna and transmissions line measurements and troubleshooting
measuring SWR, effects of high SWR, causes of feed line failures; Basic coaxial cable characteristics; Use of dummy loads when testing

## Slide 50: Feedlines
Feedlines carry RF signals from the radio to the antenna
Common feedlines are coax, twin lead, ladder or window line
The longer the feedline, the more loss that occurs
Larger feedlines generally have less loss
Loss is caused by RF energy being converted to heat
Feedline impedance must match the radio and antenna for maximum power transfer
Air dielectric in coax is low loss but may allow water entry
Ultraviolet light degrades insulation which may crack and allow water entry
Corrosion from water exposure is the #1 coax killer

## Slide 51: Antenna Analyzer and SWR
Antenna analyzers can be used to verify antenna impedance (match).
A perfect SWR of 1:1 is ideal but anything less than 2:1 is OK and over 3:1 the antenna should be checked.
SWR is not a performance measurement
Dummy loads are perfect at 1:1 but don’t transmit

## Slide 52: Antenna and SWR Analyzers

## Slide 53: T7C01 - What is the primary purpose of a dummy load?
A. To prevent transmitting signa;ls over the air when making test
B. To prevent over-modulation of your transmitter
C. To improve the efficiency of an antenna
D. To improve the signal to noise ratio of your receiver

## Slide 54: T7C01 - What is the primary purpose of a dummy load?
A. To prevent transmitting signals over the air when making test
B. To prevent over-modulation of your transmitter
C. To improve the efficiency of an antenna
D. To improve the signal to noise ratio of your receiver

## Slide 55: T7C02 - Which of the following is used to determine if an antenna is resonant at the desired operating frequency?
A. A VTVM
B. An antenna analyzer
C. A Q meter
D. A frequency counter

## Slide 56: T7C02 - Which of the following is used to determine if an antenna is resonant at the desired operating frequency?
A. A VTVM
B. An antenna analyzer
C. A Q meter
D. A frequency counter

## Slide 57: T7C03 – What does a dummy load consist of?
A. A high-gain amplifier and a TR switch
B. A non-inductive resistor mounted on a heat sink
A low-voltage power supply and a DC relay
A 50-ohm reactance used t terminate a transmission line

## Slide 58: T7C03 – What does a dummy load consist of?
A. A high-gain amplifier and a TR switch
B. A non-inductive resistor mounted on a heat sink
A low-voltage power supply and a DC relay
A 50-ohm reactance used t terminate a transmission line

## Slide 59: T7C04 - What reading on an SWR meter indicates a perfect impedance match between the antenna and the feed line?
A. 50:50
B. Zero
C. 1 to 1
D. Full Scale

## Slide 60: T7C04 - What reading on an SWR meter indicates a perfect impedance match between the antenna and the feed line?
A. 50:50
B. Zero
C. 1 to 1
D. Full Scale

## Slide 61: T7C05 – Why do most solid-state transmitters reduce output power as SWR increases beyond a certain level?
To protect the output amplifier transistors
To comply with FCC rules on spectral purity
Because power supplies cannot supply enough current at high SWR
To lower the SWR on the transmission line

## Slide 62: T7C05 – Why do most solid-state transmitters reduce output power as SWR increases beyond a certain level?
To protect the output amplifier transistors
To comply with FCC rules on spectral purity
Because power supplies cannot supply enough current at high SWR
To lower the SWR on the transmission line

## Slide 63: T7C06 - What does an SWR reading of 4:1 indicate?
A. Loss of -4dB
B. Good impedance match
C. Gain of +4dB
D. Impedance mismatch

## Slide 64: T7C06 - What does an SWR reading of 4:1 indicate?
A. Loss of -4dB
B. Good impedance match
C. Gain of +4dB
D. Impedance mismatch

## Slide 65: T7C07 - What happens to power lost in a feed line?
A. It increases the SWR
B. It is radiated as harmonics
C. It is converted into heat
D. It distorts the signal

## Slide 66: T7C07 - What happens to power lost in a feed line?
A. It increases the SWR
B. It is radiated as harmonics
C. It is converted into heat
D. It distorts the signal

## Slide 67: T7C08 - What instrument can be use to determine SWR?
A. Voltmeter
B. Ohmmeter
C. Iambic pentameter
D. Directional wattmeter

## Slide 68: T7C08 - What instrument can be use to determine SWR?
A. Voltmeter
B. Ohmmeter
C. Iambic pentameter
D. Directional wattmeter
Notes: Note: The upper right meter shows a good low SWR. The forward power needle (right one) is full scale and pointig to 11:30. The Reflected power needle is resting on the 0 Wattage line. This SWR is read where the needles cross, or on the 1 to 1 line.
The lower center meter shows high SWR. Forward power needle is on 1 and the Reverse power needle is by the 0.6 point These needles cross by the 5 to 1 line, which is high SWR.

## Slide 69: T7C09 - Which of the following causes failure of coaxial cables?
A. Moisture contamination
Solder flux contamination
Rapid fluctuation in the transmitter output power
D. Operation at 100% duty cycle for an extended period

## Slide 70: T7C09 - Which of the following causes failure of coaxial cables?
A. Moisture contamination
Solder flux contamination
Rapid fluctuation in the transmitter output power
D. Operation at 100% duty cycle for an extended period

## Slide 71: T7C10 - Why should the outer jacket of coaxial cable be resistant to ultraviolet light?
A. Ultraviolet resistant jackets prevent harmonic radiation
B. Ultraviolet light can increase losses in the cable’s jacket
C. Ultraviolet and RF signals can mix, causing interference
D. Ultraviolet light can damage the jacket and allow water to enter the cable

## Slide 72: T7C10 - Why should the outer jacket of coaxial cable be resistant to ultraviolet light?
A. Ultraviolet resistant jackets prevent harmonic radiation
B. Ultraviolet light can increase losses in the cable’s jacket
C. Ultraviolet and RF signals can mix, causing interference
D. Ultraviolet light can damage the jacket and allow water to enter the cable

## Slide 73: T7C11 - What is a disadvantage of air core coaxial cable when compared to foam or solid dielectric types?
A. It has more loss per foot
B. It cannot be used for VHF or UHF antennas
C. It requires special techniques to prevent water absorption
D. It cannot be used at below freezing temperatures

## Slide 74: T7C11 - What is a disadvantage of air core coaxial cable when compared to foam or solid dielectric types?
A. It has more loss per foot
B. It cannot be used for VHF or UHF antennas
C. It requires special techniques to prevent water absorption
D. It cannot be used at below freezing temperatures

## Slide 75: T7D – Using basic test instruments
Voltmeters ammeter, and ohmmeter; Soldering

## Slide 76: T7D01 - Which instrument would you use to measure electric potential?
A. An ammeter
B. A voltmeter
C. A wavemeter
D. An ohmmeter

## Slide 77: T7D01 - Which instrument would you use to measure electric potential?
A. An ammeter
B. A voltmeter
C. A wavemeter
D. An ohmmeter

## Slide 78: T7D02 - How is a voltmeter connected to a component to measure applied voltage?
A. In series
B. In parallel
C. In quadrature
D. In phase

## Slide 79: T7D02 - How is a voltmeter connected to a component to measure applied voltage?
A. In series
B. In parallel
C. In quadrature
D. In phase

## Slide 80: T7D03 – When configured to measure current, how is a multimeter connected to a component?
A. In series
B. In parallel
C. In quadrature
D. In phase

## Slide 81: T7D03 – When configured to measure current, how is a multimeter connected to a component?
A. In series
B. In parallel
C. In quadrature
D. In phase

## Slide 82: T7D04 - Which instrument is used to measure electric current?
A. An ohmmeter
B. A electrometer
C. A voltmeter
D. An ammeter

## Slide 83: T7D04 - Which instrument is used to measure electric current?
A. An ohmmeter
B. A electrometer
C. A voltmeter
D. An ammeter

## Slide 84: T7D06 - Which of the following can damage a multimeter?
A. Attempting to measure resistance using the voltage setting
B. Failing to connect one of the probes to ground
C. Attempting to measure voltage when using the resistance setting
D. Not allowing it to warm up properly

## Slide 85: T7D06 - Which of the following can damage a multimeter?
A. Attempting to measure resistance using the voltage setting
B. Failing to connect one of the probes to ground
C. Attempting to measure voltage when using the resistance setting
D. Not allowing it to warm up properly

## Slide 86: T7D07 - Which of the following measurements are made using a multimeter?
A. Signal strength and noise
B. Impedance and reactance
C. Voltage and resistance
D. All these choices are correct

## Slide 87: T7D07 - Which of the following measurements are made using a multimeter?
A. Signal strength and noise
B. Impedance and reactance
C. Voltage and resistance
D. All these choices are correct

## Slide 88: T7D08 - Which of the following types of solder should not be used for radio and electronic applications?
A. Acid-core solder
B. Lead-tin solder
C. Rosin-core solder
D. Tin-copper solder

## Slide 89: T7D08 - Which of the following types of solder should not be used for radio and electronic applications?
A. Acid-core solder
B. Lead-tin solder
C. Rosin-core solder
D. Tin-copper solder

## Slide 90: T7D09 - What is the characteristic appearance of a cold tin-lead solder joint?
A. Dark black spots
B. A bright or shiny surface
C. A rough or lumpy surface
D. Excessive solder

## Slide 91: T7D09 - What is the characteristic appearance of a cold tin-lead solder joint?
A. Dark black spots
B. A bright or shiny surface
C. A rough or lumpy surface
D. Excessive solder

## Slide 92: T7D10 - What reading indicates that an ohmmeter is connected across a large, discharged capacitor?
A. Increasing resistance with time
B. Decreasing resistance with time
C. Steady full-scale reading
D. Alternating between open and short circuit

## Slide 93: T7D10 - What reading indicates that an ohmmeter is connected across a large, discharged capacitor?
A. Increasing resistance with time
B. Decreasing resistance with time
C. Steady full-scale reading
D. Alternating between open and short circuit

## Slide 94: T7D11 - Which of the following precautions should be taken when measuring in-circuit resistance with an ohmmeter?
A. Ensure that the applied voltages are correct
B. Ensure that the circuit is not powered
C. Ensure that the circuit is grounded
D. Ensure that the circuit is operating at the correct frequency

## Slide 95: T7D11 - Which of the following precautions should be taken when measuring in-circuit resistance with an ohmmeter?
A. Ensure that the applied voltages are correct
B. Ensure that the circuit is not powered
C. Ensure that the circuit is grounded
D. Ensure that the circuit is operating at the correct frequency

## Slide 96: End of SUBELEMENT T7
Station equipment: common transmitter and receiver problems; antenna measurements; troubleshooting; basic repair and testing