## Slide 1: SUBELEMENT T8
Signals and Emissions
[4 Exam Questions - 4 Groups]
Notes: Subelement T8 Signals and Emissions. Technician Training Slides for 2022 Question Pool Good through June 30, 2026 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM, Howard Schultz, W7HS.

## Slide 2
T8A – Basic characteristic of FM and SB: bandwidth of various modulation modes; CW, SSB, FM, fast-scan TV; Choice of emission type: selection of USB vs LSB, use of SSB for weak signal work, use of FM for VHF packet and repeaters
T8B - Amateur satellite operation: Doppler shift, basic orbits, operating protocols; modulation mode selection, transmitter power considerations, telemetry and telecommand, satellite tracking programs, beacons, uplink and downlink mode definitions, spin fading, definition of “LEO”, setting uplink powers
T8C – Operating activities: radio direction finding;,contests, linking over the internet, exchanging grid locators
T8D – Non-voice communications: image signals and definition of NTSC, CW, packet radio, PSK, APRS, error-detection and correction, amateur radio networking, Digital Mobile Radio, WSJT modes, Broadband-Hamnet

## Slide 3: Sample Emission Modes
Mode | Type | Bandwidth | Content
CW | Telegraphy | 10 Hz | Text Data
SSB | Telephony | 2800 Hz | Voice
AM | Telephony | 6 kHz | Voice
FM | Telephony | 5-15 kHz | Voice
SSTV / Fax | Image | 2800 Hz | Image
ATV | Image | 6 MHz | Image
PSK31 | Data | 31 Hz | Text Data
RTTY | Data | 250 Hz | Text Data
Pactor (I, II, III) | Data | 500-2800 Hz | Binary Data
AX.25 Packet | Data | 10-20 kHz | Binary Data

## Slide 4: Amplitude Modulation
An unmodulated RF
carrier wave
A carrier wave amplitude
modulated (AM) with a simple audio tone
Notes: Note the identical sidebands. They peak and dip together.

## Slide 5: SDR AM Signal

## Slide 6: SSB Signal

## Slide 7: Amplitude Modulation
An unmodulated RF
carrier requires narrow
bandwidth
Modulation of the carrier
creates sidebands. This
requires more bandwidth.
Transmitter power is spread across this bandwidth

## Slide 8: AM and SSB
The carrier contains no
audio information.
The sidebands contain
duplicate audio information
By filtering out the carrier and one sideband,
we save spectrum and concentrate our RF
energy into a narrower bandwidth. SSB is
therefore more efficient.

## Slide 9: Frequency Modulation
Unmodulated carrier, full power at all times
Waveform of modulating signal
Modulated carrier with frequency deviation and constant amplitude
“Over modulation” called “over deviation” on FM, causes the signal to become wider and potentially cause adjacent channel interference. Phase Modulation (PM) uses a reactance modulator and is similar to FM and can be received with the same equipment.

## Slide 10: Common Required Bandwidth
CW – 5-10Hz
Phone / Voice
  SSB - 2-3 kHz
  AM – 4-6 kHz
  FM – 5-15 kHz
Digital
  PSK31 – 31 Hz
  RTTY – 250 Hz
Slow Scan TV – 3 KHz
Fast Scan TV – 6 Mhz

## Slide 11: Amateur Television Signal
A 6 MHz ATV video channel with the video carrier 1.25 MHz up from the lower edge. The color subcarrier is at 3.58 MHz and the sound subcarrier at 4.5 MHz above the video carrier.
The Luminance, Chrominance and Audio carriers are visible in the spectrum plot at left

## Slide 12: T8A01 - Which of the following is a form of amplitude modulation?
A. Spread-spectrum
B. Packet radio
C. Single sideband
D. Phase shift keying

## Slide 13: T8A01 - Which of the following is a form of amplitude modulation?
A. Spread-spectrum
B. Packet radio
C. Single sideband
D. Phase shift keying

## Slide 14: T8A02 - What type of modulation is commonly used for VHF packet radio transmissions?
A. FM or PM
B. SSB
C. AM
D. PSK

## Slide 15: T8A02 - What type of modulation is commonly used for VHF packet radio transmissions?
A. FM or PM
B. SSB
C. AM
D. PSK

## Slide 16: T8A03 - Which type of voice mode is often used for long-distance (weak signal) contacts on the VHF and UHF bands?
A. FM
B. DRM
C. SSB
D. PM

## Slide 17: T8A03 - Which type of voice mode is often used for long-distance (weak signal) contacts on the VHF and UHF bands?
A. FM
B. DRM
C. SSB
D. PM

## Slide 18: T8A04 - Which type of modulation is commonly used for VHF and UHF voice repeaters?
A. AM
B. SSB
C. PSK
D. FM or PM

## Slide 19: T8A04 - Which type of modulation is commonly used for VHF and UHF voice repeaters?
A. AM
B. SSB
C. PSK
D. FM or PM

## Slide 20: T8A05 - Which of the following types of signal has the narrowest bandwidth?
A. FM voice
B. SSB voice
C. CW
D. Slow-scan TV

## Slide 21: T8A05 - Which of the following types of signal has the narrowest bandwidth?
A. FM voice
B. SSB voice
C. CW
D. Slow-scan TV

## Slide 22: T8A06 - Which sideband is normally used for 10 meter HF, VHF and UHF single-sideband communications?
A. Upper sideband
B. Lower sideband
C. Suppressed sideband
D. Inverted sideband

## Slide 23: T8A06 - Which sideband is normally used for 10 meter HF, VHF and UHF single-sideband communications?
A. Upper sideband
B. Lower sideband
C. Suppressed sideband
D. Inverted sideband

## Slide 24: T8A07 - What is a characteristic of single sideband (SSB) compare to FM?
A. SSB signals are easier to tune
B. SSB signals are less susceptible to interference
C. SSB signals have narrower bandwidth
D. All of these choices are correct

## Slide 25: T8A07 - What is a characteristic of single sideband (SSB) compare to FM?
A. SSB signals are easier to tune
B. SSB signals are less susceptible to interference
C. SSB signals have narrower bandwidth
D. All of these choices are correct

## Slide 26: T8A08 - What is the approximate bandwidth of a typical single sideband ( SSB ) voice signal?
A. 1 kHz
B. 3 kHz
C. 6 kHz
D. 15 kHz

## Slide 27: T8A08 - What is the approximate bandwidth of a typical single sideband ( SSB ) voice signal?
A. 1 kHz
B. 3 kHz
C. 6 kHz
D. 15 kHz

## Slide 28: T8A09 - What is the approximate bandwidth of a VHF repeater FM voice signal?
A. Less than 500 Hz
B. About 150 kHz
C. Between 10 and 15 kHz
D. Between 50 and 125 kHz

## Slide 29: T8A09 - What is the approximate bandwidth of a VHF repeater FM voice signal?
A. Less than 500 Hz
B. About 150 kHz
C. Between 10 and 15 kHz
D. Between 50 and 125 kHz

## Slide 30: T8A10 - What is the approximate bandwidth of AM fast-scan TV transmissions?
A. More than 10 MHz
B. About 6 MHz
C. About 3 MHz
D. About 1 MHz

## Slide 31: T8A10 - What is the approximate bandwidth of AM fast-scan TV transmissions?
A. More than 10 MHz
B. About 6 MHz
C. About 3 MHz
D. About 1 MHz

## Slide 32: T8A11 - What is the approximate bandwidth required to transmit a CW signal?
A. 2.4 kHz
B. 150 Hz
C. 1000 Hz
D. 15 kHz

## Slide 33: T8A11 - What is the approximate bandwidth required to transmit a CW signal?
A. 2.4 kHz
B. 150 Hz
C. 1000 Hz
D. 15 kHz

## Slide 34: T8A12 – Which of the following is a disadvantage of FM compared with single sideband?
A. Voice quality is poorer
B. Only one signal can be received at a time
C. FM signals are harder to tune
D. All these choices ae corect

## Slide 35: T8A12 – Which of the following is a disadvantage of FM compared with single sideband?
A. Voice quality is poorer
B. Only one signal can be received at a time
C. FM signals are harder to tune
D. All these choices ae corect

## Slide 36: G4D11 How close to the upper edge of the 20 meter General Class band should your displayed carrier frequency be when using 3 kHz wide USB?
  A. 3 kHz above the edge of the band
  B. 3 kHz below the edge of the band
  C. Your displayed carrier frequency may be set at the edge of the band
  D. Center your signal on the edge of the band

## Slide 37: G4D11 How close to the upper edge of the 20 meter General Class band should your displayed carrier frequency be when using 3 kHz wide USB?
  A. 3 kHz above the edge of the band
  B. 3 kHz below the edge of the band
  C. Your displayed carrier frequency may be set at the edge of the band
  D. Center your signal on the edge of the band

## Slide 38: G8A12 What signal(s) would be found at the output of a properly adjusted balanced modulator?
  A. Both upper and lower sidebands
  B. Either upper or lower sideband, but not both
  C. Both upper and lower sidebands and the carrier
  D. The modulating signal and the unmodulated carrier

## Slide 39: G8A12 What signal(s) would be found at the output of a properly adjusted balanced modulator?
  A. Both upper and lower sidebands
  B. Either upper or lower sideband, but not both
  C. Both upper and lower sidebands and the carrier
  D. The modulating signal and the unmodulated carrier

## Slide 40: T8B - Amateur satellite operation
Doppler shift, basic orbits, operating protocols; modulation mode selection, transmitter power considerations, telemetry and telecommand, satellite tracking programs, beacons, uplink and downlink mode definitions, spin fading, definition of “LEO”, setting uplink powers

## Slide 41: G8B01 What receiver stage combines a 14.250 MHz input signal with a 13.795 MHz oscillator signal to produce a 455 kHz intermediate frequency (IF) signal?
  A. Mixer
  B. BFO
  C. VFO
  D. Discriminator

## Slide 42: G8B01 What receiver stage combines a 14.250 MHz input signal with a 13.795 MHz oscillator signal to produce a 455 kHz intermediate frequency (IF) signal?
  A. Mixer
  B. BFO
  C. VFO
  D. Discriminator

## Slide 43: Susan J. Helms, KC7NHZ Flight Engineer - ISS
Notes: Most astronauts are licensed hams. Most often they get their Technician licenses so they are allowed to operate the ISS radio station.
Photo from NASA

## Slide 44: T8B01 What telemetry information is typically transmitted by satellite beacons?
A. The signal strength of received signals
B. Time of day accurate to plus or minus 1/10 second
C. Health and status of the satellite
D. All of these choices are correct

## Slide 45: T8B01 What telemetry information is typically transmitted by satellite beacons?
A. The signal strength of received signals
B. Time of day accurate to plus or minus 1/10 second
C. Health and status of the satellite
D. All of these choices are correct

## Slide 46: T8B02 What is the impact of using excessive effective radiated power on a satellite uplink?
A. Possibility of commanding the satellite to an improper mode
B. Blocking access by other users
C. Overloading the satellite batteries
D. Possibility of rebooting the satellite control computer

## Slide 47: T8B02 What is the impact of using excessive effective radiated power on a satellite uplink?
A. Possibility of commanding the satellite to an improper mode
B. Blocking access by other users
C. Overloading the satellite batteries
D. Possibility of rebooting the satellite control computer

## Slide 48: T8B03 - Which of the following are provided by satellite tracking programs?
A. Maps showing the real-time position of the satellite track over the earth
B. The time, azimuth, and elevation of the start, maximum altitude, and end of a pass
C. The apparent frequency of the satellite transmission, including effects of Doppler shift
D. All of these answers are correct

## Slide 49: T8B03 - Which of the following are provided by satellite tracking programs?
A. Maps showing the real-time position of the satellite track over the earth
B. The time, azimuth, and elevation of the start, maximum altitude, and end of a pass
C. The apparent frequency of the satellite transmission, including effects of Doppler shift
D. All of these answers are correct

## Slide 50: T8B04 What mode of transmission is commonly used by amateur radio satellites?
A. SSB
B. FM
C. CW/data
D. All of these choices are correct

## Slide 51: T8B04 What mode of transmission is commonly used by amateur radio satellites?
A. SSB
B. FM
C. CW/data
D. All of these choices are correct

## Slide 52: T8B05 - What is a satellite beacon?
A. The primary transmit antenna on the satellite
B. An indicator light that that shows where to point your antenna
C. A reflective surface on the satellite
D. A transmission from a space satellite that contains status information

## Slide 53: T8B05 - What is a satellite beacon?
A. The primary transmit antenna on the satellite
B. An indicator light that that shows where to point your antenna
C. A reflective surface on the satellite
D. A transmission from a satellite that contains status information

## Slide 54: T8B06 - Which of the following are inputs to a satellite tracking program?
A. The satellite transmitted power
B. The Keplerian elements
C. The last observed time of zero Doppler shift
D. All of these answers are correct

## Slide 55: T8B06 - Which of the following are inputs to a satellite tracking program?
A. The satellite transmitted power
B. The Keplerian elements
C. The last observed time of zero Doppler shift
D. All of these answers are correct

## Slide 56: Keplerian Data Sample

## Slide 57: Doppler Shift
Doppler shift is a change in frequency as an object moves. The wave in front of the object is compressed and expanded behind.
To a fixed observer, the shortened wavelength in front causes the frequency to increase. As the object passes, the longer wavelength behind will cause the frequency to shift down.

## Slide 58: T8B07 - With is Doppler shift in reference to satellite communications?
A. A change in the satellite orbit
B. A mode where the satellite receives signals on one band and transmits on another
C. An observed change in signal frequency caused by relative motion between the satellite and the earth station
D. A special digital communications mode for some satellites

## Slide 59: T8B07 - With is Doppler shift in reference to satellite communications?
A. A change in the satellite orbit
B. A mode where the satellite receives signals on one band and transmits on another
C. An observed change in signal frequency caused by relative motion between the satellite and the earth station
D. A special digital communications mode for some satellites

## Slide 60: T8B08 - What is meant by the statement that a satellite is operating in mode U/V?
A. The satellite uplink is in the 15 meter band and the downlink is in the 10 meter band
B. The satellite uplink is in the 70 cm band and the downlink is in the 2 meter band
C. The satellite operates using ultraviolet frequencies
D. The satellite frequencies are usually variable

## Slide 61: T8B08 - What is meant by the statement that a satellite is operating in mode U/V?
A. The satellite uplink is in the 15 meter band and the downlink is in the 10 meter band
B. The satellite uplink is in the 70 cm band and the downlink is in the 2 meter band
C. The satellite operates using ultraviolet frequencies
D. The satellite frequencies are usually variable

## Slide 62: T8B09 - What causes spin fading of satellite signals?
A. Circular polarized noise interference radiated from the sun
B. Rotation of the satellite and its antennas
C. Doppler shift of the received signal
D. Interfering signals within the satellite uplink band

## Slide 63: T8B09 - What causes spin fading of satellite signals?
A. Circular polarized noise interference radiated from the sun
B. Rotation of the satellite and its antennas
C. Doppler shift of the received signal
D. Interfering signals within the satellite uplink band

## Slide 64: T8B10 - What is a LEO satellite?
A sun synchronous satellite
A highly elliptical orbit satellite
C. A satellite in low energy operation mode
D. A satellite in low earth orbit

## Slide 65: T8B10 - What is a LEO satellite?
A sun synchronous satellite
A highly elliptical orbit satellite
C. A satellite in low energy operation mode
D. A satellite in low earth orbit

## Slide 66: T8B11 - Who may receive telemetry from a space station?
A. Anyone B. A licensed radio amateur with a transmitter equipped for interrogating the satellite C. A licensed radio amateur who has been certified by the protocol developer
D. A licensed radio amateur who has registered for an access code from AMSAT

## Slide 67: T8B11 - Who may receive telemetry from a space station?
A. Anyone B. A licensed radio amateur with a transmitter equipped for interrogating the satellite C. A licensed radio amateur who has been certified by the protocol developer
D. A licensed radio amateur who has registered for an access code from AMSAT

## Slide 68: T8B12 Which of the following is a way to determine whether your uplink power is neither too low nor too high?
A. Check your signal strength report in the telemetry data
B. Listen for distortion on your downlink signal
C. Your signal strength on the downlink should be about the same as the beacon
D. All of these choices are correct

## Slide 69: T8B12 Which of the following is a way to determine whether your uplink power is neither too low nor too high?
A. Check your signal strength report in the telemetry data
B. Listen for distortion on your downlink signal
C. Your signal strength on the downlink should be about the same as the beacon
D. All of these choices are correct

## Slide 70: T8C – Operating activities
radio direction finding; radio control; contests; linking over the Internet; exchanging grid locators

## Slide 71: T8C01 - Which of the following methods is used to locate sources of noise interference or jamming?
A. Echolocation
B. Doppler radar
C. Radio direction finding
D. Phase locking

## Slide 72: T8C01 - Which of the following methods is used to locate sources of noise interference or jamming?
A. Echolocation
B. Doppler radar
C. Radio direction finding
D. Phase locking

## Slide 73: T8C02 - Which of these items would be useful for a hidden transmitter hunt?
A. Calibrated SWR meter
B. A directional antenna
C. A calibrated noise bridge
D. All of these choices are correct

## Slide 74: T8C02 - Which of these items would be useful for a hidden transmitter hunt?
A. Calibrated SWR meter
B. A directional antenna
C. A calibrated noise bridge
D. All of these choices are correct

## Slide 75: T8C03 - What operating activity involves contacting as many stations as possible during a specified period?
A. Simulated emergency exercises
B. Net operations
C. Public service events
D. Contesting

## Slide 76: T8C03 - What operating activity involves contacting as many stations as possible during a specified period?
A. Simulated emergency exercises
B. Net operations
C. Public service events
D. Contesting

## Slide 77: T8C04 - Which of the following is good procedure when contacting another station in a contest?
A. Sign only the last two letters of your call if there are many other stations calling
B. Contact the station twice to be sure that you are in his log
C. Send only the minimum information needed for proper identification and the contest exchange
D. All of these choices are correct

## Slide 78: T8C04 - Which of the following is good procedure when contacting another station in a contest?
A. Sign only the last two letters of your call if there are many other stations calling
B. Contact the station twice to be sure that you are in his log
C. Send only the minimum information needed for proper identification and the contest exchange
D. All of these choices are correct

## Slide 79: Maidenhead Grids
Two letters and two numbers define an area 1° latitude x 2° longitude anywhere in the world. Seattle is CN87, Portland CN85
Notes: This grid map is courtesy Icom America and is downloadable from their web site at http://www.icomamerica.com.
Two letter designator followed by a number ranging from 1 to 100 representing 1° latitude x 2° longitude square area of the earth.
  The earth is divided into 20° Latitude x 10° Longitude squares starting on the date line at the south pole and going North and East.
  Each square is given a two letter designator labeled East and North starting with AA and Ending with RR
  An – In are West of GMT, Jn – Rn are east of GMT
  nA – n I are South of the equator, nJ – nR are North of the equator
  Each square is further divided into 100 1°x2° squares and given a number starting in the lower left corner of the square and are labeled up and right
  Seattle is in CN-87, Los Angles DM-04
  Spokane is in DN-17

## Slide 80: T8C05 - What is a grid locator?
A. A letter-number designator assigned to a geographic location
B. A letter-number designator assigned to an azimuth and elevation
C. An instrument for neutralizing a final amplifier
D. An instrument for radio direction finding

## Slide 81: T8C05 - What is a grid locator?
A. A letter-number designator assigned to a geographic location
B. A letter-number designator assigned to an azimuth and elevation
C. An instrument for neutralizing a final amplifier
D. An instrument for radio direction finding

## Slide 82: EchoLink® and IRLP
EchoLink® software allows licensed Amateur Radio stations to communicate with one another over the Internet, using voice-over-IP (VoIP) technology.
Gateway
Gateway

## Slide 83: T8C06 - How is over the air to IRLP node accomplished?
A. By obtaining a password which is sent via voice to the node
B. By using DTMF signals
C. By entering the proper Internet password
D . By using CTCSS tone codes

## Slide 84: T8C06 - How is over the air to IRLP node accomplished?
A. By obtaining a password which is sent via voice to the node
B. By using DTMF signals
C. By entering the proper Internet password
D . By using CTCSS tone codes

## Slide 85: T8C07 - What is Voice Over Internet Protocol ( VoIP ) ?
A. A set of rules specifying how to identify your station when linked over the internet to another station
B. A technique employed to “spot” DX stations via the internet
C. A technique for measuring the modulation quality of a transmitter using remote sites monitored via the internet
D. A method of delivering voice communications over the internet using digital techniques

## Slide 86: T8C07 - What is Voice Over Internet Protocol ( VoIP ) ?
A. A set of rules specifying how to identify your station when linked over the internet to another station
B. A technique employed to “spot” DX stations via the internet
C. A technique for measuring the modulation quality of a transmitter using remote sites monitored via the internet
D. A method of delivering voice communications over the internet using digital techniques

## Slide 87: T8C08 - What is the Internet Radio Linking Project ( IRLP ) ?
A. A technique to connect amateur radio systems, such as repeaters, via the internet using Voice Over Internet Protocol ( VoIP )
B. A system for providing access to websites via amateur radio
C. A system for informing amateurs in real time of the frequency of active DX stations
D. A technique for measuring signal strength of an amateur transmitter via the internet

## Slide 88: T8C08 - What is the Internet Radio Linking Project ( IRLP ) ?
A. A technique to connect amateur radio systems, such as repeaters, via the internet using Voice Over Internet Protocol ( VoIP )
B. A system for providing access to websites via amateur radio
C. A system for informing amateurs in real time of the frequency of active DX stations
D. A technique for measuring signal strength of an amateur transmitter via the internet

## Slide 89: EchoLink® and IRLP
EchoLink® software allows licensed Amateur Radio stations to communicate with one another over the Internet, using voice-over-IP (VoIP) technology.
Gateway
Gateway

## Slide 90: T8C09 – Which of the following protocols enables an amateur station to transmit through a repeater without using a radio to initate the transmission?
IRLP
D-STAR
DMR
Echolink

## Slide 91: T8C09 – Which of the following protocols enables an amateur station to transmit through a repeater without using a radio to initate the transmission?
IRLP
D-STAR
DMR
Echolink

## Slide 92: T8C10 - What is required before using EchoLink system?
A. Complete the required EchoLink training B. Purchased a license to use the EchoLink software C. Register your call sign and provide proof of license
D. All these choices are correct

## Slide 93: T8C10 - What is required before using EchoLink system?
A. Complete the required EchoLink training B. Purchased a license to use the EchoLink software C. Register your call sign and provide proof of license
D. All these choices are correct

## Slide 94: T8C11 - What is an amateur radio station that connects other amateur stations to the Internet?
A. A gateway
B. A repeater
C. A digipeater
D. A beacon

## Slide 95: T8C11 - What is an amateur radio station that connects other amateur stations to the Internet?
A. A gateway
B. A repeater
C. A digipeater
D. A beacon

## Slide 96: T8D – Non-voice communications
Non-voice and digital communications; image signals and definition of NTSC, CW, packet radio, PSK, APRS, error-detection and correction, amateur radio networking, Digital Mobile Radio, WSJT ,odes, Broadband-Hamnet

## Slide 97: T8D01 - Which of the following is a digital communications mode?
A. Packet radio
B. IEEE 802.11
C. FT8
D. All of these choices are correct

## Slide 98: T8D01 - Which of the following is a digital communications mode?
A. Packet radio
B. IEEE 802.11
C. FT8
D. All of these choices are correct

## Slide 99: APRS Automatic Position Reporting System
Real-time
location
Mapping
Texting

## Slide 100: T8D02 - What is a “talkgroup” on a DMR repeater?
A. A group of operators sharing common interests
B. A way for groups of users to share a channel at different times without hearing other users on the channel
C. A protocol that increases the signal-to-noise ration when multiple repeaters are linked together
D. A net that meets at a specified time

## Slide 101: T8D02 - What is a “talkgroup” on a DMR repeater?
A. A group of operators sharing common interests
B. A way for groups of users to share a channel at different times without hearing other users on the channel
C. A protocol that increases the signal-to-noise ration when multiple repeaters are linked together
D. A net that meets at a specified time

## Slide 102: T8D03 – What kind of data can be transmitted by APRS?
A. GPS position data
B. Text messages
C. Weather data
D. All these choices are correct

## Slide 103: T8D03 – What kind of data can be transmitted by APRS?
A. GPS position data
B. Text messages
C. Weather data
D. All these choices are correct

## Slide 104: National Television Systems Committee (NTSC)
Television Standards
  NTSC – Canada, US, Japan, South Korea
  PAL
  SECAM

## Slide 105: T8D04 - What type of transmission is indicated by the term NTSC?
A. A Normal Transmission mode in Static Circuit
B. A special mode for earth satellite uplink
C. An analog fast scan color TV signal
D. A frame compression scheme for TV signals

## Slide 106: T8D04 - What type of transmission is indicated by the term NTSC?
A. A Normal Transmission mode in Static Circuit
B. A special mode for earth satellite uplink
C. An analog fast scan color TV signal
D. A frame compression scheme for TV signals

## Slide 107: T8D05 - Which of the following is an application of APRS?
A. Providing real time tactical digital communications in conjunction with a map showing the locations of stations
B. Showing automatically the number of packets transmitted via PACTOR during a specific time interval
C. Providing voice over Internet connection between repeaters
D. Providing information on the number of stations signed into a repeater

## Slide 108: T8D05 - Which of the following is an application of APRS?
A. Providing real time tactical digital communications in conjunction with a map showing the locations of stations
B. Showing automatically the number of packets transmitted via PACTOR during a specific time interval
C. Providing voice over Internet connection between repeaters
D. Providing information on the number of stations signed into a repeater

## Slide 109: PSK31 Digital Mode
PSK31 is a low speed, narrow bandwidth data mode that provides VERY EFFICIENT keyboard to keyboard chat capability. PSK31 is not error-corrected.

## Slide 110: T8D06 - What does the abbreviation PSK mean?
A. Pulse Shift Keying
B. Phase Shift Keying
C. Packet Short Keying
D. Phased Slide Keying

## Slide 111: T8D06 - What does the abbreviation PSK mean?
A. Pulse Shift Keying
B. Phase Shift Keying
C. Packet Short Keying
D. Phased Slide Keying

## Slide 112: T8D07 - Which of the following describes DMR ?
A. A technique for time-multiplexing two digital voice signals on a single 12.5 kHz repeater channel
B. An automatic position tracking mode for FM mobiles communicating through repeaters
C. An automatic computer logging technique for hands-off logging when communicating while operating a vehicle
D. A digital technique for transmitting on two repeater inputs simultaneously for automatic error correction

## Slide 113: T8D07 - Which of the following describes DMR ?
A. A technique for time-multiplexing two digital voice signals on a single 12.5 kHz repeater channel
B. An automatic position tracking mode for FM mobiles communicating through repeaters
C. An automatic computer logging technique for hands-off logging when communicating while operating a vehicle
D. A digital technique for transmitting on two repeater inputs simultaneously for automatic error correction

## Slide 114: T8D08 - Which of the following is included in packet transmissions?
A. A check sum which permits error detection
B. A header which contains the call sign of the station to which the information is being sent
C. Automatic repeat request in case of error
D. All of these choices are correct

## Slide 115: T8D08 - Which of the following is included in packet transmissions?
A. A check sum which permits error detection
B. A header which contains the call sign of the station to which the information is being sent
C. Automatic repeat request in case of error
D. All of these choices are correct

## Slide 116: T8D09 - What is CW?
A. A type of electromagnetic propagation
B. A digital mode used primarily on 2 meter FM
C. A technique for coil winding
D. Another name for a Morse code transmission

## Slide 117: T8D09 - What is CW?
A. A type of electromagnetic propagation
B. A digital mode used primarily on 2 meter FM
C. A technique for coil winding
D. Another name for a Morse code transmission

## Slide 118: T8D10 - Which of the following operating activities is supported by digital mode software in the WSJT suite?
A. Earth-Moon-Earth B. Weak-signal propagation beacons C. Meteor scatter D. All of these choices are correct

## Slide 119: T8D10 - Which of the following operating activities is supported by digital mode software in the WSJT suite?
A. Earth-Moon-Earth B. Weak-signal propagation beacons C. Meteor scatter D. All of these choices are correct

## Slide 120: T8D11 - What is an ARQ transmission system?
A. A special transmission format limited to video signals
B. A system used to encrypt command signals to an amateur radio satellite
C. An error correction method in which the receiving station detects errors and sends a request for retransmission
D. A method of compressing data using autonomous reiterative Q codes prior to final encoding

## Slide 121: T8D11 - What is an ARQ transmission system?
A. A special transmission format limited to video signals
B. A system used to encrypt command signals to an amateur radio satellite
C. An error correction method in which the receiving station detects errors and sends a request for retransmission
D. A method of compressing data using autonomous reiterative Q codes prior to final encoding

## Slide 122: T8D12 - Which of the following best describes an amateur radio mesh network?
A. An amateur-radio-based data network using commercial Wi-Fi gear with modified firmware
B. A wide-bandwidth digital voice mode employing DRM protocols
C. A satellite communications network using modified commercial satellite TV hardware
D. An internet linking protocol used to network repeaters

## Slide 123: T8D12 - Which of the following best describes an amateur radio mesh network?
A. An amateur-radio-based data network using commercial Wi-Fi gear with modified firmware
B. A wide-bandwidth digital voice mode employing DRM protocols
C. A satellite communications network using modified commercial satellite TV hardware
D. An internet linking protocol used to network repeaters

## Slide 124: T8D13 - What is FT8?
A. A wideband FM voice mode
B. A digital mode capable of operating in low signal-to-noise conditions
C. An eight channel multiplex mode for FM repeaters
D. A digital slow scan TV mode with forward error correction and automatic color compensation

## Slide 125: T8D13 - What is FT8?
A. A wideband FM voice mode
B. A digital mode capable of operating in low signal-to-noise conditions
C. An eight channel multiplex mode for FM repeaters
D. A digital slow scan TV mode with forward error correction and automatic color compensation

## Slide 126: G8B11 How does forward error correction allow the receiver to correct errors in received data packets?
  A. By controlling transmitter output power for optimum signal strength
  B. By using the varicode character set
  C. By transmitting redundant information with the data
  D. By using a parity bit with each character

## Slide 127: G8B11 How does forward error correction allow the receiver to correct errors in received data packets?
  A. By controlling transmitter output power for optimum signal strength
  B. By using the varicode character set
  C. By transmitting redundant information with the data
  D. By using a parity bit with each character

## Slide 128: G8B12 What is the relationship between transmitted symbol rate and bandwidth?
  A. Symbol rate and bandwidth are not related
  B. Higher symbol rates require higher bandwidth
  C. Lower symbol rates require higher bandwidth
  D. Bandwidth is constant for data mode signals

## Slide 129: G8B12 What is the relationship between transmitted symbol rate and bandwidth?
  A. Symbol rate and bandwidth are not related
  B. Higher symbol rates require higher bandwidth
  C. Lower symbol rates require higher bandwidth
  D. Bandwidth is constant for data mode signals

## Slide 130: End of SUBELEMENT T8
Modulation modes: amateur satellite operation; operating activities; non-voice communications