## Slide 1: SUBELEMENT T5
Electrical principles: math for electronics; electronic principles; Ohm’s Law
[4 Exam Questions - 4 Groups]
<number>
T5 - Electrical Plus
Amateur Radio Practices 2014
Notes: Subelement T5 Electrical Principles. Technician Training Slides for 2014 Question Pool Good through June 30, 2018 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM, Howard Schultz, W7HS.
Subelement T4 Amateur Radio Practices. Technician Training Slides for 2014 Question Pool Good through June 30, 2018 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM, Howard Schultz, W7HS.
<number>

## Slide 2
T5A - Electrical principles: units, and terms: current and voltage; conductors and insulators; alternating and direct current
T5B - Math for electronics: conversion of electrical units; decibels; the metric system
T5C - Electronic principles: capacitance; inductance; current flow in circuits; alternating current; definition of RF; DC power calculations; impedance
T5D – Ohm’s Law: formulas and usage
<number>
T5 - Electrical Plus

## Slide 3
Electrical Principles 2010
<number>
Conductors and Insulators
In a conductor, electric current can flow freely, in an insulator it cannot. Simply stated, most metals are good electrical conductors, most nonmetals are not. Metals are also generally good heat conductors while nonmetals are not.
Conductors – Copper, Silver, Gold, Aluminum, Platinum, Steel, …
Insulators – Glass, Wood, Rubber, Air, Plastic …
Note: Salt water is a
conductor, and so are you!
Cu
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
Neighboring electrons are repulsed by the motion of electrons, creating a chain reaction that propagates through the material at nearly the speed of light.
Cross- section of copper wire
Copper’s valence electrons move freely throughout the solid copper metal
Copper and other metals have a weak hold on their outer or “valence” electrons. Atoms of insulating materials have a tight grip on their outer electrons.
<number>
T5 - Electrical Plus
Notes: <number>

## Slide 4
Voltage, Current, Resistance
+
-
Voltage
Current
Resistance (Load)
You need a circuit for electricity to flow
Components of a circuit: Source, Conductors, Load, Sink (Ground)
<number>
T5 - Electrical Plus
Notes: <number>
<number>
Voltage is also called Electromotive Force and is an electrical “pressure”. Current is a measure of the flow of electrons (volume) from the negative to positive poles. The load presents resistance to the flow of electrons. Voltage is measured across the positive and negative poles (in parallel) to measure the difference in “pressure”. To measure the electron flow, the meter must be placed in-line (in series) with the flow.
Direct Current (DC) is a constant voltage source that causes current to flow in only one direction and has a positive and negative pole – like a battery. Alternating Current is what is available in the wall and the constantly changing polarity causes current to alternate directions.

## Slide 5
Units of Measure
Power | Watt
Resistance | Ohm
Voltage | Volt
Current | Ampere
Frequency | Hertz
<number>
T5 - Electrical Plus
Notes: <number>

## Slide 6: T5A01 - Electrical current is measured in which of the following units?
A. Volts
B. Watts
C. Ohms
D. Amperes
<number>
T5 - Electrical Plus

## Slide 7: T5A01 - Electrical current is measured in which of the following units?
A. Volts
B. Watts
C. Ohms
D. Amperes
<number>
T5 - Electrical Plus

## Slide 8: T5A02 - Electrical power is measured in which of the following units?
A. Volts
B. Watts
C. Ohms
D. Amperes
<number>
T5 - Electrical Plus

## Slide 9: T5A02 - Electrical power is measured in which of the following units?
A. Volts
B. Watts
C. Ohms
D. Amperes
<number>
T5 - Electrical Plus

## Slide 10: T5A03 - What is the name for the flow of electrons in an electric circuit?
A. Voltage
B. Resistance
C. Capacitance
D. Current
<number>
T5 - Electrical Plus

## Slide 11: T5A03 - What is the name for the flow of electrons in an electric circuit?
A. Voltage
B. Resistance
C. Capacitance
D. Current
<number>
T5 - Electrical Plus

## Slide 12: T5A04 - What is the name for a current that flows only in one direction?
A. Alternating current
B. Direct current
C. Normal current
D. Smooth current
<number>
T5 - Electrical Plus

## Slide 13: T5A04 - What is the name for a current that flows only in one direction?
A. Alternating current
B. Direct current
C. Normal current
D. Smooth current
<number>
T5 - Electrical Plus

## Slide 14: T5A06 - How much voltage does a mobile transceiver usually require?
A. About 12 volts
B. About 30 volts
C. About 120 volts
D. About 240 volts
<number>
T5 - Electrical Plus

## Slide 15: T5A06 - How much voltage does a mobile transceiver usually require?
A. About 12 volts
B. About 30 volts
C. About 120 volts
D. About 240 volts
<number>
T5 - Electrical Plus

## Slide 16
Conductors and Insulators
In a conductor, electric current can flow freely, in an insulator it cannot. Simply stated, most metals are good electrical conductors, most nonmetals are not. Metals are also generally good heat conductors while nonmetals are not.
Conductors – Copper, Silver, Gold, Aluminum, Platinum, Steel, …
Insulators – Glass, Wood, Rubber, Air, Plastic …
Note: Salt water is a
conductor, and so are you!
Cu
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
Neighboring electrons are repulsed by the motion of electrons, creating a chain reaction that propagates through the material at nearly the speed of light.
Cross- section of copper wire
Copper’s valence electrons move freely throughout the solid copper metal
Copper and other metals have a weak hold on their outer or “valence” electrons. Atoms of insulating materials have a tight grip on their outer electrons.
<number>
T5 - Electrical Plus
Notes: <number>

## Slide 17: T5A07 - Which of the following is a good electrical conductor?
A. Glass
B. Wood
C. Copper
D. Rubber
<number>
T5 - Electrical Plus

## Slide 18: T5A07 - Which of the following is a good electrical conductor?
A. Glass
B. Wood
C. Copper
D. Rubber
<number>
T5 - Electrical Plus

## Slide 19: T5A08 - Which of the following is a good electrical insulator?
A. Copper
B. Glass
C. Aluminum
D. Mercury
<number>
T5 - Electrical Plus

## Slide 20: T5A08 - Which of the following is a good electrical insulator?
A. Copper
B. Glass
C. Aluminum
D. Mercury
<number>
T5 - Electrical Plus

## Slide 21
Direct Current Alternating Current
DC
Current flows in one direction only
  Examples:
    Battery Operated Devices
    Cars
AC
Current flows in both directions, voltage and current very with time
  Example: House Wiring
DC
AC
AC
<number>
T5 - Electrical Plus
Notes: <number>

## Slide 22: T5A09 - What is the name for a current that reverses direction on a regular basis?
A. Alternating current
B. Direct current
C. Circular current
D. Vertical current
<number>
T5 - Electrical Plus

## Slide 23: T5A09 - What is the name for a current that reverses direction on a regular basis?
A. Alternating current
B. Direct current
C. Circular current
D. Vertical current
<number>
T5 - Electrical Plus

## Slide 24: T5A10 - Which term describes the rate at which electrical energy is used?
A. Resistance
B. Current
C. Power
D. Voltage
<number>
T5 - Electrical Plus

## Slide 25: T5A10 - Which term describes the rate at which electrical energy is used?
A. Resistance
B. Current
C. Power
D. Voltage
<number>
T5 - Electrical Plus

## Slide 26: T5A11 - What is the basic unit of electromotive force?
A. The volt
B. The watt
C. The ampere
D. The ohm
<number>
T5 - Electrical Plus

## Slide 27: T5A11 - What is the basic unit of electromotive force?
A. The volt
B. The watt
C. The ampere
D. The ohm
<number>
T5 - Electrical Plus

## Slide 28: T5A12 - What term describes the number of times per second that an alternating current reverses direction?
A. Pulse rate
B. Speed
C. Wavelength
D. Frequency
<number>
T5 - Electrical Plus

## Slide 29: T5A12 - What term describes the number of times per second that an alternating current reverses direction?
A. Pulse rate
B. Speed
C. Wavelength
D. Frequency
<number>
T5 - Electrical Plus

## Slide 30: T5B - Math for electronics
conversion of electrical units; decibels; the metric system
<number>
T5 - Electrical Plus

## Slide 31
109 106 103 102 101 100 10-1 10-2 10-3 10-6 10-9 10-12
G M k h da d c m µ n p
giga mega kilo hecto deca 0 deci centi milli micro nano pico
Metric Units of Measure
Gigahertz | 1,000,000,000
Megahertz | 1,000,000
Kilohertz | 1,000
Hertz | 1
Ampere | 1
Milliampere | 0.001
Microampere | 0.000001
Nanoampere | 0.000000001
Billions
Millions
Thousands
Hundreds
Tens
Tenths
Thousandths
Hundredths
Millionths
Trillionths
Billionths
LARGER than
SMALLER than 1
1
<number>
T5 - Electrical Plus
Notes: <number>
<number>
Note the shift in decimal places. This is standard metric notation. 1 Gigahertz is 1 Billion Hertz and a Nanoampere is 1 Billionth of an Ampere.

## Slide 32
System of Metric Units
giga G 109 1,000,000,000.0 f
Mega M 106 1,000,000.0 f Ω
kilo K 103 1,000.0 f Ω kV kW
basic unit 100 1.0 f Ω V W
milli m 10-3 mh mV 0.001
Micro µ 10-6 µh µV µf 0.000 001
nano n 10-9 0.000 000 001
pico p 10-12 picofarads 0.000 000 000 001
Ω
Ω
<number>
T5 - Electrical Plus
Notes: <number>

## Slide 33: T5B01 - How many milliamperes is 1.5 amperes?
A. 15 milliamperes
B. 150 milliamperes
C. 1,500 milliamperes
D. 15,000 milliamperes
<number>
T5 - Electrical Plus

## Slide 34: T5B01 - How many milliamperes is 1.5 amperes?
A. 15 milliamperes
B. 150 milliamperes
C. 1,500 milliamperes
D. 15,000 milliamperes
<number>
T5 - Electrical Plus
Ampere | 1
Milliampere | 0.001
Microampere | 0.000 001
Nanoampere | 0.000 000 001

## Slide 35: T5B02 - What is another way to specify a radio signal frequency of 1,500,000 hertz?
A. 1500 kHz
B. 1500 MHz
C. 15 GHz
D. 150 kHz
<number>
T5 - Electrical Plus

## Slide 36: T5B02 - What is another way to specify a radio signal frequency of 1,500,000 hertz?
A. 1500 kHz
B. 1500 MHz
C. 15 GHz
D. 150 kHz
<number>
T5 - Electrical Plus
Gigahertz | 1,000,000,000
Megahertz | 1,000,000
Kilohertz | 1,000
Hertz | 1

## Slide 37: T5B03 - How many volts are equal to one kilovolt?
A. One one-thousandth of a volt
B. One hundred volts
C. One thousand volts
D. One million volts
<number>
T5 - Electrical Plus

## Slide 38: T5B03 - How many volts are equal to one kilovolt?
A. One one-thousandth of a volt
B. One hundred volts
C. One thousand volts
D. One million volts
<number>
T5 - Electrical Plus
MegaVolts | 1,000,000
KiloVolts | 1,000
Volts | 1

## Slide 39: T5B04 - How many volts are equal to one microvolt?
A. One one-millionth of a volt
B. One million volts
C. One thousand kilovolts
D. One one-thousandth of a volt
<number>
T5 - Electrical Plus

## Slide 40: T5B04 - How many volts are equal to one microvolt?
A. One one-millionth of a volt
B. One million volts
C. One thousand kilovolts
D. One one-thousandth of a volt
<number>
T5 - Electrical Plus
Volts | 1
MilliVolts | 0.001
MicroVolts | 0.000 001

## Slide 41: T5B05 - Which of the following is equivalent to 500 milliwatts?
A. 0.02 watts
B. 0.5 watts
C. 5 watts
D. 50 watts
<number>
T5 - Electrical Plus

## Slide 42: T5B05 - Which of the following is equivalent to 500 milliwatts?
A. 0.02 watts
B. 0.5 watts
C. 5 watts
D. 50 watts
<number>
T5 - Electrical Plus
Watts | 1
Milliwatts | 0.001
Microwatts | 0.000 001

## Slide 43: T5B06 - If an ammeter calibrated in amperes is used to measure a 3000-milliampere current, what reading would it show?
A. 0.003 amperes
B. 0.3 amperes
C. 3 amperes
D. 3,000,000 amperes
<number>
T5 - Electrical Plus

## Slide 44: T5B06 - If an ammeter calibrated in amperes is used to measure a 3000-milliampere current, what reading would it show?
A. 0.003 amperes
B. 0.3 amperes
C. 3 amperes
D. 3,000,000 amperes
<number>
T5 - Electrical Plus
Ampere | 1
Milliampere | 0.001
Microampere | 0.000 001
Nanoampere | 0.000 000 001

## Slide 45: T5B07 - If a frequency readout calibrated in megahertz shows a reading of 3.525 MHz, what would it show if it were calibrated in kilohertz?
A. 0.003525 kHz
B. 35.25 kHz
C. 3525 kHz
D. 3,525,000 kHz
<number>
T5 - Electrical Plus

## Slide 46: T5B07 - If a frequency readout calibrated in megahertz shows a reading of 3.525 MHz, what would it show if it were calibrated in kilohertz?
A. 0.003525 kHz
B. 35.25 kHz
C. 3525 kHz
D. 3,525,000 kHz
<number>
T5 - Electrical Plus
Gigahertz | 1,000,000,000
Megahertz | 1,000,000
Kilohertz | 1,000
Hertz | 1

## Slide 47: T5B08 - How many microfarads are 1,000,000 picofarads?
A. 0.001 microfarads
B. 1 microfarad
C. 1000 microfarads
D. 1,000,000,000 microfarads
<number>
T5 - Electrical Plus

## Slide 48: T5B08 - How many microfarads are 1,000,000 picofarads?
A. 0.001 microfarads
B. 1 microfarad
C. 1000 microfarads
D. 1,000,000,000 microfarads
<number>
T5 - Electrical Plus
Farad | 1
Millifarad | 0.001
Microfarad | 0.000 001
Picofarad | 0.000 000 000 001

## Slide 49
<number>
Decibel Multipliers
10 TIMES
4 TIMES
2 TIMES
3 db
6 db
10 db
<number>
T5 - Electrical Plus
Power Increase
Notes: <number>
<number>
<number>
The Decibel scale is logarithmic. 3dB represents a 2-fold increase in power, 6dB is 4 fold, 10dB is 10-fold, 20dB is 100-fold. The S-Unit scale on a receiver meter is not an absolute scale and can vary from radio to radio. Although these meters are not calibrated, they can be useful for verifying antenna performance. One “S-Unit” represents a 4-fold change in power or 6dB.

## Slide 50: T5B09 - What is the approximate amount of change, measured in decibels ( dB ), of a power increase from 5 watts to 10 watts?
A. 2 dB
B. 3 dB
C. 5 dB
D. 10 dB
<number>
T5 - Electrical Plus

## Slide 51: T5B09 - What is the approximate amount of change, measured in decibels ( dB ), of a power increase from 5 watts to 10 watts?
A. 2 dB
B. 3 dB
C. 5 dB
D. 10 dB
<number>
T5 - Electrical Plus
3 db = 2 X
2 X 5 watts = 10 watts

## Slide 52: T5B10 - What is the approximate amount of change, measured in decibels ( dB ), of a power decrease from 12 watts to 3 watts?
A. -1 dB
B. -3 dB
C. -6 dB
D. -9 dB
<number>
T5 - Electrical Plus

## Slide 53: T5B10 - What is the approximate amount of change, measured in decibels ( dB ), of a power decrease from 12 watts to 3 watts?
A. -1 dB
B. -3 dB
C. -6 dB
D. -9 dB
<number>
T5 - Electrical Plus
12 W / 2 = 6 W = -3db
6 W / 2 = 3 W = + -3 db
6 db

## Slide 54: T5B11 - What is the approximate amount of change, measured in decibels ( dB ), of a power increase from 20 watts to 200 watts?
A. 10 dB
B. 12 dB
C. 18 dB
D. 28 dB
<number>
T5 - Electrical Plus

## Slide 55: T5B11 - What is the approximate amount of change, measured in decibels ( dB ), of a power increase from 20 watts to 200 watts?
A. 10 dB
B. 12 dB
C. 18 dB
D. 28 dB
<number>
T5 - Electrical Plus
200 Watts / 20 Watts = 10 db
10 deci bel = 1 bel

## Slide 56: T5B12 - Which of the following frequencies is equal to 28,400 kHz?
A. 28.400 MHz
B. 2.800 MHz
C. 284.00 MHz
D. 28.400 kHz
<number>
T5 - Electrical Plus

## Slide 57: T5B12 - Which of the following frequencies is equal to 28,400 kHz?
A. 28.400 MHz
B. 2.800 MHz
C. 284.00 MHz
D. 28.400 kHz
<number>
T5 - Electrical Plus
Gigahertz | 1,000,000,000
Megahertz | 1,000,000
Kilohertz | 1,000
Hertz | 1

## Slide 58: T5B13 - If a frequency readout shows a reading of 2425 MHz, what frequency is that in GHz?
A. 0.002425 GHZ
B. 24.25 GHz
C. 2.425 GHz
D. 2425 GHz
<number>
T5 - Electrical Plus

## Slide 59: T5B13 - If a frequency readout shows a reading of 2425 MHz, what frequency is that in GHz?
A. 0.002425 GHZ
B. 24.25 GHz
C. 2.425 GHz
D. 2425 GHz
<number>
T5 - Electrical Plus
Gigahertz | 1,000,000,000
Megahertz | 1,000,000
Kilohertz | 1,000
Hertz | 1

## Slide 60: T5C - Electronic principles
Capacitance; inductance; current flow in circuits; alternating current; definition of RF; DC power calculations; impedance
<number>
T5 - Electrical Plus

## Slide 61: T5C01 - What is the ability to store energy in an electric field called?
A. Inductance
B. Resistance
C. Tolerance
D. Capacitance
<number>
T5 - Electrical Plus

## Slide 62: T5C01 - What is the ability to store energy in an electric field called?
A. Inductance
B. Resistance
C. Tolerance
D. Capacitance
<number>
T5 - Electrical Plus

## Slide 63: T5C02 - What is the basic unit of capacitance?
A. The farad
B. The ohm
C. The volt
D. The henry
<number>
T5 - Electrical Plus

## Slide 64: T5C02 - What is the basic unit of capacitance?
A. The farad
B. The ohm
C. The volt
D. The henry
<number>
T5 - Electrical Plus

## Slide 65: T5C03 - What is the ability to store energy in a magnetic field called?
A. Admittance
B. Capacitance
C. Resistance
D. Inductance
<number>
T5 - Electrical Plus

## Slide 66: T5C03 - What is the ability to store energy in a magnetic field called?
A. Admittance
B. Capacitance
C. Resistance
D. Inductance
<number>
T5 - Electrical Plus

## Slide 67: T5C04 - What is the basic unit of inductance?
A. The coulomb
B. The farad
C. The henry
D. The ohm
<number>
T5 - Electrical Plus

## Slide 68: T5C04 - What is the basic unit of inductance?
A. The coulomb
B. The farad
C. The henry
D. The ohm
<number>
T5 - Electrical Plus

## Slide 69: T5C05 - What is the unit of frequency?
A. Hertz
B. Henry
C. Farad
D. Tesla
<number>
T5 - Electrical Plus

## Slide 70: T5C05 - What is the unit of frequency?
A. Hertz
B. Henry
C. Farad
D. Tesla
<number>
T5 - Electrical Plus

## Slide 71: T5C06 - What does the abbreviation “RF” refer to?
A. Radio frequency signals of all types
B. The resonant frequency of a tuned circuit
C. The real frequency transmitted as opposed to the apparent frequency
D. Reflective force in antenna transmission lines
<number>
T5 - Electrical Plus

## Slide 72: T5C06 - What does the abbreviation “RF” refer to?
A. Radio frequency signals of all types
B. The resonant frequency of a tuned circuit
C. The real frequency transmitted as opposed to the apparent frequency
D. Reflective force in antenna transmission lines
<number>
T5 - Electrical Plus

## Slide 73: T5C07 - What is a usual name for electromagnetic waves that travel through space?
A. Gravity waves
B. Sound waves
C. Radio waves
D. Pressure waves
<number>
T5 - Electrical Plus

## Slide 74: T5C07 - What is a usual name for electromagnetic waves that travel through space?
A. Gravity waves
B. Sound waves
C. Radio waves
D. Pressure waves
<number>
T5 - Electrical Plus

## Slide 75
<number>
Watts Law Voltage, Current and Power
Potential – Electromotive Force
  Electromotive Force (E)
  Units – Volts
  Unit Symbol V – 10V
  Measured across (parallel to load)
Current – Electron flow
  Current (I)
  Units – Amps, Amperes
  Unit Symbol A – 0.1A
  Measured through (inline with load)
Power (P)
  Watts
  Units – Watts
  Unit Symbol W – 60W
P
I
E
P = I x E
T5 - Electrical Plus
Notes: <number>
<number>
Potential – Voltage or Electromotive force
Units are Volts named after Count Alessandro Giuseppe Antonio Anastasio Volta (Italian Inventor), invented the baterry.
Flow – Current, measured in amps, named after André-Marie Ampère (French) scientist and mathematician. I is used as the abbreviation because it referred to the Intensity of the current.
Power – Measured in Watts, named after James Watt (Scottish/British) inventor

## Slide 76
<number>
Power, Current, and Voltage Power Unit Circle WAV
Potential – Electromotive Force
  Electromotive Force (E)
  Units – Volts (V)
  Unit Symbol V – 10V
  Measured across (parallel to load)
Current – Electron flow
  Current (I)
  Unites – Amps, Amperes (A)
  Unit Symbol A – 0.1A
  Measured through (inline with load)
Power (P)
  Watts
  Units – Watts (W)
  Unit Symbol W – 60W
W
A
V
W = A x V
P = I x E
P
I E
T5 - Electrical Plus
Notes: <number>
<number>
Potential – Voltage or Electromotive force
Units are Volts named after Count Alessandro Giuseppe Antonio Anastasio Volta (Italian Inventor), invented the baterry.
Flow – Current, measured in amps, named after André-Marie Ampère (French) scientist and mathematician. I is used as the abbreviation because it referred to the Intensity of the current.
Power – Measured in Watts, named after James Watt (Scottish/British) inventor

## Slide 77: T5C08 - What is the formula used to calculate electrical power in a DC circuit?
A. Power (P) equals voltage (E) multiplied by current (I)
B. Power (P) equals voltage (E) divided by current (I)
C. Power (P) equals voltage (E) minus current (I)
D. Power (P) equals voltage (E) plus current (I)
<number>
T5 - Electrical Plus

## Slide 78: T5C08 - What is the formula used to calculate electrical power in a DC circuit?
A. Power (P) equals voltage (E) multiplied by current (I)
B. Power (P) equals voltage (E) divided by current (I)
C. Power (P) equals voltage (E) minus current (I)
D. Power (P) equals voltage (E) plus current (I)
<number>
T5 - Electrical Plus
P
I
E
W = A x V
P = I x E

## Slide 79: T5C09 - How much power is being used in a circuit when the applied voltage is 13.8 volts DC and the current is 10 amperes?
A. 138 watts
B. 0.7 watts
C. 23.8 watts
D. 3.8 watts
<number>
T5 - Electrical Plus

## Slide 80: T5C09 - How much POWER is being used in a circuit when the applied voltage is 13.8 volts DC and the current is 10 amperes?
A. 138 watts
B. 0.7 watts
C. 23.8 watts
D. 3.8 watts
<number>
T5 - Electrical Plus
W?
A
V
What are you looking For?

## Slide 81
<number>
W ?
A
10 Amps
V
13.8 Volts
W = A x V
What info do you have?
T5C09 - How much POWER is being used in a circuit when the applied voltage is 13.8 volts DC and the current is 10 amperes?
T5 - Electrical Plus
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 82
Electrical Principles 2014
<number>
W
A
10 A
V
13.8 V
W = A x V
W = 10 A x 13.8 V = 138 W
T5C09 How much power is being used in a circuit when the applied voltage is 13.8 volts DC and the current is 10 amperes?
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 83: T5C09 - How much power is being used in a circuit when the applied voltage is 13.8 volts DC and the current is 10 amperes?
A. 138 watts
B. 0.7 watts
C. 23.8 watts
D. 3.8 watts
<number>
T5 - Electrical Plus

## Slide 84
T5C10 - How much power is being used in a circuit when the applied voltage is 12 volts DC and the current is 2.5 amperes?
  A. 4.8 watts
  B. 30 watts
  C. 14.5 watts
  D. 0.208 watts
Electrical Principles 2014
<number>
Notes: <number>

## Slide 85
Electrical Principles 2014
<number>
T5C10 - How much power is being used in a circuit when the applied voltage is 12 volts DC and the current is 2.5 amperes?
W ?
A
V
W = A x V
What are you looking For?
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 86
Electrical Principles 2014
<number>
T5C10 - How much power is being used in a circuit when the applied voltage is 12 volts DC and the current is 2.5 amperes?
W ?
2.5 A
12 V
W = A x V
What info do you have?
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 87
Electrical Principles 2014
<number>
T5C10 - How much power is being used in a circuit when the applied voltage is 12 volts DC and the current is 2.5 amperes?
W
2.5 A
12 V
W = A x V
W = 2.5 A x 12 V = 30 W
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 88
T5C10 - How much power is being used in a circuit when the applied voltage is 12 volts DC and the current is 2.5 amperes?
  A. 4.8 watts
B. 30 watts
C. 14.5 watts
  D. 0.208 watts
Electrical Principles 2014
<number>
Notes: <number>

## Slide 89
T5C11 - How many amperes are flowing in a circuit when the applied voltage is 12 volts DC and the load is 120 watts?
  A. 0.1 amperes
  B. 10 amperes
  C. 12 amperes
  D. 132 amperes
Electrical Principles 2014
<number>
Notes: <number>

## Slide 90
Electrical Principles 2014
<number>
T5C11 - How many AMPERES are flowing in a circuit when the applied voltage is 12 volts DC and the load is 120 watts?
W
A ?
V
A = W / V
What are you looking For?
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 91
Electrical Principles 2014
<number>
T5C11 - How many amperes are flowing in a circuit when the applied voltage is 12 volts DC and the load is 120 watts?
W 120 W
A ?
V 12VDC
A = W / V
What info do you have?
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 92
Electrical Principles 2014
<number>
T5C11 - How many amperes are flowing in a circuit when the applied voltage is 12 volts DC and the load is 120 watts?
120 W
A
12 V
A = W / V
A = 120 W / 12 VDC = 10 A
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 93
T5C11 - How many amperes are flowing in a circuit when the applied voltage is 12 volts DC and the load is 120 watts?
  A. 0.1 amperes
B. 10 amperes
  C. 12 amperes
  D. 132 amperes
Electrical Principles 2014
<number>
Notes: <number>

## Slide 94: T5C12 - What is meant by the term impedance?
A. It is a measure of the opposition to AC current flow in a circuit
B. It is the inverse of resistance
C. It is a measure of the Q or Quality Factor of a component
D. It is a measure of the power handling capability of a component
<number>
T5 - Electrical Plus

## Slide 95: T5C12 - What is meant by the term impedance?
A. It is a measure of the opposition to AC current flow in a circuit
B. It is the inverse of resistance
C. It is a measure of the Q or Quality Factor of a component
D. It is a measure of the power handling capability of a component
<number>
T5 - Electrical Plus

## Slide 96: T5C13 - What are the units of impedance?
A. Volts
B. Amperes
C. Coulombs
D. Ohms
<number>
T5 - Electrical Plus

## Slide 97: T5C13 - What are the units of impedance?
A. Volts
B. Amperes
C. Coulombs
D. Ohms
<number>
T5 - Electrical Plus

## Slide 98: T5D – Ohm’s Law
formulas and usage
<number>
T5 - Electrical Plus

## Slide 99
<number>
Ohms Law Voltage, Current and Resistance
Potential – Electromotive Force
  Electromotive Force (E)
  Units – Volts
  Unit Symbol V – 10V
  Measured across (parallel to load)
Current – Electron flow
  Current (I)
  Units – Amps, Amperes
  Unit Symbol A – 0.1A
  Measured through (inline with load)
Resistance (R)
  Ohms (R)
  Units – Ohms
  Unit Symbol  – 60 
E
I
R
E = I x R
T5 - Electrical Plus
Notes: <number>
<number>
Potential – Voltage or Electromotive force
Units are Volts named after Count Alessandro Giuseppe Antonio Anastasio Volta (Italian Inventor), invented the baterry.
Flow – Current, measured in amps, named after André-Marie Ampère (French) scientist and mathematician. I is used as the abbreviation because it referred to the Intensity of the current.
Power – Measured in Watts, named after James Watt (Scottish/British) inventor

## Slide 100
<number>
Ohms Law - Unit Circle Voltage, Current and Resistance
Potential – Electromotive Force
  Electromotive Force (V)
  Units – Volts
  Unit Symbol V – 10V
  Measured across (parallel to load)
Current – Electron flow
  Current (A)
  Units – Amps, Amperes
  Unit Symbol A – 0.1A
  Measured through (inline with load)
Resistance (R)
  Ohms (O)
  Units – Ohms
  Unit Symbol  – 60 
V
O
A
V = O x A
E
R I
Voice Of America
VOLTAGE CIRCLE
T5 - Electrical Plus
Notes: <number>
<number>
Potential – Voltage or Electromotive force
Units are Volts named after Count Alessandro Giuseppe Antonio Anastasio Volta (Italian Inventor), invented the baterry.
Flow – Current, measured in amps, named after André-Marie Ampère (French) scientist and mathematician. I is used as the abbreviation because it referred to the Intensity of the current.
Power – Measured in Watts, named after James Watt (Scottish/British) inventor

## Slide 101
<number>
Ohm’s Law and Power Calculations
E
I
R
P
I
E
E=Voltage (Volts)
I=Current (Amps)
R=Resistance (Ohms)
* Ω is the symbol for ohms
P=Power (Watts)
To solve for a value, cover it with your finger and solve the remaining formula
T5 - Electrical Plus
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 102
Electrical Principles 2010
<number>
Ohm’s Law and Power Calculations Unit Circles
V
O
A
W
A
V
V=Voltage (Volts)
O=Resistance (Ohms)
A=Current (Amps)
W=Power (Watts)
To solve for a value, cover it with your finger and solve the remaining formula
Voice Of America – VOLTAGE CIRCLE W A V - WATTAGE CIRCLE
T5 - Electrical Plus
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 103: T5D01 - What formula is used to calculate current in a circuit?
A. Current (I) equals voltage (E) multiplied by resistance (R)
B. Current (I) equals voltage (E) divided by resistance (R)
C. Current (I) equals voltage (E) added to resistance (R)
D. Current (I) equals voltage (E) minus resistance (R)
<number>
T5 - Electrical Plus

## Slide 104: T5D01 - What formula is used to calculate current in a circuit?
A. Current (I) equals voltage (E) multiplied by resistance (R)
B. Current (I) equals voltage (E) divided by resistance (R)
C. Current (I) equals voltage (E) added to resistance (R)
D. Current (I) equals voltage (E) minus resistance (R)
<number>
T5 - Electrical Plus
E
I
R
E = I x R
I = E / R

## Slide 105: T5D02 - What formula is used to calculate voltage in a circuit?
A. Voltage (E) equals current (I) multiplied by resistance (R)
B. Voltage (E) equals current (I) divided by resistance (R)
C. Voltage (E) equals current (I) added to resistance (R)
D. Voltage (E) equals current (I) minus resistance (R)
<number>
T5 - Electrical Plus

## Slide 106: T5D02 - What formula is used to calculate voltage in a circuit?
A. Voltage (E) equals current (I) multiplied by resistance (R)
B. Voltage (E) equals current (I) divided by resistance (R)
C. Voltage (E) equals current (I) added to resistance (R)
D. Voltage (E) equals current (I) minus resistance (R)
<number>
T5 - Electrical Plus
E
I
R
E = I x R
V = O x A

## Slide 107: T5D03 - What formula is used to calculate resistance in a circuit?
A. Resistance (R) equals voltage (E) multiplied by current (I)
B. Resistance (R) equals voltage (E) divided by current (I)
C. Resistance (R) equals voltage (E) added to current (I)
D. Resistance (R) equals voltage (E) minus current (I)
<number>
T5 - Electrical Plus

## Slide 108: T5D03 - What formula is used to calculate resistance in a circuit?
A. Resistance (R) equals voltage (E) multiplied by current (I)
B. Resistance (R) equals voltage (E) divided by current (I)
C. Resistance (R) equals voltage (E) added to current (I)
D. Resistance (R) equals voltage (E) minus current (I)
<number>
T5 - Electrical Plus
E
I
R
E = I x R
R = E / I

## Slide 109: T5D04 - What is the resistance of a circuit in which a current of 3 amperes flows through a resistor connected to 90 volts?
A. 3 ohms
B. 30 ohms
C. 93 ohms
D. 270 ohms
<number>
T5 - Electrical Plus

## Slide 110
<number>
V
O ?
A
O = V / A
What are you looking For?
T5D04 - What is the resistance of a circuit in which a current of 3 amperes flows through a resistor connected to 90 volts?
T5 - Electrical Plus
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 111
<number>
90 V
O ?
3 Amps
O = V / A
What info do you have?
T5D04 - What is the resistance of a circuit in which a current of 3 amperes flows through a resistor connected to 90 volts?
T5 - Electrical Plus
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 112
<number>
90 V
O
3 A
O = V / A
O = 90 V / 3 A = 30 Ω
T5D04 - What is the resistance of a circuit in which a current of 3 amperes flows through a resistor connected to 90 volts?
T5 - Electrical Plus
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 113
<number>
T5D04 - What is the resistance of a circuit in which a current of 3 amperes flows through a resistor connected to 90 volts?
A. 3 ohms
B. 30 ohms
C. 93 ohms
D. 270 ohms
T5 - Electrical Plus
Notes: <number>

## Slide 114
T5D05 - What is the resistance in a circuit for which the applied voltage is 12 volts and the current flow is 1.5 amperes?
  A. 18 ohms
  B. 0.125 ohms
  C. 8 ohms
  D. 13.5 ohms
<number>
T5 - Electrical Plus
Notes: <number>

## Slide 115
<number>
T5D05 - What is the resistance in a circuit for which the applied voltage is 12 volts and the current flow is 1.5 amperes?
V
O ?
A
O = V / A
T5 - Electrical Plus
What are you looking For?
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 116
<number>
T5D05 - What is the resistance in a circuit for which the applied voltage is 12 volts and the current flow is 1.5 amperes?
12 V
O ?
1.5 A
O = V / A
What info do you have?
T5 - Electrical Plus
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 117
<number>
T5D05 - What is the resistance in a circuit for which the applied voltage is 12 volts and the current flow is 1.5 amperes?
12 V
O
1.5 A
O = V / A
O = 12 V / 1.5 A = 8 Ω
T5 - Electrical Plus
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 118
T5D05 - What is the resistance in a circuit for which the applied voltage is 12 volts and the current flow is 1.5 amperes?
<number>
  A. 18 ohms
  B. 0.125 ohms
  C. 8 ohms
  D. 13.5 ohms
T5 - Electrical Plus
Notes: <number>

## Slide 119
T5D06 - What is the resistance of a circuit that draws 4 amperes from a 12-volt source?
  A. 3 ohms
  B. 16 ohms
  C. 48 ohms
  D. 8 Ohms
<number>
T5 - Electrical Plus
Notes: <number>

## Slide 120
<number>
T5D06 - What is the resistance of a circuit that draws 4 amperes from a 12-volt source?
V
O ?
A
O = V / A
What are you looking For?
T5 - Electrical Plus
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 121
<number>
T5D06 - What is the resistance of a circuit that draws 4 amperes from a 12-volt source?
V 12 Volts
O ?
A 4 Amps
O = V / A
What info do you have?
T5 - Electrical Plus
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 122
<number>
T5D06 - What is the resistance of a circuit that draws 4 amperes from a 12-volt source?
12 V
O
4 A
O = V / A
O = 12 V / 4 A = 3 Ω
T5 - Electrical Plus
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 123
T5D06 - What is the resistance of a circuit that draws 4 amperes from a 12-volt source?
<number>
  A. 3 ohms
  B. 16 ohms
  C. 48 ohms
  D. 8 Ohms
T5 - Electrical Plus
Notes: <number>

## Slide 124
T5D07 - What is the current flow in a circuit with an applied voltage of 120 volts and a resistance of 80 ohms?
  A. 9600 amperes
  B. 200 amperes
  C. 0.667 amperes
  D. 1.5 amperes
<number>
T5 - Electrical Plus
Notes: <number>

## Slide 125
<number>
V
O
A ?
A = V / O
T5D07 - What is the current flow in a circuit with an applied voltage of 120 volts and a resistance of 80 ohms?
What are you looking For?
T5 - Electrical Plus
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 126
<number>
120 V
O
80 Ohms
A ?
A = V / O
T5D07 - What is the current flow in a circuit with an applied voltage of 120 volts and a resistance of 80 ohms?
What info do you have?
T5 - Electrical Plus
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 127
<number>
120 V
O
80 Ohms
A
A = V / O
A = 120 V / 80 Ω = 1.5 A
T5D07 - What is the current flow in a circuit with an applied voltage of 120 volts and a resistance of 80 ohms?
T5 - Electrical Plus
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 128
T5D07 - What is the current flow in a circuit with an applied voltage of 120 volts and a resistance of 80 ohms?
<number>
  A. 9600 amperes
  B. 200 amperes
  C. 0.667 amperes
  D. 1.5 amperes
T5 - Electrical Plus
Notes: <number>

## Slide 129
T5D08 - What is the current flowing through a 100-ohm resistor connected across 200 volts?
  A. 20,000 amperes
  B. 0.5 amperes
  C. 2 amperes
  D. 100 amperes
<number>
T5 - Electrical Plus
Notes: <number>

## Slide 130
<number>
V
O
A ?
A = V / O
T5D08 - What is the current flowing through a 100-ohm resistor connected across 200 volts?
What are you looking For?
T5 - Electrical Plus
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 131
<number>
200 Volts
100 Ohms
A ?
A = V / O
What info do you have?
T5 - Electrical Plus
T5D08 - What is the current flowing through a 100-ohm resistor connected across 200 volts?
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 132
<number>
200 V
O
100 Ohms
A
A = V / O
A = 200 V / 100 Ω = 2 A
T5 - Electrical Plus
T5D08 - What is the current flowing through a 100-ohm resistor connected across 200 volts?
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 133
<number>
T5 - Electrical Plus
T5D08 - What is the current flowing through a 100-ohm resistor connected across 200 volts?
  A. 20,000 amperes
  B. 0.5 amperes
  C. 2 amperes
  D. 100 amperes
Notes: <number>

## Slide 134
T5D09 - What is the current flowing through a 24-ohm resistor connected across 240 volts?
  A. 24,000 amperes
  B. 0.1 amperes
  C. 10 amperes
  D. 216 amperes
<number>
T5 - Electrical Plus
Notes: <number>

## Slide 135
<number>
V
O
A ?
A = V / O
What are you looking For?
T5 - Electrical Plus
T5D09 - What is the current flowing through a 24-ohm resistor connected across 240 volts?
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 136
<number>
240 Volts
24 Ohms
A ?
A = V / O
What info do you have?
T5 - Electrical Plus
T5D09 - What is the current flowing through a 24-ohm resistor connected across 240 volts?
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 137
<number>
240 V
O
24 Ohms
A
A = V / O
A = 240 V / 24 Ω = 10 A
T5 - Electrical Plus
T5D09 - What is the current flowing through a 24-ohm resistor connected across 240 volts?
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 138
<number>
T5 - Electrical Plus
T5D09 - What is the current flowing through a 24-ohm resistor connected across 240 volts?
  A. 24,000 amperes
  B. 0.1 amperes
  C. 10 amperes
  D. 216 amperes
Notes: <number>

## Slide 139
T5D10 - What is the voltage across a 2-ohm resistor if a current of 0.5 amperes flows through it?
  A. 1 volt
  B. 0.25 volts
  C. 2.5 volts
  D. 1.5 volts
<number>
T5 - Electrical Plus
Notes: <number>

## Slide 140
<number>
V ?
O
A
V = O x A
What are you looking For?
T5 - Electrical Plus
T5D10 - What is the voltage across a 2-ohm resistor if a current of 0.5 amperes flows through it?
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 141
<number>
V ?
O
2 Ohms
A
0.5 Amps
V = O x A
What info do you have?
T5 - Electrical Plus
T5D10 - What is the voltage across a 2-ohm resistor if a current of 0.5 amperes flows through it?
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 142
<number>
V
O
2 Ohms
A
0.5 Amps
V = O x A
V = 2 Ω x 0.5 A = 1 V
T5 - Electrical Plus
T5D10 - What is the voltage across a 2-ohm resistor if a current of 0.5 amperes flows through it?
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 143
<number>
T5 - Electrical Plus
T5D10 - What is the voltage across a 2-ohm resistor if a current of 0.5 amperes flows through it?
  A. 1 volt
  B. 0.25 volts
  C. 2.5 volts
  D. 1.5 volts
Notes: <number>

## Slide 144
T5D11 - What is the voltage across a 10-ohm resistor if a current of 1 ampere flows through it?
  A. 1 volt
  B. 10 volts
  C. 11 volts
  D. 9 volts
<number>
T5 - Electrical Plus
Notes: <number>

## Slide 145
<number>
V ?
O
A
V = O x A
What are you looking For?
T5 - Electrical Plus
T5D11 - What is the voltage across a 10-ohm resistor if a current of 1 ampere flows through it?
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 146
<number>
V ?
10 Ohms
1 Amp
V = O x A
V = 10 Ω x 1 A = 10 V
What info do you have?
T5 - Electrical Plus
T5D11 - What is the voltage across a 10-ohm resistor if a current of 1 ampere flows through it?
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 147
<number>
V
O
10 Ohms
A
1 Amp
V = O x A
V= 10 x 1 = 10 V
T5 - Electrical Plus
T5D11 - What is the voltage across a 10-ohm resistor if a current of 1 ampere flows through it?
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 148
<number>
T5 - Electrical Plus
T5D11 - What is the voltage across a 10-ohm resistor if a current of 1 ampere flows through it?
  A. 1 volt
  B. 10 volts
  C. 11 volts
  D. 9 volts
Notes: <number>

## Slide 149
T5D12 - What is the voltage across a 10-ohm resistor if a current of 2 amperes flows through it?
  A. 8 volts
  B. 0.2 volts
  C. 12 volts
  D. 20 volts
<number>
T5 - Electrical Plus
Notes: <number>

## Slide 150
<number>
V ?
O
A
V = O x A
What are you looking For?
T5 - Electrical Plus
T5D12 - What is the voltage across a 10-ohm resistor if a current of 2 amperes flows through it?
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 151
<number>
V ?
O
10 Ohms
A
2 Amps
V = O x A
What info do you have?
T5 - Electrical Plus
T5D12 - What is the voltage across a 10-ohm resistor if a current of 2 amperes flows through it?
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 152
<number>
V
10 Ohms
2 Amps
V = O x A
V = 10 Ω x 2 A = 20 V
T5 - Electrical Plus
T5D12 - What is the voltage across a 10-ohm resistor if a current of 2 amperes flows through it?
Notes: <number>
<number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 153
<number>
T5 - Electrical Plus
T5D12 - What is the voltage across a 10-ohm resistor if a current of 2 amperes flows through it?
  A. 8 volts
  B. 0.2 volts
  C. 12 volts
  D. 20 volts
Notes: <number>

## Slide 154: End of SUBELEMENT T5
Electrical principles: math for electronics; electronic principles; Ohm’s Law
<number>
T5 - Electrical Plus