## Slide 1: SUBELEMENT T8
Modulation modes: amateur satellite operation; operating activities; non-voice communications
[4 Exam Questions - 4 Groups]
<number>
Modes 2014
Notes: Subelement T8 Radio Modes. Technician Training Slides for 2014 Question Pool Good through June 30, 2018 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM, Howard Schultz, W7HS.
<number>

## Slide 2
T8A – Modulation modes: bandwidth of various signals; choice of emission type
T8B - Amateur satellite operation: Doppler shift, basic orbits, operating protocols; control operator, transmitter power considerations; satellite tracking; digital modes
T8C – Operating activities: radio direction finding; radio control; contests; linking over the Internet; grid locators
T8D – Non-voice communications: image signals; digital modes; CW; packet; PSK31; APRS; error detection and correction; NTSC
<number>
Modes

## Slide 3: Sample Emission Modes
Mode | Type | Bandwidth | Content
CW | Telegraphy | 10 Hz | Text Data
SSB | Telephony | 2800 Hz | Voice
AM | Telephony | 6 kHz | Voice
FM | Telephony | 5-15 kHz | Voice
SSTV / Fax | Image | 2800 Hz | Image
ATV | Image | 6 MHz | Image
PSK31 | Data | 31 Hz | Text Data
RTTY | Data | 250 Hz | Text Data
Pactor (I, II, III) | Data | 500-2800 Hz | Binary Data
AX.25 Packet | Data | 10-20 kHz | Binary Data
Modes
<number>

## Slide 4: Amplitude Modulation
<number>
Modes
An unmodulated RF
carrier wave
A carrier wave amplitude
modulated (AM) with a simple audio tone
Notes: <number>
Note the identical sidebands. They peak and dip together.

## Slide 5: Amplitude Modulation
<number>
Modes
An unmodulated RF
carrier requires narrow
bandwidth
Modulation of the carrier
creates sidebands. This
requires more bandwidth.
Transmitter power is spread across this bandwidth

## Slide 6: AM and SSB
<number>
Modes
The carrier contains no
audio information.
The sidebands contain
duplicate audio information
By filtering out the carrier and one sideband,
we save spectrum and concentrate our RF
energy into a narrower bandwidth. SSB is
therefore more efficient.

## Slide 7: Frequency Modulation
<number>
Modes
Unmodulated carrier, full power at all times
Waveform of modulating signal
Modulated carrier with frequency deviation and constant amplitude
“Over modulation” called “over deviation” on FM, causes the signal to become wider and potentially cause adjacent channel interference. Phase Modulation (PM) uses a reactance modulator and is similar to FM and can be received with the same equipment.

## Slide 8: Common Required Bandwidth
CW – 5-10Hz
Phone / Voice
  SSB - 2-3 kHz
  AM – 4-6 kHz
  FM – 5-15 kHz
Digital
  PSK31 – 31 Hz
  RTTY – 250 Hz
Slow Scan TV – 3 KHz
Fast Scan TV – 6 Mhz
<number>
Modes

## Slide 9: Amateur Television Signal
<number>
Modes
A 6 MHz ATV video channel with the video carrier 1.25 MHz up from the lower edge. The color subcarrier is at 3.58 MHz and the sound subcarrier at 4.5 MHz above the video carrier.
The Luminance, Chrominance and Audio carriers are visible in the spectrum plot at left

## Slide 10: T8A01 - Which of the following is a form of amplitude modulation?
A. Spread-spectrum
B. Packet radio
C. Single sideband
D. Phase shift keying
<number>
Modes

## Slide 11: T8A01 - Which of the following is a form of amplitude modulation?
A. Spread-spectrum
B. Packet radio
C. Single sideband
D. Phase shift keying
<number>
Modes

## Slide 12: T8A02 - What type of modulation is most commonly used for VHF packet radio transmissions?
A. FM
B. SSB
C. AM
D. Spread Spectrum
<number>
Modes

## Slide 13: T8A02 - What type of modulation is most commonly used for VHF packet radio transmissions?
A. FM
B. SSB
C. AM
D. Spread Spectrum
<number>
Modes

## Slide 14: T8A03 - Which type of voice mode is most often used for long-distance (weak signal) contacts on the VHF and UHF bands?
A. FM
B. DRM
C. SSB
D. PM
<number>
Modes

## Slide 15: T8A03 - Which type of voice mode is most often used for long-distance (weak signal) contacts on the VHF and UHF bands?
A. FM
B. DRM
C. SSB
D. PM
<number>
Modes

## Slide 16: T8A04 - Which type of modulation is most commonly used for VHF and UHF voice repeaters?
A. AM
B. SSB
C. PSK
D. FM
<number>
Modes

## Slide 17: T8A04 - Which type of modulation is most commonly used for VHF and UHF voice repeaters?
A. AM
B. SSB
C. PSK
D. FM
<number>
Modes

## Slide 18: T8A05 - Which of the following types of emission has the narrowest bandwidth?
A. FM voice
B. SSB voice
C. CW
D. Slow-scan TV
<number>
Modes

## Slide 19: T8A05 - Which of the following types of emission has the narrowest bandwidth?
A. FM voice
B. SSB voice
C. CW
D. Slow-scan TV
<number>
Modes

## Slide 20: T8A06 - Which sideband is normally used for 10 meter HF, VHF and UHF single-sideband communications?
A. Upper sideband
B. Lower sideband
C. Suppressed sideband
D. Inverted sideband
<number>
Modes

## Slide 21: T8A06 - Which sideband is normally used for 10 meter HF, VHF and UHF single-sideband communications?
A. Upper sideband
B. Lower sideband
C. Suppressed sideband
D. Inverted sideband
<number>
Modes

## Slide 22: T8A07 - What is the primary advantage of single sideband over FM for voice transmissions?
A. SSB signals are easier to tune
B. SSB signals are less susceptible to interference
C. SSB signals have narrower bandwidth
D. All of these choices are correct
<number>
Modes

## Slide 23: T8A07 - What is the primary advantage of single sideband over FM for voice transmissions?
A. SSB signals are easier to tune
B. SSB signals are less susceptible to interference
C. SSB signals have narrower bandwidth
D. All of these choices are correct
<number>
Modes

## Slide 24: T8A08 - What is the approximate bandwidth of a single sideband voice signal?
A. 1 kHz
B. 3 kHz
C. 6 kHz
D. 15 kHz
<number>
Modes

## Slide 25: T8A08 - What is the approximate bandwidth of a single sideband voice signal?
A. 1 kHz
B. 3 kHz
C. 6 kHz
D. 15 kHz
<number>
Modes

## Slide 26: T8A09 - What is the approximate bandwidth of a VHF repeater FM phone signal?
A. Less than 500 Hz
B. About 150 kHz
C. Between 10 and 15 kHz
D. Between 50 and 125 kHz
<number>
Modes

## Slide 27: T8A09 - What is the approximate bandwidth of a VHF repeater FM phone signal?
A. Less than 500 Hz
B. About 150 kHz
C. Between 10 and 15 kHz
D. Between 50 and 125 kHz
<number>
Modes

## Slide 28: T8A10 - What is the typical bandwidth of analog fast-scan TV transmissions on the 70 cm band?
A. More than 10 MHz
B. About 6 MHz
C. About 3 MHz
D. About 1 MHz
<number>
Modes

## Slide 29: T8A10 - What is the typical bandwidth of analog fast-scan TV transmissions on the 70 cm band?
A. More than 10 MHz
B. About 6 MHz
C. About 3 MHz
D. About 1 MHz
<number>
Modes

## Slide 30: T8A11 - What is the approximate maximum bandwidth required to transmit a CW signal?
A. 2.4 kHz
B. 150 Hz
C. 1000 Hz
D. 15 kHz
<number>
Modes

## Slide 31: T8A11 - What is the approximate maximum bandwidth required to transmit a CW signal?
A. 2.4 kHz
B. 150 Hz
C. 1000 Hz
D. 15 kHz
<number>
Modes

## Slide 32: G4D11 How close to the upper edge of the 20 meter General Class band should your displayed carrier frequency be when using 3 kHz wide USB?
  A. 3 kHz above the edge of the band
  B. 3 kHz below the edge of the band
  C. Your displayed carrier frequency may be set at the edge of the band
  D. Center your signal on the edge of the band
<number>
Modes

## Slide 33: G4D11 How close to the upper edge of the 20 meter General Class band should your displayed carrier frequency be when using 3 kHz wide USB?
  A. 3 kHz above the edge of the band
  B. 3 kHz below the edge of the band
  C. Your displayed carrier frequency may be set at the edge of the band
  D. Center your signal on the edge of the band
<number>
Modes

## Slide 34: G8A12 What signal(s) would be found at the output of a properly adjusted balanced modulator?
  A. Both upper and lower sidebands
  B. Either upper or lower sideband, but not both
  C. Both upper and lower sidebands and the carrier
  D. The modulating signal and the unmodulated carrier
<number>
Modes

## Slide 35: G8A12 What signal(s) would be found at the output of a properly adjusted balanced modulator?
  A. Both upper and lower sidebands
  B. Either upper or lower sideband, but not both
  C. Both upper and lower sidebands and the carrier
  D. The modulating signal and the unmodulated carrier
<number>
Modes

## Slide 36: T8B - Amateur satellite operation
Doppler shift, basic orbits, operating protocols; control operator, transmitter power considerations; satellite tracking; digital modes
<number>
Modes

## Slide 37: G8B01 What receiver stage combines a 14.250 MHz input signal with a 13.795 MHz oscillator signal to produce a 455 kHz intermediate frequency (IF) signal?
  A. Mixer
  B. BFO
  C. VFO
  D. Discriminator
<number>
Modes

## Slide 38: G8B01 What receiver stage combines a 14.250 MHz input signal with a 13.795 MHz oscillator signal to produce a 455 kHz intermediate frequency (IF) signal?
  A. Mixer
  B. BFO
  C. VFO
  D. Discriminator
<number>
Modes

## Slide 39: Susan J. Helms, KC7NHZ Flight Engineer - ISS
<number>
Modes
Notes: <number>
Most astronauts are licensed hams. Most often they get their Technician licenses so they are allowed to operate the ISS radio station.
Photo from NASA

## Slide 40: T8B01 - Who may be the control operator of a station communicating through an amateur satellite or space station?
A. Only an Amateur Extra Class operator
B. A General Class licensee or higher licensee who has a satellite operator certification
C. Only an Amateur Extra Class operator who is also an AMSAT member
D. Any amateur whose license privileges allow them to transmit on the satellite uplink frequency
<number>
Modes

## Slide 41: T8B01 - Who may be the control operator of a station communicating through an amateur satellite or space station?
A. Only an Amateur Extra Class operator
B. A General Class licensee or higher licensee who has a satellite operator certification
C. Only an Amateur Extra Class operator who is also an AMSAT member
D. Any amateur whose license privileges allow them to transmit on the satellite uplink frequency
<number>
Modes

## Slide 42: T8B02 - How much transmitter power should be used on the uplink frequency of an amateur satellite or space station?
A. The maximum power of your transmitter
B. The minimum amount of power needed to complete the contact
C. No more than half the rating of your linear amplifier
D. Never more than 1 watt
<number>
Modes

## Slide 43: T8B02 - How much transmitter power should be used on the uplink frequency of an amateur satellite or space station?
A. The maximum power of your transmitter
B. The minimum amount of power needed to complete the contact
C. No more than half the rating of your linear amplifier
D. Never more than 1 watt
<number>
Modes

## Slide 44: T8B03 - Which of the following are provided by satellite tracking programs?
A. Maps showing the real-time position of the satellite track over the earth
B. The time, azimuth, and elevation of the start, maximum altitude, and end of a pass
C. The apparent frequency of the satellite transmission, including effects of Doppler shift
D. All of these answers are correct
<number>
Modes

## Slide 45: T8B03 - Which of the following are provided by satellite tracking programs?
A. Maps showing the real-time position of the satellite track over the earth
B. The time, azimuth, and elevation of the start, maximum altitude, and end of a pass
C. The apparent frequency of the satellite transmission, including effects of Doppler shift
D. All of these answers are correct
<number>
Modes

## Slide 46: T8B04 - Which amateur stations may make contact with an amateur station on the International Space Station using 2 meter and 70 cm band amateur radio frequencies?
A. Only members of amateur radio clubs at NASA facilities
B. Any amateur holding a Technician or higher class license
C. Only the astronaut's family members who are hams
D. You cannot talk to the ISS on amateur radio frequencies
<number>
Modes

## Slide 47: T8B04 - Which amateur stations may make contact with an amateur station on the International Space Station using 2 meter and 70 cm band amateur radio frequencies?
A. Only members of amateur radio clubs at NASA facilities
B. Any amateur holding a Technician or higher class license
C. Only the astronaut's family members who are hams
D. You cannot talk to the ISS on amateur radio frequencies
<number>
Modes

## Slide 48: T8B05 - What is a satellite beacon?
A. The primary transmit antenna on the satellite
B. An indicator light that that shows where to point your antenna
C. A reflective surface on the satellite
D. A transmission from a space station that contains information about a satellite
<number>
Modes

## Slide 49: T8B05 - What is a satellite beacon?
A. The primary transmit antenna on the satellite
B. An indicator light that that shows where to point your antenna
C. A reflective surface on the satellite
D. A transmission from a space station that contains information about a satellite
<number>
Modes

## Slide 50: T8B06 - Which of the following are inputs to a satellite tracking program?
A. The weight of the satellite
B. The Keplerian elements
C. The last observed time of zero Doppler shift
D. All of these answers are correct
<number>
Modes

## Slide 51: T8B06 - Which of the following are inputs to a satellite tracking program?
A. The weight of the satellite
B. The Keplerian elements
C. The last observed time of zero Doppler shift
D. All of these answers are correct
<number>
Modes

## Slide 52: Keplerian Data Sample
<number>
Modes

## Slide 53: Doppler Shift
<number>
Modes
Doppler shift is a change in frequency as an object moves. The wave in front of the object is compressed and expanded behind.
To a fixed observer, the shortened wavelength in front causes the frequency to increase. As the object passes, the longer wavelength behind will cause the frequency to shift down.

## Slide 54: T8B07 - With regard to satellite communications, what is Doppler shift?
A. A change in the satellite orbit
B. A mode where the satellite receives signals on one band and transmits on another
C. An observed change in signal frequency caused by relative motion between the satellite and the earth station
D. A special digital communications mode for some satellites
<number>
Modes

## Slide 55: T8B07 - With regard to satellite communications, what is Doppler shift?
A. A change in the satellite orbit
B. A mode where the satellite receives signals on one band and transmits on another
C. An observed change in signal frequency caused by relative motion between the satellite and the earth station
D. A special digital communications mode for some satellites
<number>
Modes

## Slide 56: T8B08 - What is meant by the statement that a satellite is operating in mode U/V?
A. The satellite uplink is in the 15 meter band and the downlink is in the 10 meter band
B. The satellite uplink is in the 70 cm band and the downlink is in the 2 meter band
C. The satellite operates using ultraviolet frequencies
D. The satellite frequencies are usually variable
<number>
Modes

## Slide 57: T8B08 - What is meant by the statement that a satellite is operating in mode U/V?
A. The satellite uplink is in the 15 meter band and the downlink is in the 10 meter band
B. The satellite uplink is in the 70 cm band and the downlink is in the 2 meter band
C. The satellite operates using ultraviolet frequencies
D. The satellite frequencies are usually variable
<number>
Modes

## Slide 58: T8B09 - What causes spin fading when referring to satellite signals?
A. Circular polarized noise interference radiated from the sun
B. Rotation of the satellite and its antennas
C. Doppler shift of the received signal
D. Interfering signals within the satellite uplink band
<number>
Modes

## Slide 59: T8B09 - What causes spin fading when referring to satellite signals?
A. Circular polarized noise interference radiated from the sun
B. Rotation of the satellite and its antennas
C. Doppler shift of the received signal
D. Interfering signals within the satellite uplink band
<number>
Modes

## Slide 60: T8B10 - What do the initials LEO tell you about an amateur satellite?
A. The satellite battery is in Low Energy Operation mode
B. The satellite is performing a Lunar Ejection Orbit maneuver
C. The satellite is in a Low Earth Orbit
D. The satellite uses Light Emitting Optics
<number>
Modes

## Slide 61: T8B10 - What do the initials LEO tell you about an amateur satellite?
A. The satellite battery is in Low Energy Operation mode
B. The satellite is performing a Lunar Ejection Orbit maneuver
C. The satellite is in a Low Earth Orbit
D. The satellite uses Light Emitting Optics
<number>
Modes

## Slide 62: T8B11 - What is a commonly used method of sending signals to and from a digital satellite?
A. USB AFSK
B. PSK31
C. FM Packet
D. WSJT
<number>
Modes

## Slide 63: T8B11 - What is a commonly used method of sending signals to and from a digital satellite?
A. USB AFSK
B. PSK31
C. FM Packet
D. WSJT
<number>
Modes

## Slide 64: T8C – Operating activities
radio direction finding; radio control; contests; linking over the Internet; grid locators
<number>
Modes

## Slide 65: T8C01 - Which of the following methods is used to locate sources of noise interference or jamming?
A. Echolocation
B. Doppler radar
C. Radio direction finding
D. Phase locking
<number>
Modes

## Slide 66: T8C01 - Which of the following methods is used to locate sources of noise interference or jamming?
A. Echolocation
B. Doppler radar
C. Radio direction finding
D. Phase locking
<number>
Modes

## Slide 67: T8C02 - Which of these items would be useful for a hidden transmitter hunt?
A. Calibrated SWR meter
B. A directional antenna
C. A calibrated noise bridge
D. All of these choices are correct
<number>
Modes

## Slide 68: T8C02 - Which of these items would be useful for a hidden transmitter hunt?
A. Calibrated SWR meter
B. A directional antenna
C. A calibrated noise bridge
D. All of these choices are correct
<number>
Modes

## Slide 69: T8C03 - What popular operating activity involves contacting as many stations as possible during a specified period of time?
A. Contesting
B. Net operations
C. Public service events
D. Simulated emergency exercises
<number>
Modes

## Slide 70: T8C03 - What popular operating activity involves contacting as many stations as possible during a specified period of time?
A. Contesting
B. Net operations
C. Public service events
D. Simulated emergency exercises
<number>
Modes

## Slide 71: T8C04 - Which of the following is good procedure when contacting another station in a radio contest?
A. Be sure to sign only the last two letters of your call if there is a pileup calling the station
B. Work the station twice to be sure that you are in his log
C. Send only the minimum information needed for proper identification and the contest exchange
D. All of these choices are correct
<number>
Modes

## Slide 72: T8C04 - Which of the following is good procedure when contacting another station in a radio contest?
A. Be sure to sign only the last two letters of your call if there is a pileup calling the station
B. Work the station twice to be sure that you are in his log
C. Send only the minimum information needed for proper identification and the contest exchange
D. All of these choices are correct
<number>
Modes

## Slide 73: Maidenhead Grids
<number>
Two letters and two numbers define an area 1° latitude x 2° longitude anywhere in the world. Seattle is CN87, Portland CN85
Notes: <number>
This grid map is courtesy Icom America and is downloadable from their web site at http://www.icomamerica.com.
Two letter designator followed by a number ranging from 1 to 100 representing 1° latitude x 2° longitude square area of the earth.
  The earth is divided into 20° Latitude x 10° Longitude squares starting on the date line at the south pole and going North and East.
  Each square is given a two letter designator labeled East and North starting with AA and Ending with RR
  An – In are West of GMT, Jn – Rn are east of GMT
  nA – n I are South of the equator, nJ – nR are North of the equator
  Each square is further divided into 100 1°x2° squares and given a number starting in the lower left corner of the square and are labeled up and right
  Seattle is in CN-87, Los Angles DM-04
  Spokane is in DN-17

## Slide 74: T8C05 - What is a grid locator?
A. A letter-number designator assigned to a geographic location
B. A letter-number designator assigned to an azimuth and elevation
C. An instrument for neutralizing a final amplifier
D. An instrument for radio direction finding
<number>
Modes

## Slide 75: T8C05 - What is a grid locator?
A. A letter-number designator assigned to a geographic location
B. A letter-number designator assigned to an azimuth and elevation
C. An instrument for neutralizing a final amplifier
D. An instrument for radio direction finding
<number>
Modes

## Slide 76: EchoLink® and IRLP
<number>
EchoLink® software allows licensed Amateur Radio stations to communicate with one another over the Internet, using voice-over-IP (VoIP) technology.
Gateway
Gateway

## Slide 77: T8C06 - How is access to an IRLP node accomplished?
A. By obtaining a password which is sent via voice to the node
B. By using DTMF signals
C. By entering the proper Internet password
D. By using CTCSS tone codes
<number>
Modes

## Slide 78: T8C06 - How is access to an IRLP node accomplished?
A. By obtaining a password which is sent via voice to the node
B. By using DTMF signals
C. By entering the proper Internet password
D. By using CTCSS tone codes
<number>
Modes

## Slide 79: T8C07 - What is the maximum power allowed when transmitting telecommand signals to radio controlled models?
A. 500 milliwatts
B. 1 watt
C. 25 watts
D. 1500 watts
<number>
Modes

## Slide 80: T8C07 - What is the maximum power allowed when transmitting telecommand signals to radio controlled models?
A. 500 milliwatts
B. 1 watt
C. 25 watts
D. 1500 watts
<number>
Modes

## Slide 81: T8C08 - What is required in place of on-air station identification when sending signals to a radio control model using amateur frequencies?
A. Voice identification must be transmitted every 10 minutes
B. Morse code ID must be sent once per hour
C. A label indicating the licensee’s name, call sign and address must be affixed to the transmitter
D. A flag must be affixed to the transmitter antenna with the station call sign in 1 inch high letters or larger
<number>
Modes

## Slide 82: T8C08 - What is required in place of on-air station identification when sending signals to a radio control model using amateur frequencies?
A. Voice identification must be transmitted every 10 minutes
B. Morse code ID must be sent once per hour
C. A label indicating the licensee’s name, call sign and address must be affixed to the transmitter
D. A flag must be affixed to the transmitter antenna with the station call sign in 1 inch high letters or larger
<number>
Modes

## Slide 83: T8C09 - How might you obtain a list of active nodes that use VoIP?
A. From the FCC Rulebook
B. From your local emergency coordinator
C. From a repeater directory
D. From the local repeater frequency coordinator
<number>
Modes

## Slide 84: T8C09 - How might you obtain a list of active nodes that use VoIP?
A. From the FCC Rulebook
B. From your local emergency coordinator
C. From a repeater directory
D. From the local repeater frequency coordinator
<number>
Modes

## Slide 85: T8C10 - How do you select a specific IRLP node when using a portable transceiver?
A. Choose a specific CTCSS tone
B. Choose the correct DSC tone
C. Access the repeater autopatch
D. Use the keypad to transmit the IRLP node ID
<number>
Modes

## Slide 86: T8C10 - How do you select a specific IRLP node when using a portable transceiver?
A. Choose a specific CTCSS tone
B. Choose the correct DSC tone
C. Access the repeater autopatch
D. Use the keypad to transmit the IRLP node ID
<number>
Modes

## Slide 87: T8C11 - What name is given to an amateur radio station that is used to connect other amateur stations to the Internet?
A. A gateway
B. A repeater
C. A digipeater
D. A beacon
<number>
Modes

## Slide 88: T8C11 - What name is given to an amateur radio station that is used to connect other amateur stations to the Internet?
A. A gateway
B. A repeater
C. A digipeater
D. A beacon
<number>
Modes

## Slide 89: T8C12 - What is meant by Voice Over Internet Protocol (VoIP) as used in amateur radio?
A. A set of rules specifying how to identify your station when linked over the Internet to another station
B. A set of guidelines for working DX during contests using Internet access
C. A technique for measuring the modulation quality of a transmitter using remote sites monitored via the Internet
D. A method of delivering voice communications over the Internet using digital techniques
<number>
Modes

## Slide 90: T8C12 - What is meant by Voice Over Internet Protocol (VoIP) as used in amateur radio?
A. A set of rules specifying how to identify your station when linked over the Internet to another station
B. A set of guidelines for working DX during contests using Internet access
C. A technique for measuring the modulation quality of a transmitter using remote sites monitored via the Internet
D. A method of delivering voice communications over the Internet using digital techniques
<number>
Modes

## Slide 91: T8C13 - What is the Internet Radio Linking Project (IRLP)?
A. A technique to connect amateur radio systems, such as repeaters, via the Internet using Voice Over Internet Protocol
B. A system for providing access to websites via amateur radio
C. A system for informing amateurs in real time of the frequency of active DX stations
D. A technique for measuring signal strength of an amateur transmitter via the Internet
<number>
Modes

## Slide 92: T8C13 - What is the Internet Radio Linking Project (IRLP)?
A. A technique to connect amateur radio systems, such as repeaters, via the Internet using Voice Over Internet Protocol
B. A system for providing access to websites via amateur radio
C. A system for informing amateurs in real time of the frequency of active DX stations
D. A technique for measuring signal strength of an amateur transmitter via the Internet
<number>
Modes

## Slide 93: T8D – Non-voice communications
image signals; digital modes; CW; packet; PSK31; APRS; error detection and correction; NTSC
<number>
Modes

## Slide 94: T8D01 - Which of the following is an example of a digital communications method?
A. Packet
B. PSK31
C. MFSK
D. All of these choices are correct
<number>
Modes

## Slide 95: T8D01 - Which of the following is an example of a digital communications method?
A. Packet
B. PSK31
C. MFSK
D. All of these choices are correct
<number>
Modes

## Slide 96: APRS Automatic Position Reporting System
Real-time
location
mapping
Modulation Modes 2014
<number>

## Slide 97: T8D02 - What does the term “APRS” mean?
A. Automatic Packet Reporting System
B. Associated Public Radio Station
C. Auto Planning Radio Set-up
D. Advanced Polar Radio System
<number>
Modes

## Slide 98: T8D02 - What does the term “APRS” mean?
A. Automatic Packet Reporting System
B. Associated Public Radio Station
C. Auto Planning Radio Set-up
D. Advanced Polar Radio System
<number>
Modes

## Slide 99: T8D03 - Which of the following devices provides data to the transmitter when sending automatic position reports from a mobile amateur radio station?
A. The vehicle speedometer
B. A WWV receiver
C. A connection to a broadcast FM sub-carrier receiver
D. A Global Positioning System receiver
<number>
Modes

## Slide 100: T8D03 - Which of the following devices provides data to the transmitter when sending automatic position reports from a mobile amateur radio station?
A. The vehicle speedometer
B. A WWV receiver
C. A connection to a broadcast FM sub-carrier receiver
D. A Global Positioning System receiver
<number>
Modes

## Slide 101: National Television Systems Committee (NTSC)
Television Standards
  NTSC – Canada, US, Japan, South Korea
  PAL
  SECAM
<number>
Modulation Modes 2014

## Slide 102: T8D04 - What type of transmission is indicated by the term NTSC?
A. A Normal Transmission mode in Static Circuit
B. A special mode for earth satellite uplink
C. An analog fast scan color TV signal
D. A frame compression scheme for TV signals
<number>
Modes

## Slide 103: T8D04 - What type of transmission is indicated by the term NTSC?
A. A Normal Transmission mode in Static Circuit
B. A special mode for earth satellite uplink
C. An analog fast scan color TV signal
D. A frame compression scheme for TV signals
<number>
Modes

## Slide 104: T8D05 - Which of the following is an application of APRS (Automatic Packet Reporting System)?
A. Providing real time tactical digital communications in conjunction with a map showing the locations of stations
B. Showing automatically the number of packets transmitted via PACTOR during a specific time interval
C. Providing voice over Internet connection between repeaters
D. Providing information on the number of stations signed into a repeater
<number>
Modes

## Slide 105: T8D05 - Which of the following is an application of APRS (Automatic Packet Reporting System)?
A. Providing real time tactical digital communications in conjunction with a map showing the locations of stations
B. Showing automatically the number of packets transmitted via PACTOR during a specific time interval
C. Providing voice over Internet connection between repeaters
D. Providing information on the number of stations signed into a repeater
<number>
Modes

## Slide 106: PSK31 Digital Mode
<number>
Modulation Modes 2014
PSK31 is a low speed, narrow bandwidth data mode that provides VERY EFFICIENT keyboard to keyboard chat capability. PSK31 is not error-corrected.

## Slide 107: T8D06 - What does the abbreviation PSK mean?
A. Pulse Shift Keying
B. Phase Shift Keying
C. Packet Short Keying
D. Phased Slide Keying
<number>
Modes

## Slide 108: T8D06 - What does the abbreviation PSK mean?
A. Pulse Shift Keying
B. Phase Shift Keying
C. Packet Short Keying
D. Phased Slide Keying
<number>
Modes

## Slide 109: T8D07 - What is PSK31?
A. A high-rate data transmission mode
B. A method of reducing noise interference to FM signals
C. A method of compressing digital television signals
D. A low-rate data transmission mode
<number>
Modes

## Slide 110: T8D07 - What is PSK31?
A. A high-rate data transmission mode
B. A method of reducing noise interference to FM signals
C. A method of compressing digital television signals
D. A low-rate data transmission mode
<number>
Modes

## Slide 111: T8D08 - Which of the following may be included in packet transmissions?
A. A check sum which permits error detection
B. A header which contains the call sign of the station to which the information is being sent
C. Automatic repeat request in case of error
D. All of these choices are correct
<number>
Modes

## Slide 112: T8D08 - Which of the following may be included in packet transmissions?
A. A check sum which permits error detection
B. A header which contains the call sign of the station to which the information is being sent
C. Automatic repeat request in case of error
D. All of these choices are correct
<number>
Modes

## Slide 113: T8D09 - What code is used when sending CW in the amateur bands?
A. Baudot
B. Hamming
C. International Morse
D. Gray
<number>
Modes

## Slide 114: T8D09 - What code is used when sending CW in the amateur bands?
A. Baudot
B. Hamming
C. International Morse
D. Gray
<number>
Modes

## Slide 115: T8D10 - Which of the following can be used to transmit CW in the amateur bands?
A. Straight Key
B. Electronic Keyer
C. Computer Keyboard
D. All of these choices are correct
<number>
Modes

## Slide 116: T8D10 - Which of the following can be used to transmit CW in the amateur bands?
A. Straight Key
B. Electronic Keyer
C. Computer Keyboard
D. All of these choices are correct
<number>
Modes

## Slide 117: T8D11 - What is an ARQ transmission system?
A. A special transmission format limited to video signals
B. A system used to encrypt command signals to an amateur radio satellite
C. A digital scheme whereby the receiving station detects errors and sends a request to the sending station to retransmit the information
D. A method of compressing the data in a message so more information can be sent in a shorter time
<number>
Modes

## Slide 118: T8D11 - What is an ARQ transmission system?
A. A special transmission format limited to video signals
B. A system used to encrypt command signals to an amateur radio satellite
C. A digital scheme whereby the receiving station detects errors and sends a request to the sending station to retransmit the information
D. A method of compressing the data in a message so more information can be sent in a shorter time
<number>
Modes

## Slide 119: G8B11 How does forward error correction allow the receiver to correct errors in received data packets?
  A. By controlling transmitter output power for optimum signal strength
  B. By using the varicode character set
  C. By transmitting redundant information with the data
  D. By using a parity bit with each character

## Slide 120: G8B11 How does forward error correction allow the receiver to correct errors in received data packets?
  A. By controlling transmitter output power for optimum signal strength
  B. By using the varicode character set
  C. By transmitting redundant information with the data
  D. By using a parity bit with each character

## Slide 121: G8B12 What is the relationship between transmitted symbol rate and bandwidth?
  A. Symbol rate and bandwidth are not related
  B. Higher symbol rates require higher bandwidth
  C. Lower symbol rates require higher bandwidth
  D. Bandwidth is constant for data mode signals

## Slide 122: G8B12 What is the relationship between transmitted symbol rate and bandwidth?
  A. Symbol rate and bandwidth are not related
  B. Higher symbol rates require higher bandwidth
  C. Lower symbol rates require higher bandwidth
  D. Bandwidth is constant for data mode signals

## Slide 123: End of SUBELEMENT T8
Modulation modes: amateur satellite operation; operating activities; non-voice communications
<number>
Modes 2014