## Slide 1
SUBELEMENT T2 Operating Procedures [3 Exam Questions - 3 Groups]
<number>
Operating Procedures 2014
Notes: Subelement T2 Operating Procedures. Technician Training Slides for 2014 Question Pool Good through June 30, 2018 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM, Howard Schultz, W7HS.
<number>

## Slide 2
T2A - Station operation: choosing an operating frequency; calling another station; test transmissions; procedural signs; use of minimum power; choosing an operating frequency; band plans; calling frequencies; repeater offsets T2B – VHF/UHF operating practices: SSB phone; FM repeater; simplex; splits and shifts; CTCSS; DTMF; tone squelch; carrier squelch; phonetics; operational problem resolution; Q signals T2C – Public service: emergency and non-emergency operations; applicability of FCC rules; RACES and ARES; net and traffic procedures; emergency restrictions
<number>
Operating Procedures

## Slide 3
ITU Phonetic Alphabet
A Alfa AL FAH
B Bravo BRAH VOH
C Charlie CHAR LEE
D Delta DELL TAH
E Echo ECK OH
F Foxtrot FOKS TROT
G Golf GOLF
H Hotel HOH TELL
I India IN DEE AH
J Juliet JEW LEE ETT
K Kilo KEY LOH
L Lima LEE MAH
M Mike MIKE
N November NO VEM BER
O Oscar OSS CAH
P Papa PAH PAH
Q Quebec KEH BECK
R Romeo ROW ME OH
S Sierra SEE AIR RAH
T Tango TANG GO
U Uniform YOU NEE FORM
V Victor VIK TAH
W Whiskey WISS KEY
X X-Ray ECKS RAY
Y Yankee YANG KEY
Z Zulu ZOO LOO
<number>
Operating Procedures
Agreed upon words to represent the letters of the “roman alphabet”.
The boldfaced syllables are emphasized. The pronunciations shown in this table were designed for those who speak any of the international languages.
The pronunciations given for “Oscar”, “Papa” and “Victor” may seem awkward to English-speaking people in the US.

## Slide 4
VHF/UHF Propagation
VHF / UHF signals typically travel by line of sight propagation
<number>
Operating Procedures
VHF / UHF signals can be blocked by and/or reflected off mountains and large buildings.

## Slide 5
VHF/UHF Propagation
Input Freq
144.61 MHz
<number>
Operating Procedures
Output Freq
145.21 MHz
Offset
- 600 kHz
60+ Miles Distance

## Slide 6
<number>
Operating Procedures

## Slide 7
T2A01 - What is the most common repeater frequency offset in the 2 meter band?
A. Plus 500 kHz
B. Plus or minus 600 kHz
C. Minus 500 kHz
D. Only plus 600 kHz
<number>
Operating Procedures

## Slide 8
T2A01 - What is the most common repeater frequency offset in the 2 meter band?
A. Plus 500 kHz
B. Plus or minus 600 kHz
C. Minus 500 kHz
D. Only plus 600 kHz
<number>
Operating Procedures

## Slide 9
T2A02 What is the national calling frequency for FM simplex operations in the 70 cm band?
A. 146.520 MHz
B. 145.000 MHz
C. 432.100 MHz
D. 446.000 MHz
<number>
Operating Procedures

## Slide 10
T2A02 What is the national calling frequency for FM simplex operations in the 70 cm band?
A. 146.520 MHz
B. 145.000 MHz
C. 432.100 MHz
D. 446.000 MHz
<number>
Operating Procedures

## Slide 11
T2A03 - What is a common repeater frequency offset in the 70 cm band?
A. Plus or minus 5 MHz
B. Plus or minus 600 kHz
C. Minus 600 kHz
D. Plus 600 kHz
<number>
Operating Procedures

## Slide 12
T2A03 - What is a common repeater frequency offset in the 70 cm band?
A. Plus or minus 5 MHz
B. Plus or minus 600 kHz
C. Minus 600 kHz
D. Plus 600 kHz
<number>
Operating Procedures

## Slide 13
G2A01 Which sideband is most commonly used for voice Communications on frequencies of 14 MHz or higher?
  A. Upper sideband
  B. Lower sideband
  C. Vestigial sideband
  D. Double sideband
<number>
Operating Procedures

## Slide 14
G2A01 Which sideband is most commonly used for voice Communications on frequencies of 14 MHz or higher?
  A. Upper sideband
  B. Lower sideband
  C. Vestigial sideband
  D. Double sideband
<number>
Operating Procedures

## Slide 15
T2A04 - What is an appropriate way to call another station on a repeater if you know the other station's call sign?
A. Say break, break then say the station's call sign
B. Say the station's call sign then identify with your call sign
C. Say CQ three times then the other station's call sign
D. Wait for the station to call CQ then answer it
<number>
Operating Procedures

## Slide 16
T2A04 - What is an appropriate way to call another station on a repeater if you know the other station's call sign?
A. Say break, break then say the station's call sign
B. Say the station's call sign then identify with your call sign
C. Say CQ three times then the other station's call sign
D. Wait for the station to call CQ then answer it
<number>
Operating Procedures

## Slide 17
T2A05 - How should you respond to a station calling CQ?
A. Transmit CQ followed by the other station’s call sign
B. Transmit your call sign followed by the other station’s call sign
C. Transmit the other station’s call sign followed by your call sign
D. Transmit a signal report followed by your call sign
<number>
Operating Procedures

## Slide 18
T2A05 - How should you respond to a station calling CQ?
A. Transmit CQ followed by the other station’s call sign
B. Transmit your call sign followed by the other station’s call sign
C. Transmit the other station’s call sign followed by your call sign
D. Transmit a signal report followed by your call sign
<number>
Operating Procedures

## Slide 19
T2A06 - What must an amateur operator do when making on-air transmissions to test equipment or antennas?
A. Properly identify the transmitting station
B. Make test transmissions only after 10:00 p.m. local time
C. Notify the FCC of the test transmission
D. State the purpose of the test during the test procedure
<number>
Operating Procedures

## Slide 20
T2A06 - What must an amateur operator do when making on-air transmissions to test equipment or antennas?
A. Properly identify the transmitting station
B. Make test transmissions only after 10:00 p.m. local time
C. Notify the FCC of the test transmission
D. State the purpose of the test during the test procedure
<number>
Operating Procedures

## Slide 21
T2A07 - Which of the following is true when making a test transmission?
A. Station identification is not required if the transmission is less than 15 seconds
B. Station identification is not required if the transmission is less than 1 watt
C. Station identification is only required once an hour when the transmissions are for test purposes only
D. Station identification is required at least every ten minutes during the test and at the end of the test
<number>
Operating Procedures

## Slide 22
T2A07 - Which of the following is true when making a test transmission?
A. Station identification is not required if the transmission is less than 15 seconds
B. Station identification is not required if the transmission is less than 1 watt
C. Station identification is only required once an hour when the transmissions are for test purposes only
D. Station identification is required at least every ten minutes during the test and at the end of the test
<number>
Operating Procedures

## Slide 23
Repeater Input/Output Offsets
Band Offset
6 meters 1 MHz
2 meters 600 kHz
1 25 meters 1.6 MHz
70 cm 5 MHz
33 cm 12 MHz
23 cm 20 MHz
<number>
Operating Procedures

## Slide 24
T2A08 What is the meaning of the procedural signal “CQ”?
A. Call on the quarter hour
B. A new antenna is being tested (no station should answer)
C. Only the called station should transmit
D. Calling any station
<number>
Operating Procedures

## Slide 25
T2A08 What is the meaning of the procedural signal “CQ”?
A. Call on the quarter hour
B. A new antenna is being tested (no station should answer)
C. Only the called station should transmit
D. Calling any station
<number>
Operating Procedures

## Slide 26
T2A09 - What brief statement is often transmitted in place of “CQ” to indicate that you are listening on a repeater?
A. The words “Hello test” followed by your call sign
B. Your call sign
C. The repeater call sign followed by your call sign
D. The letters “QSY” followed by your call sign
<number>
Operating Procedures

## Slide 27
T2A09 - What brief statement is often transmitted in place of “CQ” to indicate that you are listening on a repeater?
A. The words “Hello test” followed by your call sign
B. Your call sign
C. The repeater call sign followed by your call sign
D. The letters “QSY” followed by your call sign
<number>
Operating Procedures

## Slide 28
T2A10 - What is a band plan, beyond the privileges established by the FCC?
A. A voluntary guideline for using different modes or activities within an amateur band
B. A mandated list of operating schedules
C. A list of scheduled net frequencies
D. A plan devised by a club to indicate frequency band usage
<number>
Operating Procedures

## Slide 29
T2A10 - What is a band plan, beyond the privileges established by the FCC?
A. A voluntary guideline for using different modes or activities within an amateur band
B. A mandated list of operating schedules
C. A list of scheduled net frequencies
D. A plan devised by a club to indicate frequency band usage
<number>
Operating Procedures

## Slide 30
ARRL Band Plan
<number>
Operating Procedures

## Slide 31
VHF/UHF Band Plan
<number>
Operating Procedures

## Slide 32
T2A11 - Which of the following is an FCC rule regarding power levels used in the amateur bands, under normal, non-distress circumstances?
A. There is no limit to power as long as there is no interference with other services
B. No more than 200 watts PEP may be used
C. Up to 1500 watts PEP may be used on any amateur frequency without restriction
D. While not exceeding the maximum power permitted on a given band, use the minimum power necessary to carry out the desired communication
<number>
Operating Procedures

## Slide 33
T2A11 - Which of the following is an FCC rule regarding power levels used in the amateur bands, under normal, non-distress circumstances?
A. There is no limit to power as long as there is no interference with other services
B. No more than 200 watts PEP may be used
C. Up to 1500 watts PEP may be used on any amateur frequency without restriction
D. While not exceeding the maximum power permitted on a given band, use the minimum power necessary to carry out the desired communication
<number>
Operating Procedures

## Slide 34
T2A12 - Which of the following is a guideline to use when choosing an operating frequency for calling CQ?
A. Listen first to be sure that no one else is using the frequency
B. Ask if the frequency is in use
C. Make sure you are in your assigned band
D. All of these choices are correct
<number>
Operating Procedures

## Slide 35
T2A12 - Which of the following is a guideline to use when choosing an operating frequency for calling CQ?
A. Listen first to be sure that no one else is using the frequency
B. Ask if the frequency is in use
C. Make sure you are in your assigned band
D. All of these choices are correct
<number>
Operating Procedures

## Slide 36
T2B – VHF/UHF operating practices:
SSB phone; FM repeater; simplex; splits and shifts; CTCSS; DTMF; tone squelch; carrier squelch; phonetics; operational problem resolution; Q signals
<number>
Operating Procedures

## Slide 37
T2B01 - What is the term used to describe an amateur station that is transmitting and receiving on the same frequency?
A. Full duplex communication
B. Diplex communication
C. Simplex communication
D. Multiplex communication
<number>
Operating Procedures

## Slide 38
T2B01 - What is the term used to describe an amateur station that is transmitting and receiving on the same frequency?
A. Full duplex communication
B. Diplex communication
C. Simplex communication
D. Multiplex communication
<number>
Operating Procedures

## Slide 39
Repeater Access Tone
Continuous Tone Coded Squelch System (CTCSS) tones are sub-audible tones added to an FM carrier.
Some repeater systems require CTCSS tones to access.
To access a repeater, in addition to knowing the repeater offset or shift, as previously discussed, you must also know if a tone is required and what it is.
<number>
Operating Procedures

## Slide 40
<number>
Operating Procedures
Frequency
Repeater Offset +/-
Tone

## Slide 41
T2B02 - What is the term used to describe the use of a sub-audible tone transmitted with normal voice audio to open the squelch of a receiver?
A. Carrier squelch
B. Tone burst
C. DTMF
D. CTCSS
<number>
Operating Procedures

## Slide 42
T2B02 - What is the term used to describe the use of a sub-audible tone transmitted with normal voice audio to open the squelch of a receiver?
A. Carrier squelch
B. Tone burst
C. DTMF
D. CTCSS
Continuous Tone Coded Squelch System (CTCSS) tones are sub-audible tones added to an FM carrier.
<number>
Operating Procedures

## Slide 43
T2B03 - Which of the following describes the muting of receiver audio controlled solely by the presence or absence of an RF signal?
A. Tone squelch
B. Carrier squelch
C. CTCSS
D. Modulated carrier
<number>
Operating Procedures

## Slide 44
T2B03 - Which of the following describes the muting of receiver audio controlled solely by the presence or absence of an RF signal?
A. Tone squelch
B. Carrier squelch
C. CTCSS
D. Modulated carrier
<number>
Operating Procedures

## Slide 45
T2B04 - Which of the following common problems might cause you to be able to hear but not access a repeater even when transmitting with the proper offset?
A. The repeater receiver may require an audio tone burst for access
B. The repeater receiver may require a CTCSS tone for access
C. The repeater receiver may require a DCS tone sequence for access
D. All of these choices are correct
<number>
Operating Procedures

## Slide 46
T2B04 - Which of the following common problems might cause you to be able to hear but not access a repeater even when transmitting with the proper offset?
A. The repeater receiver may require an audio tone burst for access
B. The repeater receiver may require a CTCSS tone for access
C. The repeater receiver may require a DCS tone sequence for access
D. All of these choices are correct
<number>
Operating Procedures

## Slide 47
T2B05 - What determines the amount of deviation of an FM (as opposed to PM) signal?
A. Both the frequency and amplitude of the modulating signal
B. The frequency of the modulating signal
C. The amplitude of the modulating signal
D. The relative phase of the modulating signal and the carrier
<number>
Operating Procedures

## Slide 48
T2B05 - What determines the amount of deviation of an FM (as opposed to PM) signal?
A. Both the frequency and amplitude of the modulating signal
B. The frequency of the modulating signal
C. The amplitude of the modulating signal
D. The relative phase of the modulating signal and the carrier
<number>
Operating Procedures
Notes: This is because PM requires more complex receiving hardware
<number>

## Slide 49
T2B06 - What happens when the deviation of an FM transmitter is increased?
A. Its signal occupies more bandwidth
B. Its output power increases
C. Its output power and bandwidth increases
D. Asymmetric modulation occurs
<number>
Operating Procedures

## Slide 50
T2B06 - What happens when the deviation of an FM transmitter is increased?
A. Its signal occupies more bandwidth
B. Its output power increases
C. Its output power and bandwidth increases
D. Asymmetric modulation occurs
<number>
Operating Procedures

## Slide 51
T2B07 - What could cause your FM signal to interfere with stations on nearby frequencies?
A. Microphone gain too high, causing over-deviation
B. SWR too high
C. Incorrect CTCSS Tone
D. All of these choices are correct
<number>
Operating Procedures

## Slide 52
T2B07 - What could cause your FM signal to interfere with stations on nearby frequencies?
A. Microphone gain too high, causing over-deviation
B. SWR too high
C. Incorrect CTCSS Tone
D. All of these choices are correct
<number>
Operating Procedures

## Slide 53
T2B08 - Which of the following applies when two stations transmitting on the same frequency interfere with each other?
A. Common courtesy should prevail, but no one has absolute right to an amateur frequency
B. Whoever has the strongest signal has priority on the frequency
C. Whoever has been on the frequency the longest has priority on the frequency
D. The station which has the weakest signal has priority on the frequency
<number>
Operating Procedures

## Slide 54
T2B08 - Which of the following applies when two stations transmitting on the same frequency interfere with each other?
A. Common courtesy should prevail, but no one has absolute right to an amateur frequency
B. Whoever has the strongest signal has priority on the frequency
C. Whoever has been on the frequency the longest has priority on the frequency
D. The station which has the weakest signal has priority on the frequency
<number>
Operating Procedures

## Slide 55
T2B09 - Which of the following methods is encouraged by the FCC when identifying your station when using phone?
A. Use of a phonetic alphabet
B. Send your call sign in CW as well as voice
C. Repeat your call sign three times
D. Increase your signal to full power when identifying
<number>
Operating Procedures

## Slide 56
T2B09 - Which of the following methods is encouraged by the FCC when identifying your station when using phone?
A. Use of a phonetic alphabet
B. Send your call sign in CW as well as voice
C. Repeat your call sign three times
D. Increase your signal to full power when identifying
<number>
Operating Procedures

## Slide 57
CW Prosigns
DX – Distant station (outside the country)
CQ – Calling any station
AR – "+" over, end of message
K – go, invite any station to transmit
KN – "(" go only, invite a specific station to transmit
BK – invite receiving station to transmit
AS – please stand by
SK – end of contact (sent before call)
CL – going off the air (clear)
<number>
Operating Procedures

## Slide 58
Q Signals
<number>
Operating Procedures
QRM | Man-made noise | QRN | Atmospheric noise
QSY | Change frequency | QTH | Current/home location
QSB | Atmospheric fading | QSL | Confirmation of report
QSK | Full break-in keying | QRV | Ready to receive
QRS | Send more slowly | QRQ | Send more quickly

## Slide 59
T2B10 - Which Q signal indicates that you are receiving interference from other stations?
A. QRM
B. QRN
C. QTH
D. QSB
<number>
Operating Procedures

## Slide 60
T2B10 - Which Q signal indicates that you are receiving interference from other stations?
A. QRM
B. QRN
C. QTH
D. QSB
<number>
Operating Procedures

## Slide 61
T2B11 - Which Q signal indicates that you are changing frequency?
A. QRU
B. QSY
C. QSL
D. QRZ
<number>
Operating Procedures

## Slide 62
T2B11 - Which Q signal indicates that you are changing frequency?
A. QRU
B. QSY
C. QSL
D. QRZ
<number>
Operating Procedures

## Slide 63
G2B06 What is a practical way to avoid harmful interference when selecting a frequency to call CQ on CW or phone?
  A. Send "QRL?" on CW, followed by your call sign; or, if using phone, ask if the frequency is in use, followed by your call sign
  B. Listen for 2 minutes before calling CQ
  C. Send the letter "V" in Morse code several times and listen for a response
  D. Send “QSY” on CW or if using phone, announce “the frequency is in use”, then send your call and listen for a response
<number>
Operating Procedures

## Slide 64
G2B06 What is a practical way to avoid harmful interference when selecting a frequency to call CQ on CW or phone?
  A. Send "QRL?" on CW, followed by your call sign; or, if using phone, ask if the frequency is in use, followed by your call sign
  B. Listen for 2 minutes before calling CQ
  C. Send the letter "V" in Morse code several times and listen for a response
  D. Send “QSY” on CW or if using phone, announce “the frequency is in use”, then send your call and listen for a response
<number>
Operating Procedures

## Slide 65
T2B12 - Under what circumstances should you consider communicating via simplex rather than a repeater?
A. When the stations can communicate directly without using a repeater
B. Only when you have an endorsement for simplex operation on your license
C. Only when third party traffic is not being passed
D. Only if you have simplex modulation capability
<number>
Operating Procedures

## Slide 66
T2B12 - Under what circumstances should you consider communicating via simplex rather than a repeater?
A. When the stations can communicate directly without using a repeater
B. Only when you have an endorsement for simplex operation on your license
C. Only when third party traffic is not being passed
D. Only if you have simplex modulation capability
<number>
Operating Procedures

## Slide 67
T2B13 - Which of the following is true of the use of SSB phone in amateur bands above 50 MHz?
A. It is permitted only by holders of a General Class or higher license
B. It is permitted only on repeaters
C. It is permitted in at least some portion of all the amateur bands above 50 MHz
D. It is permitted only on when power is limited to no more than 100 watts
<number>
Operating Procedures

## Slide 68
T2B13 - Which of the following is true of the use of SSB phone in amateur bands above 50 MHz?
A. It is permitted only by holders of a General Class or higher license
B. It is permitted only on repeaters
C. It is permitted in at least some portion of all the amateur bands above 50 MHz
D. It is permitted only on when power is limited to no more than 100 watts
<number>
Operating Procedures

## Slide 69
T2C – Public service:
emergency and non-emergency operations; applicability of FCC rules; RACES and ARES; net and traffic procedures; emergency restrictions
<number>
Operating Procedures

## Slide 70
T2C01 - When do the FCC rules NOT apply to the operation of an amateur station?
A. When operating a RACES station
B. When operating under special FEMA rules
C. When operating under special ARES rules
D. Never, FCC rules always apply
<number>
Operating Procedures

## Slide 71
T2C01 - When do the FCC rules NOT apply to the operation of an amateur station?
A. When operating a RACES station
B. When operating under special FEMA rules
C. When operating under special ARES rules
D. Never, FCC rules always apply
<number>
Operating Procedures

## Slide 72
T2C02 - What is one way to recharge a 12-volt lead-acid station battery if the commercial power is out?
A. Cool the battery in ice for several hours
B. Add acid to the battery
C. Connect the battery in parallel with a vehicle’s battery and run the engine
D. All of these choices are correct
<number>
Operating Procedures

## Slide 73
T2C02 - What is one way to recharge a 12-volt lead-acid station battery if the commercial power is out?
A. Cool the battery in ice for several hours
B. Add acid to the battery
C. Connect the battery in parallel with a vehicle’s battery and run the engine
D. All of these choices are correct
<number>
Operating Procedures

## Slide 74
T2C03 - What should be done to insure that voice message traffic containing proper names and unusual words are copied correctly by the receiving station?
A. The entire message should be repeated at least four times
B. Such messages must be limited to no more than 10 words
C. Such words and terms should be spelled out using a standard phonetic alphabet
D. All of these choices are correct
<number>
Operating Procedures

## Slide 75
T2C03 - What should be done to insure that voice message traffic containing proper names and unusual words are copied correctly by the receiving station?
A. The entire message should be repeated at least four times
B. Such messages must be limited to no more than 10 words
C. Such words and terms should be spelled out using a standard phonetic alphabet
D. All of these choices are correct
<number>
Operating Procedures

## Slide 76
RACES / ARES
RACES – Radio Amateur Civil Emergency Service
  Work with local, state and federal government only
  When activated, you work for the government (Restricted)
  When activated, mission participants are covered by government insurance
ARES - Amateur Radio Emergency Service
  Health and welfare
  Work with government and NGO (Red Cross, Salvation Army) and support services
  When activated, you still are a civilian
Operating Procedures
<number>
Note – both groups do good work, and many hams belong to both groups,
also both groups are often combined.

## Slide 77
T2C04 - What do RACES and ARES have in common?
A. They represent the two largest ham clubs in the United States
B. Both organizations broadcast road and weather information
C. Neither may handle emergency traffic supporting public service agencies
D. Both organizations may provide communications during emergencies
<number>
Operating Procedures

## Slide 78
T2C04 - What do RACES and ARES have in common?
A. They represent the two largest ham clubs in the United States
B. Both organizations broadcast road and weather information
C. Neither may handle emergency traffic supporting public service agencies
D. Both organizations may provide communications during emergencies
<number>
Operating Procedures

## Slide 79
T2C05 - Which of the following describes the Radio Amateur Civil Emergency Service (RACES)?
A. A radio service using amateur frequencies for emergency management or civil defense communications
B. A radio service using amateur stations for emergency management or civil defense communications
C. An emergency service using amateur operators certified by a civil defense organization as being enrolled in that organization
D. All of these choices are correct
<number>
Operating Procedures

## Slide 80
T2C05 - Which of the following describes the Radio Amateur Civil Emergency Service (RACES)?
A. A radio service using amateur frequencies for emergency management or civil defense communications
B. A radio service using amateur stations for emergency management or civil defense communications
C. An emergency service using amateur operators certified by a civil defense organization as being enrolled in that organization
D. All of these choices are correct
<number>
Operating Procedures

## Slide 81
G2B10 When may the FCC restrict normal frequency operations of amateur stations participating in RACES?
  A. When they declare a temporary state of communication emergency
  B. When they seize your equipment for use in disaster communications
  C. Only when all amateur stations are instructed to stop transmitting
  D. When the President’s War Emergency Powers have been invoked
<number>
Operating Procedures

## Slide 82
G2B10 When may the FCC restrict normal frequency operations of amateur stations participating in RACES?
  A. When they declare a temporary state of communication emergency
  B. When they seize your equipment for use in disaster communications
  C. Only when all amateur stations are instructed to stop transmitting
  D. When the President’s War Emergency Powers have been invoked
<number>
Operating Procedures

## Slide 83
T2C06 - Which of the following is an accepted practice to get the immediate attention of a net control station when reporting an emergency?
A. Repeat the words SOS three times followed by the call sign of the reporting station
B. Press the push-to-talk button three times
C. Begin your transmission by saying "Priority" or "Emergency" followed by your call sign
D. Play a pre-recorded emergency alert tone followed by your call sign
<number>
Operating Procedures

## Slide 84
T2C06 - Which of the following is an accepted practice to get the immediate attention of a net control station when reporting an emergency?
A. Repeat the words SOS three times followed by the call sign of the reporting station
B. Press the push-to-talk button three times
C. Begin your transmission by saying "Priority" or "Emergency" followed by your call sign
D. Play a pre-recorded emergency alert tone followed by your call sign
<number>
Operating Procedures

## Slide 85
T2C07 - Which of the following is an accepted practice for an amateur operator who has checked into an emergency traffic net?
A. Provided that the frequency is quiet, announce the station call sign and location every 5 minutes
B. Move 5 kHz away from the net's frequency and use high power to ask other hams to keep clear of the net frequency
C. Remain on frequency without transmitting until asked to do so by the net control station
D. All of the choices are correct
<number>
Operating Procedures

## Slide 86
T2C07 - Which of the following is an accepted practice for an amateur operator who has checked into an emergency traffic net?
A. Provided that the frequency is quiet, announce the station call sign and location every 5 minutes
B. Move 5 kHz away from the net's frequency and use high power to ask other hams to keep clear of the net frequency
C. Remain on frequency without transmitting until asked to do so by the net control station
D. All of the choices are correct
<number>
Operating Procedures

## Slide 87
T2C08 - Which of the following is a characteristic of good emergency traffic handling?
A. Passing messages exactly as received
B. Making decisions as to whether or not messages should be relayed or delivered
C. Communicating messages to the news media for broadcast outside the disaster area
D. All of these choices are correct
<number>
Operating Procedures

## Slide 88
T2C08 - Which of the following is a characteristic of good emergency traffic handling?
A. Passing messages exactly as received
B. Making decisions as to whether or not messages should be relayed or delivered
C. Communicating messages to the news media for broadcast outside the disaster area
D. All of these choices are correct
<number>
Operating Procedures

## Slide 89
T2C09 - Are amateur station control operators ever permitted to operate outside the frequency privileges of their license class?
A. No
B. Yes, but only when part of a FEMA emergency plan
C. Yes, but only when part of a RACES emergency plan
D. Yes, but only if necessary in situations involving the immediate safety of human life or protection of property
<number>
Operating Procedures

## Slide 90
T2C09 - Are amateur station control operators ever permitted to operate outside the frequency privileges of their license class?
A. No
B. Yes, but only when part of a FEMA emergency plan
C. Yes, but only when part of a RACES emergency plan
D. Yes, but only if necessary in situations involving the immediate safety of human life or protection of property
<number>
Operating Procedures

## Slide 91
T2C10 - What is the preamble in a formal traffic message?
A. The first paragraph of the message text
B. The message number
C. The priority handling indicator for the message
D. The information needed to track the message as it passes through the amateur radio traffic handling system
<number>
Operating Procedures

## Slide 92
<number>
Operating Procedures
Formal Message Traffic
Preamble
Check is the word count in the message a provides basic error-checking

## Slide 93
T2C10 What is the preamble in a formal traffic message?
A. The first paragraph of the message text
B. The message number
C. The priority handling indicator for the message
D. The information needed to track the message as it passes through the amateur radio traffic handling system
<number>
Operating Procedures

## Slide 94
T2C11 - What is meant by the term “check” in reference to a formal traffic message?
A. The check is a count of the number of words or word equivalents in the text portion of the message
B. The check is the value of a money order attached to the message
C. The check is a list of stations that have relayed the message
D. The check is a box on the message form that tells you the message was received
<number>
Operating Procedures

## Slide 95
T2C11 - What is meant by the term “check” in reference to a formal traffic message?
A. The check is a count of the number of words or word equivalents in the text portion of the message
B. The check is the value of a money order attached to the message
C. The check is a list of stations that have relayed the message
D. The check is a box on the message form that tells you the message was received
<number>
Operating Procedures

## Slide 96
T2C12 - What is the Amateur Radio Emergency Service (ARES)?
A. Licensed amateurs who have voluntarily registered their qualifications and equipment for communications duty in the public service
B. Licensed amateurs who are members of the military and who voluntarily agreed to provide message handling services in the case of an emergency
C. A training program that provides licensing courses for those interested in obtaining an amateur license to use during emergencies
D. A training program that certifies amateur operators for membership in the Radio Amateur Civil Emergency Service
<number>
Operating Procedures

## Slide 97
T2C12 - What is the Amateur Radio Emergency Service (ARES)?
A. Licensed amateurs who have voluntarily registered their qualifications and equipment for communications duty in the public service
B. Licensed amateurs who are members of the military and who voluntarily agreed to provide message handling services in the case of an emergency
C. A training program that provides licensing courses for those interested in obtaining an amateur license to use during emergencies
D. A training program that certifies amateur operators for membership in the Radio Amateur Civil Emergency Service
<number>
Operating Procedures

## Slide 98
G2D01 What is the Amateur Auxiliary to the FCC?
  A. Amateur volunteers who are formally enlisted to monitor the airwaves for rules violations
  B. Amateur volunteers who conduct amateur licensing examinations
  C. Amateur volunteers who conduct frequency coordination for amateur VHF repeaters
  D. Amateur volunteers who use their station equipment to help civil defense organizations in times of emergency
<number>
Operating Procedures

## Slide 99
G2D01 What is the Amateur Auxiliary to the FCC?
  A. Amateur volunteers who are formally enlisted to monitor the airwaves for rules violations
  B. Amateur volunteers who conduct amateur licensing examinations
  C. Amateur volunteers who conduct frequency coordination for amateur VHF repeaters
  D. Amateur volunteers who use their station equipment to help civil defense organizations in times of emergency
<number>
Operating Procedures

## Slide 100
G2D02 Which of the following are objectives of the Amateur Auxiliary?
  A. To conduct efficient and orderly amateur licensing examinations
  B. To encourage amateur self regulation and compliance with the rules
  C. To coordinate repeaters for efficient and orderly spectrum usage
  D. To provide emergency and public safety communications
<number>
Operating Procedures

## Slide 101
G2D02 Which of the following are objectives of the Amateur Auxiliary?
  A. To conduct efficient and orderly amateur licensing examinations
  B. To encourage amateur self regulation and compliance with the rules
  C. To coordinate repeaters for efficient and orderly spectrum usage
  D. To provide emergency and public safety communications
<number>
Operating Procedures

## Slide 102
Azimuthal Map
The Azimuthal Projection provides accurate antenna bearings to other locations on the globe via “great circle” routes
Short path and long path bearings are easily found
<number>
Operating Procedures

## Slide 103
G2D04 Which of the following describes an azimuthal projection map?
  A. A world map that shows accurate land masses
  B. A world map projection centered on a particular location
  C. A world map that shows the angle at which an amateur satellite crosses the equator
  D. A world map that shows the number of degrees longitude that an amateur satellite appears to move westward at the equator with each orbit
<number>
Operating Procedures

## Slide 104
G2D04 Which of the following describes an azimuthal projection map?
  A. A world map that shows accurate land masses
  B. A world map projection centered on a particular location
  C. A world map that shows the angle at which an amateur satellite crosses the equator
  D. A world map that shows the number of degrees longitude that an amateur satellite appears to move westward at the equator with each orbit
<number>
Operating Procedures

## Slide 105
G2E11 What does the abbreviation "MFSK" stand for?
  A. Manual Frequency Shift Keying
  B. Multi (or Multiple) Frequency Shift Keying
  C. Manual Frequency Sideband Keying
  D. Multi (or Multiple) Frequency Sideband Keying
<number>
Operating Procedures

## Slide 106
G2E11 What does the abbreviation "MFSK" stand for?
  A. Manual Frequency Shift Keying
  B. Multi (or Multiple) Frequency Shift Keying
  C. Manual Frequency Sideband Keying
  D. Multi (or Multiple) Frequency Sideband Keying
<number>
Operating Procedures

## Slide 107
G2E12 How does the receiving station respond to an ARQ data mode packet containing errors?
  A. Terminates the contact
  B. Requests the packet be retransmitted
  C. Sends the packet back to the transmitting station
  D. Requests a change in transmitting protocol
<number>
Operating Procedures

## Slide 108
G2E12 How does the receiving station respond to an ARQ data mode packet containing errors?
  A. Terminates the contact
  B. Requests the packet be retransmitted
  C. Sends the packet back to the transmitting station
  D. Requests a change in transmitting protocol
<number>
Operating Procedures

## Slide 109
End of SUBELEMENT T2 Operating Procedures
<number>
Operating Procedures
Notes: <number>