## Slide 1: SUBELEMENT T4
Amateur radio practices and station set up
[2 Exam Questions - 2 Groups]
Amateur Radio Practices 2014
Notes: Subelement T4 Amateur Radio Practices. Technician Training Slides for 2014 Question Pool Good through June 30, 2018 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM, Howard Schultz, W7HS.
<number>

## Slide 2
T4A – Station setup: connecting microphones; reducing unwanted emissions; power source; connecting a computer; RF grounding; connecting digital equipment; connecting an SWR meter
T4B - Operating controls: tuning; use of filters; squelch function; AGC; repeater offset; memory channels
Amateur Radio Practices 2014
<number>

## Slide 3: Communications Headset
<number>
Radio Practices 2014
HiFi headphones are designed to cover the entire range of human hearing (20-20,000Hz) equally well. Communications headphones are only designed to reproduce the 300-3000Hz voice frequencies which helps reduce non-voice noise that might come out of the receiver. This model includes a boom microphone that minimizes background noise and insures consistent voice quality.
Push-to-Talk (PTT) is via a foot switch on the floor to leave the operators hands free.
Notes: <number>
Good communications headphones are not the same as HiFi headphones. HiFi headphones are designed to cover the entire range of human hearing (20-20,000Hz) equally well. Communications headphones are only designed to reproduce the 300-3000Hz voice frequencies which helps reduce non-voice noise that might come out of the receiver. This model includes a boom microphone that minimizes background noise and insures consistent voice quality. Push-to-Talk (PTT) is via a foot switch on the floor to leave the operators hands free.

## Slide 4: Power Supply
<number>
Radio Practices 2014
This Daiwa 12v regulated power supply has a meter that can display voltage and current
Notes: <number>
If your power supply has volt and ammeters, it can be used to calculate power consumption of your rig at various power levels. This will help determine proper fuse sizing, appropriate wire gauge, anticipated battery life, etc.

## Slide 5: Low Pass, High Pass Filters
<number>
Radio Practices 2014
Low Pass
Frequency
Stop Band
Pass Band
40 dB
0 dB
fc
-3 dB
High Pass
Frequency
Pass Band
Stop Band
0 dB
40 dB
-3 dB
fc

## Slide 6: Band Pass Filter
<number>
Radio Practices 2014
Stop Band
High Frequency
Low Frequency
40 dB
0 dB
fc
fc
-3 dB
Stop Band
Pass Band

## Slide 7: Notch (Band Stop) Filter
<number>
Radio Practices 2014
Stop Band
High Frequency
Low Frequency
40 dB
0 dB
fc
fc
-3 dB
Pass Band
Pass Band
There are notch filters built to notch out the powerful pager transmitters located just above the 2m band.
Very effective notch filters can be made with a 1/2 wavelength piece of coax shorted on one end connected to a coaxial “T” connector on the other. These are often called “stubs”.
Repeaters use cavity notch filters that have very sharp skirts to keep the transmitter from interfering with the receiver, since they’re both active at the same time on very close frequencies.

## Slide 8: T4A01 - Which of the following is true concerning the microphone connectors on amateur transceivers?
A. All transceivers use the same microphone connector type
B. Some connectors include push-to-talk and voltages for powering the microphone
C. All transceivers using the same connector type are wired identically
D. Un-keyed connectors allow any microphone to be connected
Amateur Radio Practices 2014
<number>

## Slide 9: T4A01 - Which of the following is true concerning the microphone connectors on amateur transceivers?
A. All transceivers use the same microphone connector type
B. Some connectors include push-to-talk and voltages for powering the microphone
C. All transceivers using the same connector type are wired identically
D. Un-keyed connectors allow any microphone to be connected
Amateur Radio Practices 2014
<number>

## Slide 10: T4A02 - How might a computer be used as part of an amateur radio station?
A. For logging contacts and contact information
B. For sending and/or receiving CW
C. For generating and decoding digital signals
D. All of these choices are correct
Amateur Radio Practices 2014
<number>

## Slide 11: T4A02 - How might a computer be used as part of an amateur radio station?
A. For logging contacts and contact information
B. For sending and/or receiving CW
C. For generating and decoding digital signals
D. All of these choices are correct
Amateur Radio Practices 2014
<number>

## Slide 12: T4A03 - Which is a good reason to use a regulated power supply for communications equipment?
A. It prevents voltage fluctuations from reaching sensitive circuits
B. A regulated power supply has FCC approval
C. A fuse or circuit breaker regulates the power
D. Power consumption is independent of load
Amateur Radio Practices 2014
<number>

## Slide 13: T4A03 - Which is a good reason to use a regulated power supply for communications equipment?
A. It prevents voltage fluctuations from reaching sensitive circuits
B. A regulated power supply has FCC approval
C. A fuse or circuit breaker regulates the power
D. Power consumption is independent of load
Amateur Radio Practices 2014
<number>

## Slide 14: T4A04 - Where must a filter be installed to reduce harmonic emissions from your station?
A. Between the transmitter and the antenna
B. Between the receiver and the transmitter
C. At the station power supply
D. At the microphone
Amateur Radio Practices 2014
<number>

## Slide 15: T4A04 - Where must a filter be installed to reduce harmonic emissions from your station?
A. Between the transmitter and the antenna
B. Between the receiver and the transmitter
C. At the station power supply
D. At the microphone
Amateur Radio Practices 2014
<number>

## Slide 16: G4A01 What is the purpose of the "notch filter" found on many HF transceivers?
  A. To restrict the transmitter voice bandwidth
  B. To reduce interference from carriers in the receiver passband
  C. To eliminate receiver interference from impulse noise sources
  D. To enhance the reception of a specific frequency on a crowded band
Amateur Radio Practices 2014
<number>

## Slide 17: G4A01 What is the purpose of the "notch filter" found on many HF transceivers?
  A. To restrict the transmitter voice bandwidth
  B. To reduce interference from carriers in the receiver passband
  C. To eliminate receiver interference from impulse noise sources
  D. To enhance the reception of a specific frequency on a crowded band
Amateur Radio Practices 2014
<number>

## Slide 18: T4A05 - Where should an in-line SWR meter be connected to monitor the standing wave ratio of the station antenna system?
A. In series with the feed line, between the transmitter and antenna
B. In series with the station's ground
C. In parallel with the push-to-talk line and the antenna
D. In series with the power supply cable, as close as possible to the radio
Amateur Radio Practices 2014
<number>

## Slide 19: T4A05 - Where should an in-line SWR meter be connected to monitor the standing wave ratio of the station antenna system?
A. In series with the feed line, between the transmitter and antenna
B. In series with the station's ground
C. In parallel with the push-to-talk line and the antenna
D. In series with the power supply cable, as close as possible to the radio
Amateur Radio Practices 2014
<number>

## Slide 20: T4A06 - Which of the following would be connected between a transceiver and computer in a packet radio station?
A. Transmatch
B. Mixer
C. Terminal node controller
D. Antenna
Amateur Radio Practices 2014
<number>

## Slide 21: T4A06 - Which of the following would be connected between a transceiver and computer in a packet radio station?
A. Transmatch
B. Mixer
C. Terminal node controller
D. Antenna
Amateur Radio Practices 2014
<number>

## Slide 22: T4A07 - How is a computer’s sound card used when conducting digital communications using a computer?
A. The sound card communicates between the computer CPU and the video display
B. The sound card records the audio frequency for video display
C. The sound card provides audio to the microphone input and converts received audio to digital form
D. All of these choices are correct
Amateur Radio Practices 2014
<number>

## Slide 23: T4A07 - How is a computer’s sound card used when conducting digital communications using a computer?
A. The sound card communicates between the computer CPU and the video display
B. The sound card records the audio frequency for video display
C. The sound card provides audio to the microphone input and converts received audio to digital form
D. All of these choices are correct
Amateur Radio Practices 2014
<number>

## Slide 24: T4A08 - Which type of conductor is best to use for RF grounding?
A. Round stranded wire
B. Round copper-clad steel wire
C. Twisted-pair cable
D. Flat strap
Amateur Radio Practices 2014
<number>

## Slide 25: T4A08 - Which type of conductor is best to use for RF grounding?
A. Round stranded wire
B. Round copper-clad steel wire
C. Twisted-pair cable
D. Flat strap
Amateur Radio Practices 2014
<number>

## Slide 26: T4A09 - Which of the following could you use to cure distorted audio caused by RF current flowing on the shield of a microphone cable?
A. Band-pass filter
B. Low-pass filter
C. Preamplifier
D. Ferrite choke
Amateur Radio Practices 2014
<number>

## Slide 27: T4A09 - Which of the following could you use to cure distorted audio caused by RF current flowing on the shield of a microphone cable?
A. Band-pass filter
B. Low-pass filter
C. Preamplifier
D. Ferrite choke
Amateur Radio Practices 2014
<number>

## Slide 28: T4A10 - What is the source of a high-pitched whine that varies with engine speed in a mobile transceiver’s receive audio?
A. The ignition system
B. The alternator
C. The electric fuel pump
D. Anti-lock braking system controllers
Amateur Radio Practices 2014
<number>

## Slide 29: T4A10 - What is the source of a high-pitched whine that varies with engine speed in a mobile transceiver’s receive audio?
A. The ignition system
B. The alternator
C. The electric fuel pump
D. Anti-lock braking system controllers
Amateur Radio Practices 2014
<number>

## Slide 30: T4A11 - Where should the negative return connection of a mobile transceiver's power cable be connected?
A. At the battery or engine block ground strap
B. At the antenna mount
C. To any metal part of the vehicle
D. Through the transceiver’s mounting bracket
Amateur Radio Practices 2014
<number>

## Slide 31: T4A11 - Where should the negative return connection of a mobile transceiver's power cable be connected?
A. At the battery or engine block ground strap
B. At the antenna mount
C. To any metal part of the vehicle
D. Through the transceiver’s mounting bracket
Amateur Radio Practices 2014
<number>

## Slide 32: T4A12 - What could be happening if another operator reports a variable high-pitched whine on the audio from your mobile transmitter?
A. Your microphone is picking up noise from an open window
B. You have the volume on your receiver set too high
C. You need to adjust your squelch control
D. Noise on the vehicle’s electrical system is being transmitted along with your speech audio
Amateur Radio Practices 2014
<number>

## Slide 33: T4A12 - What could be happening if another operator reports a variable high-pitched whine on the audio from your mobile transmitter?
A. Your microphone is picking up noise from an open window
B. You have the volume on your receiver set too high
C. You need to adjust your squelch control
D. Noise on the vehicle’s electrical system is being transmitted along with your speech audio
Amateur Radio Practices 2014
<number>

## Slide 34: T4B - Operating controls
Tuning; use of filters; squelch function; AGC; repeater offset; memory channels
Amateur Radio Practices 2014
<number>

## Slide 35: Icom IC-7000 Multimode Transceiver
<number>
Radio Practices 2014
Keypad for band changes and frequency entry
Volume/Squelch Control
VFO or Tuning Knob
Noise Blanker
Up/Down Buttons
RIT
Tune Step (TS)

## Slide 36: T4B01 - What may happen if a transmitter is operated with the microphone gain set too high?
A. The output power might be too high
B. The output signal might become distorted
C. The frequency might vary
D. The SWR might increase
Amateur Radio Practices 2014
<number>

## Slide 37: T4B01 - What may happen if a transmitter is operated with the microphone gain set too high?
A. The output power might be too high
B. The output signal might become distorted
C. The frequency might vary
D. The SWR might increase
Amateur Radio Practices 2014
<number>

## Slide 38: T4B02 - Which of the following can be used to enter the operating frequency on a modern transceiver?
A. The keypad or VFO knob
B. The CTCSS or DTMF encoder
C. The Automatic Frequency Control
D. All of these choices are correct
Amateur Radio Practices 2014
<number>

## Slide 39: T4B02 - Which of the following can be used to enter the operating frequency on a modern transceiver?
A. The keypad or VFO knob
B. The CTCSS or DTMF encoder
C. The Automatic Frequency Control
D. All of these choices are correct
Amateur Radio Practices 2014
<number>

## Slide 40: T4B03 - What is the purpose of the squelch control on a transceiver?
A. To set the highest level of volume desired
B. To set the transmitter power level
C. To adjust the automatic gain control
D. To mute receiver output noise when no signal is being received
Amateur Radio Practices 2014
<number>

## Slide 41: T4B03 - What is the purpose of the squelch control on a transceiver?
A. To set the highest level of volume desired
B. To set the transmitter power level
C. To adjust the automatic gain control
D. To mute receiver output noise when no signal is being received
Amateur Radio Practices 2014
<number>

## Slide 42: T4B04 - What is a way to enable quick access to a favorite frequency on your transceiver?
A. Enable the CTCSS tones
B. Store the frequency in a memory channel
C. Disable the CTCSS tones
D. Use the scan mode to select the desired frequency
Amateur Radio Practices 2014
<number>

## Slide 43: T4B04 - What is a way to enable quick access to a favorite frequency on your transceiver?
A. Enable the CTCSS tones
B. Store the frequency in a memory channel
C. Disable the CTCSS tones
D. Use the scan mode to select the desired frequency
Amateur Radio Practices 2014
<number>

## Slide 44: T4B05 - Which of the following would reduce ignition interference to a receiver?
A. Change frequency slightly
B. Decrease the squelch setting
C. Turn on the noise blanker
D. Use the RIT control
Amateur Radio Practices 2014
<number>

## Slide 45: T4B05 - Which of the following would reduce ignition interference to a receiver?
A. Change frequency slightly
B. Decrease the squelch setting
C. Turn on the noise blanker
D. Use the RIT control
Amateur Radio Practices 2014
<number>

## Slide 46: T4B07 - What does the term “RIT” mean?
A. Receiver Input Tone
B. Receiver Incremental Tuning
C. Rectifier Inverter Test
D. Remote Input Transmitter
Amateur Radio Practices 2014
<number>

## Slide 47: T4B07 - What does the term “RIT” mean?
A. Receiver Input Tone
B. Receiver Incremental Tuning
C. Rectifier Inverter Test
D. Remote Input Transmitter
Amateur Radio Practices 2014
<number>

## Slide 48: T4B06 - Which of the following controls could be used if the voice pitch of a single-sideband signal seems too high or low?
A. The AGC or limiter
B. The bandwidth selection
C. The tone squelch
D. The receiver RIT or clarifier
Amateur Radio Practices 2014
<number>

## Slide 49: T4B06 - Which of the following controls could be used if the voice pitch of a single-sideband signal seems too high or low?
A. The AGC or limiter
B. The bandwidth selection
C. The tone squelch
D. The receiver RIT or clarifier
Amateur Radio Practices 2014
<number>

## Slide 50: T4B08 - What is the advantage of having multiple receive bandwidth choices on a multimode transceiver?
A. Permits monitoring several modes at once
B. Permits noise or interference reduction by selecting a bandwidth matching the mode
C. Increases the number of frequencies that can be stored in memory
D. Increases the amount of offset between receive and transmit frequencies
Amateur Radio Practices 2014
<number>

## Slide 51: T4B08 - What is the advantage of having multiple receive bandwidth choices on a multimode transceiver?
A. Permits monitoring several modes at once
B. Permits noise or interference reduction by selecting a bandwidth matching the mode
C. Increases the number of frequencies that can be stored in memory
D. Increases the amount of offset between receive and transmit frequencies
Amateur Radio Practices 2014
<number>

## Slide 52: Sample Emission Modes
Mode | Type | Bandwidth | Content
CW | Telegraphy | 10 Hz | Text Data
SSB | Telephony | 2800 Hz | Voice
AM | Telephony | 6 kHz | Voice
FM | Telephony | 5-15 kHz | Voice
SSTV / Fax | Image | 2800 Hz | Image
ATV | Image | 6 MHz | Image
PSK31 | Data | 31 Hz | Text Data
RTTY | Data | 250 Hz | Text Data
Pactor (I, II, III) | Data | 500-2800 Hz | Binary Data
AX.25 Packet | Data | 10-20 kHz | Binary Data
Radio Practices 2014
<number>

## Slide 53: T4B09 - Which of the following is an appropriate receive filter bandwidth to select in order to minimize noise and interference for SSB reception?
A. 500 Hz
B. 1000 Hz
C. 2400 Hz
D. 5000 Hz
Amateur Radio Practices 2014
<number>

## Slide 54: T4B09 - Which of the following is an appropriate receive filter bandwidth to select in order to minimize noise and interference for SSB reception?
A. 500 Hz
B. 1000 Hz
C. 2400 Hz
D. 5000 Hz
Amateur Radio Practices 2014
<number>

## Slide 55: T4B10 - Which of the following is an appropriate receive filter bandwidth to select in order to minimize noise and interference for CW reception?
A. 500 Hz
B. 1000 Hz
C. 2400 Hz
D. 5000 Hz
Amateur Radio Practices 2014
<number>

## Slide 56: T4B10 - Which of the following is an appropriate receive filter bandwidth to select in order to minimize noise and interference for CW reception?
A. 500 Hz
B. 1000 Hz
C. 2400 Hz
D. 5000 Hz
Amateur Radio Practices 2014
<number>

## Slide 57: T4B11 - Which of the following describes the common meaning of the term "repeater offset"?
A. The distance between the repeater’s transmit and receive antennas
B. The time delay before the repeater timer resets
C. The difference between the repeater’s transmit and receive frequencies
D. Matching the antenna impedance to the feed line impedance
Amateur Radio Practices 2014
<number>

## Slide 58: T4B11 - Which of the following describes the common meaning of the term "repeater offset"?
A. The distance between the repeater’s transmit and receive antennas
B. The time delay before the repeater timer resets
C. The difference between the repeater’s transmit and receive frequencies
D. Matching the antenna impedance to the feed line impedance
Amateur Radio Practices 2014
<number>

## Slide 59: Repeater Operation
<number>
Radio Practices 2014
70+ miles
Repeater
Output Freq
(You Listen)
147.000 MHz
Repeater
Input Freq
(You talk on)
147.600 MHz
Offset
+ 600 kHz

## Slide 60
<number>
Radio Practices 2014
Offset
Freq.
Tone Enabled
103.5
Listen on 146.980 (- .600) Talk on 146.380

## Slide 61: Repeater Input/Output Offsets
Band Offset
<number>
Radio Practices 2014
6 meters 1 MHz
2 meters 600 kHz
1.25 meters 1.6 MHz
70 cm 5 MHz
33 cm 12 MHz
23 cm 20 MHz
Notes: <number>
This is the national band plan. Note that Western Washington uses a different split on 6 meters.

## Slide 62: T4B12 - What is the function of automatic gain control or AGC?
A. To keep received audio relatively constant
B. To protect an antenna from lightning
C. To eliminate RF on the station cabling
D. An asymmetric goniometer control used for antenna matching
Amateur Radio Practices 2014
<number>

## Slide 63: T4B12 - What is the function of automatic gain control or AGC?
A. To keep received audio relatively constant
B. To protect an antenna from lightning
C. To eliminate RF on the station cabling
D. An asymmetric goniometer control used for antenna matching
Amateur Radio Practices 2014
<number>

## Slide 64: MEASURING INSTRUMENTS
Oscillascope - a slice of time
Field Strength Meter - frequencies
Multi-Meter - volts, ohms, amps
Bi-Directional Watt Meter - watts, SWR
Antenna Analizer - SWR, feedlines
Speech Processor - boost average audio

## Slide 65: Oscilloscope
<number>
Amateur Radio Practices
By connecting the RF output of a transmitter (through appropriate connections) to the vertical input of the scope, the quality of a transmitted signal can be seen on the display.
An Oscilloscope has the ability to display complex waveforms. Signals are fed into the scope and the internal horizontal and vertical amplifiers generate the display of waveform amplitude vertically and time horizontally.
Notes: <number>
<number>
This is a current model Tektronix oscilloscope. It has four signal inputs along the lower right edge and can display the waveforms from those inputs. There are three main sections to the right of the screen; vertical, horizontal and trigger. The horizontal and vertical controls adjust how the waveform appears on the screen by adjusting the horizontal and vertical amplifiers. The trigger controls allow the oscilloscope to synchronize to external events.
Newer oscilloscopes are digital and can record data to the floppy seen here on the left or send to other external devices. By connecting the RF output of a transmitter (through appropriate connections) to the vertical input of the scope, the quality of a transmitted signal can be seen on the display.

## Slide 66: Audio Distortion
Amateur Radio Practices
<number>
Two tone audio tests are used on an oscilloscope to test proper linearity. The pure tones fed in will give you a stable picture on the scope if the amplifier is properly adjusted. The lower image shows a signal with some noise that it also overdriven (overmodulated) and is clipping or flattopping.
Any two audio tones may be used, but they must be within the transmitter audio passband, and should not be harmonically related.
Notes: <number>
<number>
Two tone audio tests are used on an oscilloscope to test proper linearity. The pure tones fed in will give you a stable picture on the scope if the amplifier is properly adjusted. The lower image shows a signal with some noise that it also overdriven (overmodulated) and is clipping or flattopping. Any two audio tones may be used, but they must be within the transmitter audio passband, and should not be harmonically related.
Speech Processors are used to keep input audio close to a perfect level for 100% modulation. If they are not adjusted properly, they can cause the distortion seen here. Overdriving causes very distorted audio and no additional power output.

## Slide 67: Field Strength Meter
Amateur Radio Practices
<number>
Here are two digital Field Strength Meter models. Some SWR meters and frequency counters can also be used as field strength meters.
Field Strength Meters are used to test the density of an RF field when near the transmitter (near field). This can help determine the radiation pattern of an antenna and locate a nearby transmitter.
Notes: <number>
<number>
Here are two digital Field Strength Meter models. Some SWR meters and frequency counters can also be used as field strength meters. Field Strength Meters are used to test the density of an RF field. This allows testing of antenna patterns and ambient RF levels at repeater and home sites to insure safe levels.

## Slide 68: Multimeter
Multimeters generally include voltmeters, ammeters and can measure resistance. They have a high internal impedance in voltage mode to minimize impact on the circuit under test.
<number>
Digital models can be very precise but analog models are often favored for tuning circuits.
Amateur Radio Practices 2014

## Slide 69: Directional Wattmeter
A directional wattmeter can measure both forward (to the load/antenna) and reflected power. This ratio determines the Standing Wave Ratio (SWR). A perfect match will have all forward power and none reflected or a 1:1 SWR. The meter installs between the transmitter and antenna.
<number>
This unit has two needles. One shows forward power, the other reflected. The SWR can be read where they cross (on the red scale).
Amateur Radio Practices 2014
Notes: <number>
This Diawa meter has two meters. One reads forward power and the other reflected power and SWR can be read where the needles cross in the middle.

## Slide 70: Antenna Analyzer
Antenna analyzers can be used to verify antenna impedance (match). The connect directly to the antenna and use a small internal transmitter to read the resulting match.
This does make them sensitive to other transmitters operating in the area.
They can also be used to read the impedance of connectors and coax.
<number>
Amateur Radio Practices 2014

## Slide 71: Station Grounding
Amateur Radio Practices
<number>
A common RF ground reduces shock/RF burn hazard and hum in devices
Notes: <number>
<number>
For a proper RF ground, it’s important to use a heavy gauge copper (not aluminum) braid or foil and keep the run length to a minimum. Standard wire, even heavy gauge, or long runs can cause your ground lead to act as an antenna and resonate. A good ground will reduce RFI to other equipment, minimize the risk of shock and reduce electrical interference. At a minimum a ground rod should be 8 feet long. This can be difficult to achieve in some locations and multiple shorter rods tied together can be used.

## Slide 72: Icom IC-756ProIII IF DSP Receiver
Amateur Radio Practices
<number>
Once the signal has been digitized, Digital Signal Processing (DSP) notch filter, adjustable bandpass filters and noise reduction filters can be applied. The primary advantage of an IF DSP system is that virtually any type of filter can be created and the unwanted signals can be removed without affecting AGC performance. DSP filtering allows virtually any filter shape to be created including a dual peak filter specifically to filter the mark and space tones of an RTTY signal.
Notes: <number>
<number>
This is the 2nd IF (intermediate frequency) stage of the Icom IC-756ProIII receiver. The 455kHz IF frequency is converted to 36kHz and digitized through an analog to digital converter. Once the signal has been digitized, DSP notch filter, adjustable bandpass filters and noise reduction filters can be applied.
The level of the resulting signal is sampled and used to determine the gain of the first IF stage. This level information is fed back through a digital to analog converter to the automatic gain control circuit on the 1st IF stage. Finally the signal is fed through the DSP detector, then a digital to analog converter to convert the signal back to analog audio and sent to the amplifier and speaker.
The primary advantage of an IF DSP system is that virtually any type of filter can be created and the unwanted signals can be removed without affecting AGC performance. Common filters include manual and automatic notch filters, noise reduction filters and adjustable bandpass filters. DSP filtering allows virtually any filter shape to be created including a dual peak filter specifically to filter the mark and space tones of an RTTY signal.
Although many of these filters can be implemented more easily in the AF (audio frequency) stage, any desense caused by large interfering signals will have already impacted the AGC. AF DSP is effective at reducing listener fatigue but cannot actually improve system performance.

## Slide 73: Speech Processor
A speech processor is internal to modern radios and is designed to compress the dynamic range of transmitted audio which increases the average power output. When properly adjusted, this will increase the signal intelligibility. They are often overused to the point of distortion.
Amateur Radio Practices 2014
<number>

## Slide 74: End of SUBELEMENT T4
Amateur radio practices and station set up
Amateur Radio Practices 2014
<number>