## Slide 1: SUBELEMENT T10
Electrical safety: AC and DC power circuits; antenna installation; RF hazards
[3 Exam Questions - 3 Groups]
<number>
Electrical Safety 2014
Notes: Subelement T10 Electrical and RF Safety. Technician Training Slides for 2014 Question Pool Good through June 30, 2018 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM, Howard Schultz, W7HS.
<number>

## Slide 2
T10A – Power circuits and hazards: hazardous voltages; fuses and circuit breakers; grounding; lightning protection; battery safety; electrical code compliance
T10B – Antenna safety: tower safety; erecting an antenna support; overhead power lines; installing an antenna
T10C - RF hazards: radiation exposure; proximity to antennas; recognized safe power levels; exposure to others; radiation types; duty cycle
<number>
Electrical Safety

## Slide 3: T0A01 - Which of the following is a safety hazard of a 12-volt storage battery?
A. Touching both terminals with the hands can cause electrical shock
B. Shorting the terminals can cause burns, fire, or an explosion
C. RF emissions from the battery
D. All of these choices are correct
<number>
Electrical Safety

## Slide 4: T0A01 - Which of the following is a safety hazard of a 12-volt storage battery?
A. Touching both terminals with the hands can cause electrical shock
B. Shorting the terminals can cause burns, fire, or an explosion
C. RF emissions from the battery
D. All of these choices are correct
<number>
Electrical Safety

## Slide 5: T0A02 - How does current flowing through the body cause a health hazard?
A. By heating tissue
B. It disrupts the electrical functions of cells
C. It causes involuntary muscle contractions
D. All of these choices are correct
<number>
Electrical Safety

## Slide 6: T0A02 - How does current flowing through the body cause a health hazard?
A. By heating tissue
B. It disrupts the electrical functions of cells
C. It causes involuntary muscle contractions
D. All of these choices are correct
<number>
Electrical Safety

## Slide 7: T0A03 - What is connected to the green wire in a three-wire electrical AC plug?
A. Neutral
B. Hot
C. Safety ground
D. The white wire
<number>
Electrical Safety

## Slide 8: T0A03 - What is connected to the green wire in a three-wire electrical AC plug?
A. Neutral
B. Hot
C. Safety ground
D. The white wire
<number>
Electrical Safety

## Slide 9: T0A04 - What is the purpose of a fuse in an electrical circuit?
A. To prevent power supply ripple from damaging a circuit
B. To interrupt power in case of overload
C. To limit current to prevent shocks
D. All of these choices are correct
<number>
Electrical Safety

## Slide 10: T0A04 - What is the purpose of a fuse in an electrical circuit?
A. To prevent power supply ripple from damaging a circuit
B. To interrupt power in case of overload
C. To limit current to prevent shocks
D. All of these choices are correct
<number>
Electrical Safety

## Slide 11: T0A05 - Why is it unwise to install a 20-ampere fuse in the place of a 5-ampere fuse?
A. The larger fuse would be likely to blow because it is rated for higher current
B. The power supply ripple would greatly increase
C. Excessive current could cause a fire
D. All of these choices are correct
<number>
Electrical Safety

## Slide 12: T0A05 - Why is it unwise to install a 20-ampere fuse in the place of a 5-ampere fuse?
A. The larger fuse would be likely to blow because it is rated for higher current
B. The power supply ripple would greatly increase
C. Excessive current could cause a fire
D. All of these choices are correct
<number>
Electrical Safety

## Slide 13: T0A06 - What is a good way to guard against electrical shock at your station?
A. Use three-wire cords and plugs for all AC powered equipment
B. Connect all AC powered station equipment to a common safety ground
C. Use a circuit protected by a ground-fault interrupter
D. All of these choices are correct
<number>
Electrical Safety

## Slide 14: T0A06 - What is a good way to guard against electrical shock at your station?
A. Use three-wire cords and plugs for all AC powered equipment
B. Connect all AC powered station equipment to a common safety ground
C. Use a circuit protected by a ground-fault interrupter
D. All of these
choices are correct
<number>
Electrical Safety

## Slide 15: T0A07 - Which of these precautions should be taken when installing devices for lightning protection in a coaxial cable feed line?
A. Include a parallel bypass switch for each protector so that it can be switched out of the circuit when running high power
B. Include a series switch in the ground line of each protector to prevent RF overload from inadvertently damaging the protector
C. Keep the ground wires from each protector separate and connected to station ground
D. Ground all of the protectors to a common plate which is in turn connected to an external ground
<number>
Electrical Safety

## Slide 16: T0A07 - Which of these precautions should be taken when installing devices for lightning protection in a coaxial cable feed line?
A. Include a parallel bypass switch for each protector so that it can be switched out of the circuit when running high power
B. Include a series switch in the ground line of each protector to prevent RF overload from inadvertently damaging the protector
C. Keep the ground wires from each protector separate and connected to station ground
D. Ground all of the protectors to a common plate which is in turn connected to an external ground
<number>
Electrical Safety

## Slide 17: T0A08 - What safety equipment should always be included in home-built equipment that is powered from 120V AC power circuits?
A. A fuse or circuit breaker in series with the AC hot conductor
B. An AC voltmeter across the incoming power source
C. An inductor in series with the AC power source
D. A capacitor across the AC power source
<number>
Electrical Safety

## Slide 18: T0A08 - What safety equipment should always be included in home-built equipment that is powered from 120V AC power circuits?
A. A fuse or circuit breaker in series with the AC hot conductor
B. An AC voltmeter across the incoming power source
C. An inductor in series with the AC power source
D. A capacitor across the AC power source
<number>
Electrical Safety

## Slide 19: Hydrogen Gas Explosion
<number>
Safety 2010
Notes: <number>
The facility was formerly a large computer/data center with battery room and emergency generators in Sacramento, CA. The company vacated the building, moved out the computer equipment but left the battery backup system behind.
The ventilation for the battery room appeared to be tied to a hydrogen monitoring system (which is pretty common). The Hydrogen sensor was in alarm upon emergency responders arriving at the scene (post-explosion). 911 callers reporting the explosion also reported hearing an alarm for 3 days prior to the explosion. This appears to have been a local alarm as it was not relayed to the Fire Department. Given how slowly batteries generate hydrogen gas, it appears the batteries were charging for a long period of time with no ventilation - the detector was alarming and hydrogen gas continued to build up until it found an ignition source. The best guess is the ignition occurred at or near a grounding strap on the battery racks but in a room full of batteries and electrical equipment, ignition sources are plentiful...especially when considering the sensitivity of hydrogen.
The lesson to pass on is that ventilation is CRITICAL with lead acid batteries. Great care should be taken to insure ventilation is adequate or even better that the batteries can NOT be charged without the ventilation system properly working.

## Slide 20: T0A09 - What kind of hazard is presented by a conventional 12-volt storage battery?
A. It emits ozone which can be harmful to the atmosphere
B. Shock hazard due to high voltage
C. Explosive gas can collect if not properly vented
D. All of these choices are correct
<number>
Electrical Safety

## Slide 21: T0A09 - What kind of hazard is presented by a conventional 12-volt storage battery?
A. It emits ozone which can be harmful to the atmosphere
B. Shock hazard due to high voltage
C. Explosive gas can collect if not properly vented
D. All of these choices are correct
<number>
Electrical Safety

## Slide 22: T0A10 - What can happen if a lead-acid storage battery is charged or discharged too quickly?
A. The battery could overheat and give off flammable gas or explode
B. The voltage can become reversed
C. The memory effect will reduce the capacity of the battery
D. All of these choices are correct
<number>
Electrical Safety

## Slide 23: T0A10 - What can happen if a lead-acid storage battery is charged or discharged too quickly?
A. The battery could overheat and give off flammable gas or explode
B. The voltage can become reversed
C. The memory effect will reduce the capacity of the battery
D. All of these choices are correct
<number>
Electrical Safety

## Slide 24: T0A11 - What kind of hazard might exist in a power supply when it is turned off and disconnected?
A. Static electricity could damage the grounding system
B. Circulating currents inside the transformer might cause damage
C. The fuse might blow if you remove the cover
D. You might receive an electric shock from the charged stored in large capacitors
<number>
Electrical Safety

## Slide 25: T0A11 - What kind of hazard might exist in a power supply when it is turned off and disconnected?
A. Static electricity could damage the grounding system
B. Circulating currents inside the transformer might cause damage
C. The fuse might blow if you remove the cover
D. You might receive an electric shock from the charged stored in large capacitors
<number>
Electrical Safety

## Slide 26: T10B – Antenna safety
tower safety; erecting an antenna support; overhead power lines; installing an antenna
<number>
Electrical Safety

## Slide 27: T0B01 - When should members of a tower work team wear a hard hat and safety glasses?
A. At all times except when climbing the tower
B. At all times except when belted firmly to the tower
C. At all times when any work is being done on the tower
D. Only when the tower exceeds 30 feet in height
<number>
Electrical Safety

## Slide 28: T0B01 - When should members of a tower work team wear a hard hat and safety glasses?
A. At all times except when climbing the tower
B. At all times except when belted firmly to the tower
C. At all times when any work is being done on the tower
D. Only when the tower exceeds 30 feet in height
<number>
Electrical Safety

## Slide 29: T0B02 - What is a good precaution to observe before climbing an antenna tower?
A. Make sure that you wear a grounded wrist strap
B. Remove all tower grounding connections
C. Put on a climbing harness and safety glasses
D. All of the these choices are correct
<number>
Electrical Safety

## Slide 30: T0B02 - What is a good precaution to observe before climbing an antenna tower?
A. Make sure that you wear a grounded wrist strap
B. Remove all tower grounding connections
C. Put on a climbing harness and safety glasses
D. All of the these choices are correct
<number>
Electrical Safety

## Slide 31: T0B03 - Under what circumstances is it safe to climb a tower without a helper or observer?
A. When no electrical work is being performed
B. When no mechanical work is being performed
C. When the work being done is not more than 20 feet above the ground
D. Never
<number>
Electrical Safety

## Slide 32: T0B03 - Under what circumstances is it safe to climb a tower without a helper or observer?
A. When no electrical work is being performed
B. When no mechanical work is being performed
C. When the work being done is not more than 20 feet above the ground
D. Never
<number>
Electrical Safety

## Slide 33: T0B04 - Which of the following is an important safety precaution to observe when putting up an antenna tower?
A. Wear a ground strap connected to your wrist at all times
B. Insulate the base of the tower to avoid lightning strikes
C. Look for and stay clear of any overhead electrical wires
D. All of these choices are correct
<number>
Electrical Safety

## Slide 34: T0B04 - Which of the following is an important safety precaution to observe when putting up an antenna tower?
A. Wear a ground strap connected to your wrist at all times
B. Insulate the base of the tower to avoid lightning strikes
C. Look for and stay clear of any overhead electrical wires
D. All of these choices are correct
<number>
Electrical Safety

## Slide 35: T0B05 - What is the purpose of a gin pole?
A. To temporarily replace guy wires
B. To be used in place of a safety harness
C. To lift tower sections or antennas
D. To provide a temporary ground
<number>
Electrical Safety

## Slide 36: T0B05 - What is the purpose of a gin pole?
A. To temporarily replace guy wires
B. To be used in place of a safety harness
C. To lift tower sections or antennas
D. To provide a temporary ground
<number>
Electrical Safety

## Slide 37: T0B05 - What is the purpose of a gin pole?
A. To temporarily replace guy wires
B. To be used in place of a safety harness
C. To lift tower sections or antennas
D. To provide a temporary ground
<number>
Electrical Safety

## Slide 38
<number>
Safety 2010
Using a Gin Pole
Full body harness

## Slide 39: T0B06 - What is the minimum safe distance from a power line to allow when installing an antenna?
A. Half the width of your property
B. The height of the power line above ground
C. 1/2 wavelength at the operating frequency
D. So that if the antenna falls unexpectedly, no part of it can come closer than 10 feet to the power wires
<number>
Electrical Safety

## Slide 40: T0B06 - What is the minimum safe distance from a power line to allow when installing an antenna?
A. Half the width of your property
B. The height of the power line above ground
C. 1/2 wavelength at the operating frequency
D. So that if the antenna falls unexpectedly, no part of it can come closer than 10 feet to the power wires
<number>
Electrical Safety

## Slide 41: T0B07 - Which of the following is an important safety rule to remember when using a crank-up tower?
A. This type of tower must never be painted
B. This type of tower must never be grounded
C. This type of tower must never be climbed unless it is in the fully retracted position
D. All of these choices are correct
<number>
Electrical Safety

## Slide 42: T0B07 - Which of the following is an important safety rule to remember when using a crank-up tower?
A. This type of tower must never be painted
B. This type of tower must never be grounded
C. This type of tower must never be climbed unless it is in the fully retracted position
D. All of these choices are correct
<number>
Electrical Safety

## Slide 43
<number>
Safety 2014
Crank Up Towers

## Slide 44: T0B08 - What is considered to be a proper grounding method for a tower?
A. A single four-foot ground rod, driven into the ground no more than 12 inches from the base
B. A ferrite-core RF choke connected between the tower and ground
C. Separate eight-foot long ground rods for each tower leg, bonded to the tower and each other
D. A connection between the tower base and a cold water pipe
<number>
Electrical Safety

## Slide 45: T0B08 - What is considered to be a proper grounding method for a tower?
A. A single four-foot ground rod, driven into the ground no more than 12 inches from the base
B. A ferrite-core RF choke connected between the tower and ground
C. Separate eight-foot long ground rods for each tower leg, bonded to the tower and each other
D. A connection between the tower base and a cold water pipe
<number>
Electrical Safety

## Slide 46
<number>
Electrical Safety
Tower Base and Grounding
Ground rods are 8 foot long and bonded together

## Slide 47: T0B09 - Why should you avoid attaching an antenna to a utility pole?
A. The antenna will not work properly because of induced voltages
B. The utility company will charge you an extra monthly fee
C. The antenna could contact high-voltage power wires
D. All of these choices are correct
<number>
Electrical Safety

## Slide 48: T0B09 - Why should you avoid attaching an antenna to a utility pole?
A. The antenna will not work properly because of induced voltages
B. The utility company will charge you an extra monthly fee
C. The antenna could contact high-voltage power wires
D. All of these choices are correct
<number>
Electrical Safety

## Slide 49: T0B10 - Which of the following is true concerning grounding conductors used for lightning protection?
A. Only non-insulated wire must be used
B. Wires must be carefully routed with precise right-angle bends
C. Sharp bends must be avoided
D. Common grounds must be avoided
<number>
Electrical Safety

## Slide 50: T0B10 - Which of the following is true concerning grounding conductors used for lightning protection?
A. Only non-insulated wire must be used
B. Wires must be carefully routed with precise right-angle bends
C. Sharp bends must be avoided
D. Common grounds must be avoided
<number>
Electrical Safety

## Slide 51: T0B11 - Which of the following establishes grounding requirements for an amateur radio tower or antenna?
A. FCC Part 97 Rules
B. Local electrical codes
C. FAA tower lighting regulations
D. Underwriters Laboratories' recommended practices
<number>
Electrical Safety

## Slide 52: T0B11 - Which of the following establishes grounding requirements for an amateur radio tower or antenna?
A. FCC Part 97 Rules
B. Local electrical codes
C. FAA tower lighting regulations
D. Underwriters Laboratories' recommended practices
<number>
Electrical Safety

## Slide 53: T0B12 - Which of the following is good practice when installing ground wires on a tower for lightning protection?
A. Put a loop in the ground connection to prevent water damage to the ground system
B. Make sure that all bends in the ground wires are clean, right angle bends
C. Ensure that connections are short and direct
D. All of these choices are correct
<number>
Electrical Safety

## Slide 54: T0B12 - Which of the following is good practice when installing ground wires on a tower for lightning protection?
A. Put a loop in the ground connection to prevent water damage to the ground system
B. Make sure that all bends in the ground wires are clean, right angle bends
C. Ensure that connections are short and direct
D. All of these choices are correct
<number>
Electrical Safety

## Slide 55: T10C - RF hazards
radiation exposure; proximity to antennas; recognized safe power levels; exposure to others; radiation types; duty cycle
<number>
Electrical Safety

## Slide 56: T0C01 - What type of radiation are VHF and UHF radio signals?
A. Gamma radiation
B. Ionizing radiation
C. Alpha radiation
D. Non-ionizing radiation
<number>
Electrical Safety

## Slide 57: T0C01 - What type of radiation are VHF and UHF radio signals?
A. Gamma radiation
B. Ionizing radiation
C. Alpha radiation
D. Non-ionizing radiation
<number>
Electrical Safety

## Slide 58: T0C02 - Which of the following frequencies has the lowest value for Maximum Permissible Exposure limit?
A. 3.5 MHz
B. 50 MHz
C. 440 MHz
D. 1296 MHz
<number>
Electrical Safety

## Slide 59: T0C02 - Which of the following frequencies has the lowest value for Maximum Permissible Exposure limit?
A. 3.5 MHz
B. 50 MHz
C. 440 MHz
D. 1296 MHz
<number>
Electrical Safety

## Slide 60
<number>
Band (Wavelength) | Transmitter Power (Watts)
160 m | 500
75 m | 500
80 m | 500
40 m | 500
30 m | 425
20 m | 225
17 m | 125
15 m | 100
12 m | 75
10 m | 50
6 - 1.23 m | 50
70 cm | 70
33 cm | 150
23 cm | 200
13 cm and up | 250
Power Thresholds for Routine Evaluation
<number>
Safety 2010
The FCC requires a station RF safety evaluation if these power levels are exceeded
Note power level varies by band because the human body is more sensitive (Specific Absorption Rate or SAR) to some frequencies than others
Notes: <number>
Notice that power levels that trigger a station evaluation vary with frequency
<number>

## Slide 61: Duty Cycle
<number>
Safety 2014
Mode | Duty Cycle
CW Morse telegraphy | 40%
SSB voice | 20%
SSB voice, heavy speech processing | 50%
SSB AFSK | 100%
SSB SSTV | 100%
FM voice or data | 100%
FSK | 100%
AM voice, 50% modulation | 50%
AM voice, 100% modulation | 30%
Duty cycle refers to both the transmit vs. receive time and the average power level during transmission. Because CW has gaps between symbols the average power is less than 100%. SSB power output varies with modulation. FM is full power regardless of modulation.
Notes: <number>

## Slide 62: Time Averaged Exposure Calculations
<number>
G0 - RF Safety
The FCC averages RF exposure times over a 10 and 30 minute periods. These graphs show the same exposure amount whether long, low-level or short, high-level. Lower duty cycle modes cause lower exposures.
Notes: <number>
The vertical axis is power level, with time on the horizontal axis. The shaded areas in the diagrams above represent RF exposure. As power or duty cycle is decreased, exposure time can be increased and maintain a comparable exposure level. Time, field strength, frequency and specific absorption rate (SAR) are critical factors to consider. The body is most sensitive to VHF frequencies (30-300 MHZ). The eyes are particularly sensitive to energy at 1270MHz which can cause cataracts.

## Slide 63: T0C03 - What is the maximum power level that an amateur radio station may use at VHF frequencies before an RF exposure evaluation is required?
A. 1500 watts PEP transmitter output
B. 1 watt forward power
C. 50 watts PEP at the antenna
D. 50 watts PEP reflected power
<number>
Electrical Safety

## Slide 64: T0C03 - What is the maximum power level that an amateur radio station may use at VHF frequencies before an RF exposure evaluation is required?
A. 1500 watts PEP transmitter output
B. 1 watt forward power
C. 50 watts PEP at the antenna
D. 50 watts PEP reflected power
<number>
Electrical Safety

## Slide 65: T0C04 - What factors affect the RF exposure of people near an amateur station antenna?
A. Frequency and power level of the RF field
B. Distance from the antenna to a person
C. Radiation pattern of the antenna
D. All of these choices are correct
<number>
Electrical Safety

## Slide 66: T0C04 - What factors affect the RF exposure of people near an amateur station antenna?
A. Frequency and power level of the RF field
B. Distance from the antenna to a person
C. Radiation pattern of the antenna
D. All of these choices are correct
<number>
Electrical Safety

## Slide 67: T0C05 - Why do exposure limits vary with frequency?
A. Lower frequency RF fields have more energy than higher frequency fields
B. Lower frequency RF fields do not penetrate the human body
C. Higher frequency RF fields are transient in nature
D. The human body absorbs more RF energy at some frequencies than at others
<number>
Electrical Safety

## Slide 68: T0C05 - Why do exposure limits vary with frequency?
A. Lower frequency RF fields have more energy than higher frequency fields
B. Lower frequency RF fields do not penetrate the human body
C. Higher frequency RF fields are transient in nature
D. The human body absorbs more RF energy at some frequencies than at others
<number>
Electrical Safety

## Slide 69: T0C06 - Which of the following is an acceptable method to determine that your station complies with FCC RF exposure regulations?
A. By calculation based on FCC OET Bulletin 65
B. By calculation based on computer modeling
C. By measurement of field strength using calibrated equipment
D. All of these choices are correct
<number>
Electrical Safety

## Slide 70: T0C06 - Which of the following is an acceptable method to determine that your station complies with FCC RF exposure regulations?
A. By calculation based on FCC OET Bulletin 65
B. By calculation based on computer modeling
C. By measurement of field strength using calibrated equipment
D. All of these choices are correct
<number>
Electrical Safety

## Slide 71: T0C07 - What could happen if a person accidentally touched your antenna while you were transmitting?
A. Touching the antenna could cause television interference
B. They might receive a painful RF burn
C. They might develop radiation poisoning
D. All of these choices are correct
<number>
Electrical Safety

## Slide 72: T0C07 - What could happen if a person accidentally touched your antenna while you were transmitting?
A. Touching the antenna could cause television interference
B. They might receive a painful RF burn
C. They might develop radiation poisoning
D. All of these choices are correct
<number>
Electrical Safety

## Slide 73: T0C08 - Which of the following actions might amateur operators take to prevent exposure to RF radiation in excess of FCC-supplied limits?
A. Relocate antennas
B. Relocate the transmitter
C. Increase the duty cycle
D. All of these choices are correct
<number>
Electrical Safety

## Slide 74: T0C08 - Which of the following actions might amateur operators take to prevent exposure to RF radiation in excess of FCC-supplied limits?
A. Relocate antennas
B. Relocate the transmitter
C. Increase the duty cycle
D. All of these choices are correct
<number>
Electrical Safety

## Slide 75: T0C09 - How can you make sure your station stays in compliance with RF safety regulations?
A. By informing the FCC of any changes made in your station
B. By re-evaluating the station whenever an item of equipment is changed
C. By making sure your antennas have low SWR
D. All of these choices are correct
<number>
Electrical Safety

## Slide 76: T0C09 - How can you make sure your station stays in compliance with RF safety regulations?
A. By informing the FCC of any changes made in your station
B. By re-evaluating the station whenever an item of equipment is changed
C. By making sure your antennas have low SWR
D. All of these choices are correct
<number>
Electrical Safety

## Slide 77: T0C10 - Why is duty cycle one of the factors used to determine safe RF radiation exposure levels?
A. It affects the average exposure of people to radiation
B. It affects the peak exposure of people to radiation
C. It takes into account the antenna feed line loss
D. It takes into account the thermal effects of the final amplifier
<number>
Electrical Safety

## Slide 78: T0C10 - Why is duty cycle one of the factors used to determine safe RF radiation exposure levels?
A. It affects the average exposure of people to radiation
B. It affects the peak exposure of people to radiation
C. It takes into account the antenna feed line loss
D. It takes into account the thermal effects of the final amplifier
<number>
Electrical Safety

## Slide 79: T0C11 - What is the definition of duty cycle during the averaging time for RF exposure?
A. The difference between the lowest power output and the highest power output of a transmitter
B. The difference between the PEP and average power output of a transmitter
C. The percentage of time that a transmitter is transmitting
D. The percentage of time that a transmitter is not transmitting
<number>
Electrical Safety

## Slide 80: T0C11 - What is the definition of duty cycle during the averaging time for RF exposure?
A. The difference between the lowest power output and the highest power output of a transmitter
B. The difference between the PEP and average power output of a transmitter
C. The percentage of time that a transmitter is transmitting
D. The percentage of time that a transmitter is not transmitting
<number>
Electrical Safety

## Slide 81: T0C12 - How does RF radiation differ from ionizing radiation (radioactivity)?
A. RF radiation does not have sufficient energy to cause genetic damage
B. RF radiation can only be detected with an RF dosimeter
C. RF radiation is limited in range to a few feet
D. RF radiation is perfectly safe
<number>
Electrical Safety

## Slide 82: T0C12 - How does RF radiation differ from ionizing radiation (radioactivity)?
A. RF radiation does not have sufficient energy to cause genetic damage
B. RF radiation can only be detected with an RF dosimeter
C. RF radiation is limited in range to a few feet
D. RF radiation is perfectly safe
<number>
Electrical Safety

## Slide 83: T0C13 - If the averaging time for exposure is 6 minutes, how much power density is permitted if the signal is present for 3 minutes and absent for 3 minutes rather than being present for the entire 6 minutes?
A. 3 times as much
B. 1/2 as much
C. 2 times as much
D. There is no adjustment allowed for shorter exposure times
<number>
Electrical Safety

## Slide 84: T0C13 - If the averaging time for exposure is 6 minutes, how much power density is permitted if the signal is present for 3 minutes and absent for 3 minutes rather than being present for the entire 6 minutes?
A. 3 times as much
B. 1/2 as much
C. 2 times as much
D. There is no adjustment allowed for shorter exposure times
<number>
Electrical Safety

## Slide 85: End of SUBELEMENT T10
Electrical safety: AC and DC power circuits; antenna installation; RF hazards
<number>
Electrical Safety