## Slide 1: SUBELEMENT T7
Station equipment: common transmitter and receiver problems; antenna measurements; troubleshooting; basic repair and testing
[4 Exam Questions - 4 Groups]
Station Equipment 2014
Notes: Subelement T7 Station Equipment. Technician Training Slides for 2014 Question Pool Good through June 30, 2018 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM, Howard Schultz, W7HS.
<number>

## Slide 2
T7A – Station equipment: receivers; transmitters; transceivers; modulation; transverters; low power and weak signal operation; transmit and receive amplifiers
T7B – Common transmitter and receiver problems: symptoms of overload and overdrive; distortion; causes of interference; interference and consumer electronics; part 15 devices; over and under modulation; RF feedback; off frequency signals; fading and noise; problems with digital communications interfaces
T7C – Antenna measurements and troubleshooting: measuring SWR; dummy loads; coaxial cables; feed line failure modes
T7D – Basic repair and testing: soldering; using basic test instruments; connecting a voltmeter, ammeter, or ohmmeter
<number>
Station Equipment

## Slide 3: Receiver Technology
Current receivers are largely superheterodyne
Superheterodyne receivers convert the receive frequency to lower Intermediate Frequencies (IF) to allow filtering
Multiple conversions makes a more selective receiver
The final stage includes a Detector that extracts the audio from the modulated carrier
A CW/SSB detector is called a Product Detector
An FM detector is called a Discriminator
<number>
Station Equipment

## Slide 4: T7A01 - Which term describes the ability of a receiver to detect the presence of a signal?
A. Linearity
B. Sensitivity
C. Selectivity
D. Total Harmonic Distortion
Station Equipment 2014

## Slide 5: T7A01 - Which term describes the ability of a receiver to detect the presence of a signal?
A. Linearity
B. Sensitivity
C. Selectivity
D. Total Harmonic Distortion
Station Equipment 2014

## Slide 6: T7A02 - What is a transceiver?
A. A type of antenna switch
B. A unit combining the functions of a transmitter and a receiver
C. A component in a repeater which filters out unwanted interference
D. A type of antenna matching network
<number>
Station Equipment

## Slide 7: T7A02 - What is a transceiver?
A. A type of antenna switch
B. A unit combining the functions of a transmitter and a receiver
C. A component in a repeater which filters out unwanted interference
D. A type of antenna matching network
<number>
Station Equipment

## Slide 8: T7A03 - Which of the following is used to convert a radio signal from one frequency to another?
A. Phase splitter
B. Mixer
C. Inverter
D. Amplifier
<number>
Station Equipment

## Slide 9: T7A03 - Which of the following is used to convert a radio signal from one frequency to another?
A. Phase splitter
B. Mixer
C. Inverter
D. Amplifier
<number>
Station Equipment

## Slide 10: T7A04 - Which term describes the ability of a receiver to discriminate between multiple signals?
A. Discrimination ratio
B. Sensitivity
C. Selectivity
D. Harmonic Distortion
<number>
Station Equipment

## Slide 11: T7A04 - Which term describes the ability of a receiver to discriminate between multiple signals?
A. Discrimination ratio
B. Sensitivity
C. Selectivity
D. Harmonic Distortion
<number>
Station Equipment

## Slide 12: T7A05 - What is the name of a circuit that generates a signal of a desired frequency?
A. Reactance modulator
B. Product detector
C. Low-pass filter
D. Oscillator
<number>
Station Equipment

## Slide 13: T7A05 - What is the name of a circuit that generates a signal of a desired frequency?
A. Reactance modulator
B. Product detector
C. Low-pass filter
D. Oscillator
<number>
Station Equipment

## Slide 14: T7A06 - What device takes the output of a low-powered 28 MHz SSB exciter and produces a 222 MHz output signal?
A. High-pass filter
B. Low-pass filter
C. Transverter
D. Phase converter
<number>
Station Equipment

## Slide 15: T7A06 - What device takes the output of a low-powered 28 MHz SSB exciter and produces a 222 MHz output signal?
A. High-pass filter
B. Low-pass filter
C. Transverter
D. Phase converter
<number>
Station Equipment

## Slide 16: T7A07 - What is meant by term “PTT”?
A. Pre-transmission tuning to reduce transmitter harmonic emission
B. Precise tone transmissions used to limit repeater access to only certain signals
C. A primary transformer tuner use to match antennas
D. The push to talk function which switches between receive and transmit
<number>
Station Equipment

## Slide 17: T7A07 - What is meant by term “PTT”?
A. Pre-transmission tuning to reduce transmitter harmonic emission
B. Precise tone transmissions used to limit repeater access to only certain signals
C. A primary transformer tuner use to match antennas
D. The push to talk function which switches between receive and transmit
<number>
Station Equipment

## Slide 18: T7A08 - Which of the following describes combining speech with an RF carrier signal?-
A. Impedance matching
B. Oscillation
C. Modulation
D. Low-pass filtering
<number>
Station Equipment

## Slide 19: T7A08 - Which of the following describes combining speech with an RF carrier signal?-
A. Impedance matching
B. Oscillation
C. Modulation
D. Low-pass filtering
<number>
Station Equipment

## Slide 20: T7A09 - Which of the following devices is most useful for VHF weak-signal communication?
A. A quarter-wave vertical antenna
B. A multi-mode VHF transceiver
C. An omni-directional antenna
D. A mobile VHF FM transceiver
<number>
Station Equipment

## Slide 21: T7A09 - Which of the following devices is most useful for VHF weak-signal communication?
A. A quarter-wave vertical antenna
B. A multi-mode VHF transceiver
C. An omni-directional antenna
D. A mobile VHF FM transceiver
<number>
Station Equipment

## Slide 22: T7A10 - What device increases the low-power output from a handheld transceiver?
A. A voltage divider
B. An RF power amplifier
C. An impedance network
D. All of these choices are correct
<number>
Station Equipment

## Slide 23: T7A10 - What device increases the low-power output from a handheld transceiver?
A. A voltage divider
B. An RF power amplifier
C. An impedance network
D. All of these choices are correct
<number>
Station Equipment

## Slide 24: T7A11 - Where is an RF preamplifier installed?
A. Between the antenna and receiver
B. At the output of the transmitter's power amplifier
C. Between a transmitter and antenna tuner
D. At the receiver's audio output
<number>
Station Equipment

## Slide 25: T7A11 - Where is an RF preamplifier installed?
A. Between the antenna and receiver
B. At the output of the transmitter's power amplifier
C. Between a transmitter and antenna tuner
D. At the receiver's audio output
<number>
Station Equipment

## Slide 26: T7B – Common transmitter and receiver problems:
symptoms of overload and overdrive; distortion; causes of interference; interference and consumer electronics; part 15 devices; over and under modulation; RF feedback; off frequency signals; fading and noise; problems with digital communications interfaces
<number>
Station Equipment

## Slide 27: T7B01 - What can you do if you are told your FM handheld or mobile transceiver is over-deviating?
A. Talk louder into the microphone
B. Let the transceiver cool off
C. Change to a higher power level
D. Talk farther away from the microphone
<number>
Station Equipment

## Slide 28: T7B01 - What can you do if you are told your FM handheld or mobile transceiver is over-deviating?
A. Talk louder into the microphone
B. Let the transceiver cool off
C. Change to a higher power level
D. Talk farther away from the microphone
<number>
Station Equipment

## Slide 29: T7B02 - What would cause a broadcast AM or FM radio to receive an amateur radio transmission unintentionally?
A. The receiver is unable to reject strong signals outside the AM or FM band
B. The microphone gain of the transmitter is turned up too high
C. The audio amplifier of the transmitter is overloaded
D. The deviation of an FM transmitter is set too low
<number>
Station Equipment

## Slide 30: T7B02 - What would cause a broadcast AM or FM radio to receive an amateur radio transmission unintentionally?
A. The receiver is unable to reject strong signals outside the AM or FM band
B. The microphone gain of the transmitter is turned up too high
C. The audio amplifier of the transmitter is overloaded
D. The deviation of an FM transmitter is set too low
<number>
Station Equipment

## Slide 31: T7B03 - Which of the following may be a cause of radio frequency interference?
A. Fundamental overload
B. Harmonics
C. Spurious emissions
D. All of these choices are correct
<number>
Station Equipment

## Slide 32: T7B03 - Which of the following may be a cause of radio frequency interference?
A. Fundamental overload
B. Harmonics
C. Spurious emissions
D. All of these choices are correct
<number>
Station Equipment

## Slide 33: T7B04 - Which of the following is a way to reduce or eliminate interference by an amateur transmitter to a nearby telephone?
A. Put a filter on the amateur transmitter
B. Reduce the microphone gain
C. Reduce the SWR on the transmitter transmission line
D. Put a RF filter on the telephone
<number>
Station Equipment

## Slide 34: T7B04 - Which of the following is a way to reduce or eliminate interference by an amateur transmitter to a nearby telephone?
A. Put a filter on the amateur transmitter
B. Reduce the microphone gain
C. Reduce the SWR on the transmitter transmission line
D. Put a RF filter on the telephone
<number>
Station Equipment

## Slide 35: T7B05 - How can overload of a non-amateur radio or TV receiver by an amateur signal be reduced or eliminated?
A. Block the amateur signal with a filter at the antenna input of the affected receiver
B. Block the interfering signal with a filter on the amateur transmitter
C. Switch the transmitter from FM to SSB
D. Switch the transmitter to a narrow-band mode
<number>
Station Equipment

## Slide 36: T7B05 - How can overload of a non-amateur radio or TV receiver by an amateur signal be reduced or eliminated?
A. Block the amateur signal with a filter at the antenna input of the affected receiver
B. Block the interfering signal with a filter on the amateur transmitter
C. Switch the transmitter from FM to SSB
D. Switch the transmitter to a narrow-band mode
<number>
Station Equipment

## Slide 37: T7B06 - Which of the following actions should you take if a neighbor tells you that your station’s transmissions are interfering with their radio or TV reception?
A. Make sure that your station is functioning properly and that it does not cause interference to your own radio or television when it is tuned to the same channel
B. Immediately turn off your transmitter and contact the nearest FCC office for assistance
C. Tell them that your license gives you the right to transmit and nothing can be done to reduce the interference
D. Install a harmonic doubler on the output of your transmitter and tune it until the interference is eliminated
<number>
Station Equipment

## Slide 38: T7B06 - Which of the following actions should you take if a neighbor tells you that your station’s transmissions are interfering with their radio or TV reception?
A. Make sure that your station is functioning properly and that it does not cause interference to your own radio or television when it is tuned to the same channel
B. Immediately turn off your transmitter and contact the nearest FCC office for assistance
C. Tell them that your license gives you the right to transmit and nothing can be done to reduce the interference
D. Install a harmonic doubler on the output of your transmitter and tune it until the interference is eliminated
<number>
Station Equipment

## Slide 39: T7B07 - Which of the following may be useful in correcting a radio frequency interference problem?
A. Snap-on ferrite chokes
B. Low-pass and high-pass filters
C. Band-reject and band-pass filters
D. All of these choices are correct
<number>
Station Equipment

## Slide 40: T7B07 - Which of the following may be useful in correcting a radio frequency interference problem?
A. Snap-on ferrite chokes
B. Low-pass and high-pass filters
C. Band-reject and band-pass filters
D. All of these choices are correct
<number>
Station Equipment

## Slide 41: T7B08 - What should you do if something in a neighbor’s home is causing harmful interference to your amateur station?
A. Work with your neighbor to identify the offending device
B. Politely inform your neighbor about the rules that prohibit the use of devices which cause interference
C. Check your station and make sure it meets the standards of good amateur practice
D. All of these choices are correct
<number>
Station Equipment

## Slide 42: T7B08 - What should you do if something in a neighbor’s home is causing harmful interference to your amateur station?
A. Work with your neighbor to identify the offending device
B. Politely inform your neighbor about the rules that prohibit the use of devices which cause interference
C. Check your station and make sure it meets the standards of good amateur practice
D. All of these choices are correct
<number>
Station Equipment

## Slide 43: T7B09 - What is a Part 15 device?
A. An unlicensed device that may emit low powered radio signals on frequencies used by a licensed service
B. A type of amateur radio that can legally be used in the citizen’s band
C. A device for long distance communications using special codes sanctioned by the International Amateur Radio Union
D. A type of test set used to determine whether a transmitter is in compliance with FCC regulation 91.15
<number>
Station Equipment

## Slide 44: T7B09 - What is a Part 15 device?
A. An unlicensed device that may emit low powered radio signals on frequencies used by a licensed service
B. A type of amateur radio that can legally be used in the citizen’s band
C. A device for long distance communications using special codes sanctioned by the International Amateur Radio Union
D. A type of test set used to determine whether a transmitter is in compliance with FCC regulation 91.15
<number>
Station Equipment

## Slide 45: T7B10 - What might be the problem if you receive a report that your audio signal through the repeater is distorted or unintelligible?
A. Your transmitter may be slightly off frequency
B. Your batteries may be running low
C. You could be in a bad location
D. All of these choices are correct
<number>
Station Equipment

## Slide 46: T7B10 - What might be the problem if you receive a report that your audio signal through the repeater is distorted or unintelligible?
A. Your transmitter may be slightly off frequency
B. Your batteries may be running low
C. You could be in a bad location
D. All of these choices are correct
<number>
Station Equipment

## Slide 47: T7B11 - What is a symptom of RF feedback in a transmitter or transceiver?
A. Excessive SWR at the antenna connection
B. The transmitter will not stay on the desired frequency
C. Reports of garbled, distorted, or unintelligible transmissions
D. Frequent blowing of power supply fuses
<number>
Station Equipment

## Slide 48: T7B11 - What is a symptom of RF feedback in a transmitter or transceiver?
A. Excessive SWR at the antenna connection
B. The transmitter will not stay on the desired frequency
C. Reports of garbled, distorted, or unintelligible transmissions
D. Frequent blowing of power supply fuses
<number>
Station Equipment

## Slide 49: T7B12 - What might be the first step to resolve cable TV interference from your ham radio transmission?
A. Add a low pass filter to the TV antenna input
B. Add a high pass filter to the TV antenna input
C. Add a preamplifier to the TV antenna input
D. Be sure all TV coaxial connectors are installed properly
<number>
Station Equipment

## Slide 50: T7B12 - What might be the first step to resolve cable TV interference from your ham radio transmission?
A. Add a low pass filter to the TV antenna input
B. Add a high pass filter to the TV antenna input
C. Add a preamplifier to the TV antenna input
D. Be sure all TV coaxial connectors are installed properly
<number>
Station Equipment

## Slide 51: T7C – Antenna measurements and troubleshooting
measuring SWR; dummy loads; coaxial cables; feed line failure modes
<number>
Station Equipment

## Slide 52: Feedlines
Feedlines carry RF signals from the radio to the antenna
Coax, twin lead, ladder or window line are common feedlines
The longer the feedline, the more loss that occurs
Larger feedlines generally have less loss
Loss is caused by RF energy being converted to heat
Feedline impedance must match the radio and antenna for maximum power transfer
Air dielectric in coax is low loss but may allow water entry
Ultraviolet light degrades insulation which may crack and allow water entry
Corrosion from water exposure is the #1 coax killer
<number>
Station Equipment 2014

## Slide 53: Antenna Analyzer and SWR
Antenna analyzers can be used to verify antenna impedance (match). A perfect SWR of 1:1 is ideal but anything less than 2:1 is OK and over 3:1 the antenna should be checked.
SWR is not a performance measurement (dummy loads are perfect at 1:1) but is important to verify proper operation.
<number>
Station Equipment 2014

## Slide 54: Antenna and SWR Analyzers
<number>
Station Equipment 2014

## Slide 55: T7C01 - What is the primary purpose of a dummy load?
A. To prevent the radiation of signals when making tests
B. To prevent over-modulation of your transmitter
C. To improve the radiation from your antenna
D. To improve the signal to noise ratio of your receiver
<number>
Station Equipment

## Slide 56: T7C01 - What is the primary purpose of a dummy load?
A. To prevent the radiation of signals when making tests
B. To prevent over-modulation of your transmitter
C. To improve the radiation from your antenna
D. To improve the signal to noise ratio of your receiver
<number>
Station Equipment

## Slide 57: T7C02 - Which of the following instruments can be used to determine if an antenna is resonant at the desired operating frequency?
A. A VTVM
B. An antenna analyzer
C. A Q meter
D. A frequency counter
<number>
Station Equipment

## Slide 58: T7C02 - Which of the following instruments can be used to determine if an antenna is resonant at the desired operating frequency?
A. A VTVM
B. An antenna analyzer
C. A Q meter
D. A frequency counter
<number>
Station Equipment

## Slide 59: T7C03 - What, in general terms, is standing wave ratio (SWR)?
A. A measure of how well a load is matched to a transmission line
B. The ratio of high to low impedance in a feed line
C. The transmitter efficiency ratio
D. An indication of the quality of your station’s ground connection
<number>
Station Equipment

## Slide 60: T7C03 - What, in general terms, is standing wave ratio (SWR)?
A. A measure of how well a load is matched to a transmission line
B. The ratio of high to low impedance in a feed line
C. The transmitter efficiency ratio
D. An indication of the quality of your station’s ground connection
<number>
Station Equipment

## Slide 61: T7C04 - What reading on an SWR meter indicates a perfect impedance match between the antenna and the feed line?
A. 2 to 1
B. 1 to 3
C. 1 to 1
D. 10 to 1
<number>
Station Equipment

## Slide 62: T7C04 - What reading on an SWR meter indicates a perfect impedance match between the antenna and the feed line?
A. 2 to 1
B. 1 to 3
C. 1 to 1
D. 10 to 1
<number>
Station Equipment

## Slide 63: T7C05 - What is the approximate SWR value above which the protection circuits in most solid-state transmitters begin to reduce transmitter power?
A. 2 to 1
B. 1 to 2
C. 6 to 1
D. 10 to 1
<number>
Station Equipment

## Slide 64: T7C05 - What is the approximate SWR value above which the protection circuits in most solid-state transmitters begin to reduce transmitter power?
A. 2 to 1
B. 1 to 2
C. 6 to 1
D. 10 to 1
<number>
Station Equipment

## Slide 65: T7C06 - What does an SWR reading of 4:1 indicate?
A. Loss of -4dB
B. Good impedance match
C. Gain of +4dB
D. Impedance mismatch
<number>
Station Equipment

## Slide 66: T7C06 - What does an SWR reading of 4:1 indicate?
A. Loss of -4dB
B. Good impedance match
C. Gain of +4dB
D. Impedance mismatch
<number>
Station Equipment

## Slide 67: T7C07 - What happens to power lost in a feed line?
A. It increases the SWR
B. It comes back into your transmitter and could cause damage
C. It is converted into heat
D. It can cause distortion of your signal
<number>
Station Equipment

## Slide 68: T7C07 - What happens to power lost in a feed line?
A. It increases the SWR
B. It comes back into your transmitter and could cause damage
C. It is converted into heat
D. It can cause distortion of your signal
<number>
Station Equipment

## Slide 69: T7C08 - What instrument other than an SWR meter could you use to determine if a feed line and antenna are properly matched?
A. Voltmeter
B. Ohmmeter
C. Iambic pentameter
D. Directional wattmeter
<number>
Station Equipment

## Slide 70: T7C08 - What instrument other than an SWR meter could you use to determine if a feed line and antenna are properly matched?
A. Voltmeter
B. Ohmmeter
C. Iambic pentameter
D. Directional wattmeter
<number>
Station Equipment

## Slide 71: T7C09 - Which of the following is the most common cause for failure of coaxial cables?
A. Moisture contamination
B. Gamma rays
C. The velocity factor exceeds 1.0
D. Overloading
<number>
Station Equipment

## Slide 72: T7C09 - Which of the following is the most common cause for failure of coaxial cables?
A. Moisture contamination
B. Gamma rays
C. The velocity factor exceeds 1.0
D. Overloading
<number>
Station Equipment

## Slide 73: T7C10 - Why should the outer jacket of coaxial cable be resistant to ultraviolet light?
A. Ultraviolet resistant jackets prevent harmonic radiation
B. Ultraviolet light can increase losses in the cable’s jacket
C. Ultraviolet and RF signals can mix together, causing interference
D. Ultraviolet light can damage the jacket and allow water to enter the cable
<number>
Station Equipment

## Slide 74: T7C10 - Why should the outer jacket of coaxial cable be resistant to ultraviolet light?
A. Ultraviolet resistant jackets prevent harmonic radiation
B. Ultraviolet light can increase losses in the cable’s jacket
C. Ultraviolet and RF signals can mix together, causing interference
D. Ultraviolet light can damage the jacket and allow water to enter the cable
<number>
Station Equipment

## Slide 75: T7C11 - What is a disadvantage of air core coaxial cable when compared to foam or solid dielectric types?
A. It has more loss per foot
B. It cannot be used for VHF or UHF antennas
C. It requires special techniques to prevent water absorption
D. It cannot be used at below freezing temperatures
<number>
Station Equipment

## Slide 76: T7C11 - What is a disadvantage of air core coaxial cable when compared to foam or solid dielectric types?
A. It has more loss per foot
B. It cannot be used for VHF or UHF antennas
C. It requires special techniques to prevent water absorption
D. It cannot be used at below freezing temperatures
<number>
Station Equipment

## Slide 77: T7C12 - Which of the following is a common use of coaxial cable?
A. Carrying dc power from a vehicle battery to a mobile radio
B. Carrying RF signals between a radio and antenna
C. Securing masts, tubing, and other cylindrical objects on towers
D. Connecting data signals from a TNC to a computer
<number>
Station Equipment

## Slide 78: T7C12 - Which of the following is a common use of coaxial cable?
A. Carrying dc power from a vehicle battery to a mobile radio
B. Carrying RF signals between a radio and antenna
C. Securing masts, tubing, and other cylindrical objects on towers
D. Connecting data signals from a TNC to a computer
<number>
Station Equipment

## Slide 79: T7C13 - What does a dummy load consist of?
A. A high-gain amplifier and a TR switch
B. A non-inductive resistor and a heat sink
C. A low voltage power supply and a DC relay
D. A 50 ohm reactance used to terminate a transmission line
<number>
Station Equipment

## Slide 80: T7C13 - What does a dummy load consist of?
A. A high-gain amplifier and a TR switch
B. A non-inductive resistor and a heat sink
C. A low voltage power supply and a DC relay
D. A 50 ohm reactance used to terminate a transmission line
<number>
Station Equipment

## Slide 81: T7D – Basic repair and testing
soldering; using basic test instruments; connecting a voltmeter, ammeter, or ohmmeter
<number>
Station Equipment

## Slide 82: T7D01 - Which instrument would you use to measure electric potential or electromotive force?
A. An ammeter
B. A voltmeter
C. A wavemeter
D. An ohmmeter
<number>
Station Equipment

## Slide 83: T7D01 - Which instrument would you use to measure electric potential or electromotive force?
A. An ammeter
B. A voltmeter
C. A wavemeter
D. An ohmmeter
<number>
Station Equipment

## Slide 84: T7D02 - What is the correct way to connect a voltmeter to a circuit?
A. In series with the circuit
B. In parallel with the circuit
C. In quadrature with the circuit
D. In phase with the circuit
<number>
Station Equipment

## Slide 85: T7D02 - What is the correct way to connect a voltmeter to a circuit?
A. In series with the circuit
B. In parallel with the circuit
C. In quadrature with the circuit
D. In phase with the circuit
<number>
Station Equipment

## Slide 86: T7D03 - How is an ammeter usually connected to a circuit?
A. In series with the circuit
B. In parallel with the circuit
C. In quadrature with the circuit
D. In phase with the circuit
<number>
Station Equipment

## Slide 87: T7D03 - How is an ammeter usually connected to a circuit?
A. In series with the circuit
B. In parallel with the circuit
C. In quadrature with the circuit
D. In phase with the circuit
<number>
Station Equipment

## Slide 88: T7D04 - Which instrument is used to measure electric current?
A. An ohmmeter
B. A wavemeter
C. A voltmeter
D. An ammeter
<number>
Station Equipment

## Slide 89: T7D04 - Which instrument is used to measure electric current?
A. An ohmmeter
B. A wavemeter
C. A voltmeter
D. An ammeter
<number>
Station Equipment

## Slide 90: T7D05 - What instrument is used to measure resistance?
A. An oscilloscope
B. A spectrum analyzer
C. A noise bridge
D. An ohmmeter
<number>
Station Equipment

## Slide 91: T7D05 - What instrument is used to measure resistance?
A. An oscilloscope
B. A spectrum analyzer
C. A noise bridge
D. An ohmmeter
<number>
Station Equipment

## Slide 92: T7D06 - Which of the following might damage a multimeter?
A. Measuring a voltage too small for the chosen scale
B. Leaving the meter in the milliamps position overnight
C. Attempting to measure voltage when using the resistance setting
D. Not allowing it to warm up properly
<number>
Station Equipment

## Slide 93: T7D06 - Which of the following might damage a multimeter?
A. Measuring a voltage too small for the chosen scale
B. Leaving the meter in the milliamps position overnight
C. Attempting to measure voltage when using the resistance setting
D. Not allowing it to warm up properly
<number>
Station Equipment

## Slide 94: T7D07 - Which of the following measurements are commonly made using a multimeter?
A. SWR and RF power
B. Signal strength and noise
C. Impedance and reactance
D. Voltage and resistance
<number>
Station Equipment

## Slide 95: T7D07 - Which of the following measurements are commonly made using a multimeter?
A. SWR and RF power
B. Signal strength and noise
C. Impedance and reactance
D. Voltage and resistance
<number>
Station Equipment

## Slide 96: T7D08 - Which of the following types of solder is best for radio and electronic use?
A. Acid-core solder
B. Silver solder
C. Rosin-core solder
D. Aluminum solder
<number>
Station Equipment

## Slide 97: T7D08 - Which of the following types of solder is best for radio and electronic use?
A. Acid-core solder
B. Silver solder
C. Rosin-core solder
D. Aluminum solder
<number>
Station Equipment

## Slide 98: T7D09 - What is the characteristic appearance of a cold solder joint?
A. Dark black spots
B. A bright or shiny surface
C. A grainy or dull surface
D. A greenish tint
<number>
Station Equipment

## Slide 99: T7D09 - What is the characteristic appearance of a cold solder joint?
A. Dark black spots
B. A bright or shiny surface
C. A grainy or dull surface
D. A greenish tint
<number>
Station Equipment

## Slide 100: T7D10 - What is probably happening when an ohmmeter, connected across an unpowered circuit, initially indicates a low resistance and then shows increasing resistance with time?
A. The ohmmeter is defective
B. The circuit contains a large capacitor
C. The circuit contains a large inductor
D. The circuit is a relaxation oscillator
<number>
Station Equipment

## Slide 101: T7D10 - What is probably happening when an ohmmeter, connected across an unpowered circuit, initially indicates a low resistance and then shows increasing resistance with time?
A. The ohmmeter is defective
B. The circuit contains a large capacitor
C. The circuit contains a large inductor
D. The circuit is a relaxation oscillator
<number>
Station Equipment

## Slide 102: T7D11 - Which of the following precautions should be taken when measuring circuit resistance with an ohmmeter?
A. Ensure that the applied voltages are correct
B. Ensure that the circuit is not powered
C. Ensure that the circuit is grounded
D. Ensure that the circuit is operating at the correct frequency
<number>
Station Equipment

## Slide 103: T7D11 - Which of the following precautions should be taken when measuring circuit resistance with an ohmmeter?
A. Ensure that the applied voltages are correct
B. Ensure that the circuit is not powered
C. Ensure that the circuit is grounded
D. Ensure that the circuit is operating at the correct frequency
<number>
Station Equipment

## Slide 104: T7D12 - Which of the following precautions should be taken when measuring high voltages with a voltmeter?
A. Ensure that the voltmeter has very low impedance
B. Ensure that the voltmeter and leads are rated for use at the voltages to be measured
C. Ensure that the circuit is grounded through the voltmeter
D. Ensure that the voltmeter is set to the correct frequency
<number>
Station Equipment

## Slide 105: T7D12 - Which of the following precautions should be taken when measuring high voltages with a voltmeter?
A. Ensure that the voltmeter has very low impedance
B. Ensure that the voltmeter and leads are rated for use at the voltages to be measured
C. Ensure that the circuit is grounded through the voltmeter
D. Ensure that the voltmeter is set to the correct frequency
<number>
Station Equipment

## Slide 106: End of SUBELEMENT T7
Station equipment: common transmitter and receiver problems; antenna measurements; troubleshooting; basic repair and testing
Station Equipment 2014