## Slide 1: SUBELEMENT T6
Electrical components: semiconductors; circuit diagrams; component functions
[4 Exam Questions - 4 Groups]
<number>
Electrical Components 2014
Notes: Subelement T6 Electrical Components. Technician Training Slides for 2014 Question Pool Good through June 30, 2018 Assembled by Washington Ham Trainers, Daniel Stevens KL7WM, Howard Schultz, W7HS.
<number>

## Slide 2
T6A - Electrical components: fixed and variable resistors; capacitors and inductors; fuses; switches; batteries
T6B – Semiconductors: basic principles and applications of solid state devices; diodes and transistors
T6C - Circuit diagrams: schematic symbols
T6D - Component functions: rectification; switches; indicators; power supply components; resonant circuit; shielding; power transformers; integrated circuits
<number>
Electrical Components 2014

## Slide 3: Resistors
<number>
Electrical Components 2014
Resistors oppose the flow of current in a DC (or AC) circuit). Their values are represented with the colored strips or numbers and will vary slightly with temperature.
A variable resistor is called a potentiometer and is often used for volume controls
Notes: <number>

## Slide 4: Capacitors
<number>
Electrical Components 2014
Electrolytic capacitors (polarized)
Ceramic capacitors
Capacitors are conductive plates separated by an insulator and stores energy in an electric field (electrostatically)
Air Variable Capacitor
Notes: <number>

## Slide 5: Inductors
<number>
Electrical Components 2014
Inductors are generally coils of wire that store energy in a magnetic field
Notes: <number>

## Slide 6: Diode
<number>
Electrical Components 2014
  Electronic one-way “valve”, used e.g. in rectifiers
  Mostly made of Si, Ga
  Different types: PN diodes, Schottky
  Electrodes are called anode and cathode with the cathode indicated by a stripe
Notes: <number>

## Slide 7: Transistors
<number>
Electrical Components 2014
Can be used as an electronic switch or amplifier
Comprised of three layers of semiconductor (PNP, NPN)
Generally have three electrodes (emitter, base, collector)
Field Effect Transistors (FET) have source, drain and gate instead
Notes: <number>

## Slide 8: T6A01 - What electrical component is used to oppose the flow of current in a DC circuit?
A. Inductor
B. Resistor
C. Voltmeter
D. Transformer
<number>
Electrical Components 2014

## Slide 9: T6A01 - What electrical component is used to oppose the flow of current in a DC circuit?
A. Inductor
B. Resistor
C. Voltmeter
D. Transformer
<number>
Electrical Components 2014

## Slide 10: T6A02 - What type of component is often used as an adjustable volume control?
A. Fixed resistor
B. Power resistor
C. Potentiometer
D. Transformer
<number>
Electrical Components 2014

## Slide 11: T6A02 - What type of component is often used as an adjustable volume control?
A. Fixed resistor
B. Power resistor
C. Potentiometer
D. Transformer
<number>
Electrical Components 2014

## Slide 12: T6A03 - What electrical parameter is controlled by a potentiometer?
A. Inductance
B. Resistance
C. Capacitance
D. Field strength
<number>
Electrical Components 2014

## Slide 13: T6A03 - What electrical parameter is controlled by a potentiometer?
A. Inductance
B. Resistance
C. Capacitance
D. Field strength
<number>
Electrical Components 2014

## Slide 14: T6A04 - What electrical component stores energy in an electric field?
A. Resistor
B. Capacitor
C. Inductor
D. Diode
<number>
Electrical Components 2014

## Slide 15: T6A04 - What electrical component stores energy in an electric field?
A. Resistor
B. Capacitor
C. Inductor
D. Diode
<number>
Electrical Components 2014

## Slide 16: T6A05 - What type of electrical component consists of two or more conductive surfaces separated by an insulator?
A. Resistor
B. Potentiometer
C. Oscillator
D. Capacitor
<number>
Electrical Components 2014

## Slide 17: T6A05 - What type of electrical component consists of two or more conductive surfaces separated by an insulator?
A. Resistor
B. Potentiometer
C. Oscillator
D. Capacitor
<number>
Electrical Components 2014

## Slide 18: T6A06 - What type of electrical component stores energy in a magnetic field?
A. Resistor
B. Capacitor
C. Inductor
D. Diode
<number>
Electrical Components 2014

## Slide 19: T6A06 - What type of electrical component stores energy in a magnetic field?
A. Resistor
B. Capacitor
C. Inductor
D. Diode
<number>
Electrical Components 2014

## Slide 20: T6A07 - What electrical component is usually composed of a coil of wire?
A. Switch
B. Capacitor
C. Diode
D. Inductor
<number>
Electrical Components 2014

## Slide 21: T6A07 - What electrical component is usually composed of a coil of wire?
A. Switch
B. Capacitor
C. Diode
D. Inductor
<number>
Electrical Components 2014

## Slide 22: T6A08 - What electrical component is used to connect or disconnect electrical circuits?
A. Magnetron
B. Switch
C. Thermistor
D. All of these choices are correct
<number>
Electrical Components 2014

## Slide 23: T6A08 - What electrical component is used to connect or disconnect electrical circuits?
A. Magnetron
B. Switch
C. Thermistor
D. All of these choices are correct
<number>
Electrical Components 2014

## Slide 24: T6A09 - What electrical component is used to protect other circuit components from current overloads?
A. Fuse
B. Capacitor
C. Inductor
D. All of these choices are correct
<number>
Electrical Components 2014

## Slide 25: T6A09 - What electrical component is used to protect other circuit components from current overloads?
A. Fuse
B. Capacitor
C. Inductor
D. All of these choices are correct
<number>
Electrical Components 2014

## Slide 26: T6A10 - Which of the following battery types is rechargeable?
A. Nickel-metal hydride
B. Lithium-ion
C. Lead-acid gel-cell
D. All of these choices are correct
<number>
Electrical Components 2014

## Slide 27: T6A10 - Which of the following battery types is rechargeable?
A. Nickel-metal hydride
B. Lithium-ion
C. Lead-acid gel-cell
D. All of these choices are correct
<number>
Electrical Components 2014

## Slide 28: T6A11 - Which of the following battery types is not rechargeable?
A. Nickel-cadmium
B. Carbon-zinc
C. Lead-acid
D. Lithium-ion
<number>
Electrical Components 2014

## Slide 29: T6A11 - Which of the following battery types is not rechargeable?
A. Nickel-cadmium
B. Carbon-zinc
C. Lead-acid
D. Lithium-ion
<number>
Electrical Components 2014

## Slide 30: T6B – Semiconductors:
basic principles and applications of solid state devices; diodes and transistors
<number>
Electrical Components 2014

## Slide 31: T6B01 - What class of electronic components is capable of using a voltage or current signal to control current flow?
A. Capacitors
B. Inductors
C. Resistors
D. Transistors
<number>
Electrical Components 2014

## Slide 32: T6B01 - What class of electronic components is capable of using a voltage or current signal to control current flow?
A. Capacitors
B. Inductors
C. Resistors
D. Transistors
<number>
Electrical Components 2014

## Slide 33: T6B02 - What electronic component allows current to flow in only one direction?
A. Resistor
B. Fuse
C. Diode
D. Driven Element
<number>
Electrical Components 2014

## Slide 34: T6B02 - What electronic component allows current to flow in only one direction?
A. Resistor
B. Fuse
C. Diode
D. Driven Element
<number>
Electrical Components 2014

## Slide 35: T6B03 - Which of these components can be used as an electronic switch or amplifier?
A. Oscillator
B. Potentiometer
C. Transistor
D. Voltmeter
<number>
Electrical Components 2014

## Slide 36: T6B03 - Which of these components can be used as an electronic switch or amplifier?
A. Oscillator
B. Potentiometer
C. Transistor
D. Voltmeter
<number>
Electrical Components 2014

## Slide 37: T6B04 - Which of the following components can be made of three layers of semiconductor material?
A. Alternator
B. Transistor
C. Triode
D. Pentagrid converter
<number>
Electrical Components 2014

## Slide 38: T6B04 - Which of the following components can be made of three layers of semiconductor material?
A. Alternator
B. Transistor
C. Triode
D. Pentagrid converter
<number>
Electrical Components 2014

## Slide 39: T6B05 - Which of the following electronic components can amplify signals?
A. Transistor
B. Variable resistor
C. Electrolytic capacitor
D. Multi-cell battery
<number>
Electrical Components 2014

## Slide 40: T6B05 - Which of the following electronic components can amplify signals?
A. Transistor
B. Variable resistor
C. Electrolytic capacitor
D. Multi-cell battery
<number>
Electrical Components 2014

## Slide 41: T6B06 - How is the cathode lead of a semiconductor diode usually identified?
A. With the word cathode
B. With a stripe
C. With the letter C
D. All of these choices are correct
<number>
Electrical Components 2014

## Slide 42: T6B06 - How is the cathode lead of a semiconductor diode usually identified?
A. With the word cathode
B. With a stripe
C. With the letter C
D. All of these choices are correct
<number>
Electrical Components 2014

## Slide 43: T6B07 - What does the abbreviation LED stand for?
A. Low Emission Diode
B. Light Emitting Diode
C. Liquid Emission Detector
D. Long Echo Delay
<number>
Electrical Components 2014

## Slide 44: T6B07 - What does the abbreviation LED stand for?
A. Low Emission Diode
B. Light Emitting Diode
C. Liquid Emission Detector
D. Long Echo Delay
<number>
Electrical Components 2014

## Slide 45: T6B08 - What does the abbreviation FET stand for?
A. Field Effect Transistor
B. Fast Electron Transistor
C. Free Electron Transition
D. Field Emission Thickness
<number>
Electrical Components 2014

## Slide 46: T6B08 - What does the abbreviation FET stand for?
A. Field Effect Transistor
B. Fast Electron Transistor
C. Free Electron Transition
D. Field Emission Thickness
<number>
Electrical Components 2014

## Slide 47: T6B09 - What are the names of the two electrodes of a diode?
A. Plus and minus
B. Source and drain
C. Anode and cathode
D. Gate and base
<number>
Electrical Components 2014

## Slide 48: T6B09 - What are the names of the two electrodes of a diode?
A. Plus and minus
B. Source and drain
C. Anode and cathode
D. Gate and base
<number>
Electrical Components 2014

## Slide 49: T6B10 - What are the three electrodes of a PNP or NPN transistor?
A. Emitter, base, and collector
B. Source, gate, and drain
C. Cathode, grid, and plate
D. Cathode, drift cavity, and collector
<number>
Electrical Components 2014

## Slide 50: T6B10 - What are the three electrodes of a PNP or NPN transistor?
A. Emitter, base, and collector
B. Source, gate, and drain
C. Cathode, grid, and plate
D. Cathode, drift cavity, and collector
<number>
Electrical Components 2014

## Slide 51: T6B11 - What at are the three electrodes of a field effect transistor?
A. Emitter, base, and collector
B. Source, gate, and drain
C. Cathode, grid, and plate
D. Cathode, gate, and anode
<number>
Electrical Components 2014

## Slide 52: T6B11 - What at are the three electrodes of a field effect transistor?
A. Emitter, base, and collector
B. Source, gate, and drain
C. Cathode, grid, and plate
D. Cathode, gate, and anode
<number>
Electrical Components 2014

## Slide 53: T6B12 - What is the term that describes a transistor's ability to amplify a signal?
A. Gain
B. Forward resistance
C. Forward voltage drop
D. On resistance
<number>
Electrical Components 2014

## Slide 54: T6B12 - What is the term that describes a transistor's ability to amplify a signal?
A. Gain
B. Forward resistance
C. Forward voltage drop
D. On resistance
<number>
Electrical Components 2014

## Slide 55
T6C - Circuit diagrams; schematic symbols
<number>
Electrical Components 2014

## Slide 56: Schematic Symbols
Resistor |  | Capacitor |  | SPST Switch | 
Variable Resistor |  | Lamp |  | LED | 
Transistor |  | Transformer |  | Antenna | 
Battery |  | Variable Inductor |  |  | 
<number>
Electrical Components 2014

## Slide 57
<number>
Electrical Components 2014

## Slide 58: T6C01 - What is the name for standardized representations of components in an electrical wiring diagram?
A. Electrical depictions
B. Grey sketch
C. Schematic symbols
D. Component callouts
<number>
Electrical Components 2014

## Slide 59: T6C01 - What is the name for standardized representations of components in an electrical wiring diagram?
A. Electrical depictions
B. Grey sketch
C. Schematic symbols
D. Component callouts
<number>
Electrical Components 2014

## Slide 60: T6C02 - What is component 1 in figure T1?
A. Resistor
B. Transistor
C. Battery
D. Connector
<number>
Electrical Components 2014

## Slide 61: T6C02 - What is component 1 in figure T1?
A. Resistor
B. Transistor
C. Battery
D. Connector
<number>
Electrical Components 2014

## Slide 62: T6C03 - What is component 2 in figure T1?
A. Resistor
B. Transistor
C. Indicator lamp
D. Connector
<number>
Electrical Components 2014

## Slide 63: T6C03 - What is component 2 in figure T1?
A. Resistor
B. Transistor
C. Indicator lamp
D. Connector
<number>
Electrical Components 2014

## Slide 64: T6C04 - What is component 3 in figure T1?
A. Resistor
B. Transistor
C. Lamp
D. Ground symbol
<number>
Electrical Components 2014

## Slide 65: T6C04 - What is component 3 in figure T1?
A. Resistor
B. Transistor
C. Lamp
D. Ground symbol
<number>
Electrical Components 2014

## Slide 66: T6C05 - What is component 4 in figure T1?
A. Resistor
B. Transistor
C. Battery
D. Ground symbol
<number>
Electrical Components 2014

## Slide 67: T6C05 - What is component 4 in figure T1?
A. Resistor
B. Transistor
C. Battery
D. Ground symbol
<number>
Electrical Components 2014

## Slide 68: T6C06 - What is component 6 in figure T2?
A. Resistor
B. Capacitor
C. Regulator IC
D. Transistor
<number>
Electrical Components 2014

## Slide 69: T6C06 - What is component 6 in figure T2?
A. Resistor
B. Capacitor
C. Regulator IC
D. Transistor
<number>
Electrical Components 2014

## Slide 70: T6C07 - What is component 8 in figure T2?
A. Resistor
B. Inductor
C. Regulator IC
D. Light emitting diode
<number>
Electrical Components 2014

## Slide 71: T6C07 - What is component 8 in figure T2?
A. Resistor
B. Inductor
C. Regulator IC
D. Light emitting diode
<number>
Electrical Components 2014

## Slide 72: T6C08 - What is component 9 in figure T2?
A. Variable capacitor
B. Variable inductor
C. Variable resistor
D. Variable transformer
<number>
Electrical Components 2014

## Slide 73: T6C08 - What is component 9 in figure T2?
A. Variable capacitor
B. Variable inductor
C. Variable resistor
D. Variable transformer
<number>
Electrical Components 2014

## Slide 74: T6C09 - What is component 4 in figure T2?
A. Variable inductor
B. Double-pole switch
C. Potentiometer
D. Transformer
<number>
Electrical Components 2014

## Slide 75: T6C09 - What is component 4 in figure T2?
A. Variable inductor
B. Double-pole switch
C. Potentiometer
D. Transformer
<number>
Electrical Components 2014

## Slide 76: T6C10 - What is component 3 in figure T3?
A. Connector
B. Meter
C. Variable capacitor
D. Variable inductor
<number>
Electrical Components 2014

## Slide 77: T6C10 - What is component 3 in figure T3?
A. Connector
B. Meter
C. Variable capacitor
D. Variable inductor
<number>
Electrical Components 2014

## Slide 78: T6C11 - What is component 4 in figure T3?
A. Antenna
B. Transmitter
C. Dummy load
D. Ground
<number>
Electrical Components 2014

## Slide 79: T6C11 - What is component 4 in figure T3?
A. Antenna
B. Transmitter
C. Dummy load
D. Ground
<number>
Electrical Components 2014

## Slide 80: T6C12 - What do the symbols on an electrical circuit schematic diagram represent?
A. Electrical components
B. Logic states
C. Digital codes
D. Traffic nodes
<number>
Electrical Components 2014

## Slide 81: T6C12 - What do the symbols on an electrical circuit schematic diagram represent?
A. Electrical components
B. Logic states
C. Digital codes
D. Traffic nodes
<number>
Electrical Components 2014

## Slide 82: T6C13 - Which of the following is accurately represented in electrical circuit schematic diagrams?
A. Wire lengths
B. Physical appearance of components
C. The way components are interconnected
D. All of these choices are correct
<number>
Electrical Components 2014

## Slide 83: T6C13 - Which of the following is accurately represented in electrical circuit schematic diagrams?
A. Wire lengths
B. Physical appearance of components
C. The way components are interconnected
D. All of these choices are correct
<number>
Electrical Components 2014

## Slide 84
<number>
Electrical Components 2014
Simple AM radio

## Slide 85: T6D - Component functions
rectification; switches; indicators; power supply components; resonant circuit; shielding; power transformers; integrated circuits
<number>
Electrical Components 2014

## Slide 86: T6D01 - Which of the following devices or circuits changes an alternating current into a varying direct current signal?
A. Transformer
B. Rectifier
C. Amplifier
D. Reflector
<number>
Electrical Components 2014

## Slide 87: T6D01 - Which of the following devices or circuits changes an alternating current into a varying direct current signal?
A. Transformer
B. Rectifier
C. Amplifier
D. Reflector
<number>
Electrical Components 2014

## Slide 88: T6D02 - What best describes a relay?
A. A switch controlled by an electromagnet
B. A current controlled amplifier
C. An optical sensor
D. A pass transistor
<number>
Electrical Components 2014

## Slide 89: T6D02 - What best describes a relay?
A. A switch controlled by an electromagnet
B. A current controlled amplifier
C. An optical sensor
D. A pass transistor
<number>
Electrical Components 2014

## Slide 90: T6D03 - What type of switch is represented by component 3 in figure T2?
A. Single-pole single-throw
B. Single-pole double-throw
C. Double-pole single-throw
D. Double-pole double-throw
<number>
Electrical Components 2014

## Slide 91: T6D03 - What type of switch is represented by component 3 in figure T2?
A. Single-pole single-throw
B. Single-pole double-throw
C. Double-pole single-throw
D. Double-pole double-throw
<number>
Electrical Components 2014

## Slide 92: T6D04 - Which of the following can be used to display signal strength on a numeric scale?
A. Potentiometer
B. Transistor
C. Meter
D. Relay
<number>
Electrical Components 2014

## Slide 93: T6D04 - Which of the following can be used to display signal strength on a numeric scale?
A. Potentiometer
B. Transistor
C. Meter
D. Relay
<number>
Electrical Components 2014

## Slide 94: T6D05 - What type of circuit controls the amount of voltage from a power supply?
A. Regulator
B. Oscillator
C. Filter
D. Phase inverter
<number>
Electrical Components 2014

## Slide 95: T6D05 - What type of circuit controls the amount of voltage from a power supply?
A. Regulator
B. Oscillator
C. Filter
D. Phase inverter
<number>
Electrical Components 2014

## Slide 96: T6D06 - What component is commonly used to change 120V AC house current to a lower AC voltage for other uses?
A. Variable capacitor
B. Transformer
C. Transistor
D. Diode
<number>
Electrical Components 2014

## Slide 97: T6D06 - What component is commonly used to change 120V AC house current to a lower AC voltage for other uses?
A. Variable capacitor
B. Transformer
C. Transistor
D. Diode
<number>
Electrical Components 2014

## Slide 98: T6D07 - Which of the following is commonly used as a visual indicator?
A. LED
B. FET
C. Zener diode
D. Bipolar transistor
<number>
Electrical Components 2014

## Slide 99: T6D07 - Which of the following is commonly used as a visual indicator?
A. LED
B. FET
C. Zener diode
D. Bipolar transistor
<number>
Electrical Components 2014

## Slide 100: T6D08 - Which of the following is used together with an inductor to make a tuned circuit?
A. Resistor
B. Zener diode
C. Potentiometer
D. Capacitor
<number>
Electrical Components 2014

## Slide 101: T6D08 - Which of the following is used together with an inductor to make a tuned circuit?
A. Resistor
B. Zener diode
C. Potentiometer
D. Capacitor
<number>
Electrical Components 2014

## Slide 102: T6D09 - What is the name of a device that combines several semiconductors and other components into one package?
A. Transducer
B. Multi-pole relay
C. Integrated circuit
D. Transformer
<number>
Electrical Components 2014

## Slide 103: T6D09 - What is the name of a device that combines several semiconductors and other components into one package?
A. Transducer
B. Multi-pole relay
C. Integrated circuit
D. Transformer
<number>
Electrical Components 2014

## Slide 104: T6D10 - What is the function of component 2 in Figure T1?
A. Give off light when current flows through it
B. Supply electrical energy
C. Control the flow of current
D. Convert electrical energy into radio waves
<number>
Electrical Components 2014

## Slide 105: T6D10 - What is the function of component 2 in Figure T1?
A. Give off light when current flows through it
B. Supply electrical energy
C. Control the flow of current
D. Convert electrical energy into radio waves
<number>
Electrical Components 2014

## Slide 106: T6D11 - What is a simple resonant or tuned circuit?
A. An inductor and a capacitor connected in series or parallel to form a filter
B. A type of voltage regulator
C. A resistor circuit used for reducing standing wave ratio
D. A circuit designed to provide high fidelity audio
<number>
Electrical Components 2014

## Slide 107: T6D11 - What is a simple resonant or tuned circuit?
A. An inductor and a capacitor connected in series or parallel to form a filter
B. A type of voltage regulator
C. A resistor circuit used for reducing standing wave ratio
D. A circuit designed to provide high fidelity audio
<number>
Electrical Components 2014

## Slide 108: T6D12 - Which of the following is a common reason to use shielded wire?
A. To decrease the resistance of DC power connections
B. To increase the current carrying capability of the wire
C. To prevent coupling of unwanted signals to or from the wire
D. To couple the wire to other signals
<number>
Electrical Components 2014

## Slide 109: T6D12 - Which of the following is a common reason to use shielded wire?
A. To decrease the resistance of DC power connections
B. To increase the current carrying capability of the wire
C. To prevent coupling of unwanted signals to or from the wire
D. To couple the wire to other signals
<number>
Electrical Components 2014

## Slide 110: Vacuum Tubes
<number>
Electrical Components 2014
Tubes regulate current flow between cathode and plate with a control grid. Their size can also create unwanted capacitances. A screen grid can be added to reduce grid-to-plate capacitance.
Although still used in high power applications (large amplifiers), they have been largely replaced with transistors. The Field Effect Transistor (FET) has characteristics most similar to a tube.

## Slide 111
<number>
Electrical Components 2014
Vacuum Tubes

## Slide 112: G6A07 Which of the following is a reason not to use wire-wound resistors in an RF circuit?
  A. The resistor's tolerance value would not be adequate for such a circuit
  B. The resistor's inductance could make circuit performance unpredictable
  C. The resistor could overheat
  D. The resistor's internal capacitance would detune the circuit
<number>
Electrical Components 2014

## Slide 113: G6A07 Which of the following is a reason not to use wire-wound resistors in an RF circuit?
  A. The resistor's tolerance value would not be adequate for such a circuit
  B. The resistor's inductance could make circuit performance unpredictable
  C. The resistor could overheat
  D. The resistor's internal capacitance would detune the circuit
<number>
Electrical Components 2014

## Slide 114: G6A08 Which of the following describes a thermistor?
  A. A resistor that is resistant to changes in value with temperature variations
  B. A device having a specific change in resistance with temperature variations
  C. A special type of transistor for use at very cold temperatures
  D. A capacitor that changes value with temperature
<number>
Electrical Components 2014

## Slide 115: G6A08 Which of the following describes a thermistor?
  A. A resistor that is resistant to changes in value with temperature variations
  B. A device having a specific change in resistance with temperature variations
  C. A special type of transistor for use at very cold temperatures
  D. A capacitor that changes value with temperature
<number>
Electrical Components 2014

## Slide 116: G6A11 Why would it be important to minimize the mutual inductance between two inductors?
  A. To increase the energy transfer between circuits
  B. To reduce unwanted coupling between circuits
  C. To reduce conducted emissions
  D. To increase the self-resonant frequency of the inductors
<number>
Electrical Components 2014

## Slide 117: G6A11 Why would it be important to minimize the mutual inductance between two inductors?
  A. To increase the energy transfer between circuits
  B. To reduce unwanted coupling between circuits
  C. To reduce conducted emissions
  D. To increase the self-resonant frequency of the inductors
<number>
Electrical Components 2014

## Slide 118: G6B02 What are two major ratings that must not be exceeded for silicon diode rectifiers?
  A. Peak inverse voltage; average forward current
  B. Average power; average voltage
  C. Capacitive reactance; avalanche voltage
  D. Peak load impedance; peak voltage
<number>
Electrical Components 2014

## Slide 119: G6B02 What are two major ratings that must not be exceeded for silicon diode rectifiers?
  A. Peak inverse voltage; average forward current
  B. Average power; average voltage
  C. Capacitive reactance; avalanche voltage
  D. Peak load impedance; peak voltage
<number>
Electrical Components 2014

## Slide 120: Connectors
DE-9 | Serial data | PL-259 | RF, Good to ~150MHz
DIN | Multiconductor audio/control | N | Waterproof RF, Good to ~10GHz
RCA | Audio/ Video | SMA | Small RF, Good to several GHz
<number>
Electrical Components 2014

## Slide 121: End of SUBELEMENT T6
Electrical components: semiconductors; circuit diagrams; component functions
<number>
Electrical Components 2014